Learning Objectives:

At the end of this topic you will be able to;

- recall the conditions under which a thyristor conducts;

- explain the significance of the following terms:

holding current, minimum gate voltage, minimum gate current;

- describe the advantages of using a thyristor to switch a high power load, compared to using a transistor or a relay;

- explain the process of capacitor commutation to switch off a thyristor;

- use given data to design a DC thyristor switching circuit;

- draw the circuit diagram for a phase control circuit, using a

RC network and a diac;

- draw and analyse graphs that show the phase difference between supply voltage and capacitor voltage in RC circuits;

- sketch voltage/time graphs for the waveforms across the capacitor, thyristor and load in a phase control circuit;

- select and use the formula:

= tan-1(R / XC)

to calculate the phase shift between the supply voltage and the voltage across the capacitor.

General Thyristor Characteristics:

The thyristor is a three-terminal device, made from a

semiconducting material. The diagram shows the circuit

symbol and identifies the three terminals.

It is also known as a silicon controlled rectifier, which describes its DC behaviour very well.  It is a special type of diode that allows current to flow only when a control signal is applied to its gate.  Once turned on, the thyristor will not turn off, even after the gate signal has been removed, provided a sufficiently large current flows through the it from anode to cathode..

The conditions needed to make the thyristor conduct, then, are:

- forward bias – the anode more positive than the cathode;

- a sufficiently large pulse of current flowing into the gate;

- a sufficiently large current then flowing from anode to cathode.

A typical arrangement for switching on a thyristor in a DC circuit is shown in the next diagram.

When the switch S is closed, a current IG flows into

the thyristor gate. Providing this current is big enough,

i.e. bigger than a value known as the minimum gate

current, IGT, typically between 0.1 mA and 20mA, the

thyristor will switch on.

Similarly, the voltage applied between the gate and the

cathode, VG, must be greater than a value, called the minimum gate voltage, VGT. This is typically between 0.6V and 1.0V.

The thyristor then latches on, and so a current, IA, flows through the load even when switch S is opened again. However, if this current drops below a minimum value, called the holding current, IH, the thyristor switches off and no more load current flows. Typically, IH is around 10mA.

A resistor, R, is used to protect the thyristor gate from excessive current.

To calculate a suitable value for R, use the minimum values of gate current and voltage to calculate a maximum value for R.

Hence, the boundary values are:

Voltage VR across R = VS – VG0;

Current IR through R = IG0;

Applying the Ohm’s law formula,

maximum value for R = (VS – VG0) / IG0

Exercise 1 (The solutions are given at the end of the topic.)

The circuit diagram shows a 2N5060 thyristor

controlling the current through a load.

The table contains information from the

datasheet for this thyristor:

| Characteristic | Value |
| --- | --- |
| Minimum gate current IGT | 0.2mA |
| Minimum gate voltage VGT | 0.8V |

Use this information to calculate the maximum value for resistor R.

DC Switching Circuit:

Before looking at the switching properties of a thyristor, we look back at the behaviour of a switching circuit, in particular, the power dissipated in the switch.

When the switch is open (off):

current I = 0;

voltage V1 across the switch = VS;

voltage V2 across the load = 0V;

so the power dissipated in the switch = I x V1

= 0 x VS

=  0W.

When the switch is closed (on):

current I = VS / R;

voltage V1 across the switch = 0V;

voltage V2 across the load =  VS;

so the power dissipated in the switch = I x V1 = (VS/R) x 0 = 0W.

In other words, in both the ‘off’ and ‘on’ states, there is no power dissipated in the switch. It does not overheat. It is not damaged.

We have assumed that this is a perfect switch, with infinite resistance when open, and zero resistance when closed, and that it changes instantly from one state to the other!

The power dissipated in the switch is zero throughout, only if the current is zero when there is a voltage across the switch, and the voltage across the switch is zero when a current flows through it. We must avoid any situation where there is both a non-zero current and non-zero voltage across the switch.

Let’s look at the transistor as a switching device in

this context. The transistor behaviour is controlled

by the voltage, VIN, applied to the base.

(More accurately, it is controlled by the current

flowing in the base.)

Typically, when VIN rises to about 0.5V, the

transistor starts to switch on, and conduct

appreciable current. By the time VIN has

reached around 1.0V, the transistor is switched

on fully. This behaviour is shown in the graph.

The problem is the region of the graph between

VIN = 0.5V and VIN = 1.0V. In this region, the

transistor is neither off nor on. It is starting to

conduct, so the current I is growing. It is not

switched on fully, so voltage V1 is not zero.

As a result, the transistor is dissipating power.

It is getting hot!

(The only major weakness for semiconducting materials is that they cannot tolerate high temperatures.)

The ideal switching device is one which moves very rapidly from ‘off’ to ‘on.’

The transistor is not good at this. With very high currents and voltages (high  power,) transistors do not make good switching devices.

Thyristors, on the other hand, make superb high power switching devices. They move extremely quickly from the

forward-blocking state, where the device is

forward-biased, but not conducting, into the

conducting state when it receives a sufficient

gate pulse. As a result, it dissipates very little

power in the process.

In the conducting state, there is a residual

voltage drop of around one volt between anode

and cathode, VAK, so there is still some power

dissipation, which may mean that the device has

to be cooled in some way (by use of a heat sink for example.)

As a switching device, the thyristor has another major advantage over a transistor. It is a self-latching switch. Once the device is switched on, (and passing a current larger than the holding current,) the gate signal can be removed. With a transistor switch, a collector current flows only while the base current is present. Remove the signal from the base and the transistor switches off.

In some ways then, the thyristor behaves like a self-latching relay. However, the thyristor is a solid-state device. It has no moving parts to wear out through friction, unlike the relay. Its switching takes place in microseconds, compared to the tenths of a second that it takes the relay contacts to close.

Like the relay, it is capable of handling high currents.

Capacitor commutation:

Once triggered into the conducting state, the basic thyristor cannot be turned off by signals applied to the gate. (In other devices, such as the GTO (gate-turn-off thyristor, this is not true.) The standard thyristor turns off only when either:

- the anode-cathode current falls below the holding current threshold;

or

the device is reverse-biased – with the anode being less positive than the cathode.

The customary way to switch off a thyristor

in a DC switching circuit is to use capacitor

commutation. The circuit diagram for this is

shown opposite. We are using a supply voltage

of 12V, only to help with the description of

what happens. Any reasonable supply voltage

can be used.

Suppose that we start from the beginning,

with the thyristor switched off. The full supply voltage, VS, sits across the thyristor. In other words, the voltage at point P = +12V. The voltage drop across the load is zero, and no current flows through it.

Switch S2 is open, and so the voltage at Q = VS = +12V.

Next, switch S1 is pressed, sending a pulse of current into the gate. This switches on the thyristor. The voltage at P drops to 0V (nearly) and the supply voltage now appears across the load, causing a current to flow through it. Switch S1 can be released because the thyristor is latched on.

The voltage at Q = +12V still.

The capacitor has a voltage of 0V on its left-hand terminal, and +12V on its right-hand terminal. Put another way, Q sits 12V higher than P.

The significant feature about capacitors is that the voltage drop across them cannot change until charge flows to or from one of the terminals. If we suddenly change the voltage of one terminal, the other one must change by the same amount until there is time for charge to flow to adjust that voltage.

To switch off the thyristor, switch S2 is pressed for an instant. As a result, the voltage at Q falls to 0V. However, there has been no time for charge to move. As a result, Q must still be 12V higher than P. In other words, when the voltage at Q dropped by 12V from 12V to 0V, the capacitor forced the voltage at P down the same amount, from 0V to -12V.

Looking at the thyristor, the anode, connected to P, is now at around -12V, while the cathode is connected to 0V. We have reverse-biased it. It switches off.

In reality, the voltage at P may not reach -12V. That does not matter. All that is needed is that it drops below 0V to reverse-bias the thyristor.

The load usually has a low resistance, and so when the thyristor switches off, a large current flows through the load and onto the left-hand plate of the capacitor. The voltage at P rises quickly to +12V. Similarly, when S2 is released, current flows through the pull-up resistor R2, returning the voltage at Q to +12V.

Exercise 2 (The solutions are given at the end of the topic.)

Here is a DC lamp switching circuit that uses capacitor commutation:

Complete the table to show the effect of the changes made to switches S1 and S2.

| Action | State of thyristor | Voltage at: |
| --- | --- | --- |
| Switch S1 | Switch S2 |  | P | Q |
| Open | Open | Off | 15V | 15V |
| Closed | Open |  |  |  |
| Open | Open |  |  |  |
| Open | Closed |  |  |  |
| Open | Open |  |  |  |

AC Switching Circuit:

The issues in an AC circuit are different. It is not difficult to switch off the thyristor – it becomes reverse-biased during every cycle of the supply, when the current direction reverses!

The problem is to keep turning it on. One way to

do this, called phase control, is shown in the

circuit diagram.

Consider the two parallel limbs of the circuit

separately.

1. Capacitor and variable resistor:

The capacitor is connected to the AC supply through the variable resistor.

It tries to charge up and then discharge

so that the voltage across it, VC, follows

the supply voltage.

When the variable resistor is set to zero,

VC follows the AC supply exactly

(shown in the middle graph.)

When the variable resistor offers some

resistance to the flow of current, the

capacitor is not able to charge and

discharge fast enough, and so a phase

lag is created between VC, and the supply

voltage, VS, ( shown in the bottom graph.)

This phase shift can be specified as an

angle   with value between 00 and 900.

The graphs below show three values of phase angle - 00, 450 and 900.

A phase angle,,  of 00 means that VC, is in phase with the supply voltage, VS.

A phase angle, ,  of 900 means that VC, is zero when VS is a maximum.

2. Thyristor and load:

Now look at the limb of the circuit containing the thyristor and the load.

The gate terminal is connected to the top of the capacitor, and so follows voltage VC. Providing that the thyristor is forward-biased, it will switch on as soon as the voltage across the capacitor, VC, reaches the minimum gate voltage, VGT. It switches off when it becomes reverse-biased.

When switched on, the voltage

across the thyristor, VT,  is

(ideally) 0V, and so all the supply

voltage appears across the load.

When switched off, all the supply

voltage appears across the

thyristor, and so the voltage

across the load, VL, is zero,

and no current flows.

Study the graphs opposite and

compare them with the descriptions

given above.

Calculating the phase shift:

The phase angle can be calculated using the formula:

 = tan-1(R / XC)

where XC = reactance of the capacitor = 1 / 2  f C

Re-arranging this:

tan  = (2  f C R)

For example, given the following phase control circuit:

tan  	= (2 x x 50 x 0.1 x 10-6  x 22 x 103)

= 0.6912

giving:

	= 34.70

Exercise 3 (The solutions are given at the end of

the topic.)

Calculate the phase angle produced in the phase control

circuit shown opposite when the variable resistor is

set to a resistance of 50k.

Improved AC Switching Circuit:

An improved switching arrangement relies on

the properties of a device called a diac.

This behaves rather like a double zener

diode. It does not conduct until the

voltage across it exceeds  a certain level,

known as the breakover voltage. Above this ,

it conducts freely, offering very little

electrical resistance. This behaviour is shown

in the current/voltage graph.

The important thing is that switching occurs

as rapidly as possible, to reduce power

dissipation in the thyristor. The voltage, VC,

across the capacitor rises relatively slowly, as

can be seen in the graphs shown on earlier

pages. Adding a diac, as shown in the circuit

diagram, makes the switch-on sharper.

Other advantages of this arrangement are that it overcomes the variability in switch-on. This is due to two factors. Firstly, these devices are mass-produced, and so there is variability in their operating parameters.

Secondly, the switch-on voltage varies slightly with temperature.

The breakdown voltage of the diac, around 30V, is high enough to mask

any effects due to mass-production and temperature variation.

The graphs show the effect on the

thyristor and the load of using a

30V diac in the triggering circuit.

Practice Exam Questions:

1.			The following circuit shows part of a car security alarm.   S1 and S2 are microswitches attached to the

front doors of the car.   When either door is opened, the attached switch closes.   The siren switches

on, and stays on, if either switch closes.

(a)		The siren is switched off initially.   What is the voltage at point X:

- before either switch is pressed;	[1]

……………………………………………….

- after either switch is pressed?	[1]

……………………………………………….

(b)		The table gives data for the thyristor used in this system.

| Property | Typical value |
| --- | --- |
| Max. forward current | 16A |
| Holding current | 50mA |
| Minimum gate current | 40mA |
| Gate voltage | 1.5V |
| Peak reverse voltage | 200V |

Using relevant data, calculate the

maximum value which resistor R can have in this circuit.	[2]

……………………………………………………………………………………………………..

……………………………………………………………………………………………………..

……………………………………………………………………………………………………..

……………………………………………………………………………………………………..

……………………………………………………………………………………………………..

……………………………………………………………………………………………………..

2.	(a)		In industrial control systems, high power electrical equipment, such as heaters and motors, used to be operated by relays, but are now usually controlled by a thyristor circuit.

Give one advantage of using a thyristor instead of a relay in these applications.	[1]

……………………………………………………………………………………………………..

……………………………………………………………………………………………………..

(b)		The following circuit is used to control the output of a heater.

The thyristor fires when VC , the voltage across the capacitor, reaches the firing voltage shown on the graph.

Use the axes to draw graphs to illustrate the phase relationship between the supply voltage VS, VC , the voltage VT across the thyristor and the voltage VH across the heater.

An outline of the supply voltage waveform is provided to assist you.	[5]

3.	(a)		State two conditions necessary to make a thyristor conduct.	[2]

First condition  ………………………………………………………………………………..

Second condition  ……………………………………………………………………………..

(b)	(i)	The behaviour of a thyristor depends on the signal applied to the gate terminal and the voltage bias

applied between its anode and cathode. The table lists various combinations of these conditions.

Complete the third column of the table to show whether the thyristor will be switched on or off

under each of the conditions shown.	[3]

(ii)	The diagram shows part of a circuit in which a thyristor is used to control a heater.

(i)	Complete the table by adding the values of VH and VT when switch S1 is closed and

then re-opened.   The thyristor is initially switched off.	[3]

| Switch S1 | Voltage VT across thyristor | Voltage VH across heater |
| --- | --- | --- |
| Initially off |  |  |
| Momentarily on |  |  |
| Switched off |  |  |

(ii)	Complete the circuit diagram by adding a switch S2 and other components

needed to turn off the thyristor using capacitor commutation.	[3]

4.			A thyristor is used to control the heat output of a heating element.

Part of the AC control circuit is shown in the next diagram.

(i)	What is the name of component X?   ………………………………………………..	[1]

(ii)	What is the function of component X in this circuit?	[1]

……………………………………………………………………………………………………..

……………………………………………………………………………………………………..

(iii)	Complete the circuit diagram by adding components to allow phase control of the thyristor.	[2]

(iv)	The upper graph shows the AC waveform VT across the thyristor when this phase control is

in place. Use the axes provided to sketch the corresponding AC waveform VH across the heater.   The supply voltage VS is shown as a dotted line.	[2]

Solutions to Exercises:

Exercise 1:

Voltage VR across R = VS – VG0 = 10 – 0.8 = 9.2V;

Current IR through R = IG0 = 0.2mA;

Applying the Ohm’s law formula,

maximum value for R = (VS – VG0) / IG0

= 9.2 / 0.2 = 46k

This is the maximum value for R. Anything bigger would reduce the current below 0.2mA, so choose the next lower value from the E24 series, i.e. 43k.

Exercise 2:

| Action | State of thyristor | Voltage at: |
| --- | --- | --- |
| Switch S1 | Switch S2 |  | P | Q |
| Open | Open | Off | 15V | 15V |
| Closed | Open | On | 0V | 15V |
| Open | Open | On | 0V | 15V |
| Open | Closed | Off | ~ -15V | 0V |
| Open | Open | Off | 15V | 15V |

Exercise 3:

tan  	= (2 x x 50 x 220 x 10-9  x 50 x 103)

= 3.456

giving:

	= 73.90