## Slide 1: PowerPoint 2: Benefits of good design (2)
PowerPoint presentation
3. Construction design principles
3.1 Benefits of good design

## Slide 2: Introduction
In this presentation, we will examine some of the factors that can influence design:
Corporate social responsibility
Vernacular construction
Code for Sustainable Homes
Brownfield versus greenfield sites

## Slide 3: Corporate social responsibility (CSR)
      CSR is valued in the construction industry as a factor that contributes to sustainable business development. Construction enterprises typically develop CSR reports as one way to maintain a positive corporate image.
      Look at these examples.
      Well-designed buildings that improve quality of life and wellbeing.
      Supporting local community groups and educational programmes.
      Giving time and resources to charitable organisations.
      Developing community spaces such as cycle paths and landscaping.
      Offering work experience programmes and supporting apprenticeships.
      Responsible purchasing and minimising waste.

## Slide 4: Vernacular architecture
Vernacular architecture is characterised by its reliance on local needs, its construction materials and the traditions specific to its locality. It is a type of architecture indigenous to a specific time and region, and is not replicated from elsewhere. Historically, vernacular architecture has used the skills and expertise of local builders rather than formally trained architects.

## Slide 5: Code for Sustainable Homes
The Code for Sustainable Homes (2006) was set up to help reduce carbon emissions and create more sustainable homes. It sets out technical requirements plus details of the assessment process.
It requires performance assessment of new dwellings both during the design stage and when construction is complete and measures sustainability against nine categories (shown), giving a final code rating between Levels 1 and 6.
Before 2015 it could be mandated as part of a local authority's development plan. Currently, it is a voluntary code.
Categories | 
1 | Energy and CO2 emissions
2 | Water
3 | Materials
4 | Surface water run-off
5 | Waste
6 | Pollution
7 | Health and wellbeing
8 | Management
9 | Ecology
Notes: For more information and to read the code, go to: 1161997.pdf (publishing.service.gov.uk)

## Slide 6: Brownfield sites – definition
1. vacant
2. derelict
3. contaminated
4. partially occupied or utilised.
A brownfield site is land previously used for industrial or commercial purposes. Often, this land is contaminated with hazardous waste. There are four classes of brownfield sites:
Notes: To see a map of the Brownfield sites in the UK, see: https://cdn.shortpixel.ai/client/q_lossy,ret_img,w_905/https://www.lgafirst.co.uk/wp-content/uploads/2019/04/Brownfield-sites-small-1-905x1024.jpg

## Slide 7: Brownfield sites – advantages and disadvantages
Advantages
Planning permissions easier to obtain because local authority is trying to improve run-down and derelict land within/surrounding existing urban area.
Can stimulate local regeneration – e.g. new shops, business, etc.
Services and infrastructure are normally already in place.
Disadvantages
Contaminated ground is expensive to clear.

## Slide 8: Greenfield sites – definition
Greenfield sites are pieces of land not previously been built on. They are normally agricultural or local amenity land considered for urban development within the green belt.
The green belt we have today was introduced in 1955 by the Minister of Housing. It is designed to stop urban spread into open countryside.
Notes: To see a map of Greenfield sites in the UK, see: https://www.northascot.org.uk/image/greenbelts.jpg

## Slide 9: Greenfield site – advantages and disadvantages
Advantages
Land is normally free from contaminates, and homes can command a premium/high price.
Disadvantages
Government and local authorities have increased restrictions on the development of green belt land to protect wildlife and the countryside.
Planning permissions can be difficult to obtain.
Services and infrastructure need to be provided.
Urban sprawl will result in increased pollution.

## Slide 10
Notes: A Level Geography - Contemporary urban environments case studies

## Slide 11: Potential implications of poor design
reduced sale ability
reduced efficiencies
damage to reputation
poor safety standards including fire and health risks
mould infestation

## Slide 12
Any questions?