## Slide 1: PowerPoint 5: Design process from conception to completion
3. Construction design principles
3.3 Design process from conception to completion

## Slide 2: Project planning – before work begins
Before any building work can start, you need to plan to ensure the work is completed to the clients’ requirements and within the timescale and budgets agreed.
Planning any construction or building services project starts well before any personnel arrive on site, and includes writing Programmes Of Work, method statements and risk assessments. It also includes planning site layouts, and organising suppliers, sub-contractors, welfare facilities, plant and equipment hire – to name a few.
Remember the 6 Ps
Proper Planning and Preparation Prevents Poor Performance

## Slide 3: Site analysis
Before any design is formulated, the proposed site needs to be carefully researched. This involves conducting site analysis in terms of:
size
location
topography (surveying the land and measuring its features e.g. levels)
current and proposed characteristics (existing buildings, trees, other structures)

## Slide 4: Planning approvals – before building begins
Before work starts, you need to know if planning approval is required to construct or demolish a building.
Outline planning: normally the first stage, where a brief description and drawings showing the planned position size, layout and intended use, are submitted. If the local authority approve in principal, full planning permission can then be submitted. This is advisable before commissioning architects and so on to produce full drawings and other details.
Full planning: requires all the necessary plans/drawings relating to the proposed development – including all supporting documentation along with a completed application form and relevant fees.

## Slide 5: National mandatory planning documents
Mandatory National document | Details
Planning Application Form | Can be submitted in paper or online
Combined Ownership Certificates and Agricultural Land Declaration | Certifies that the applicant is the owner and whether the land is in agricultural use
Site location plan | Showing the site outlined in red at a metric scale of 1:1250 or 1:2500 with a north point shown.
Site block plan | Showing site boundaries, other buildings and trees on or adjacent to the site. Drawn to a metric scale of 1:200 or 1:500 with a north point shown.
Design and Access Statement | Short report accompanying and supporting a planning application.
Sustainable Drainage System Proposals (SUDS) | For major applications.
Planning application fee | The appropriate fee should be included

## Slide 6: Local requirements
There are also local requirements which will vary depending upon the local area. Applicants should check their Local Planning Authority (LPA) to determine what other supporting documentation may be required. This could include documents such as:
Community Infrastructure Levy.
Affordable Housing statement.
Contaminated land, ecological, levels, utilities and tree surveys.
Archaeological, sustainability, transport, daylight, flood risk and noise assessments.
Other requirements required as required by the LPA.

## Slide 7: Planning process step by step
The process for applying for planning permission is straightforward and is completed with the local authority planning department.

## Slide 8: Permitted development rights
Homeowners can make certain minor changes to their property without the need to apply for planning permission. These are called ‘permitted development rights. They can vary from one local authority to another but cannot be made in conservation areas or national parks. Examples of permitted developments include small extensions, garages, out buildings, conversion of a garage or roof space.
Before 2008, only 20m2 of new floor space was permitted without planning permission. Now, single or two storey extensions, attic conversions and outbuildings may be permissible.

## Slide 9: Specific planning consents
Listed building consent: this must be sought from the local planning authority before work can begin on any listed building that will affect its appearance.
Conservation area consent: it is a criminal offence to demolish an unlisted building in a conservation area without obtaining planning permission.
Tree consents: some trees outside of conservation areas are protected by a tree preservation order. Special permission must be granted before any work can be done to them.

## Slide 10: Retrospective planning permissions
Any building or structure that has been built without the proper planning approval in place is known as a planning breach and may require submission of a retrospective planning application.
If planning has already been rejected, the council can issue an enforcement notice requiring the building to be demolished or returned to its original form.
Failure to comply with an enforcement notice can lead to prosecution with fines up to £20,000.
Notes: NOTE: £20,000 was the fine at the time of writing in 2021.

## Slide 11: Appeals procedure
If a planning application has been declined, the decision can be appealed. There are three main methods of appealing, depending on the original application.
Written representation: the easiest and cheapest method. Best suited for smaller development projects such as extensions or change of use. It is reviewed by the planning inspectorate, an independent government body.
Hearings: all parties meet to present their own cases to an independent planning inspector who leads on the appeals process. Hearings are best suited for more complicated cases where the benefits/merits need to be discussed.
Public inquiry: most often used when the proposed development is substantial and might impact the local environment – especially if there has been a lot of public opposition.

## Slide 12: Feasibility study – what is looked at?
A feasibility study is carried out in the very early stages of a project. The purpose is to ascertain if the whole project is going to be viable.
Will it meet the needs of the client/customer?
What barriers are in the way?
Is the demand there?
Will it make profit?

## Slide 13: Feasibility study
Technical
Technical feasibility
If the resources are available to deliver the project successfully and if the technical team can meet the requirements of the project.
Economic
Economic feasibility
A cost benefit analysis of the project to ensure it is economically feasible
Operational
Operational feasibility
How well the work will satisfy requirements
Legal
Legal feasibility
Any aspect of the project which may conflict with legal requirements
Time
Scheduling feasibility
How much time the project will take to complete, and whether the schedule will meet the target delivery date

## Slide 14: Wildlife Assessment check
A Wildlife Assessment check is part of the initial survey of any land proposed for development. It looks at all fauna and flora within the boundaries and surrounding areas such as the infrastructure required to access, run and maintain the proposed development.
Development sites can put pressure on a range of habitats that are home to protected and vulnerable species.
Notes: See link below for further information on the planning portal.
https://www.planningportal.co.uk/info/200187/your_responsibilities/39/other_considerations_before_you_start_work/6
For more on construction and wildlife, visit: Construction near protected areas and wildlife - GOV.UK (www.gov.uk)

## Slide 15: Infestation
If Japanese knotweed is found on a proposed building plot, it can affect planning permission. This is because it is classed as an invasive species that can cause damage to buildings.
It is an offence under the Wildlife and Countryside Act 1981 not to declare the presence of knotweed. A strict management plan must be in place to manage and prevent it spreading to nearby properties as part of the planning process.
Japanese knotweed may devalue a property and make it hard to sell because of the structural damage it can cause.

## Slide 16: Sites of Special Scientific Interest (SSSI)
Any land can be designated an SSSI if it has special geological features or is home to rare or endangered species.
This may include grassland, heathland, woodland, open water or wetlands, plus inland rock or coastal areas.
Permission is required to carry out any work within a designated area. Not having permission can result in heavy fine, plus the cost of all remedial work.
Winnats Pass, Derbyshire, is a Site of Special Scientific Interest (SSSI). This limestone valley was once under a tropical sea- the limestone is full of fossils of sea creatures which lived here over 350 million years ago. Rocks and plants are not allowed to be removed from the site.
Notes: For more on SSSIs, visit Natural England: Natural England - GOV.UK (www.gov.uk)

## Slide 17: Utilities and services
All buildings designed to be lived in require basic services – e.g. water, gas/electric, and the removal of waste/sewage.
Modern dwellings have all of these plus telecommunications (broadband). These require careful planning at the design stage to ensure they meet the needs of the proposed development with sufficient capacity to grow/adapt to change. They should also be installed in a coordinated way to minimise costs and disruption.
Water utility network | Gas utility network | Electric utility network | Telecoms utility network
Structural | Structural | Structural | Structural
Water | Gas | Transmission | Fibre
Sewer | Cathodic protection | Distribution | 
Cathodic protection |  |  | 

## Slide 18: Factors affecting design and construction
Buildings of the future will be even more environmentally friendly as non-renewable natural resources become more limited. Renewable energy sources will power and heat homes/businesses. Low carbon materials such as timber, blended cements, compacted fly ash blocks and rammed earth walls, may all be used more.
Insulation and the positing of buildings and windows will play a crucial part in reducing the carbon footprint of future developments.
Increased use of technology will allow more people to work from ‘smart’ homes that monitor and control lighting, heating, communications and security. This means that planning for the installation and upgrading of building services is becoming more important at the very start of the planning/design process.

## Slide 19: What will the homes of the future look like?

## Slide 20: Frontage line and building line – definitions
A frontage line is defined as the line that coincides with the public frontage and gives the minimum plot width. The building line can be the same as the frontage line but is normally stepped back.
The exact positions of each can be found in the working drawings.

## Slide 21: Gantt chart
A Gantt chart (named after its inventor Henry Gantt) lists all tasks needed on the vertical axis and time intervals on the horizontal axis in hours, days or weeks – depending on the size of the project.
Labour plant and equipment can also be shown, allowing for effective planning and ordering of materials.
Designated times for each task are added during the planning process. Actual times taken are recorded during the construction process. This allows for any necessary actions to be implemented, and any changes planned for offsetting the impact of any delays on the overall project.

## Slide 22: Example of a basic Gantt chart

## Slide 23: Critical path analysis (CPA)
CPA is a method used to sequence tasks required to complete a project. It shows:
what must be completed in an orderly sequence, and
what can be completed simultaneously to achieve the planned outcome in a timely manner.

## Slide 24
Any questions?