## Slide 1
Occupational Specialism: Refrigeration Engineering
K1.3 Key requirements of environmental legislation
PowerPoint 1.3

## Slide 2: Objectives
You should be able to:
Recall current environmental legislation.
Explain good practice of achieving zero leaks and ensuring minimal loss.
You might also be able to:
Explain key responsibilities and requirements for environmental legislation.
Explain and justify the phasing out of environmentally damaging refrigerants.

## Slide 3: Introduction
What legal requirements do you have to the environment?
What would you do if someone was maliciously damaging the environment?
What would you do? Who would you inform?
Should you inform anyone?
How can we ensure that we minimise any environmental damage?

## Slide 4: Current legislation in relation to RACHP industry
This is a list of current legislation and regulation. There are of course others, but these are some of the most important:
Environmental Protection Act 1990
Climate Change Act 2008
Control on ozone-depleting substances
F gas regulations
Hazardous Waste (England and Wales) Regulations 2005.

## Slide 5: Environmental Protection Act 2008
Scope: Outlines provisions that promote environmental sustainability and safeguard our planet for future generations.
Key requirements:
Climate change targets
Waste management
Air and water quality
Biodiversity conservation and sustainable development.

## Slide 6: Environmental Protection Act 2008
Establishes the duty of care for handling controlled waste, including waste refrigerants, oils, and contaminated materials.
Section 33
Section 34

## Slide 7: Environmental Protection Act 2008 - Section 33
Section 33 of the Environmental Protection Act 1990 states:
It is Illegal to treat, keep or dispose of controlled waste in a manner likely to cause pollution to the environment or harm to human health.

## Slide 8: Environmental Protection Act 2008 - Section 34
Section 34 of the Environmental Protection Act 1990 states:
That it shall be the duty of any person who imports, produces, carries, keeps, treats or disposes of controlled waste to take all measures applicable to him/her as are reasonable in the circumstances:
To prevent any contravention by any other person of Section 33.
To prevent the escape of the waste from his/her control or that of any other person.

## Slide 9: Environmental Protection Act 2008 - Section 34
Section 34 continued:
On the transfer of waste, to secure:
That the transfer is only to an authorised person or to a person authorised for transport purposes.
That there is transferred such a written description of the waste as will enable other persons to avoid a contravention of that section and to comply with the duty under this subsection as respect to the control of waste.

## Slide 10: Environmental Protection Act 2008 - summary
The Act ensures:
That to release refrigerants to the atmosphere is an offence.
Refrigeration waste requires safe storage, transport, and disposal.
Enforcement actions are supported for pollution incidents (e.g., refrigerant leaks, ammonia spills).
In practice: Refrigerants and associated waste must be treated as hazardous pollutants, and engineers must prevent environmental damage.

## Slide 11: Climate Change Act 2008
Scope: Outlines the UK's commitment to reducing greenhouse gas emissions.
Key provisions: ​
The mandate and setting of carbon budgets.
Annual ranges for the net UK carbon account.
Emission reporting all major greenhouse gases, including carbon dioxide, methane, and fluorinated gases.

## Slide 12: Climate Change Act 2008
It defines essential terms such as:
Carbon budget: Set limits on the total amount of greenhouse gases that can be emitted over a specific period. Influences energy‑efficiency requirements for refrigeration equipment, since energy usage contributes to carbon emissions.
Net UK emissions: Encourages the phase‑down of high‑GWP refrigerants (e.g., older HFCs), pushing industry toward low‑carbon refrigerants such as ammonia, CO₂, hydrocarbons, and low‑GWP HFOs.

## Slide 13: Climate Change Act 2008
Targeted greenhouse gas emissions.
Establishes a clear framework for measuring emissions and setting reduction pathways. The original requirements of the act were to reduce greenhouse gas emissions by at least 80% of the 1990 levels by 2050.
In 2019, more ambitious targets were set, committing the UK to a legally binding ‘net-zero’ target by 2050.
In practice: Refrigeration systems must increasingly use low‑GWP refrigerants and be designed for high efficiency to support national carbon‑reduction targets.

## Slide 14: Ozone Depleting Substances (ODS) Regulation 2015
Scope: Implements the Montreal Protocol, to control the production, use and release of ozone depleting substances.
Key requirements:
You must not use ODS in new equipment or to service existing equipment, unless they are recycled halons for critical uses. You can still use equipment that contains ODS if it is not leaking.
For permitted uses of ODS, the guidance applies to anyone who produces, imports, exports, sells or services ODS or equipment containing ODS, like refrigeration equipment and fire extinguishers.

## Slide 15: Ozone Depleting Substances (ODS) Regulation 2015
You MUST NOT use ODS in new equipment or to service existing equipment, unless they are recycled halons for critical uses.
You can still use equipment that contains ODS if it is not leaking.
The regulation applies to anyone who: produces, imports, exports or sells or services using ODS or equipment containing ODS, like refrigeration equipment.

## Slide 16: Fluorinated Greenhouse Gases Regulations 2015
Scope: The F gas regulation includes measures to reduce the use and emissions of fluorinated greenhouse gases.
Key requirements:
Mandates certified engineers, record keeping, leak checking, storage, use, recovery, transport, and destruction of F gases.
Imposing conditions on the specific uses of F gases.
Imposing conditions establishing quantitative limits for the placing on the market of hydrofluorocarbons (HFCs) and specific products, and equipment containing F gases.

## Slide 17
The latest revision came into force on March 11, 2024.​
A much stricter phase-down plan than the Kigali amendment provided from 2025 onwards.
A total phase-out of virgin HFCs by 2050, with a planned review in 2030.
Stricter GWP limits for specific types of products.​
Products placed on the market before a GWP limit comes into force can continue to be sold, installed, operated and serviced throughout their entire lifetime​​.
F gas regulations – HFC phase down plan

## Slide 18: Hazardous Waste Regulation 2005
Requires:
Proper classification and labelling. Storage in appropriate containers.
Completion of hazardous waste consignment notes.
Use of licensed waste carriers. Disposal at authorised facilities.
In practice: Any removed refrigerant, oil, filters, or contaminated water (e.g., ammonia‑contaminated condensate) must be handled under strict hazardous‑waste controls.

## Slide 19: Environmental regulation and legislation summary
Regulation | Main Focus | Refrigeration Impact
Climate Change Act 2008 | National carbon‑reduction targets. | Push toward low‑GWP refrigerants and efficient systems.
ODS Regulations | Ozone‑depleting substances banned unless specific criteria is met. | No HCFC use; mandatory recovery and safe disposal.
F gas Regulations | Control HFC emissions. | Leak checks, records, certified engineers, phase‑down.
Environmental Protection Act 1990 | Prevent environmental pollution. | Illegal to vent refrigerants; duty of care for waste.
Hazardous Waste Regs 2005 | Safe handling of hazardous waste. | Refrigerants/oils classed as hazardous; strict disposal rules.

## Slide 20
Refrigerant leaks are not acceptable!

## Slide 21
Correct service, maintenance, leak checks and repair practice will significantly reduce refrigerant loss.
System design and installation will also impact on refrigerant loss.
Refrigerant leaks are not acceptable.
Good practice for zero leaks

## Slide 22: Costs of system refrigerant leakage
Increased costs in service, refrigerant, electricity, downtime
Leaking refrigerant
Increases adverse climate change, the “direct” effect
Reduces system efficiency
Increases power consumption
Increases CO2 emissions (at the power station)
Increases adverse climate change, the “indirect” effect

## Slide 23
Leak testing is an essential practice to minimise refrigerant leaks.
The process is simple, select the correct method.
Leak detection spray.
Electronic leak detector.
Fluorescent dye additive.
Fixed leak detection.
Ensure the equipment is regularly maintained and calibrated.
Leak testing

## Slide 24
Method | Effectiveness​ | Compliance
Leak detection spray | Good for pinpointing leak location. | F gas compliant.
Electronic Leak Detector | Good for localizing leaks, essential that sensitivity is 5g/year. | F gas compliant.
Fluorescent Dye additive | An effective leak detector, an additive is injected into the refrigerant, but oil separators remove the additive. | F gas compliant but can void warranties so check with manufacturer.
Fixed Leak Detection | Not effective at pinpointing leak. | F gas compliant for systems with over 500 tonne CO2 equivalent.
Leak testing methods

## Slide 25
Put leak reduction at the top of your list. Reducing the potential for leakage from the outset will have a significant long-term impact.
New systems should last 20+ years.
Modifications to old systems should be brought up to current standards.
Design standards – new systems should be designed to comply with EN378:2016, the IOR Minimisation of Leakage Code of Practice, and the Pressure Equipment Directive (PED).
Design considerations

## Slide 26
Capping valves.
Access to pipework. If you can’t access it, you can’t test it for leaks.
Pipework joints. Use brazed or welded joints wherever possible, minimise the number of joints. Do not use flared joints unless necessary.
Eliminate or reduce vibration and stress.
System register and labelling. New equipment must, by law, be handed over to the customer suitably labelled and with a system register.
Specify service and maintenance requirements.
Installation considerations

## Slide 27: Ensuring minimum loss of refrigerant
When accessing or removing gauge lines from refrigeration systems, it is essential to follow F gas procedures.
To ensure min loss of refrigerant the following procedure on the next slides can be followed.

## Slide 28
Electronic leak detector should be turned on and located close to the port being accessed.
Stem valve cover should be removed, following manufacturers guidelines ensure stem is fully back seated.
Remove access port cap.
Gauge lines should be inspected to ensure gaskets are in good order, replace if damaged or show signs of wear.
Attach gauge line ensuring a good tight seal but not overtightened. Gauge lines should be evacuated to negate the need to purge air from the line.
Mid seat value stem in accordance with manufacturers instructions.
Minimum loss when accessing systems

## Slide 29
Always be hesitant to access a system through a Schrader port.
Schrader valves if damaged can result in loss of refrigerant and personal injury.
Always be vigilant to hissing sounds, oil residue or patches, difficulty in removing the cap or attaching gauge.
The use of a core removal tool with a ball valve should be used to isolate the system.
Remove the faulty valve core and install new core valve so system access and connection can be made.
This process ensures minimal refrigerant loss, maintaining system performance, sustainability, and safety.
Minimum loss when accessing systems

## Slide 30: Summary
You should be able to:
Recall current environmental legislation.
Explain good practice of achieving zero leaks and ensuring minimal loss.
You might also be able to:
Explain key responsibilities and requirements for environmental legislation.
Explain and justify the phasing out of environmentally damaging refrigerants.

## Slide 31
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.