## Slide 1
Occupational Specialism: Air Conditioning Engineering
K1.3 Scientific principles of air conditioning
PowerPoint 1.3i: Use of electricity

## Slide 2
Objectives
By the end of this session, you should be able to:
Understand and apply key electrical principles.
Explain how electricity powers air conditioning.
Describe what electricity does inside the system.
Identify how much electricity air conditioning systems use.
Describe what affects electricity consumption.

## Slide 3
      Starter: What do you already know?
Work in small groups and identify:
How does an air conditioning system use electricity to power its components and create cooling?
Notes: Air conditioning systems rely on electricity to run the parts that move heat, circulate air, and control the cooling process. Electricity doesn’t create the ‘cold’—it powers the components that remove heat from the indoor space.
Main components are:
Compressor
Fans / Blowers
Controls and Sensors e.g. Thermostats, relays, circuit boards, and safety sensors
Expansion and metering devices e.g. electronic expansion valves
Auxiliary components e.g. crankcase heaters, reversing valves (in heat pumps), defrost controls
Key Idea: Electricity powers the motors, fans, and controls that make the refrigeration cycle work. Without electricity, the refrigerant wouldn’t move, air wouldn’t circulate, and no cooling would happen.

## Slide 4
      Electrical principles
Voltage provides the push
Current flows through components
Resistance controls load
Power determines energy use
Capacitance starts motors
Inductance creates motor magnetic fields
AC electricity runs the entire system
Low‑voltage controls manage operation
Relays/Contactors switch power safely
Grounding protects users and equipment

## Slide 5
      Electrical principles
Voltage (V)
Used in: compressor motors, fan motors, contactors, control boards, capacitors.
Current (I)
Used in: compressor start-up, fan motor running current, power consumption measurement.
Resistance (R) – in every electrical load.
Ohms Law:
Voltage (V) = Current (I) x Resistance (R)

## Slide 6
      Electrical principles
Power (W, kW) is how fast electricity is used.
Energy (kWh) is how much electricity is used over time.
Formula: Power (W) = Voltage (V) × Current (A)
Used to measure:
AC energy efficiency
running costs
load calculations.

## Slide 7
      Electrical principles
Capacitors (μF) – store and release electrical energy to start and run motors.
In AC systems:
start capacitors give the compressor an extra boost to start.
run capacitors keep motors running smoothly and efficiently.

## Slide 8
      Electrical principles
Inductance (L)
Air conditioners use induction motors.
These rely on magnetic fields created by AC electricity.
Alternating Current (AC)
Air conditioners run on AC power, which constantly changes direction (50 Hz in the UK).

## Slide 9
      Electrical principles
• Control circuits (Low‑voltage)
Modern air conditioners have electronic control systems that operate at 5V, 12V, or 24V.
Relays and Contactors.
These are electrically controlled switches.
Relays operate small circuits (board → fan motor).
Contactors switch high power (board → compressor).
They are activated by low‑voltage signals but switch high-current loads.

## Slide 10
      Electrical principles
• Earthing/Grounding
Critical for safety.
Protects against:
electric shock
fault currents
static electricity
short circuits.
Most AC faults involving a metal chassis rely on the grounding system to trip the breaker.

## Slide 11
      Powering air conditioning components
Air conditioners use electricity to move heat, not create cold.
Key components:
1. Compressor (Biggest electricity user)
Uses electric power to pump refrigerant around the system.
This is where 70–80% of electricity consumption happens.
2. Fans/Blowers
Indoor fan circulates air inside your home.
Outdoor fan releases the heat absorbed indoors.
3. Controls and Electronics
Thermostat, sensors, control board, etc.
Low electricity use compared to the compressor.

## Slide 12
      What electricity does inside the system
Electricity runs mechanical and electronic components:
Compressor: Pressurises refrigerant → makes it hot → helps move heat outside.
Condenser fan (outdoor): Removes heat from the refrigerant.
Evaporator fan (indoor): Pushes air over cold coils to cool your room.
Reversing valve (in heat pumps): Lets the unit switch between cooling and heating.

## Slide 13
      Electricity usage
Varies widely depending on size and technology.

## Slide 14
      What affects electricity consumption
Size of room vs. size of air conditioning unit.
Outside temperature.
Insulation of the home.
Compressor type (inverter vs. non‑inverter).
Thermostat setting (every 1°C cooler = higher use).

## Slide 15: Summary
You should now be able to:
Understand and apply key electrical principles.
Explain how electricity powers air conditioning.
Describe what electricity does inside the system.
Identify how much electricity air conditioning systems use.
Describe what affects electricity consumption.

## Slide 16
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.