## Slide 1
Occupational Specialism: Plumbing & Heating Engineering
K1.7 Plumbing and heating systems
K1.8 Components used in plumbing and heating systems
K1.10 Types of control systems required for plumbing systems
K1.14 Safety devices applicable to heating systems
Control components (Part 2)

## Slide 2: Starter
Warm-up:
Write down three controls discussed last session. Share with the class.

## Slide 3: Objectives
You should be able to:
Explain advanced controls such as smart stats and pump control units
Identify solenoid valves and bypass valves
You might also be able to:
Understand safety devices such as overheat and control thermostats
Review control siting and manufacturers’ designs
Explore zoning and regulation compliance

## Slide 4: Smart controls
Smart thermostats connect to Wi-Fi and allow remote control via apps. They use algorithms to learn heating patterns and can optimise energy use.
Some integrate weather data and occupancy sensors. They are increasingly common in modern installations.

## Slide 5: Pump control units
Regulate pump operation separately from boiler.
Prevent continuous running.
Reduce wear and energy use.
Often part of advanced heating packages.
Improve system efficiency.
Question: Why should pumps not run continuously when no heating is required?

## Slide 6: Automatic by-pass valves
Automatic by-pass valves (ABVs) protect pumps and boilers when motorised valves close.
They allow a small flow of water to circulate, preventing pressure build-up. ABVs improve efficiency and prolong pump life.
Notes: Stock image unavailable

## Slide 7: Solenoid valves
Electrically operated on/off valves.
Used in specialist heating and DHW systems.
Provide rapid shut-off for safety.
Common in industrial or commercial applications.
Controlled by thermostats or sensors.

## Slide 8: Overheat thermostats
Overheat thermostats cut off boiler operation if water temperature rises above safe levels.
Usually set around 90–100°C.
Provide essential protection against dangerous overheating.

## Slide 9: Control thermostats
Standard thermostats for boiler flow temperature.
Maintain set operating level (typically 70°C but lower on condensing boilers).
Prevent boiler short cycling.
Work with programmers and timers.
Ensure stable system operation.
Question: Why do boilers need both control thermostats and overheat thermostats?

## Slide 10: Tutor demonstration – safety devices
Tutor shows overheat and control thermostats.
Students discuss temperature ranges and why each is critical.

## Slide 11: Student activity – manufacturers’ websites
Students use laptops to explore control options from commonly installed components, such as Honeywell, Drayton, and Nest.
Compare wiring diagrams, features, and installation notes.
Discuss compatibility between manufacturers – note similarities in design and wiring diagrams.

## Slide 12: Location of controls
Thermostats: away from direct heat/draughts (not in a room with a TRV).
Frost stats: unheated spaces.
Pump units: near pipework access.
Smart hubs: central location for Wi-Fi reach.
Correct siting ensures reliable operation.

## Slide 13: Student discussion – control positioning
List some examples of poor siting of room thermostats.
What is the issue with having a wireless room stat on a stand which can be moved around a property?
How will this affect performance?
Why is hand-over an essential part of the commissioning process?

## Slide 14: Zoning requirements – part L
Part L requires heating to be zoned in new dwellings.
Hot water must be separately controlled.
Larger homes need multiple zones with independent thermostats.
Improves comfort and reduces wasted energy.

## Slide 15: BS 7593:2019 – commissioning & water quality
Standard sets requirements for system flushing, chemical treatment, water testing.
Ensures controls operate correctly.
Prevents pump/valve blockages.
Mandatory for compliance.
BS 7593:2019

## Slide 16: Case study – zoned heating
A large house features a S Plan+ system which is split into upstairs and downstairs zones.
Students discuss and list advantages of this control and pipework arrangement.

## Slide 17: Knowledge check 1
What does an automatic by-pass valve do?
Why are overheat thermostats critical?
Give one advantage of smart controls.
What is the typical set point for a control thermostat?
Which regulation requires zoning?

## Slide 18: Knowledge check 1 – answers
Maintains flow when motorised valves close and prolongs pump life if TRVs start to close.
Prevents dangerous overheating.
Remote control, energy savings, learning patterns.
Typically 70°C but lower on condensing boilers
Part L Building Regulations.

## Slide 19: Practical demonstrations
Tutor removes and reinstalls pump.
Students observe isolation, wiring, and sealing.
Pairs of students attempt to sketch simplified wiring for boiler, pump, programmer, thermostat.
Tutor provides feedback.

## Slide 20: Case study – smart control savings
A household installs smart thermostat and achieves 15% lower bills.
Students discuss how savings were achieved.
Students write two advantages and one disadvantage of smart heating controls.

## Slide 21: Knowledge check 2
What is the consequence if an ABV is not installed?
Which controls are used for safety protection?
What document covers water treatment in heating systems?
Give one example of poor thermostat location.
Why do large houses need zones?

## Slide 22: Knowledge check 2 – answers
Pressure build-up when valves shut will put strain on the pump and cause a dead-head scenario (no route for water to return to boiler – TRVs shut).
Overheat thermostats, frost stats.
BS 7593:2019
Above a radiator/in direct sun.
To save energy and improve comfort.

## Slide 23: Student tasks
Option 1: Groups assigned control component (TRV, stat, programmer, ABV, smart control). Prepare 5-minute presentation for next session.
Option 2: Groups look at 2 manufacturers for same control (e.g. Drayton vs Honeywell programmer). Present key differences.

## Slide 24: Final knowledge check
Name one example of a safety control.
What does a pump control unit do?
Why is siting of thermostats important?
What document requires heating zones?
Why are smart controls becoming more popular?

## Slide 25: Final knowledge check – answers
Overheat thermostat, frost stat.
Controls pump independently, prevents waste.
Avoids false readings and inefficiency.
Part L.
Energy savings, convenience, integration.

## Slide 26: Summary
You should be able to:
Explain advanced controls such as smart stats and pump control units
Identify solenoid valves and bypass valves
You might also be able to:
Understand safety devices such as overheat and control thermostats
Review control siting and manufacturers’ designs
Explore zoning and regulation compliance

## Slide 27
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.