## Slide 1
Occupational Specialism: Plumbing & Heating Engineering
K1.7 Plumbing and heating systems
Unvented hot water principles

## Slide 2: Starter
Greeting and warm-up: Why do unvented hot water systems require more safety controls than traditional vented systems?

## Slide 3: Objectives
You should be able to:
Understand requirements of Approved Document G3 Schedule 2
Explain the principles of water under pressure
Compare vented and unvented components
You might also be able to:
Describe how expansion is managed without a cistern
Explain temperature and pressure control in unvented systems
Identify key components in live systems

## Slide 4: Requirements of approved document G3
Approved Document G3 of the Building Regulations sets out strict conditions for unvented systems. Schedule 2 specifies safety devices, discharge arrangements, and installation requirements.
It also details the qualifications required for installers and the need for Building Control notification or Competent Person Scheme certification.
Compliance ensures systems are installed safely, protecting both property and occupants.

## Slide 5: G3 schedule 2 key points
Mandatory safety devices: thermostat, overheat cut-out, TPRV.
Discharge must terminate safely and visibly.
Expansion must be managed by vessel or internal device.
System must be serviceable and accessible.
Installation restricted to G3-qualified engineers.
Question: Why does G3 require visible discharge from a TPRV?

## Slide 6: Principles of water under pressure
Water is almost incompressible, so when heated it expands in volume rather than compressing. In vented systems, this expansion is released into the feed and expansion cistern.
In unvented systems, expansion must be absorbed by an expansion vessel or internal air gap.
This principle underlines why multiple safety devices are required: if expansion is not managed, dangerous pressures can develop rapidly.

## Slide 7: Pressure and expansion basics
Water expands ~4% when heated from 0–100°C.
Expansion cannot be compressed in pipework.
Pressure rises unless managed by vessel or air gap.
Unvented systems rely on pre-charged expansion vessels or internal baffle/pocket.
Relief valves provide last-resort protection.
Question: What happens to pressure in a sealed system if expansion is not managed?

## Slide 8: Comparing vented vs unvented systems
Vented systems use a feed and expansion cistern, open vent pipe, and gravity-fed supply. Unvented systems operate directly from mains pressure, using expansion vessels and relief valves. This means unvented systems deliver stronger, balanced flow but require more advanced safety controls.
The component layout is different: cisterns and vents are removed, replaced by sealed controls and discharge pipework.

## Slide 9: Vented system components
Feed and expansion cistern.
Cold water storage tank.
Open vent pipe.
Gravity-fed hot water cylinder.
Overflow discharge.

## Slide 10: Unvented system components
Expansion vessel or internal bubble top.
Control thermostat.
Overheat thermostat.
PRV and TPRV.
Tundish and discharge pipe.
Question: Which component replaces the open vent pipe in an unvented system?
Notes: Note to tutor: Link to pre-plumbed cylinder example
https://professional.vaillant.co.uk/downloads/product-manuals/unistor-1/unistor-pre-plumbed-boiler-cylinder-domestic-installation-and-maintenance-instructions-1956774.pdf

## Slide 11: Managing expansion without a cistern
In the absence of a feed and expansion cistern, unvented systems use either a separate expansion vessel or an internal air gap. The vessel’s diaphragm compresses to absorb increased volume when water heats. If the vessel fails or loses charge, the PRV will open to release pressure.
This system ensures expansion is managed safely without requiring a cistern.

## Slide 12: Expansion vessel
Pre-charged with air or nitrogen.
Flexible diaphragm absorbs volume increase.
Must be correctly sized for cylinder.
Requires regular re-charging and testing.
Prevents nuisance discharge from valves.

## Slide 13: System layout
Cylinder
Expansion vessel
Safety valve set
Tundish and discharge pipe
Heat source and controls.
Notes: Tutor to source system layout image.

## Slide 14: Temperature control without open vent
In vented systems, excess heat could escape via the open vent pipe. In unvented systems, temperature must be strictly controlled by thermostats. The control thermostat maintains operating temperature (60°C), and an overheat thermostat cuts out at 85–90°C.
If these fail, the TPRV will discharge to prevent dangerous overheating. This closed-loop protection replaces the open vent’s safety function.

## Slide 15: Examining live systems
Observe cylinder in training rig.
Identify expansion vessel, PRV, TPRV, and tundish.
Trace discharge pipe route.
Check thermostat settings.
Compare against schematic diagram.

## Slide 16: Servicing requirements
Unvented hot water cylinders must be serviced annually by a G3-qualified engineer. This includes testing the control and overheat thermostats, operating the PRV and TPRV, recharging the expansion vessel, cleaning the strainer and inspecting the tundish and discharge pipework.
In hard water areas, immersion heaters may need descaling. All checks are recorded in the Benchmark logbook to demonstrate compliance.

## Slide 17: Key service tasks
Test thermostat operation.
Manually operate relief valves.
Recharge expansion vessel.
Check discharge pipe termination.
Record findings in logbook.
Question: Why is it important to operate the relief valves during servicing?

## Slide 18: Common faults
Typical faults include dripping tundishes caused by failed expansion vessels, loss of charge in vessels, or PRV wear.
Thermostat failure can result in overheating, while limescale build-up reduces efficiency and can trigger safety cut-outs. Incorrectly installed discharge pipework may cause water damage or fail to indicate faults properly.
Early fault recognition prevents unsafe conditions.

## Slide 19: Key service tasks
Continuous tundish discharge.
Poor hot water flow.
Excessive noise during heating.
No hot water output.
Discharge pipe incorrectly positioned.
Question: What does continuous water discharge from a tundish usually indicate?

## Slide 20: Legal requirements
Part G3 of the Building Regulations makes it a legal requirement that only trained and certified engineers install or service unvented systems.
Installations must either be notified to Building Control or carried out under a Competent Person Scheme.
Failure to comply can result in fines, invalidated warranties, or enforcement action by authorities.

## Slide 21: Knowledge check 1
What regulation governs unvented hot water systems?
How is expansion managed without a cistern?
Which valve combines pressure and temperature safety?
What replaces the open vent pipe in an unvented system?
Why must discharge be visible?

## Slide 22: Knowledge check 1 – answers
Part G3 of the Building Regulations.
By an expansion vessel or internal air gap.
The Temperature & Pressure Relief Valve (TPRV).
Expansion vessel and safety valves.
To allow faults to be identified quickly.

## Slide 23: Installer responsibilities
Hold G3 qualification.
Notify or self-certify installation.
Follow manufacturer’s instructions.
Record commissioning in Benchmark logbook.
Provide end-user handover.
Question: What document proves an unvented cylinder was correctly commissioned?

## Slide 24: Comparing vented and unvented
Vented: open vent pipe, cistern, gravity feed, lower pressure.
Unvented: sealed, mains-fed, expansion vessel, higher pressure.
Vented: expansion absorbed in cistern.
Unvented: expansion absorbed by vessel and relief valves.
Both require safe management of heat and pressure.
Question: Which system (vented or unvented) delivers balanced high-pressure hot water at all outlets?

## Slide 25: Comparing vented and unvented
Feature | Vented System | Unvented System
Water Supply | Cold water storage cistern in loft | Direct from mains supply
Operating Pressure | Low – gravity fed | High – mains pressure
Expansion Management | Open vent pipe and feed cistern absorb expansion | Expansion vessel or internal air gap absorbs expansion
Contamination Risk | Higher – cistern exposed to dust, insects, freezing | Lower – sealed, cistern not required
Components | Feed & expansion cistern, open vent, hot water cylinder | Cylinder, expansion vessel, PRV, TPRV, tundish
Temperature Safety | Excess heat vented via open vent pipe | Controlled by thermostat, overheat cut-out, TPRV
Installation Complexity | Simpler, less regulatory control | Requires G3-qualified installer, more complex
Performance at Outlets | Variable flow and pressure, often poor shower performance | Balanced mains pressure at all outlets, strong showers
Space Requirements | Requires loft space for cistern | Saves space, no cistern needed
Regulatory Control | General plumbing standards | Strict compliance with Part G3, Building Regulations
Maintenance | Check cistern hygiene, vent pipe, insulation | Annual service of vessel, valves, thermostats, Benchmark logbook

## Slide 26: Tutor demonstration – live system
Show learners a training rig or live cylinder.
Identify expansion vessel, TPRV, PRV, thermostats, tundish.
Demonstrate operation of safety devices.
Trace pipework to discharge termination.
Discuss how expansion is managed.

## Slide 27: Knowledge check 2
What is the role of Approved Document G3 Schedule 2?
What principle explains why water expansion must be managed?
List three key differences between vented and unvented systems.
Why must only G3-qualified engineers install unvented systems?
What is the function of the tundish?

## Slide 28: Knowledge check 2 – answers
Specifies safety, installation, and compliance requirements.
Water is incompressible and expands when heated.
Cistern vs expansion vessel, open vent vs sealed, gravity vs mains pressure.
Legal and safety requirements; prevents unsafe work.
Provides visible discharge and air gap to prevent backflow.

## Slide 29: UVHW - basic diagnostic fault table
Symptom | Likely Cause | Corrective Action
Water discharging through tundish (intermittent) | Expansion vessel losing charge / undersized vessel | Check vessel pressure, recharge to manufacturer’s spec, replace if faulty
Water discharging continuously through tundish | Faulty PRV or TPRV | Test valve operation; clean/replace faulty valve
No hot water | Failed thermostat, immersion heater, or boiler input | Check power/fuse, test thermostat continuity, replace immersion heater if required
Water too hot | Control thermostat failed, overheat stat not tested | Test/replace control thermostat, check overheat stat cut-out
Unusual noises (banging/whistling) | Scale build-up on immersion heater; pressure fluctuations | Descale immersion heater; check incoming mains pressure and fit pressure reducing valve if needed
Poor flow rate at outlets | Blocked strainers/filters; insufficient mains pressure | Clean strainer; measure mains flow/pressure; fit booster if necessary
Discharge pipe not visibly terminating | Incorrect installation | Correct termination point as per G3; ensure visible and safe location
Expansion vessel not functioning | Diaphragm failure or loss of charge | Test with gauge; recharge or replace vessel
End-user unaware of tundish function | Lack of commissioning handover | Provide clear instructions; show role of tundish as warning device

## Slide 30: Summary
You should be able to:
Understand requirements of Approved Document G3 Schedule 2
Explain the principles of water under pressure
Compare vented and unvented components
You might also be able to:
Describe how expansion is managed without a cistern
Explain temperature and pressure control in unvented systems
Identify key components in live systems

## Slide 31
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.