## Slide 1
Occupational Specialism: Plumbing & Heating Engineering
K1.22 Heating systems and the combustion process
Combustion and incomplete combustion in fuels

## Slide 2: Starter
Warm-up:
What three things are required for combustion to take place?

## Slide 3: Objectives
You should be able to:
Describe the combustion process for gas, oil, and solid fuels.
Differentiate between complete and incomplete combustion.
You might also be able to:
Explain the signs and dangers of incomplete combustion.
Understand the combustion triangle and apply it.

## Slide 4: What is combustion?
Combustion is a chemical reaction between a fuel and oxygen that releases heat and light. It's the foundation of heating systems using gas, oil, or solid fuels.
For combustion to occur, the right fuel-to-air ratio must be maintained.
The energy released is used to heat water or air in plumbing systems.

## Slide 5: The combustion triangle
The combustion triangle includes:
Fuel (e.g. gas, oil, solid fuels)
Oxygen (typically from air)
Heat/ignition source.
All three are required. Removing one will stop combustion. This model helps us understand how to manage fire safety and efficient heating.

## Slide 6: Complete combustion
Complete combustion occurs when there is enough oxygen to fully burn the fuel. It produces:
Carbon dioxide (CO₂)
Water (H₂O)
Heat.
This is the most efficient form of combustion. It reduces harmful emissions and maximises energy output.
Question: Why is complete combustion desirable in heating appliances?

## Slide 7: Incomplete combustion
Incomplete combustion happens when there isn’t enough oxygen.
This results in:
Carbon monoxide (CO)
Soot (carbon particles)
Less heat produced.

## Slide 8: Signs of incomplete combustion
Yellow/orange (lazy) flames
Soot build-up on appliances
Condensation near burners
Unusual smells (acrid)
Carbon monoxide alarms triggering.

## Slide 9: Dangers of carbon monoxide (CO)
CO is a colourless, odourless gas. It binds to haemoglobin, reducing oxygen transport in the body.
Symptoms of exposure:
Headaches
Dizziness
Nausea
Death in extreme cases.
Installers must fit alarms and check combustion regularly.
Question: Why is carbon monoxide considered more dangerous than carbon dioxide?

## Slide 10: Combustion in gas-fired appliances
Gas (natural gas or LPG) combusts cleanly when air-to-fuel mix is correct.
Flame colour is an indicator:
Blue flame = complete combustion.
Yellow flame = incomplete combustion.

## Slide 11: Combustion in oil systems
Oil needs atomisation and pre-heating to burn efficiently. Burners must be set for correct spray pattern and air mix. Oil combustion can be less clean than gas and requires regular nozzle cleaning and adjustment.
This is because oil contains more impurities and tends to produce soot and carbon deposits if not properly maintained. Incomplete combustion can also lead to higher emissions of pollutants such as carbon monoxide and particulates.
Routine servicing and correct burner calibration are essential to maintain safe, efficient, and environmentally compliant operation.

## Slide 12: Combustion in solid fuel systems
Solid fuels (coal, wood, pellets) vary in quality. Air must flow through and around the fuel for full combustion. Incomplete combustion is common in poorly vented or damp fuels. Chimney maintenance is critical.
Poor-quality or wet fuel can produce excessive smoke, creosote, and tar deposits, increasing the risk of chimney fires. Regular cleaning ensures safe flue operation and prevents blockages that could lead to dangerous fume buildup.
Efficient burning also relies on proper storage of fuel to keep it dry and ready for use.

## Slide 13
Comparing fuels for combustion
Fuel Type | Complete Products | Risks of Incomplete Combustion
Gas | CO₂ + H₂O | CO, soot
Oil | CO₂ + H₂O | CO, smoke, odour
Solid | CO₂ + H₂O | CO, soot, creosote

## Slide 14: Causes of incomplete combustion
Lack of ventilation
Blocked flue
Incorrect burner setup
Poor maintenance
Fuel contamination
Question: Which boiler type is more likely to suffer incomplete combustion - open flue or room sealed?

## Slide 15: The importance of air supply
Air contains only 21% oxygen. Appliances must have adequate air supply for full combustion. Sealed rooms or tight enclosures can starve appliances of oxygen. Use ventilation grills or air bricks.
Without proper airflow, combustion becomes incomplete, leading to the production of harmful gases like carbon monoxide. This can pose serious health risks and reduce appliance efficiency.
Ensuring a consistent and sufficient air supply is essential for both safety and optimal performance.

## Slide 16: Flue design and maintenance
The flue must remove combustion products effectively. Poorly installed or blocked flues lead to backdraft and incomplete combustion. Regular inspection is a legal and safety requirement.
A properly functioning flue ensures harmful gases like carbon monoxide are safely vented outside.
Blockages from debris, nests, or soot buildup can restrict flow and create hazardous conditions. Annual checks by a qualified professional help maintain safe operation and compliance with regulations.

## Slide 17: Midpoint knowledge check
What are the products of complete combustion?
What colour flame indicates good combustion?
Name two signs of incomplete combustion.
What does the combustion triangle represent?

## Slide 18: Midpoint knowledge check - answers
CO₂ and H₂O
Blue
Yellow flame, soot
Fuel, oxygen, heat

## Slide 19: Burner settings and adjustments
While many modern gas boilers will automatically calibrate their burner settings during commissioning, technicians must:
Set correct air-fuel mix
Clean burner jets
Use flue gas analysers
Check flue draught
Incorrect settings = incomplete combustion risk
Question: What tools are used to confirm combustion is correct?

## Slide 20: Flue gas analyser use
Measures gases in exhaust:
CO
CO₂
Oxygen levels
Flue temperature
Used to assess the efficiency and safety of combustion. Readings outside normal ranges indicate faults.
Notes: Note to tutor: Link to Flue gas analyser - https://www.test-meter.co.uk/testo-310-2ndgen-domestic-flue-gas-analyser

## Slide 21: Appliance maintenance and checks
Regular maintenance prevents incomplete combustion.
Technicians should:
Check flues
Inspect burner heads
Test safety devices
Service according to manufacturer guidelines.

## Slide 22: Installation requirements
Regulations require combustion appliances to be installed with:
Correct flue
Adequate ventilation
Manufacturer's clearances
Alarms for CO where required.

## Slide 23: Case study – CO incident
A gas fire was installed in a sealed room with adequate ventilation. The customer placed cushions over the air vents near the fire to stop the draught during a cold period.
After use repeated use, the occupant reported headaches. Investigation showed elevated CO due to oxygen starvation. CO alarm was absent.
Question: What simple installation steps or advice could have prevented this incident?

## Slide 24: Combustion efficiency and environment
Efficient combustion means:
Less fuel used
Lower emissions
Lower running costs
Greater system reliability.
Installers must aim for clean, complete combustion to meet regulations and protect the environment.

## Slide 25: Combustion regulation overview
Building Regulations Part J (combustion appliances)
Gas Safety (Installation and Use) Regulations
OFTEC/Building Control for oil
HETAS for solid fuels
Compliance ensures safe installation and operation.

## Slide 26: Appliance labelling and ratings
Appliances are rated for combustion efficiency. Labels may show:
Seasonal efficiency
Emissions class (e.g., NOx)
Required air flow.
Check labels during commissioning to confirm compatibility.
Notes: Note to tutor: Link to energy efficiency ratings diagram - https://www.gassafe-bristol.com/boiler-efficiency-ratings-explained/

## Slide 27: Flue types and air supply
Open flue: relies on room air
Balanced flue: uses outside air
Fan-assisted: provides forced draught.
Always check the type as this affects installation and safety design.
Question: Which type of flue is most at risk in a sealed kitchen?

## Slide 28: Combustion in modern appliances
Modern appliances have:
Electronic ignition
Modulating burners
Sealed combustion
High-efficiency flue recovery.
Combustion must be fine-tuned for best results.

## Slide 29: Recap – combustion types
Complete = CO₂ + H₂O + heat
Incomplete = CO + soot + less heat
Good combustion = clean flame, good draught
Poor combustion = danger, inefficiency.

## Slide 30: Final knowledge check
Name the three parts of the combustion triangle.
What are signs of incomplete combustion?
Why is CO dangerous?
How does a flue gas analyser help?
What regulation applies to combustion appliances?

## Slide 31: Midpoint knowledge check - answers
Fuel, oxygen, heat
Yellow flames, soot, condensation
Toxic, odourless gas that displaces oxygen
Measures CO, CO₂, O₂ and temperature
Building Regulations Part J

## Slide 32: Reflection task
Think about a boiler or appliance you've worked with.
Was it set up for complete combustion?
How did you know?

## Slide 33: Useful references
Gas Safety (Installation and Use) Regulations
Building Regulations Part J
HSE Gas Safety Guidance
OFTEC, HETAS resources.

## Slide 34: Summary
You should now be able to:
Identify the combustion process for gas, oil, and solid fuels.
Recognise the signs and causes of incomplete combustion.
You might also be able to:
Use testing equipment to analyse combustion.
Apply safe design practices in combustion systems.

## Slide 35: Extended learning and review
Flue gas analyser simulation walkthrough
Group task: combustion fault diagnosis

## Slide 36
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.