## Slide 1
Occupational Specialism: Plumbing & Heating Engineering
K1.23 Flues/Chimneys in relation to gas and the combustion process
Flue systems and combustion

## Slide 2: Starter
Warm-up:
What is the purpose of a flue in a gas appliance system?

## Slide 3: Objectives
You should be able to:
Identify and describe types of flue systems.
Explain how flues support combustion.
You might also be able to:
Understand components and safe operation of flues.
Perform basic flue inspections in line with industry standards.

## Slide 4: What is a flue system?
A flue system is an essential component in combustion appliance setups. Its primary role is to safely remove the by-products of combustion, such as carbon monoxide, carbon dioxide, and water vapour.
These systems are critical for maintaining indoor air quality and ensuring user safety. A properly designed flue will assist in drawing in air needed for combustion. Without an effective flue, appliances can suffer from incomplete combustion.
The design and installation play a part in its performance. Flues must comply with building and gas safety regulations.

## Slide 5: Operating principles of flues
Removing combustion products
Drawing in combustion air (where applicable)
Maintaining correct draught
Preventing gas leakage
Ensuring safe combustion

## Slide 6: Primary flue
The primary flue is the initial section attached directly to the appliance. It leads combustion products into the wider flue system. Proper sealing and sizing are essential to avoid leakage.
Question: Why is it important that the primary flue is correctly installed and sealed?

## Slide 7: Draught diverter
A draught diverter prevents excessive airflow from disturbing the burner flame. It allows air to mix with combustion gases and maintain safe flow.
It also protects the appliance from downdraught.

## Slide 8: Secondary flue
The secondary flue carries gases away from the draught diverter to the flue terminal. It often includes bends and must be adequately supported and insulated to maintain flow.

## Slide 9: Flue terminal
The terminal is where combustion gases are discharged to open air. It must be positioned away from windows and vents to prevent gas re-entry. Blocked or incorrect terminals can cause backflow of harmful gases. Terminals must be unobstructed and checked during servicing.
Their design depends on appliance type, but function remains the same. Condensing appliances may include drainage points. Nearby structures must be considered during placement.
Question: What could happen if a flue terminal is blocked or incorrectly located?

## Slide 10: Types of flues – overview
Open flue
Room-sealed (balanced flue)
Flueless.
Each has unique features and installation requirements.

## Slide 11: Open flue systems
Open flue systems draw combustion air from the room and use natural draught to expel gases. Adequate ventilation is critical; otherwise, combustion may become unstable.
These systems must not be installed in sealed or poorly ventilated rooms. Regular checks are needed to identify blockages and corrosion.
They are common in older appliances and less common in modern homes. Installers must ensure room vents are clear. Proper clearances are vital to ensure safe operation.

## Slide 12: Room-sealed flues
Use external air for combustion.
Have sealed combustion chambers.
Are safer and more efficient.
Suitable for modern boilers as they greatly reduce risk of CO leakage.

## Slide 13: Flueless systems
Have no external flue.
Rely on room ventilation and catalytic converters.
Must meet strict location and air volume requirements.
Are typically used for small heating appliances.
Question: What are the key safety concerns with flueless systems?

## Slide 14: Flueless systems
In the UK, flueless gas appliances (such as flueless fires and flueless water heaters) are regulated by BS 5440‑2:2009 and Approved Document J of the Building Regulations, which set limits based on net heat input and room volume:
For flueless gas fires in habitable rooms, the maximum is 0.045 kW per m³ of room volume. The room must also be large enough to give at least 22.22 m³ per kW of heat input (net).
The allowable kW depends on the room size. For example, in a 50 m³ room you’d be limited to 50 × 0.045 = 2.25 kW net. In a larger space, you could go higher accordingly.

## Slide 15: Flueless systems
Under The Gas Safety (Installation and Use) Regulations 1998:
Appliances with gross heat input greater than 14 kW must not be installed in a normal room (this includes gas fires, space heaters, or water heaters) (Provision 30).
Converting gross to net (divide by 1.1) yields approximately 12.7 kW net maximum if based purely on that absolute cap.

## Slide 16: Combustion and flue efficiency
An efficient flue supports complete combustion and ensures harmful gases are expelled correctly. If a flue is undersized or blocked, the combustion process can become incomplete, producing dangerous carbon monoxide. A properly sized and routed flue promotes stable burner performance and optimises energy use.
Poor flue performance can lead to appliance lockouts and user complaints. Combustion efficiency is closely linked to flue integrity.
Proper slope and insulation of the flue improves draught performance and reduces condensation risk.

## Slide 17: Material types in flue systems
Common materials used include stainless steel, aluminium, and plastic (for condensing boilers).
These materials must resist heat and corrosion over time. Flue material must be approved for gas use and meet manufacturer standards. Using the wrong material could result in leaks or premature failure.
Condensate must not damage the material. Maintenance and inspection help identify early signs of material degradation.

## Slide 18: Flue route planning
Minimise bends and restrictions.
Maintain correct slope for condensate drainage.
Avoid running through occupied spaces without casing.
Ensure accessibility for inspection and maintenance.

## Slide 19: Importance of flue termination position
The location of a flue terminal is critical to safety. It must be far enough away from windows, doors, and air vents to prevent combustion gases from re-entering a building. Terminal clearance requirements vary depending on appliance type and flue system.
Installers should refer to manufacturer’s guidance and Building Regulations. The terminal must also be located where wind conditions won’t cause downdraught. Failure to follow these rules can result in dangerous CO accumulation inside the property. Positioning affects not just safety but also the efficiency of the flue’s performance.

## Slide 20: Flue positioning
Flue positioning must adhere to BS 5440 Pt. 1
Notes: Note to tutor: Images for this slide can be found here (page 32) - https://www.freeboilermanuals.com/assets/pdf/baxi/Baxi%20800%20Combi%20Installation%20and%20Service%20Manual.pdf

## Slide 21: Inspection tools and tests
Flue gas analysers.
Smoke pellets.
Mirror and torch for internal checks.
Visual inspection camera for inaccessible runs.
Question: What tool would help you check for backdraughts in an older flue?

## Slide 22: Regulations and standards
Regulatory compliance is essential in flue system design and maintenance. Installers must follow Building Regulations Part J and the Gas Safety (Installation and Use) Regulations. Manufacturer instructions always take precedence, particularly regarding flue dimensions and terminal placement.
BS 5440 offers detailed guidance on ventilation and flueing standards for gas appliances. These rules ensure consistent safety and performance across installations.
Compliance is not only a legal obligation but a crucial safety practice. Failing to meet standards can lead to dangerous conditions and liability for installers.

## Slide 23: Case study
A homeowner reported headaches and drowsiness. Investigation revealed a damaged flue pipe in the loft from a suitcase being thrown onto it.
The damage allowed carbon monoxide to enter the property. The boiler was open-flued, and ventilation was inadequate.
Question: How would you resolve this issue?

## Slide 24: Midpoint knowledge check
What are the main types of flue systems?
Why must the flue terminal be properly located?
What material is typically used in condensing boiler flues?
What does BS 5440 cover?
Name one key function of a draught diverter.

## Slide 25: Midpoint knowledge check - answers
Open flue, room-sealed, flueless
To prevent re-entry of combustion gases
Plastic (condensate-resistant)
Flue and ventilation standards
Prevent excess airflow disturbing flame

## Slide 26: Sealing and support of flue joints
All flue joints must be sealed correctly.
Use heat-resistant sealant where required.
Flue runs must be fully supported.
Inadequate support leads to disconnections or sagging.
Support spacing depends on material and route.
Question: What problems might occur if a flue joint becomes loose or unsupported?

## Slide 27: Condensing boilers and flues
Condensing appliances extract more heat from combustion gases, lowering flue temperature. This causes condensation to form in the flue.
Condensing boiler flues must be watertight and installed with a continuous fall toward the boiler or drain. Plastic flue materials are common, but they must be certified for condensing use.
Installers must also manage condensate discharge safely. Blocked condensate traps or pipes can lead to appliance shutdowns.
Notes: Note to tutor: Images for this slide can be found here (page 30) - https://www.freeboilermanuals.com/assets/pdf/baxi/Baxi%20800%20Combi%20Installation%20and%20Service%20Manual.pdf

## Slide 28: CO alarms and monitoring
CO alarms are a vital safety feature near gas appliances.
Not a substitute for proper flue installation.
Must comply with BS EN 50291.
Should be fitted at breathing height.
Occupants should be trained to recognise the alarm.

## Slide 29: Manufacturer instructions – always follow them
Each appliance comes with installation instructions that detail specific flue requirements. These include minimum and maximum flue lengths, permitted bends, and termination locations.
Ignoring these instructions can invalidate warranties and breach legal requirements. The manufacturer’s manual should always be consulted first. It’s part of commissioning and servicing documentation.
Question: What action should be taken if you are servicing an appliance and suspect the flue has been installed incorrectly?

## Slide 30: Horizontal and vertical flues
Flue systems may be installed horizontally or vertically, depending on the appliance and location. Horizontal flues are often used with room-sealed appliances and must be angled slightly upwards to aid gas expulsion.
Vertical flues typically run through roofs and require appropriate flashing and weatherproofing. Vertical systems may experience more downdraught, so terminals must be correctly located.
Each system must comply with BS 5440 and be assessed for safety and effectiveness. Incorrect routing can reduce appliance efficiency and create unsafe conditions.
Notes: Note to tutor: Images for this slide can be found here (page 34) - https://www.freeboilermanuals.com/assets/pdf/baxi/Baxi%20800%20Combi%20Installation%20and%20Service%20Manual.pdf

## Slide 31: Flue inspection during servicing
Inspect for signs of corrosion or leakage.
Check flue support brackets and fixings.
Confirm integrity of seals and joints.
Ensure terminal is unobstructed.
Check condensate drains (if applicable).
Question: What visible signs might indicate that a flue system is not functioning safely?

## Slide 32: Temporary vs. Permanent flues
Temporary flues are used during construction or commissioning but must be replaced before use in occupied spaces.
Permanent flues must be properly installed, tested, and commissioned.
Both types must meet safety standards and not allow leakage. Temporary setups may include testing flues for commercial boilers or open temporary cowls.
Always follow procedures and remove temporary systems after testing.

## Slide 33: Flue guards and protection
Guards prevent debris, birds, or animals from blocking terminals.
Required in areas accessible to the public.
Must not obstruct gas discharge.
Often made from stainless steel or coated metal.
Should be checked annually during servicing.

## Slide 34: Specialist systems – fan-assisted flues
Some appliances use a fan to assist flue gas expulsion. These systems allow longer flue runs and more flexible routing. The fan ensures proper draught is maintained even with bends.
Power must be supplied, and sensors may shut the appliance down if fan operation fails. These systems require specific knowledge during installation and servicing.
Question: Why might a fan-assisted flue be used in a commercial or restricted layout?

## Slide 35: Final knowledge check
Which document will show the suitable location for flue termination for a specific appliance?
What standard governs flue ventilation?
Why is condensate management essential in condensing boilers?
What does a flue terminal guard do?
What issues might fan-assisted flues prevent?

## Slide 36: Final knowledge check – answers
Manufacturer's instructions
BS 5440
Prevents flue blockage and appliance shutdown
Stops birds, debris, and accidental blockage
Poor draught, excess bends, long flue runs

## Slide 37: Summary
You should now be able to:
Identify key components in flue systems.
Describe safe flue operation for different types.
Understand the role of flues in combustion safety.
You might also be able to:
Perform basic flue system inspections.
Assess compliance against regulations.
Recommend improvements for poor installations.

## Slide 38: Reflection task
Why is flue system design considered just as important as the appliance itself in ensuring occupant safety?
Summarise the session and 5 key points you will take away from it.
Share your points with your peers.

## Slide 39
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.