## Slide 1
Occupational Specialism: Plumbing & Heating Engineering
K1.34 Potential impact of installation activities
Potential impacts of installation activities on customer essential services

## Slide 2: Starter
Warm-up:
Can you think of any time when an installation or building service activity affected your home or school?
What essential service was impacted, and how was it resolved?
Have you ever experienced a planned water outage, gas service disruption, or power cut?
What notice were you given?
How did the contractor deal with the situation?

## Slide 3: Objectives
You should be able to:
      Identify essential services commonly affected.
      Explain the impact of installation activities.
      Describe methods to reduce service disruption.
You might also be able to:
      Apply best practices in real scenarios.
      Evaluate how different approaches affect customer satisfaction.

## Slide 4: What are essential services? (1)
Essential services include water, heating, electricity, and sanitation. These allow occupants to live safely and comfortably in their homes. When interrupted, they affect health, hygiene, and quality of life.
These services are the backbone of any dwelling and are regulated for safety and reliability. Installers must take care not to compromise them unnecessarily.

## Slide 5: What are essential services? (2)
Water supply (cold and hot) Approved Document G (G1/G2/G3).
Sanitation (toilets, basins, showers) Approved Document G (G4/G5).
Drainage Approved Document H.
Heating systems.
Electrical supply and lighting.
Data and communication lines.

## Slide 6: What are essential services? (3)
Service interruptions can affect vulnerable individuals disproportionately. Planning and consultation help avoid inconvenience and danger.
Understanding how each service functions and interlinks is crucial and clear mapping of the service layout is vital for isolation and reinstatement.
Installers must treat these services with care and professionalism.

## Slide 7: Types of installation work that cause disruption (1)
      Full pipework replacements.
      Boiler changes or upgrades.
      Bathroom/kitchen refits.
      Sanitation system reworks.
      Radiator relocations.

## Slide 8: Types of installation work that cause disruption (2)
      Groundworks often affect incoming mains or waste lines.
      Ceiling and wall access can interrupt electrical and water lines.
      Storage tank or CWSC changes may require long drainage and refill times.
      Any fixture disconnection can impact more than one service.
      Staged work may reduce impact but requires planning.

## Slide 9: Types of installation work that cause disruption (3)
Disruption depends on property layout and system design. Older homes may lack modern isolation features. Working without proper preparation can extend outages.
Installers should factor in unforeseen problems like access or material quality. Client consultation before work begins is essential. Prolonged system shutdown could increase legionella risk due to water stagnation.
​Legionnaires disease - Technical Guidance HSG274 - page 79​

## Slide 10: Summary: Risk areas in common works
      Water: system alterations (indirect to direct), pipe rerouting, legionella.
      Sanitation: drainage system interference.
      Heating: radiator alterations/changes (system drain down).
      Gas: boiler/cookers/fires/water heaters – work only to be completed by Gas Safe registered installer.
      Electrical: showers, boilers, pumps.
      Impact is often felt across multiple systems simultaneously.

## Slide 11: Impact: No water (1)
      No access to water affects drinking, cleaning, hygiene, and cooking.
      This impact is critical in homes with babies, elderly, or ill residents.
      Even temporary loss can be distressing.
      Clear warning and mitigation are key.
      Planned outages must be carefully timed and explained.

## Slide 12: Impact: No water (2)
      Stops toilets, taps, and appliance use (direct systems).
      Halts hot water in direct systems (unvented/combi).
      Affects personal hygiene.
      Risks customer dissatisfaction.
      May require bottled water provision.

## Slide 13: Impact: No water (3)
      Isolation valves and freezing kits help limit the affected area.
      Supply cisterns or hoses can offer a temporary fix.
      Keeping outages under 2 hours is best practice.
      Even short periods without water should be avoided without notice.
      Test system fully before re-enabling customer access.
      Ensure WRAS approved fittings are used in the installation/repair – Water Regs 1999

## Slide 14: Impact: No water (4)
      Confirm water supply isolation before work.
      Inform occupants clearly in advance.
      Schedule for times of least impact.
      Plan for emergency restoration if needed.
      Record and monitor supply loss duration.

## Slide 15: Temporary water loss (1)
      Even short interruptions can be frustrating if not communicated.
      Airlocks and debris may be present when supply resumes.
      Pressure changes can affect appliances.
      Water may appear cloudy after restart.
      These can be avoided or reduced with proper method.

## Slide 16: Temporary water loss (2)
Use stop valves and re-pressurise carefully and notify of any post-installation flushing.
Keep the customer informed during work and provide bottled water where needed.
You should always test and clear the line after work.

## Slide 17: Temporary water loss (3)
Plan work phases to keep some taps operational.
Avoid isolating main in the morning or dinner time and use temporary bypasses where possible.
Train staff to respond quickly to complaints or confusion and log all interruptions as part of quality control.

## Slide 18: No sanitation access (1)
Losing access to WCs, showers, or sinks creates hygiene issues. This is especially problematic in single-bathroom properties.
Portable toilets may be required.
Work should be timed to suit the client’s daily routine and the risk to vulnerable persons must be carefully managed.

## Slide 19: No sanitation access (2)
      Only isolate one fixture at a time where possible.
      Communicate downtime in hours.
      Minimise duration with team coordination.
      Provide workarounds when needed.
      Keep sanitary conditions safe and controlled.

## Slide 20: No sanitation access (3)
Notify users of what not to use during the job and ventilation must be maintained if odours are present. Proper signage helps prevent misuse of isolated systems.
All services must be reinstated fully and tested and avoid working during school runs or meal times (factor in customer stress and discomfort).
Verify WC flush, basin, and trap seals on completion. Consider legal minimum service requirements.

## Slide 21: Cost-related disability issues (1)
Low-income households may not have backup resources like bottled water or access to alternative facilities.
They may also be unable to take time off work or afford to stay elsewhere.
Disruptions may be seen as threatening or stressful without the right reassurance. Installers need to plan with these circumstances in mind.
Every decision should aim to reduce customer burden where possible.

## Slide 22: Cost-related disability issues (2)
Being inclusive means understanding how disruptions affect people differently. What is a minor nuisance to some can be a major setback to others.
Vulnerable people may include elderly individuals, those with learning disabilities, or people who rely on powered equipment.
Services should be adapted to the user, not the other way around. Effective communication and sensitivity are part of a professional installer’s role.

## Slide 23: Isolation of services (1)
Isolating services ensures safe working conditions and protects property. It prevents unwanted leaks, shorts, or pressure surges. Knowing where and how to isolate correctly is a core installer skill. Shut-off must be secure, but should also allow for phased work.
After isolation, systems must be tested to confirm effectiveness.

## Slide 24: Isolation of services (2)
      Confirm the presence of individual appliance valves.
      Check pressure and system bleed points before starting work.
      Electric showers, immersion heaters, and pumps may also need to be isolated.
      Ensure boiler controls are also turned off if required.
      Document all isolation points in your job sheet or plan.

## Slide 25: Knowledge check Q1
Which of the following is not typically considered an essential service in a domestic property?
Garden irrigation
Sanitation
Cold Water Main
Gas

## Slide 26: Knowledge check Q2
Why is it important to map out the layout of essential services before starting installation work?
To meet legal requirements
To reduce aesthetic issues
To avoid disruption and allow safe isolation
To improve resale value

## Slide 27: Knowledge check Q3
What is the recommended maximum duration for a planned water outage?
30 minutes
2 hours
4 hours
1 day

## Slide 28: Knowledge check Q4
Which group is most at risk when essential services are interrupted?
Teenagers
Skilled tradespeople
Vulnerable individuals (e.g. elderly or unwell)
Neighbours

## Slide 29: Knowledge check Q5
What is a key reason for consulting clients before beginning work that affects services?
To sell them additional upgrades
To plan social activities
To avoid having to do paperwork
To ensure they are prepared and mitigate risks

## Slide 30: Knowledge check – answers
Q1 ✅ A) Garden irrigation
Q2 ✅ C) To avoid disruption and allow safe isolation
Q3 ✅ B) 2 hours
Q4 ✅ C) Vulnerable individuals (e.g. elderly or unwell)
Q5 ✅ D) To ensure they are prepared and mitigate risks

## Slide 31: Temporary services (1)
Temporary services keep water, power, and sanitation running during works. This may involve hose feeds, RCD-protected extension leads, or hired welfare units.
Setups must be safe, hygienic, and clearly explained to the client. Avoid trip hazards, carry out risk assessments, and test for safety. Remove all temporary systems fully and leave no trace when work is complete.

## Slide 32: Temporary services (2)
      Use secure, hygienic temporary feeds (e.g. hose taps, power leads with RCDs).
      Provide clear instructions and customer briefings.
      Regularly test for leaks, faults, and pressure issues.
      Avoid trip hazards – no trailing hoses or cables across walkways.
      Fully document, clean, and remove all temporary setups after work.

## Slide 33: Working out of hours (1)
Out-of-hours work can reduce disruption in homes, schools, offices, and healthcare settings. It requires careful planning, client agreement, and adherence to lone working and working time policies.
Weekend or evening work may need extra staff, pre-delivered materials, and coordination with neighbours if noise is involved.
Installers may need access to keys or alarm systems, so trust and clear documentation are essential. Updates via job tracking or photos can reassure absent clients.
Question: Can you think of a situation in which working outside of hours would be the safest or most considerate option?

## Slide 34: Working out of hours (2)
      Plan with client approval and respect quiet hours.
      Ensure lone working and emergency procedures are in place.
      Deliver materials and arrange access in advance.
      Update clients with photos or shift notes if unattended.
      Secure, clean, and log each shift before leaving.

## Slide 35: Communication with customers (1)
Communication should begin before the job starts. Customers need to know when work begins, how long it will last, and what will be affected. Clear, simple language should be used. Visual aids or checklists may help. Offer reassurance that services will be restored safely and promptly.

## Slide 36: Communication with customers (2)
      Give advance written notice for major works.
      Use phone, text, or door cards for reminders.
      Explain risks and the steps taken to reduce them.
      Be clear about timings and delays.
      Provide a single point of contact.
      Question: Why is consistency in updates important for customer trust?

## Slide 37: Legal and regulatory considerations (1)
      Building Regs Part G: Sanitation, hot water safety.
      Part H: Drainage and waste disposal.
      Health and Safety at Work Act: Workplace safety.
      Employers have a duty to protect workers and clients.
      Installers must use suitable PPE and method statements.

## Slide 38: Legal and regulatory considerations (2)
Licensing bodies and insurers may require proof of compliance. Gas and electrical works must be performed by qualified persons. Some installations must be registered with local building control. Failure to do so may invalidate warranties or result in fines. Professional standards protect both the client and the installer.
Question: What are the risks of working outside your qualification area?

## Slide 39: Legal and regulatory considerations (3)
      Always check the latest standards and revisions.
      Use manufacturer guidelines alongside legal regs.
      Attend CPD or toolbox talks to stay current.
      Carry evidence of competence and insurance.
      Be confident in explaining the importance of regulation to clients.
      Question: How can continued learning benefit both you and your customers?

## Slide 40: Summary of impacts (1)
      Work on plumbing or heating systems can cause:
      Complete water shut-off.
      Reduced pressure or flow.
      Temporary loss of sanitation.
      Electrical disconnection of pumps or boilers & other appliances.
      Inconvenience and customer complaints.
      Question: Which of these impacts would be most serious in a care home? Discuss.

## Slide 41: Summary of impacts (2)
Some impacts may not be obvious at first.
For example, disturbing pipework could loosen debris or create airlocks. Electrical surges may occur if systems are restarted too quickly. Damage to finishes or decoration may result from leaks. These all affect customer satisfaction and safety.
Question: What ‘hidden’ impacts should be checked after reinstating services?

## Slide 42: Summary of impacts (3)
      Delays in material delivery extend downtime.
      Unplanned work may increase costs.
      Lack of preparation frustrates clients.
      Reputational harm if not resolved properly.
      Customer anxiety, especially among vulnerable people.

## Slide 43: Case study
Scenario: Family home. Bathroom refit scheduled for a weekend.
Challenge: One toilet, used by four people.
Action: Discuss.
Outcome: ?

## Slide 44: Case study
Option 1: Installer hired a portable toilet and pre-installed shut-off valves.
Option 2: Installer removed and installed WC within 2 hours (last out, first in).
Outcome: Work completed with minimal disruption.
Feedback: Customer left 5-star review and recommended the service.
Case studies show how good planning avoids disruption. In this case, the installer thought about the family’s routine. They chose a weekend to avoid school/work needs. They communicated well and arrived fully prepared. Their professionalism avoided stress and delays.

## Slide 45: Case study
      Lessons:
      Always confirm how many bathrooms are in use.
      Never assume customers can manage without sanitation.
      Consider cost, convenience, and care.
      Plan for alternatives.
      Follow up after work is completed.

## Slide 46: Final questions
      What would you do if a customer had no water for 24 hours?
      How would you explain a delay in parts or delivery?
      Can you think of a time better planning could have helped?
      What temporary setups could maintain services?
      Why must installers communicate clearly and quickly?

## Slide 47: Recap
You’ve now explored the impact of installation work on water, sanitation, and power. We’ve looked at how disruptions happen and how they can be reduced. We examined planning, communication, temporary systems, and legal duties. Through real examples, you saw what good practice looks like.
Keep asking:
      What’s the impact on the customer?
      How can I do this better, safer, and more professionally?

## Slide 48: Summary
You should now be able to:
      Identify different types of essential services affected by installation activities.
      Explain the potential impacts of disruptions, including water and sanitation loss.
      Describe methods to minimise disruption, such as isolation and temporary services.
You might also be able to:
      Plan for unexpected delays and maintain service continuity.
      Justify choices made to reduce disruption and improve customer satisfaction.

## Slide 49
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.