## Slide 1
Occupational Specialism: Gas Engineering
K1.29 Procedures involved in decommissioning
PowerPoint 1.29: Decommissioning principles, planning and isolation

## Slide 2: Starter
Scenario: Charlie visits a customer with a 25-year-old open-flued boiler. It shows signs of corrosion around the heat exchanger, and CO readings are above acceptable limits. The customer refuses to replace it.
Questions:
What action should Charlie take?
Is this an installation, servicing, or decommissioning job?
What legal responsibilities are involved?

## Slide 3: Objective
By the end of this session, you should be able to:
Explain when and why gas systems or appliances should be decommissioned.
Describe the process of planning and preparing a decommissioning task.
Identify relevant safety standards and legal duties.
Carry out isolation procedures in accordance with MI and IGEM/G/11.

## Slide 4: What is decommissioning?
Decommissioning in gas engineering is the safe, permanent removal of a gas system or appliance to prevent hazards.
Unlike temporary isolation, it creates a lasting safety barrier, requiring a qualified Gas Safe engineer to reconnect the system if needed.

## Slide 5: What is decommissioning?
Core elements of decommissioning
Making the gas system or appliance permanently safe.
Ensuring no gas can re-enter without deliberate reconnection.
Preventing unauthorised use or tampering.
Creating a documented record of decommissioned status.
Communicating clearly with the responsible person.

## Slide 6: What is decommissioning?
Decommissioning may involve:
Physical disconnection from the gas supply.
Purging or venting residual gas from pipework.
Capping, plugging or sealing open pipe ends.
Applying appropriate warning labels.
Formal documentation and notification.
Electrical isolation where applicable.

## Slide 7: When is decommissioning required?
Gas engineers must recognise situations requiring decommissioning to ensure safety and legal compliance.
These circumstances range from emergency scenarios to planned system upgrades.

## Slide 8: When is decommissioning required?
Situation | Reason | Classification | Response required
Unsafe appliance (ID) | Immediate danger scenario | Emergency | Immediate disconnection, with or without permission
Unsafe appliance (AR) | At-risk scenario | Urgent | Isolation with warning, customer notification
End-of-life boiler/system | Scheduled upgrade or replacement | Planned | Coordinated decommissioning with replacement
Redundant installation | No longer required but still connected | Preventative | Permanent isolation to prevent future risk
Gas leak on unused section | To prevent future leaks or tampering | Remedial | Section isolation and sealing
Appliance moved/removed | Renovation or reinstallation | Transitional | Temporary caps with future plan

## Slide 9: When is decommissioning required?
All decommissioning work must follow GSIUR Regulation 34 which requires that "Any person who knows or has reason to suspect that any gas fitting is dangerous must take all reasonable steps to cause the gas supply to be shut off." Additionally, the industry standard IGEM/G/11 provides detailed procedures for safe decommissioning.
Critical safety note
Failure to properly decommission an unsafe gas appliance or system could result in serious safety risks, including carbon monoxide poisoning, gas leaks, fire, or explosion. It may also constitute a breach of the Gas Safety (Installation and Use) Regulations, potentially leading to prosecution.

## Slide 10: Planning for safe decommissioning
Pre-work assessment
Before starting decommissioning, thorough planning is crucial.
The gas engineer must assess risks like confined spaces, asbestos, shared systems, vulnerable occupants, and weather.
Consent from the responsible person is required unless there’s an immediate safety risk.

## Slide 11: Planning for safe decommissioning
Identification - Confirm the correct appliance/system to be decommissioned and its relationship to the overall gas installation.
Preparation - Gather required tools, appropriate warning labels, caps/plugs, and personal protective equipment.
Inspection - Check meter status, locate Emergency Control Valve (ECV), and verify current gas tightness status.
Documentation - Prepare necessary paperwork including warning notices, certificates, and customer information.

## Slide 12: Gas isolation procedures
Proper gas isolation is the critical first step in any decommissioning process. Following established procedures ensures safety for both the engineer and building occupants.
Identify isolation point
Determine the appropriate isolation valve for the specific appliance or section to be decommissioned. This may be an appliance isolation valve, a branch isolation valve, or in some cases, the Emergency Control Valve (ECV).

## Slide 13: Gas isolation procedures
Close valve and apply warning
Turn the isolation valve to the fully closed position and immediately apply a 'DO NOT USE – DECOMMISSIONED' warning label. For ECVs, use appropriate locking devices where available.
Verify zero pressure
Connect a manometer to a suitable test point downstream of the isolation valve and confirm zero gas pressure. This verifies that gas is no longer flowing to the isolated section.

## Slide 14: Gas isolation procedures
Perform tightness test
Conduct a tightness test on the remaining live gas system to confirm that isolation has not affected the integrity of the rest of the installation. This is critical when isolating branches from a larger system.
Document actions
Record the isolation details, including who performed the work, when it was completed, the reason for isolation, and any specific instructions for future engineers.

## Slide 15: Gas isolation procedures
Industry best practice
Always use a properly calibrated electronic gas detector to sweep the area around isolation points after completing the procedure. This provides an additional safety check beyond visual inspection and pressure testing.

## Slide 16: Electrical isolation for gas appliances
Modern gas appliances include electrical parts that need safe isolation when decommissioned to avoid shock or damage.
The level of isolation varies by appliance; for example, fan-assisted boilers require full electrical isolation to stop the fan from operating and drawing gas through a faulty valve.

## Slide 17: Electrical isolation for gas appliances
Switch off at Fused Connection Unit (FCU) - Locate and turn off the dedicated FCU for the appliance, typically located adjacent to the appliance.
Isolate at spur or consumer unit - For permanent decommissioning, isolate at the spur connection or main consumer unit and apply a lock-off device where possible.

## Slide 18: Electrical isolation for gas appliances
Verify dead circuit - Use a calibrated voltage tester or multimeter to confirm zero voltage at all relevant terminals before proceeding with further work.
Apply warning label - Attach appropriate electrical isolation warning to the FCU and note in documentation that the electrical supply has been isolated.

## Slide 19: Legal duties and standards
Regulation/Standard | Requirements
GSIUR Regulation 34 | Requires a competent person to take all reasonable steps to prevent the use of any gas fitting known or suspected to be unsafe. This forms the legal basis for mandatory decommissioning of unsafe appliances.
IGEM/G/11 | Provides detailed technical standards for gas installation pipework on industrial and commercial premises, including specific procedures for decommissioning various system types.
HSE Guidance | Offers approved guidance on interpretation of the regulations, documentation requirements, and notification procedures. Engineers must maintain comprehensive records of all decommissioning work.
Manufacturer's Instructions (MI) | Contains appliance-specific isolation and decommissioning guidance that may supplement or expand upon general industry standards, particularly for complex or specialised equipment.
Gas Industry Unsafe Situations Procedure (GIUSP) | Classifies unsafe situations and prescribes appropriate actions for AR (At Risk) and ID (Immediately Dangerous) scenarios, including decommissioning requirements.

## Slide 20: Purging considerations during decommissioning
Purging is the process of removing gas from pipework and appliances during decommissioning to eliminate explosion risks.
The purging method depends on pipe volume and installation type.
Never purge to atmosphere in:
Confined spaces, areas with poor ventilation, near ignition sources, or where gas could accumulate. Always follow IGEM/UP/1B for domestic purging and IGEM/UP/1 for larger installations.

## Slide 21: Purging considerations during decommissioning
Small domestic installations
For typical domestic installations with relatively small gas volumes:
Natural ventilation is usually sufficient.
Disconnect the appliance after isolation.
Allow gas to safely dissipate into a well-ventilated area.
Avoid ignition sources during the process.
Check with the electronic gas detector before completing work.

## Slide 22: Purging considerations during decommissioning
Larger commercial/industrial installations
For installations with larger pipe volumes or in sensitive locations:
Formal purging procedure required.
May need controlled purging with nitrogen.
Calculate gas volume to determine method.
Consider temporary vent pipes to safe locations.
Continuous gas monitoring throughout.
May require a specific purging team for complex sites.

## Slide 23: Purging considerations during decommissioning
Small domestic - 0.6 m3
Typical maximum gas volume in a domestic installation requiring only natural ventilation purging.
Lower explosive limit – 5%
Concentration of gas in the air above which an explosion risk exists during purging operations.
Minimum ventilation – 30Min
Typical minimum ventilation time after purging before declaring the area safe.

## Slide 24: Documentation and reporting requirements
Proper documentation is a critical component of the decommissioning process, providing legal protection for the engineer and essential safety information for property owners and future workers.

## Slide 25: Documentation and reporting requirements
Warning notice
Clearly state that the appliance/system is decommissioned.
Specify reason for decommissioning (unsafe, redundant, etc.).
Include date of decommissioning.
Provide Gas Safe registration details.
Attach securely to appliance/isolation valve.
Use weatherproof labels for external installations.

## Slide 26: Documentation and reporting requirements
Documentation for customer
Detailed explanation of work carried out.
Reason for decommissioning in plain language.
Safety implications and recommendations.
Copy of any test results or readings.
Future requirements for recommissioning.
Signed acknowledgement from the responsible person.

## Slide 27: Documentation and reporting requirements
Engineer's records
Comprehensive job sheet with all actions taken.
Photographic evidence where appropriate.
Gas tightness test results for the remaining system.
Details of components removed or capped.
Risk assessment documentation.
Copy of warning notice and customer information.

## Slide 28: Documentation and reporting requirements
Notification requirements
In certain circumstances, additional notifications are required:
Immediately dangerous situations must be reported to the Gas Emergency Service Provider if isolation is refused.
Landlord properties require notification to the property owner.
Commercial premises may require updates to gas safety logbooks.
Shared flue systems may require notification to other users.

## Slide 29: Physical disconnection methods
After isolation, physical disconnection and sealing of gas pipes are essential to ensure permanent safety.
The method chosen depends on pipe material, location, and whether future reconnection is anticipated.
Temporary capping methods
Suitable when reconnection is planned within a reasonable timeframe:
Compression caps: Used on copper or steel pipes with an appropriate olive and nut.
Blanking plugs: Used on threaded connections like BSP fittings.
Isolation valves: Closed, locked, and labelled (not a permanent solution).

## Slide 30: Physical disconnection methods
Permanent sealing methods
Required when pipework is being permanently decommissioned:
Soldered caps: For permanent copper pipe termination
Welded caps: For steel pipes in industrial settings
Cut and sealed: Removing the section and installing a permanent end cap
Plugged and sealed: Threaded connections filled and sealed

## Slide 31: Key takeaways
Fundamental principles of decommissioning
Decommissioning is a critical safety process requiring careful planning, execution, and documentation to eliminate risks from unsafe or outdated gas installations.
It follows a structured approach prioritising safety and legal compliance.
Although sometimes part of larger projects, it demands the same rigorous standards.

## Slide 32: Summary
You should now be able to:
Explain when and why gas systems or appliances should be decommissioned.
Describe the process of planning and preparing a decommissioning task.
Identify relevant safety standards and legal duties.
Carry out isolation procedures in accordance with MI and IGEM/G/11.

## Slide 33
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.