## Slide 1
Occupational Specialism: Gas Engineering
K1.30 Requirements for recording, labelling and reporting decommissioned systems
PowerPoint 1.30: Documenting and reporting decommissioned gas systems

## Slide 2: Starter
Simon attends a property and finds a disconnected gas fire with the gas supply still open. There’s no label or paperwork.
Discussion question
What are the risks?
Notes: Group discussion – link to illegal re-use, unsafe reconnection, and risk to other trades.

## Slide 3: Objectives
By the end of this session, you should be able to:
Explain the legal and procedural steps for decommissioning.
Identify the purpose and content of warning notices and labels.
Describe how to inform the responsible parties.
Apply recording and reporting principles to real scenarios.

## Slide 4: What is decommissioning?
Decommissioning means:
Permanently or temporarily disabling a gas appliance, meter, or installation.
Making it safe for removal or disuse.
Preventing future accidental use.
May be done due to:
Faults or unsafe conditions (ID, AR under IGEM/G/11).
End of service life.
Change of use or renovation.

## Slide 5: Step 1: Recording the decommissioning
Documentation must include:
Appliance or system details (location, make, model).
Date and reason for decommissioning.
Action taken (e.g. capping, isolation, disconnection).
Pressure test results if applicable.
Signature of engineer and identification number.
Reference to IGEM/G/11 classification if used.

## Slide 6: Step 1: Recording the decommissioning
Where it goes:
Job sheet / maintenance log.
Customer records.
Gas Safety Certificate or warning notice.

## Slide 7: Step 2: Labelling the system
Permanent warning labels:
Clearly state:
  “Do Not Use – Gas Supply Isolated” or “Appliance Decommissioned”
  Date, engineer name/contact
  Reason (e.g. ID – Unsafe Situation)
Fixed directly on:
  Appliance, Meter, Control valves
Must be durable, weather-resistant (if external).

## Slide 8: Informing the responsible person
Who? Landlord, homeowner, site manager, duty holder
When? Before leaving the site
How? Verbal and written (use warning notice form or system log)
Explain:
  Why system was decommissioned.
  What must happen next (repair, replace, re-commission by a qualified engineer).
  Legal implications of unauthorised reconnection.

## Slide 9: Why this matters?
Prevents accidental re-use of unsafe systems.
Protects other trades, tenants, and public.
Required under Gas Safety (Installation & Use) Regulations 1998.
Essential for compliance with IGEM/G/11, Part J, and Building Control.
May be reviewed during audits or legal investigations.

## Slide 10: Summary
You should now be able to:
Explain the legal and procedural steps for decommissioning.
Identify the purpose and content of warning notices and labels.
Describe how to inform the responsible parties.
Apply recording and reporting principles to real scenarios.

## Slide 11
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.