## Slide 1
Occupational Specialism: Gas Engineering
K1.10 Safety devices applicable to gas systems, their characteristics and operation
PowerPoint 1.10c: System monitoring devices – thermostats and low water pressure switches

## Slide 2: Starter
Scenario:
Maya reports her combi boiler keeps cutting out when running the shower. The hot water goes scalding hot, then cold.
Discuss:
Which components might be faulty or misconfigured?
Why would this pose a safety risk?

## Slide 3: Objectives
By the end of this session, you should be able to:
Identify key monitoring devices: thermostats and low water pressure switches.
Describe how these devices protect appliances from thermal and hydraulic faults.
Explain their testing and fault diagnosis procedures.
Apply safe replacement and reset methods following MI.

## Slide 4: Thermostats: Purpose and positioning
Thermostats are critical safety and control devices that maintain appropriate operating temperatures within gas appliances.
Their precise positioning is essential for accurate temperature sensing and timely response.
Thermostats must be correctly positioned with appropriate thermal contact to ensure accurate temperature sensing. Poor contact can lead to delayed response and potential overheating scenarios.
Never bypass thermostats as temporary fixes. This removes critical safety devices from the system and places users at risk.

## Slide 5: Thermostats: Purpose and positioning
Type | Function | Typical location
Flow Thermostat | Monitors hot water temperature leaving boiler | Clipped to flow pipe or integrated in heat exchanger
Return Thermostat | Measures temperature returning from system | Attached to return pipe before pump
Cylinder Thermostat | Controls stored hot water temperature | External to cylinder or immersed in pocket
Overheat Thermostat | Backup cut-off if primary thermostat fails | Built into appliance at critical heat point

## Slide 6: How thermostats work
Temperature sensing
Modern thermostats use thermistors (Negative Temperature Coefficient sensors) whose electrical resistance decreases as temperature rises.
At 25°C, a typical NTC sensor will have a resistance of approximately 10kΩ, falling to around 1kΩ at 100°C.

## Slide 7: How thermostats work
Signal processing
The PCB (Printed Circuit Board) constantly monitors resistance values from thermistors, converting them to temperature readings.
These signals are used to determine when to modulate flame, adjust pump speed, or trigger safety lockouts.

## Slide 8: How thermostats work
System response
Based on temperature readings, the PCB controls:
Burner modulation (flame height).
Pump operation (speed adjustment).
Overheat lockout (safety shutdown).

## Slide 9: How thermostats work
Symptoms of thermostat failure:
Boiler consistently overheating or short cycling.
Domestic hot water temperature fluctuations.
Random lockouts triggered by high limit stats.
Poor modulation of burner flame.
Thermostats must always be replaced like-for-like using manufacturer-approved parts. Incorrect thermostats may have different resistance values or temperature thresholds, leading to unsafe operation.

## Slide 10: Low water pressure switches
Function and importance
Low water pressure switches are critical safety components that protect the boiler from operating under potentially damaging conditions.
Their primary functions include:
Detecting loss of pressure in sealed heating systems (typically below 0.5-0.7 bar).
Preventing burner ignition under low-pressure conditions.
Protecting the heat exchanger from "dry firing" which can cause cracking.
Alerting users to potential leaks in the system.

## Slide 11: Low water pressure switches
Resetting after activation
When a low water pressure switch activates:
Re-pressurise system via filling loop to 1.0-1.5 bar (cold).
The switch will typically reset automatically once pressure is restored.
Some models require a manual reset via the PCB or the control panel.
Check for potential leaks if pressure drops again.
Frequent pressure drops indicate a system leak that must be located and repaired. Continuously topping up without addressing the underlying issue can lead to accelerated corrosion within the system.

## Slide 12: Testing and fault finding
Device | Testing method | Expected values | Symptoms if faulty
Flow/return thermostat (NTC) | Resistance check with multimeter | ~10kΩ at 25°C, ~2kΩ at 60°C | Inaccurate temperature, poor modulation, sporadic operation.
Overheat thermostat | Manual test/reset or continuity check | Closed circuit (0Ω) in normal operation | Lockout with no obvious flame fault, repeated resets needed.
Low pressure switch | Check system pressure + continuity | Open circuit below 0.5 bar, closed above | Boiler won't ignite despite normal pressure, error code displayed.
Cylinder thermostat | Visual check of dial setting vs. actual water temperature | Water temperature within ±3°C of setting | Stored water too hot/cold, inconsistent temperature.

## Slide 13: Testing and fault finding
When testing components:
Always isolate electrical supply before testing.
Disconnect wiring from PCB to get accurate readings.
Use manufacturer's instructions to confirm correct test values for specific models.
Consider ambient temperature when checking resistance values.
Temperature sensors typically use NTC thermistors which show decreased resistance as temperature increases. A reading of infinity (open circuit) usually indicates a broken sensor or wiring.

## Slide 14: Integration with appliance control
Combi-boiler operation sequence
Hot water demand detected
Tap opens → flow sensor detects water movement → signals demand to PCB.
PCB checks all safety devices are in the correct state (pressure switch closed, thermostats within range).
Ignition sequence
Burner ignites → fan and gas valve activate → flame supervision confirms ignition.
Flow thermistor begins measuring the outlet water temperature in real-time.

## Slide 15: Integration with appliance control
Combi-boiler operation sequence
Temperature regulation
PCB modulates flame based on flow thermistor readings to maintain the set output temperature.
Pump speed may be adjusted to help regulate temperature based on demand.
Safety monitoring
If pressure drops below threshold → pressure switch opens → burner shuts off.
If temperature exceeds limit → overheat thermostat triggers → safety lockout initiated.

## Slide 16: Integration with appliance control
Combi-boiler operation sequence
Failure scenarios
If the flow sensor fails → no DHW operation despite water flow.
If the thermistor reads incorrectly → temperature fluctuations or shutdown.
All sensors and switches communicate with the PCB, which acts as the central "brain" controlling appliance behaviour and enforcing safety parameters. The PCB continuously monitors these inputs to ensure safe operation.

## Slide 17: Common real-world issues
Radiators are cold despite the boiler running
Potential causes:
Return thermistor fault that is causing poor modulation.
Pump issue is preventing circulation.
Air locks in the system are restricting flow.
Diagnosis: Check return thermistor resistance, verify pump operation, bleed radiators to remove air.

## Slide 18: Common real-world issues
Domestic hot water too hot
Potential causes:
Faulty flow thermostat giving incorrect readings.
Scale buildup affecting sensor contact.
PCB not responding correctly to temperature signals.
Diagnosis: Compare actual water temperature with sensor reading, check for scale, and verify PCB response.

## Slide 19: Common real-world issues
Intermittent ignition issues
Potential causes:
Low water pressure or a faulty pressure switch.
Borderline overheat condition triggering the safety cutout.
Water hammer affecting the pressure readings.
Diagnosis: Monitor system pressure during operation, check pressure switch continuity, inspect for system leaks.

## Slide 20: Common real-world issues
No central heating function
Potential causes:
Overheat stat triggered and requiring manual reset.
The flow sensor failure is preventing activation.
Room thermostat or timer issues.
Diagnosis: Check for lockout codes, test flow sensor resistance, verify external controls are calling for heat.

## Slide 21: Common real-world issues
These symptoms often mimic other faults, requiring a methodical step-by-step diagnosis approach rather than immediate component replacement.
Always consult manufacturer's troubleshooting guides for model-specific diagnostic procedures.

## Slide 22: Knowledge check
Question 1
What is the most likely cause of a boiler refusing to light when pressure reads 0.3 bar?
Gas valve fault.
Flow sensor misreading.
Low pressure switch triggered.
Overheat thermostat tripped.

## Slide 23: Knowledge check
Question 2
Which thermostat acts as a safety backup to cut power if overheating occurs?
Return thermostat.
Cylinder thermostat.
Flow thermistor.
Overheat thermostat.

## Slide 24: Knowledge check
Question 3
When replacing a flow thermistor on a combi boiler, which of the following is most important?
Using high-temperature thermal paste on the sensor.
Ensuring the replacement has identical resistance values to the original.
Calibrating the PCB after installation.
Insulating the sensor with heat-resistant tape.

## Slide 25: Thermostat testing procedures
NTC Thermistor testing
Isolate electrical supply to boiler.
Disconnect thermistor leads from PCB or connector.
Set the multimeter to resistance (Ω) mode.
Connect probes to thermistor leads.
Compare reading with the manufacturer's chart.
Typical values: 10kΩ at 25°C, 2kΩ at 60°C.
A significant deviation from expected values or an open/short circuit reading indicates a faulty thermistor requiring replacement.

## Slide 26: Thermostat testing procedures
Overheat Thermostat testing
Isolate electrical supply to boiler.
Disconnect both wires from the thermostat.
Set the multimeter to continuity or resistance mode.
Connect probes to thermostat terminals.
Should read 0Ω (closed circuit) at normal temperature.
If open circuit, press reset button (if present).
Still open circuit? Thermostat likely faulty.

## Slide 27: Low water pressure switch operation
Feature | Mechanical Switch | Electronic Sensor
Operation | Diaphragm deflection opens/closes circuit | Pressure transducer provides variable signal
Output | Binary (on/off at set threshold) | Continuous pressure reading
Integration | Simple circuit connection | Requires PCB interpretation
Testing | Continuity check at different pressures | Voltage/resistance measurement
Mechanical vs Electronic pressure switches

## Slide 28: Low water pressure switch operation
Pressure switch function in a system
The pressure switch plays a vital role in protecting boiler components:
Prevents operation when system pressure is dangerously low.
Protects the pump from damage due to insufficient water.
Safeguards the heat exchanger from thermal stress.
Provides early warning of potential system leaks.
Prevents dry firing which can crack the heat exchanger.

## Slide 29: Low water pressure switch operation
Pressure switch function in a system
The activation point is typically set between 0.5-0.7 bar, but can vary by manufacturer.
Modern boilers display both the pressure reading and fault codes specifically related to pressure issues, making diagnosis more straightforward for engineers.

## Slide 30: System integration case study
Worcester Bosch Greenstar Combi safety systems
The Worcester Bosch Greenstar range demonstrates a comprehensive approach to thermal and pressure safety.
Multiple temperature monitoring points
Flow NTC monitors outgoing water temperature (located on primary heat exchanger).
Return NTC checks water returning from heating system (positioned before pump).
DHW NTC measures hot water temperature to tap (on plate heat exchanger).
Flue gas NTC detects excessive exhaust temperatures (in the flue assembly).

## Slide 31: System integration case study
Layered safety approach
Primary control via modulating gas valve based on NTC readings.
Secondary protection via independent overheat thermostat (manual reset required).
Electronic pressure sensor provides continuous pressure monitoring to PCB.
Automatic air vent helps prevent air locks that could cause local overheating.
This multi-layered approach ensures that if one safety system fails, another will provide backup protection. The integration of these components through the PCB allows for sophisticated fault detection and diagnostic capabilities.

## Slide 32: Safe replacement procedures
Preparation
Before replacing any thermostat or pressure switch:
Isolate electrical supply at fused spur.
Turn off gas supply at appliance isolation valve.
Allow appliance to cool if recently operational.
Drain system if necessary for hydraulic components.
Take photo of wiring configuration before disconnection.

## Slide 33: Safe replacement procedures
Component removal
When removing the faulty component:
Label all wires before disconnecting if not colour-coded.
Use appropriate tools to avoid damage to the surrounding parts.
Note the exact position and orientation of the sensor/switch.
Check mounting surfaces for corrosion or scale build-up.

## Slide 34: Safe replacement procedures
Installation
When fitting the replacement:
Verify replacement is exact manufacturer-approved part.
Apply heat transfer compound if specified for thermostats.
Ensure secure mounting with proper thermal contact.
Reconnect wiring exactly as original configuration.
Secure all clips, brackets and fasteners.

## Slide 35: Safe replacement procedures
Testing and Commissioning
Before returning to service:
Re-pressurise system if drained (1.0-1.5 bar cold).
Restore electrical and gas supplies.
Reset any lockout conditions on the PCB.
Operate the appliance and verify correct function.
Document replacement in the service record.

## Slide 36: Key learning points
Safety device identification: You can now identify the various thermostats and pressure switches used in gas systems, understanding their specific locations and functions within the appliance.
Protection mechanisms: You understand how these devices protect appliances from thermal and hydraulic faults, preventing damage to components and ensuring user safety.
Testing procedures: You can apply appropriate testing methodologies and fault diagnosis procedures for thermostats and pressure switches using proper tools and techniques.
Safe replacement: You can implement correct replacement and reset procedures following manufacturer's instructions, ensuring like-for-like component substitution.

## Slide 37: Summary
You should now be able to:
Identify key monitoring devices: thermostats and low water pressure switches.
Describe how these devices protect appliances from thermal and hydraulic faults.
Explain their testing and fault diagnosis procedures.
Apply safe replacement and reset methods following MI.

## Slide 38
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.