## Slide 1
Occupational Specialism: Gas Engineering
K1.12 – Mechanical heat ventilation recovery
PowerPoint 1.12: Principles and components of MVHR systems

## Slide 2: Starter
Tracy installs a new room-sealed boiler in a passive house with triple glazing and no air bricks. Why might a Mechanical Ventilation system be essential?
Discuss in pairs → highlight the need for balanced air change, condensation control, and heat recovery.

## Slide 3: Objectives
By the end of this session, you should be able to:
Describe how MVHR systems operate and their role in energy efficiency.
Identify key components of an MVHR system.
Explain how MVHR systems interact with combustion appliances.
Evaluate maintenance and safety considerations.

## Slide 4: What is MVHR?
Dual-function technology
MHVR combines ventilation with heat recovery in a single system, significantly reducing energy consumption whilst maintaining healthy indoor environments.
Fresh air exchange
Provides continuous fresh air circulation throughout the building, essential for occupant health and comfort, whilst removing stale air and pollutants.

## Slide 5: What is MVHR?
High efficiency
Modern systems can recover up to 90% of heat from exhaust air that would otherwise be lost to the outside environment, dramatically improving overall energy efficiency.

## Slide 6: Why heat recovery? Industry background
In the UK, around 25–30% of building heat is lost solely through ventilation, presenting a major challenge for improving energy efficiency among property owners and developers.
This considerable heat loss has made energy conservation the main motivation for adopting MHVR systems in both residential and commercial buildings, especially as energy prices increase and building regulations become more stringent.
Thermal imaging reveals significant heat loss through traditional ventilation systems, driving the need for efficient recovery solutions.

## Slide 7: MHVR: How the process works
The MHVR process operates on a continuous cycle:
Stale, warm air is extracted from moisture-prone areas such as kitchens and bathrooms
This air passes through a heat exchanger before being expelled outside
Simultaneously, fresh air is drawn in from outside
The incoming fresh air absorbs heat from the outgoing air within the exchanger
Warmed fresh air is distributed to living spaces, maintaining comfortable temperatures.

## Slide 8: Components of an MVHR system
Supply and extract ductwork - Insulated pipes distribute air throughout the building, carefully designed to minimise pressure drops and noise.
Heat exchanger unit - High-efficiency core components where thermal energy transfer occurs between outgoing and incoming air streams without mixing.
Filters (supply and extract) - Multiple filtration stages to remove particulates, allergens and pollutants from both incoming and outgoing air.
Fans (low-energy DC) - Energy-efficient motors and sophisticated control systems that regulate airflow rates, temperature settings and operating modes.
Bypass mechanisms - Allow the system to circumvent heat recovery during summer months when heating is not required, preventing overheating.

## Slide 9: Flue gas heat recovery
Flue gas heat recovery is a system that captures and reuses heat from the hot gases produced during combustion in boilers. Instead of allowing this heat to escape through the flue, the system extracts it and uses it to preheat cold water entering the boiler. This process improves overall energy efficiency, reduces fuel consumption, and lowers carbon emissions.

## Slide 10: Why it matters in gas engineering
Room-sealed appliances still require air quality control. This:
prevents negative pressure that could cause flue gas spillage in older systems
reduces condensation and damp risk in sealed homes
must be commissioned properly to maintain air balance.

## Slide 11: Safety and servicing
Filters must be cleaned or replaced (typically every 6–12 months)
Heat exchangers may require de-dusting or vacuuming
Fans must be checked for bearing noise or failure
Must not obstruct combustion or flue operation
MI and Part F must be followed
Systems must be labelled and documented if integrated with gas appliances

## Slide 12: Summary
You should now be able to:
Describe how MVHR systems operate and their role in energy efficiency.
Identify key components of an MVHR system.
Explain how MVHR systems interact with combustion appliances.
Evaluate maintenance and safety considerations.

## Slide 13
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.