## Slide 1
Occupational Specialism: Gas Engineering
K1.13 Types of chimneys and chimney systems in
relation to gas appliance types
PowerPoint 1.13: Chimney Systems in Relation to Appliance Types

## Slide 2: Starter
Fault scenario
Georgia installs a decorative gas fire in a lounge with no chimney. The appliance is open-flued and was designed for installation in a chimney breast.
What key system has been missed?
Why is this unsafe?
What type of appliance is it?

## Slide 3: Objective
By the end of this session, you should be able to:
Classify appliance types A, B and C by flue/chimney requirement.
Describe the fundamental operating principles of chimney/flue systems.
Compare the suitability of different flue types to appliance categories.
Identify appropriate testing procedures for flue safety and performance.

## Slide 4: Why chimney systems matter
Chimney systems are not merely traditional architectural features but essential safety components in UK gas installations. They serve multiple critical functions that directly impact both occupant safety and appliance efficiency. They:
safely remove harmful combustion products including carbon monoxide (CO), carbon dioxide (CO₂), water vapour, and other potentially dangerous gases
establish and maintain a stable draught or balanced pressure system to ensure proper combustion
prevent spillage of combustion products or backdrafts that could introduce toxic gases into living spaces.

## Slide 5: Why chimney systems matter
Ensure compliance with Building Regulations Part J (Combustion Appliances and Fuel Storage Systems)
Protect occupant health while maintaining optimal appliance performance and efficiency.
In the UK, the consequences of improper chimney specification or installation can be severe. They can potentially result in carbon monoxide poisoning, increased fire risk, and legal liability for the gas engineer.

## Slide 6: Why chimney systems matter
Proper chimney function depends on multiple factors including height, diameter, insulation, terminal design and positioning.
UK regulations are particularly stringent regarding these specifications.

## Slide 7: Appliance types A, B and C
Gas appliances in the UK are classified according to BS EN standards and IGEM/G/11 guidance based on their combustion air source and flue requirements:
Type | Appliance category | Flue/Chimney requirement | UK examples
A | Flueless | No chimney – must have fixed ventilation | Portable gas heaters, some cookers
B | Open-flued | Chimney/flue needed (natural draught) | Decorative fires, back boiler units
C | Room-sealed | Balanced flue – sealed combustion system | Modern combi boilers, high-efficiency systems

## Slide 8: Appliance types A, B and C
This classification system is fundamental to UK gas engineering practice and forms the basis for appliance selection, installation requirements, and safety considerations. Each type presents unique challenges and requirements that must be understood to ensure safe, compliant installations.
As a professional gas engineer in the UK, you must verify that the installation environment is suitable for the appliance type, particularly regarding room size, ventilation provision, and chimney/flue availability. The Domestic Building Services Compliance Guide provides additional specifications relevant to these classifications.

## Slide 9: Type B appliances: Open-flued systems
Air intake
Combustion air is drawn directly from the room where the appliance is installed. This creates negative pressure within the room, requiring adequate ventilation to replace consumed oxygen.
Combustion process
Fuel burns using room air, creating hot gases that expand and become less dense than the surrounding air. This density difference is crucial for proper draught formation.

## Slide 10: Type B appliances: Open-flued systems
Natural draught
Hot gases rise through the chimney using natural convection (thermal buoyancy). The height differential between the appliance and terminal creates the necessary draught effect.
External factors
System is sensitive to atmospheric conditions, indoor pressure drops, ventilation issues, and wind effects that can disrupt the natural draught.

## Slide 11: Type B appliances: Open-flued systems
Examples of Type B appliances common in UK properties include back boiler units (BBUs), decorative gas fires, conventional floor-standing boilers, and older water heaters.
These systems require particular attention to ventilation requirements as specified in BS 5440-2 and must undergo spillage testing as part of commissioning and servicing.

## Slide 12: Type C appliances: Room-sealed systems
Operating principles
Room-sealed (Type C) appliances represent the evolution of gas technology with significant safety advantages over open-flued systems.
Their key operational characteristics include:
the combustion chamber is completely sealed from the room environment
combustion air is drawn from outside via dedicated air intake.

## Slide 13: Type C appliances: Room-sealed systems
Operating principles
Flue gases expelled through terminal without entering living space
Often utilise coaxial (pipe-within-pipe) or twin-pipe terminal arrangements
Many modern units incorporate fan-assistance, creating positive pressure within the flue system.
These systems are categorised further (C1–C8) based on their specific terminal configuration and pressure characteristics.

## Slide 14: Type C appliances: Room-sealed systems
Advantages for UK installations
Room-sealed systems offer significant benefits in the UK context:
safer for installation in kitchens, bedrooms, and bathrooms
independent of room ventilation requirements
resistant to negative pressure effects from extractor fans
higher efficiency potential, especially with condensing models
greater flexibility in positioning within the property.

## Slide 15: Type C appliances: Room-sealed systems
Common examples in UK building services include wall-mounted combi boilers, system boilers, and modern high-efficiency condensing appliances.
These systems must comply with the flue positioning requirements detailed in BS 5440-1.

## Slide 16: Type A appliances: Flueless systems
Operating principle
Type A appliances operate without a dedicated flue system, releasing all combustion products directly into the room where they are installed.
This fundamental characteristic necessitates strict limitations on their use and installation within UK properties.

## Slide 17: Type A appliances: Flueless systems
UK regulatory requirements
The installation of flueless appliances in the UK is governed by specific requirements:
Installation is permitted only in rooms of sufficient volume (as specified in manufacturer's instructions and BS 5871-4).
Permanent ventilation may be required, typically high-level with minimum free area of 100 cm² per kW of input. This varies on the type of appliance and heat input.
Some appliances may require an openable window.

## Slide 18: Type A appliances: Flueless systems
UK regulatory requirements
CO detectors mandatory in accordance with BS EN 50291
Oxygen depletion sensors (ODS) required as a safety feature.

## Slide 19: Type A appliances: Flueless systems
Installation restrictions
UK regulations and best practice guidance explicitly prohibit Type A appliances in:
bedrooms, bathrooms or shower rooms
small, poorly ventilated spaces
locations with high occupancy turnover (e.g., holiday rentals) without proper user education
properties with vulnerable occupants unless additional safeguards are implemented.

## Slide 20: Type A appliances: Flueless systems
Installation restrictions
Examples include certain flueless space heaters, some gas cookers without extraction hoods, and certain decorative fuel effect fires.
All installations must comply with The Gas Safety (Installation and Use) Regulations 1998 as amended.

## Slide 21: Chimney inspection and testing requirements
Test/Check | Purpose | Method | UK Standard/Guidance
Visual inspection | Identify visible defects, obstructions or deterioration | Physical examination of accessible parts, CCTV for internal inspection | BS 5440, IGEM/G/11
Flue flow test | Verify presence of natural draught | Smoke match or smoke pellet test at draught diverter | BS 5440-1, Gas Safe TB 200
Spillage test | Check for combustion products entering room | Smoke match around appliance draught diverter or pressure test | BS 5440-1, IGEM/UP/11
Terminal check | Ensure compliant positioning and condition | Visual inspection and measurement of distances | BS 5440-1, Building Regs Part J
CO alarm verification | Confirm presence and functionality | Test alarm operation and check installation position | BS EN 50291, Building Regs Part J
Flue integrity test | Check for leaks in the flue system | Pressure testing for room-sealed systems | Manufacturer instructions, BS 5440

## Slide 22: Chimney inspection and testing requirements
These inspections must be conducted at installation, during annual servicing, and whenever alterations are made to the property that might affect flue performance.
All findings must be documented on the Benchmark commissioning checklist or equivalent documentation as required by UK regulations.
Gas engineers in the UK must be competent in these testing procedures and understand how to interpret results correctly, as mandated by Gas Safe Register and IGEM technical guidance.

## Slide 23: Flue flow testing procedure
The importance of flue flow testing
Flue flow testing is a critical safety procedure for Type B (open-flued) appliances in UK installations.
It verifies that the chimney or flue is capable of establishing and maintaining the natural draught necessary to safely remove combustion products from the building.

## Slide 24: Flue flow testing procedure
Step-by-step testing procedure
Ensure all doors, windows and vents are in their normal operating position
Turn off the appliance and allow it to cool if previously operating
Position a lit smoke match or smoke pellet at the draught diverter or flue connection
Observe the smoke movement; it should be drawn up into the flue
Check for any smoke spillage into the room
Repeat test with extract fans and air movement devices operating.

## Slide 25: Flue flow testing procedure
Interpreting results
According to UK standards:
Clear upward movement of smoke indicates acceptable flue performance
Hesitation or temporary reversal during extract fan operation may be acceptable if clearing within 30 seconds
Continued spillage or downward smoke movement indicates flue failure requiring immediate investigation
Results must be recorded on appropriate documentation.

## Slide 26: Spillage testing for open-flued appliances
When to perform spillage tests
UK regulations and industry guidance require spillage testing:
during the commissioning of new installations
as part of annual servicing
following property modifications (extensions, double glazing, etc.)
after installation of extract fans or ventilation systems
when investigating reports of fumes or CO alarm activation.

## Slide 27: Spillage testing for open-flued appliances
Test procedure
Follow this sequence in accordance with BS 5440-1:
Close all doors and windows in the room containing the appliance
Operate the appliance at maximum rate for at least 5 minutes
Hold a smoke match 5mm from the edge of the draught diverter
Move the match around the entire perimeter
Observe smoke behaviour for at least 30 seconds
Repeat with all extract fans in the property running.

## Slide 28: Spillage testing for open-flued appliances
Result interpretation
According to Gas Safe Technical Bulletin 200:
Pass: Smoke is drawn into the draught diverter with no spillage
Fail: Smoke spills from the draught diverter into the room
Borderline: Temporary spillage clearing within 30 seconds may be acceptable depending on appliance type and manufacturer guidance.
Failed tests require immediate action under GIUSP.

## Slide 29: Terminal positioning requirements
Critical safety considerations
Correct terminal positioning is essential for the safe operation of all flued gas appliances in UK installations. The location must:
allow safe dispersal of combustion products
prevent re-entry of flue gases into the building
maintain sufficient clearance from openings, obstructions and boundaries
account for prevailing wind conditions and potential pressure zones
consider the impact on neighbouring properties.

## Slide 30: Terminal positioning requirements
Critical safety considerations
Terminal positioning requirements vary significantly between natural draught and fan-assisted systems, with the latter generally allowing more flexibility but requiring careful attention to minimum clearances.

## Slide 31: Terminal positioning requirements
Key dimensional requirements
BS 5440-1 specifies minimum clearances including:
300mm from openings (windows, doors, vents)
300mm horizontally from gas/electric meters
1000mm from a facing wall or boundary (conventional flue)
600mm from an internal or external corner
2100mm from ground level, where people have access
specific dimensions for terminals near balconies, carports or adjacent flue terminals.

## Slide 32: Terminal positioning requirements
As a gas engineer in the UK, you must consult the current version of BS 5440-1 and manufacturer's instructions, as requirements may vary based on appliance type, flue gas temperature, and terminal design.

## Slide 33: Understanding natural draught mechanics
Physical principles
Natural draught chimney systems, common in many UK properties, operate on fundamental thermodynamic principles:
Thermal buoyancy: Hot flue gases are less dense than ambient air, creating upward pressure.
Stack effect: The height differential between the appliance and the terminal creates a pressure difference.
Temperature differential: Greater temperature difference between flue gases and outside air creates a stronger draught.

## Slide 34: Understanding natural draught mechanics
Physical principles
Flue resistance: Bends, restrictions and internal surface roughness impede flow.
The effectiveness of natural draught systems is described by the equation:
Where ΔP is pressure difference (Pa), h is chimney height (m), To is outside temperature (K) and Ti is flue gas temperature (K).

## Slide 35: Understanding natural draught mechanics
Factors affecting performance
UK gas engineers must consider several factors that influence natural draught:
Chimney height: Taller chimneys create stronger draught
Flue diameter: Must match appliance requirements
Insulation: Reduces cooling of flue gases
External conditions: Wind, temperature, atmospheric pressure
Terminal design: Must prevent downdraught
Building pressure: Extract fans can create negative pressure.

## Slide 36: Understanding natural draught mechanics
Failure to account for these factors can result in poor combustion, spillage, or condensation issues within the flue system.

## Slide 37: Knowledge check
Appliance classification
Which appliance type requires no chimney or flue?
Type A
Type B
Type C
All of them

## Slide 38: Knowledge check
Appliance classification
Which appliance type requires no chimney or flue?
Correct answer: A. Type A (flueless) appliances operate without a chimney or flue system but require specific ventilation provisions and safety devices.

## Slide 39: Knowledge check
Testing procedures
Which test specifically checks whether combustion gases are leaking into a room?
Tightness test
Combustion analysis
Spillage test
Standing pressure test

## Slide 40: Knowledge check
Testing procedures
Which test specifically checks whether combustion gases are leaking into a room?
Correct answer: C. Spillage testing is designed to detect whether combustion products are escaping from the appliance into the room rather than passing up the flue.

## Slide 41: Key takeaways
Appliance classification
You should now be able to confidently identify and classify gas appliances according to their flue requirements:
Type A: Flueless appliances requiring specific ventilation
Type B: Open-flued appliances using natural or mechanical draught
Type C: Room-sealed appliances with balanced flue systems.
This knowledge forms the foundation for proper specification and installation decisions.

## Slide 42: Key takeaways
System principles
You should now understand the fundamental operating principles of:
natural draught systems and factors affecting their performance
room-sealed systems and their safety advantages
the critical importance of proper terminal positioning
special precautions required for flueless installations.
These principles inform your technical decision-making process.

## Slide 43: Key takeaways
Testing and compliance
You can now identify appropriate testing procedures for flue safety:
visual inspection requirements
flue flow and spillage testing methodology
terminal positioning compliance checks
documentation requirements per UK regulations.
These skills ensure you can verify safe operation and meet regulatory obligations.

## Slide 44: Key takeaways
As a gas engineer in the UK building services sector, your understanding of chimney systems and their relationship to appliance types is essential for safe, compliant installations.
Remember that regulations and standards evolve; always refer to current versions of BS 5440, IGEM/UP guidelines, and Building Regulations Approved Document J when making installation decisions.

## Slide 45: Summary
You should now be able to:
Classify appliance types A, B and C by flue/chimney requirement.
Describe the fundamental operating principles of chimney/flue systems.
Compare the suitability of different flue types to appliance categories.
Identify appropriate testing procedures for flue safety and performance.

## Slide 46
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.