## Slide 1
Occupational Specialism: Gas Engineering
K1.15 Types of gas appliances and their system
requirements
PowerPoint 1.15a: Appliance types and functional differences

## Slide 2: Starter
Scenario: You walk into a kitchen and see a flueless gas heater on the wall and a gas hob. A water heater sits under the sink.
List the appliance types you’ve identified.
What system each one might be connected to
How you know it’s gas-powered
What makes each appliance type different.

## Slide 3: Objective
By the end of this session, you will be able to:
Identify the main categories of domestic and light commercial gas appliances.
Describe how each appliance type functions in delivering heat, hot water or cooking.
Compare operational differences between appliance types.
Explain why different systems are used for different applications.

## Slide 4: Water heaters: types and characteristics
Instantaneous water heaters
Also known as single point or multipoint heaters, these compact units heat water on demand as it flows through the appliance. Common in smaller properties where space is limited.
No storage cylinder required
Typically wall-hung for easy installation
Output ranges from 10-28kW depending on model
Flow rates typically 5-12 litres per minute

## Slide 5: Water heaters: types and characteristics
Storage water heaters
Contain an internal cylinder (10-150 litres) that preheats and stores hot water for later use.
Better for simultaneous hot water demands.
Requires more space than instantaneous models.
Lower flow rates but more consistent delivery.

## Slide 6: Water heaters: types and characteristics
Vented vs unvented systems
Affects pressure delivery and safety requirements:
Vented: Connected to cold water storage cistern, operates at low pressure, requires a vent pipe
Unvented: Connected directly to mains, high pressure, requires multiple safety valves including expansion, temperature relief and pressure relief valves.

## Slide 7: Water heaters: types and characteristics
Common brands and applications
Popular manufacturers include Rinnai, Morco, and Ariston.
Primarily used for domestic hot water (DHW) only, not connected to central heating systems.

## Slide 8: Central heating boilers: categories and operation
Combi boilers
The most popular boiler type in the UK, combination boilers provide both domestic hot water and central heating without requiring a cylinder.
Heats water directly from the mains
Space-saving design with no tanks or cylinders
Instant hot water but limited to one outlet at a time
Typically 24-35kW for domestic properties

## Slide 9: Central heating boilers: categories and operation
Regular boilers
Also called conventional or heat-only boilers, these work with traditional heating systems.
Sealed system:
A sealed central heating system is a closed-loop system where water circulates under pressure without exposure to the atmosphere, this is filled via a filling loop.

## Slide 10: Central heating boilers: categories and operation
Regular boilers
Also called conventional or heat-only boilers, these work with traditional heating systems.
Open vented system:
A vented central heating system is an open system that uses a feed and expansion cistern, typically located in the loft, to supply water and accommodate pressure changes, allowing air to escape and preventing over-pressurisation during heating.

## Slide 11: Central heating boilers: categories and operation
All modern boilers feature modulating burners that adjust output based on demand, increasing efficiency.
Common outputs range from 18-35kW for domestic properties, with leading brands including Vaillant, Worcester Bosch, and Ideal.
The selection of boiler type depends on property size, hot water demand, and existing system infrastructure.

## Slide 12: Space heaters: classifications and requirements
Types of gas space heaters
1. Open flued heaters
Draw combustion air from the room and vent products via a flue system.
Requires proper room ventilation
Minimum room size requirements
Traditional fireplace conversions often use this type

## Slide 13: Space heaters: classifications and requirements
2. Room-sealed heaters
Draw air and vent combustion products via a balanced flue terminal.
More efficient than open-flued models
Can be installed in smaller rooms
Less ventilation requirements
Often feature glass fronts for visual appeal

## Slide 14: Space heaters: classifications and requirements
3. Flueless heaters
Operate without a flue, requiring specific safety features.
Must have a built-in catalytic converter
Strict ventilation requirements
Limited to specific room sizes
Cannot be installed in bedrooms or bathrooms

## Slide 15: Space heaters: classifications and requirements
Applications and requirements
Space heaters are commonly used for heating:
Conservatories and extensions
Office spaces and commercial premises
Large rooms where central heating is insufficient
Properties without central heating systems.

## Slide 16: Space heaters: classifications and requirements
Installation considerations
When installing space heaters, engineers must consider:
Room volume calculations for adequate ventilation
Proximity to combustible materials
Flue routing and termination positions
CO detector requirements
Appropriate gas supply sizing.

## Slide 17: Space heaters: classifications and requirements
Popular brands include Superser, Valor, and Dimplex, with outputs typically ranging from 2-7kW depending on the model and application.

## Slide 18: Cookers and hobs: safety features and requirements
Types of gas cooking appliances
Free-standing cookers: Complete appliances featuring both oven and hob units, typically 50-60cm wide.
Built-in hobs: Integrated into worktops, with various burner configurations.
Built-in ovens: Installed within kitchen cabinetry, often at eye level.
Range cookers: Larger professional-style units, often 90-120cm wide with multiple ovens and burners.

## Slide 19: Cookers and hobs: safety features and requirements
Mandatory safety features
All modern gas cooking appliances must include:
Flame Supervision Devices (FSDs): Required by law to cut gas supply if flame is extinguished
Thermocouple: Senses heat from flame and keeps gas valve open
Flame failure devices: Automatic shut-off if flame detection fails
Pressure regulators: Ensure consistent gas pressure to burners.

## Slide 20: Cookers and hobs: safety features and requirements
Installation requirements
When installing gas cooking appliances, engineers must ensure:
Connection via rigid copper pipework or approved flexible connector (must comply with BS 669-1 or BS 669-2)
Appropriate ventilation based on room volume calculations
Minimum clearances from combustible materials
Correct burner settings using manufacturer's instructions (MI)
Stability brackets fitted where required
Accessible isolation valve within 1 metre of appliance.

## Slide 21: Cookers and hobs: safety features and requirements
Testing and Commissioning
After installation, engineers must:
Conduct tightness testing of the installation
Check standing and working pressures
Verify correct operation of all safety devices
Test combustion performance
Complete appropriate certification.

## Slide 22: Gas meters: types and installation
Domestic gas meters (≤6 m³/h)
Gas meters measure the volume of gas consumed and are typically rated according to their maximum flow capacity.
On the next slide, we will look at the common types of gas meters.

## Slide 23: Gas meters: types and installation
Common types:
Diaphragm (displacement) meters: Most common domestic type, using internal chambers that fill and empty with gas.
U6 Rating: Standard domestic meter with maximum capacity of approximately 6 cubic metres per hour.
Smart meters: Digital meters with remote reading capabilities, often still containing a diaphragm measuring element.
Credit meters: Traditional billing method where payment follows usage.
Prepayment meters: Requires payment before gas can be used, via card, key or app.

## Slide 24: Gas meters: types and installation
Location and installation requirements
Gas meters may be located:
Internally: Under stairs, in cupboards, or in purpose-built meter housings.
Externally: In weatherproof wall boxes or standalone meter kiosks.

## Slide 25: Gas meters: types and installation
System components
A typical domestic gas meter installation includes:
PE (polyethylene) supply pipe: Yellow underground pipe delivering gas to the property.
Emergency Control Valve (ECV): Located before the meter to isolate the entire property.
Regulator: Reduces gas pressure from medium pressure (75mbar) to low pressure (21mbar).
Meter outlet: Connection point for the consumer's installation pipework.
Electrical bonding: Required within 600mm of the meter outlet.

## Slide 26: Comparison of gas appliance types
Engineers must ensure meters are accessible for reading and maintenance, protected from damage, and installed in well-ventilated locations away from sources of heat or electrical hazards.

## Slide 27: Comparison of gas appliance types
Appliance type | Main use | Fuel type | System support needed | Key safety features
Water Heater | Domestic Hot Water (DHW) only | Natural Gas (NG) or Liquefied Petroleum Gas (LPG) | Cold feed, flue system, ventilation | Thermostat, overheat protection, flue gas analysis points
Combi Boiler | Central Heating (CH) + DHW | NG/LPG | Radiators, controls, flue, PRV | Pressure relief valve, low water pressure sensor, flame supervision device
System Boiler | CH + stored DHW | NG/LPG | Radiators, controls, flue, cylinder | Expansion vessel, pressure gauge, automatic air vent
Regular Boiler | CH + DHW via cylinder | NG/LPG | Feed/expansion tanks, cylinder, vent | Thermostat, pressure relief, overheat protection
Open Flued Space Heater | Room heating only | NG/LPG | Flue, ventilation | Thermocouple, spillage detection
Room-Sealed Space Heater | Room heating only | NG/LPG | Balanced flue terminal | Flame supervision device, pressure sensing
Flueless Space Heater | Room heating only | NG/LPG | Ventilation, ODS | Oxygen depletion sensor, catalytic converter
Cooker/Hob | Cooking | NG/LPG | Ventilation, stable surface | FSDs, flame failure devices
Gas Meter (U6) | Supply metering | NG | Regulator, ECV, bonding | Emergency control valve, protective housing

## Slide 28: Flue systems and classifications
Open flued systems (Type B)
These systems draw combustion air from the room where the appliance is installed:
Natural draught (B1): Relies on thermal buoyancy to remove products of combustion.
Fan-assisted (B2): Uses fan to assist removal of combustion products.
Vertex and SE-Duct: Specialised systems for multi-floor properties.

## Slide 29: Flue systems and classifications
Room-sealed systems (Type C)
These systems draw combustion air from outside the building:
Horizontal balanced flue (C1): Terminal through external wall
Vertical balanced flue (C3): Terminal through roof
Twin-pipe system (C5): Separate pipes for air intake and exhaust
Concentric ducts: Inner pipe for products, outer for fresh air.

## Slide 30: Flue systems and classifications
Installation requirements
When installing flue systems, engineers must consider:
Terminal positions and clearances from openings, boundaries, and other terminals
Flue sizing based on appliance output and length of run
Support brackets at appropriate intervals
Condensate disposal for condensing appliances
Fire stopping where flues pass through building elements
Access for inspection and maintenance.

## Slide 31: Flue systems and classifications
Testing and Commissioning
Flue performance must be verified by:
Visual inspection for correct installation
Spillage testing for open flued appliances
Flue gas analysis to verify combustion efficiency
Draught measurement where applicable
CO₂ and CO readings within manufacturer's specifications.

## Slide 32: Ventilation requirements for gas appliances
Open flued appliances
Require purpose-provided ventilation based on appliance input rating:
5cm² of free area per kW of input above 7kW
For example: 15kW appliance requires (15-7) × 5 = 40cm² ventilation
Ventilation must be direct to outside air
Openable windows do not constitute ventilation.

## Slide 33: Ventilation requirements for gas appliances
Room-sealed appliances
Typically do not require additional ventilation for combustion air, but may need ventilation for cooling:
No ventilation needed for most domestic installations
Compartment ventilation may be required in some cases
Boiler housings may need high and low level vents

## Slide 34: Ventilation requirements for gas appliances
Flueless appliances
Have strict ventilation requirements due to products of combustion entering room:
Minimum room size requirements (typically >40m³)
Permanent ventilation of at least 100cm²
Cannot be installed in bedrooms or bathrooms
Require specific air change rates.

## Slide 35: Ventilation requirements for gas appliances
Cooking appliances
Ventilation requirements depend on the installation scenario:
For domestic cooking appliances in rooms >10m³, no additional ventilation is typically required
Extract fans are recommended but not mandatory for domestic installations
Commercial cooking requires mechanical extraction and additional ventilation.

## Slide 36: Ventilation requirements for gas appliances
All ventilation requirements must comply with BS 5440-2 and Building Regulations Approved Document J.
Engineers must calculate requirements based on total input rating of all appliances in the room.
Ventilation grilles should be correctly sized, considering that decorative covers can significantly reduce effective free area.

## Slide 37: Gas pressure and flow requirements
Supply pressures
Understanding gas pressure is essential for proper appliance function:
Natural gas:
  Nominal working pressure: 21 mbar
  Acceptable range: 19-23 mbar

## Slide 38: Gas pressure and flow requirements
Supply pressures
LPG (Propane):
  Nominal working pressure: 37 mbar
  Acceptable range: 35-39 mbar
LPG (Butane):
  Nominal working pressure: 28 mbar
  Acceptable range: 26-30 mbar

## Slide 39: Gas pressure and flow requirements
Standing vs Working pressure
Standing pressure: Measured with appliance off, indicates gas supply pressure to property.
Working pressure: Measured with appliance running, indicates actual pressure at the appliance.

## Slide 40: Gas pressure and flow requirements
Flow rates and pipe sizing
Appropriate pipe sizing ensures adequate gas flow to appliances:
Pipe sizing depends on:
  Total load of all appliances
  Length of pipe run
  Number of fittings (elbows, tees)
  Acceptable pressure drop.
Maximum permissible pressure drop: 1 mbar
Sizing calculations must follow IGEM/UP/2

## Slide 41: Gas pressure and flow requirements
Typical gas consumption rates
Combi boiler (24kW): 2.5 m³/h
Gas fire (5kW): 0.5 m³/h
Gas cooker: 1.0 m³/h
Gas hob: 0.7 m³/h

## Slide 42: Combustion and efficiency
Combustion process
The chemical reaction in gas appliances:
Complete combustion requires the correct gas/air ratio and produces:
Carbon dioxide (CO₂), Water vapour (H₂O), Heat energy.
Incomplete combustion occurs with insufficient oxygen and produces:
Carbon monoxide (CO) - highly toxic, Carbon (soot), Less heat energy.

## Slide 43: Combustion and efficiency
Measuring combustion efficiency
Engineers test combustion performance using flue gas analysers, measuring:
CO₂ percentage (typically 8-10% for natural gas)
CO levels (should be <150ppm)
Flue gas temperature
Oxygen content
Calculated efficiency.

## Slide 44: Gas appliance controls and components
Gas valves
Control the flow of gas to the burner. Modern gas valves are multifunctional, incorporating:
Pressure regulation
On/off control
Flow modulation
Safety shut-off functions.

## Slide 45: Gas appliance controls and components
Thermostats
Measure and control temperature by switching the appliance on/off or modulating output:
Room thermostats
Cylinder thermostats
Limit thermostats
Frost protection thermostats.

## Slide 46: Gas appliance controls and components
Flame supervision devices
Safety components that detect the presence of flame:
Thermocouples: Generate a small voltage when heated
Flame rectification: Uses the electrical properties of flame
Shuts off gas if flame is extinguished.

## Slide 47: Gas appliance controls and components
PCBs and electronics
Printed Circuit Boards control modern appliance functions:
Sequencing operations
Monitoring safety parameters
Diagnostic capabilities
Communication with external controls.

## Slide 48: Gas appliance controls and components
Fans and pumps
Provide mechanical movement of air or water:
Circulation pumps in heating systems
Combustion fans for forced draught
Extract fans for ventilation.

## Slide 49: Gas appliance controls and components
Heat exchangers
Transfer heat from the combustion process to water or air:
Primary heat exchangers
Secondary (condensing) heat exchangers
Plate heat exchangers for instant hot water.

## Slide 50: Gas appliance controls and components
Understanding the function and operation of these components is essential for fault diagnosis, maintenance, and repair of gas appliances.
Modern appliances increasingly integrate smart controls and connectivity features, allowing remote operation and monitoring via smartphone applications.

## Slide 51: Operational differences between appliance types
Water heaters
Instantaneous water heaters activate only when hot water taps are opened, sensing water flow through a diaphragm or flow switch.
Heat is transferred directly to the flowing water without storage.
In contrast, storage water heaters maintain a cylinder of hot water at a preset temperature, using a thermostat to control heating cycles.

## Slide 52: Operational differences between appliance types
Boilers
A ‘Traditional Boiler’ is a boiler where the central heating system controls such as the pump, zone valves and other auxiliary controls are external to the appliance casing as supplied by the manufacturer.
A ‘System Boiler’ is boiler where one or more of the central heating system controls such as the pump, zone valves and other auxiliary controls are internal to the appliance casing as supplied by the manufacturer.
A ‘Combination Boiler’ is a boiler that provides instantaneous hot water to single or multiple hot water outlets, such as taps, with no water storage capacity

## Slide 53: Operational differences between appliance types
Space heaters
Space heaters transfer heat primarily through radiation and convection directly to the room air.
They operate independently from central heating systems, with controls focused on room temperature rather than water temperature.
Safety systems differ significantly from water-based appliances, with oxygen depletion sensors being critical for flueless models.

## Slide 54: Operational differences between appliance types
Cooking appliances
Cooking appliances have unique burner designs optimised for visible flames and heat distribution rather than efficiency.
They typically use simpler manual controls without electronic regulation, and safety systems focus on preventing gas leakage when flames are extinguished rather than temperature control.

## Slide 55: Operational requirements by appliance type
These operational differences directly affect installation requirements, maintenance procedures, and troubleshooting approaches.
Engineers must understand not only how each appliance functions individually but also how they interact when multiple appliances are installed in the same property.

## Slide 56: System requirements by appliance type
Appliance type | Water supply | Electrical requirements | Ventilation | Flue system
Instantaneous Water Heater | Minimum 0.5 bar pressure, flow rate >2 L/min | Battery or 230V depending on model | Required for open flued models | Open flued or room-sealed
Storage Water Heater | Header tank or mains pressure system | Typically 230V for controls | Required for open flued models | Open flued or room-sealed
Combi Boiler | Minimum 1.0 bar mains pressure | 230V, fused spur | Compartment ventilation may be needed | Room-sealed concentric or twin pipe
System Boiler | Feed and expansion tank or sealed system | 230V, fused spur | Compartment ventilation may be needed | Room-sealed concentric or twin pipe
Regular Boiler | Feed and expansion tank | 230V, fused spur | Compartment ventilation may be needed | Open flued or room-sealed
Open Flued Space Heater | None | None or 230V depending on model | Required based on input rating | Natural draught open flue
Room-sealed Space Heater | None | None or 230V depending on model | Typically not required | Balanced flue terminal
Flueless Space Heater | None | None | Permanent ventilation required | None (requires ODS)
Gas Cooker/Hob | None | None or 230V for ignition/clock | Typically not required in large rooms | None (extraction recommended)

## Slide 57: System requirements by appliance type
Understanding these system requirements is crucial for planning installations and ensuring that the property infrastructure can support the chosen appliance.
Engineers must verify that all necessary services are available and compatible before specifying or installing gas equipment.

## Slide 58: Appliance selection criteria and applications
Factors influencing appliance selection
When selecting the appropriate gas appliance for a property, engineers must consider:
Property size and heat demand: Calculate heat loss to determine required output
Hot water requirements: Number of outlets, simultaneous usage patterns
Available space: Physical dimensions and location constraints.

## Slide 59: Appliance selection criteria and applications
Existing infrastructure: Pipework, flue options, ventilation possibilities.
Energy efficiency goals: Carbon footprint reduction, running costs.
Budget constraints: Initial investment vs. operational savings.
User preferences: Ease of use, control requirements, aesthetic considerations.

## Slide 60: Appliance selection criteria and applications
Common applications by property type
Small apartments:
Combi boilers (24-28kW)
Integrated cooking appliances
Wall-mounted flueless heaters as secondary heat source.

## Slide 61: Appliance selection criteria and applications
Common applications by property type
Family homes:
Combi boilers (28-35kW) or system boilers with cylinders
Range cookers or built-in cooking appliances
Decorative gas fires.

## Slide 62: Appliance selection criteria and applications
Common applications by property type
Older properties:
Regular boilers working with existing gravity systems
Open flued gas fires in existing chimneys
Free-standing cookers.

## Slide 63: Appliance selection criteria and applications
Common applications by property type
Commercial premises:
Multiple boilers in cascade arrangements
Direct-fired air heaters
Commercial cooking equipment.

## Slide 64: Regulatory framework and standards
Gas Safety (Installation and Use) Regulations
The primary legislation governing gas work in the UK:
Requires all gas engineers to be Gas Safe registered
Mandates standards for installation, maintenance, and use of gas appliances
Sets requirements for landlords and gas safety checks
Establishes reporting procedures for unsafe installations.

## Slide 65: Regulatory framework and standards
British Standards
Key standards relevant to gas appliance installation:
BS 5440: Installation of flues and ventilation
BS 6891: Installation of low pressure gas pipework
BS 6172/6173: Installation of domestic/commercial cooking appliances
BS 5546: Installation of hot water supplies for domestic purposes.

## Slide 66: Regulatory framework and standards
Building Regulations
Relevant Approved Documents:
Part J: Combustion appliances and fuel storage systems
Part L: Conservation of fuel and power
Part F: Ventilation
Part P: Electrical safety (for appliances requiring electrical connections).

## Slide 67: Regulatory framework and standards
Industry Standards
Additional guidance documents:
IGEM/UP standards (Institution of Gas Engineers & Managers)
Gas Safe Technical Bulletins
Manufacturer's Instructions (MI)
ECA Technical Standards (Electrical Contractors' Association).

## Slide 68: Regulatory framework and standards
Compliance with these regulations and standards is mandatory for all gas installations.
Engineers must stay current with updates and amendments to ensure work meets the latest requirements.
Documentation of compliance through appropriate certification is a legal requirement for all gas work.

## Slide 69: Future trends in gas appliance technology
Hydrogen-ready appliances
The UK is exploring the potential of hydrogen as a replacement for natural gas:
Hydrogen-ready boilers capable of running on natural gas then converting to hydrogen
Initial blending of up to 20% hydrogen into existing gas networks
Zero carbon emissions at point of use when burning pure hydrogen
Different combustion properties requiring modified burners and controls.

## Slide 70: Future trends in gas appliance technology
Smart technology integration
Increasing connectivity and automation:
Internet-connected appliances with remote monitoring
Predictive maintenance using machine learning
Integration with home automation systems
Energy optimization through AI-driven control algorithms
Fault diagnosis and remote support capabilities.

## Slide 71: Future trends in gas appliance technology
Hybrid systems
Combining gas with renewable technologies:
Gas boilers working alongside heat pumps
Solar thermal integration with gas backup
Battery storage systems balancing energy demands
Intelligent switching based on efficiency and cost.

## Slide 72: Future trends in gas appliance technology
Enhanced efficiency
Continuing improvements in performance:
Higher efficiency condensing technology approaching theoretical limits
Micro-CHP (Combined Heat and Power) for simultaneous electricity generation
Advanced materials for better heat transfer
Improved modulation ranges for better part-load efficiency
Lower NOx emissions through improved burner design.

## Slide 73: Summary
You should now be able to:
Identify the main categories of domestic and light commercial gas appliances.
Describe how each appliance type functions in delivering heat, hot water or cooking.
Compare operational differences between appliance types.
Explain why different systems are used for different applications.

## Slide 74
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.