## Slide 1
Occupational Specialism: Gas Engineering
K1.6 Types of components and their suitability for different appliances and types of systems
PowerPoint 1.6e: Fans and air movement in gas appliances

## Slide 2: Starter
Starter task: Breathing boilers
Consider the following points when formulating your answer:
What are the fundamental requirements for complete combustion?
How does a room-sealed system differ from an open-flued system?
What safety benefits might a fan provide compared to natural draught?
How does a fan contribute to combustion efficiency?

## Slide 3: Objectives
By the end of this session, you should be able to:
Explain the role of fans in gas appliance combustion.
Describe pre-purge and post-purge sequences.
Identify common fan-related safety controls and components.
You might also be able to:
Diagnose airflow-related faults using APS and PCB logic.
Compare natural draught vs. fan-assisted systems.

## Slide 4: Why are fans used in modern appliances?
Modern gas appliances in the UK market have almost universally adopted fan-assisted combustion systems for several critical reasons:
Ensure forced draught combustion
Fans create positive pressure differentials that ensure combustion air and waste gases flow in the intended direction regardless of external conditions. This is essential for room-sealed systems which must maintain complete separation between the combustion process and the living space.

## Slide 5: Why are fans used in modern appliances?
Maintain correct air/gas ratio
Precise control of combustion air volumes is critical for achieving proper stoichiometric ratios, especially in modulating appliances where the heat output varies. Fans allow for this precision that natural draught systems cannot provide.
Remove products of combustion safely
Positive expulsion of waste gases is guaranteed through mechanical means rather than relying on thermal buoyancy effects. This is particularly important in condensing appliances where flue gas temperatures are significantly lower.

## Slide 6: Why are fans used in modern appliances?
Trigger safety interlocks
Fans create measurable pressure differentials that can be monitored by Air Pressure Switches (APS), providing positive confirmation of airflow before ignition is permitted, enhancing safety considerably.

## Slide 7: Why are fans used in modern appliances?
The integration of fans allows manufacturers to design more compact appliances with higher efficiencies (>90%) that would be impossible with traditional natural draught systems.
This has been crucial for meeting the UK's increasingly stringent energy efficiency requirements and building regulations.
Additionally, fan-assisted systems enable much greater flexibility in flue routing, allowing for horizontal flue terminations and longer flue runs that are often necessary in modern construction where traditional chimney access may be limited or non-existent.

## Slide 8: Combustion cycle – fan role
Cycle stage | Fan function | Technical details
Pre-purge | Clears flue of residual gases | Typically runs for 5-30 seconds (appliance specific). Must achieve sufficient flow to close the APS before ignition sequence proceeds. Creates positive pressure differential across the heat exchanger.
Ignition | Confirms air pressure for safety | Maintains consistent airflow during ignition to ensure proper air/gas mixture. APS must remain closed during this critical phase or lockout occurs.
Combustion | Maintains air flow for flame stability | In modulating appliances, fan speed varies proportionally with gas rate to maintain proper stoichiometric ratio. In fixed-rate appliances, maintains constant pressure differential.
Post-purge | Clears out remaining POC after shut-down | Continues running after gas valve closure (typically 5-120 seconds) to evacuate any unburned gas and cool the heat exchanger. Reduces condensation and thermal stress.

## Slide 9: Types of fans in gas appliances
Centrifugal fan
Most common in boilers and high-efficiency appliances.
Features a wheel with backwards-curved blades that draw air in axially and discharge it radially.
Provides high pressure differential suitable for overcoming resistance in heat exchangers and long flue runs.
Typically operates at 40-60W with speeds between 1500-5000 RPM depending on demand.

## Slide 10: Types of fans in gas appliances
Tangential fan
Used primarily in gas fires and some water heaters.
Features a cylindrical impeller with forward-curved blades that move air perpendicular to the axis.
Provides lower pressure but more uniform airflow across a wider area.
Its quieter operation makes it suitable for living-space appliances. It typically operates at 25-45W with lower RPM than centrifugal designs.

## Slide 11: Types of fans in gas appliances
Variable speed fan
Used in modulating and premium appliances.
Features DC motors with electronic speed control, allowing precise RPM adjustment based on demand.
Enables wider modulation ranges and better efficiency at part-load. Control methods include voltage variation (0-10V) or PWM (Pulse Width Modulation) signals from the PCB.
Higher cost but better performance and energy efficiency.

## Slide 12: Types of fans in gas appliances
Fan selection is determined by appliance design requirements including required pressure differential, noise constraints, physical space limitations, and modulation capabilities.
Understanding these differences is essential when diagnosing issues or selecting replacement components during service and repair work.

## Slide 13: Fan-assisted boiler operation
Airflow pathway
Primary air enters through the dedicated air inlet (often coaxial with flue).
Fan creates positive pressure differential across the system.
Air passes through venturi where gas is introduced.
Air/gas mixture enters burner for combustion.
Products of combustion (POC) pass through primary heat exchanger.
In condensing appliances, POC then pass through secondary heat exchanger.
Cooled POC exit via flue terminal.

## Slide 14: Fan-assisted boiler operation
Monitoring points
Air Pressure Switch (APS) connects via silicon tubes to measure the differential pressure created by the fan.
PCB monitors fan electrical feedback (speed sensor or current draw).
Flue Gas Temperature sensor monitors POC temperature.
Flue Gas Analysis test point provides access for combustion analysis.
Condensate trap collects and drains condensed water vapour.

## Slide 15: Fan-assisted boiler operation
This arrangement ensures that proper airflow is confirmed before ignition, combustion occurs with the correct air/gas ratio, and products of combustion are safely removed from the property as required by BS 5440 and manufacturer specifications.

## Slide 16: Fan safety interlocks
Air Pressure Switch (APS)
A differential pressure-activated switch that confirms adequate airflow before permitting ignition.
Connects to two pressure points via silicon tubes - one at positive pressure (fan outlet) and one at negative or atmospheric pressure (reference point).
Typically calibrated to specific pressure thresholds (e.g., 1.5-2.5 mbar). Must close its circuit before PCB will initiate ignition sequence.
Provides primary protection against insufficient combustion air or flue blockage.

## Slide 17: Fan safety interlocks
PCB feedback monitoring
Modern appliances monitor fan operation via electrical feedback:
Hall effect sensors detect actual rotation speed
Current monitoring detects electrical load
Voltage feedback confirms proper operation.
The PCB compares actual performance against expected parameters and will prevent or terminate operation if discrepancies are detected. This provides redundant protection beyond the APS.

## Slide 18: Fan safety interlocks
Flue thermostats/sensors
Temperature monitoring devices positioned in the flue passage that detect abnormal temperatures indicative of:
Restricted flue flow (temperature rise)
Heat exchanger fouling (temperature rise)
Excessive condensation (temperature drop).
These act as secondary safeguards that will shut down the appliance if temperatures exceed or fall below predetermined thresholds, even if the fan appears to be operating correctly.

## Slide 19: Fan safety interlocks
These interlocks form a comprehensive safety system that ensures the fundamental principle: NO FAN SIGNAL = NO IGNITION.
This multi-layered approach satisfies the requirements of British Standards and Gas Safety Regulations by preventing unsafe combustion conditions that could lead to carbon monoxide production or other hazards.
All these components must be functioning correctly for the appliance to operate, and any service or maintenance work must ensure they remain uncompromised.

## Slide 20: What happens if the fan fails?
Fan fault | Result | Risk | Classification
No pre-purge | Lockout | No ignition – safe failure mode | NCS (Not to Current Standards)
Fan running but no APS response | Lockout | Unsafe combustion / POC spillage if override attempted | ID (Immediately Dangerous)
Intermittent speed | Flame instability, cycling, noise | Incomplete combustion, efficiency loss | AR (At Risk) or ID depending on severity
Stuck post-purge | Fan continues running after shutdown | Excess energy use, premature component failure | NCS or AR depending on consequences
Delayed start-up | Extended ignition sequence | Potential for gas build-up before ignition | AR or ID depending on delay duration

## Slide 21: What happens if the fan fails?
Common fan fault causes:
Seized bearings due to dust accumulation or lubricant failure.
Blocked airways from debris, insect nests or condensate.
PCB fault affecting power supply or control signal.
Burnt-out windings from an electrical surge or component ageing.
Damaged impeller from foreign object impact.
Silicon tube disconnection or deterioration affecting APS.
Voltage fluctuations causing erratic operation.

## Slide 22: What happens if the fan fails?
When encountering fan issues, remember that the GIUSP (Gas Industry Unsafe Situations Procedure) classification determines your required action.
ID situations require immediate disconnection from the gas supply, while AR situations may permit continued operation with customer notification and scheduled repair.

## Slide 23: Fan testing and diagnostics
Visual inspection
Check for physical damage to fan housing or impeller.
Look for debris accumulation, soot deposits or signs of overheating.
Inspect silicon tubes for splits, disconnection or blockage.
Examine electrical connections for security and corrosion.
Check for oil leakage around bearings.

## Slide 24: Fan testing and diagnostics
Electrical testing
Measure voltage at fan terminals during call for heat (typically 230V AC).
Check resistance of fan windings against manufacturer specifications.
Test continuity of APS circuit when fan running at normal speed.
Measure current draw during operation (typically 0.15-0.30A).
Test for correct PWM signal in variable speed models (0-10V or digital pulse).

## Slide 25: Fan testing and diagnostics
Pressure testing
Use manometer to measure differential pressure across APS points.
Compare readings with manufacturer specifications (typically 1.5-2.5 mbar).
Verify APS closes at specified pressure and opens when pressure drops.
Check for pressure drop across the heat exchanger.
Verify flue performance using a smoke pellet or an analyser.

## Slide 26: Fan testing and diagnostics
Operational assessment
Observe complete start-up sequence including pre-purge timing.
Listen for unusual noises indicating bearing wear or imbalance.
Monitor post-purge operation and duration.
Check modulation response to changing demand (if applicable).
Observe shut-down sequence for proper termination.

## Slide 27: Fan testing and diagnostics
Always refer to manufacturer's technical documentation for specific test points, expected values, and diagnostic procedures.
Modern appliances often include self-diagnostic capabilities accessed through fault codes displayed on the user interface or through manufacturer-specific test modes.
Document all test results thoroughly as required by Gas Safe Register's inspection criteria and maintain appropriate records for future reference.

## Slide 28: Natural draught vs Fan-assisted systems
Feature | Natural draught | Fan-assisted
Combustion air source | Room air (requires permanent ventilation) | Forced via fan (typically room-sealed)
Flue type | Open flue / conventional chimney | Balanced flue (often coaxial design)
Efficiency | Lower (typically 65-78%) | Higher (typically 85-94%)
Safety controls | FSD (Flame Supervision Device) only | APS, PCB, multiple sensors
Draught dependence | Highly affected by weather conditions | Minimal weather influence
Installation flexibility | Requires vertical rise, chimney access | Horizontal flues possible, greater distances
Common in UK market | Pre-2000 installations, reducing rapidly | Standard in most post-2000 installations

## Slide 29: Natural draught vs. Fan-assisted systems
Over the past 30 years, domestic gas appliances have shifted from natural draught to fan-assisted systems due to efficiency, safety, and building needs.
UK gas engineers mainly install fan-assisted systems today, but must still know natural draught appliances, especially in older homes.

## Slide 30: Formative check – fan and airflow
Question 1
What is the main purpose of the pre-purge cycle in a fan-assisted boiler?
Warm the heat exchanger before ignition
Clear the flue and combustion chamber of residual gases
Dry the burner surface to prevent condensation
Pressurise the system to check for gas leaks

## Slide 31: Formative check – fan and airflow
Question 2
What component typically triggers the ignition sequence after the fan starts?
Overheat thermostat
Thermistor
Air Pressure Switch (APS) closure
Flow switch

## Slide 32: Formative check – fan and airflow
Question 3
Which of the following would be classified as "Immediately Dangerous" according to GIUSP?
A fan that continues to run during post-purge longer than specified
A fan that makes occasional noise but operates normally
A fan that runs but the APS has been bypassed with a wire link
A fan that starts slowly but achieves proper pressure

## Slide 33: Formative check – fan and airflow
Question 4
Which statement about centrifugal fans is correct?
They are primarily used in decorative gas fires
They draw air in axially and discharge it radially
They operate at lower pressures than tangential fans
They cannot be used with modulating gas valves

## Slide 34: Formative check – fan and airflow
Answers: 1-B, 2-C, 3-C, 4-B
These questions cover key concepts regarding fan operation, safety implications, and technical characteristics.
If you struggled with any of these questions, please review the relevant sections or ask for clarification before we proceed.

## Slide 35: Summary
You should now be able to:
Explain the role of fans in gas appliance combustion.
Describe pre-purge and post-purge sequences.
Identify common fan-related safety controls and components.
You might also be able to:
Diagnose airflow-related faults using APS and PCB logic.
Compare natural draught vs. fan-assisted systems.

## Slide 36
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.