## Slide 1
Occupational Specialism: Gas Engineering
K1.8 Factors that affect the choice and suitability of components included in a system
PowerPoint 1.8b: Certification, legislation, efficiency and environmental considerations

## Slide 2: Starter
Scenario: A technician fits a low-cost solenoid valve from an online retailer. It is not CE or UKCA marked. The appliance operates, but two weeks later the valve jams, causing a lockout.
Should this valve have been used?
What are the risks of non-certified parts?
What should have been checked before installation?

## Slide 3: Objectives
By the end of this session, you should be able to:
Explain why certification is required for gas components.
Identify relevant regulations and compliance standards.
Evaluate component suitability in terms of efficiency and environmental impact.
Apply knowledge of legislation to safe part selection.

## Slide 4: Certification and approval marks
Certification marks provide assurance that components meet specific safety, quality and performance standards.
Understanding these marks is essential for compliant gas installations.
It is illegal under the Gas Safety (Installation and Use) Regulations (GSIUR) to fit non-compliant components in gas systems.
This can result in prosecution, loss of Gas Safe registration, and potential harm to customers.

## Slide 5: Certification and approval marks
Marking | What it means
CE Mark | European conformity standard (still valid for older legacy systems in the UK)
UKCA Mark | UK Conformity Assessment (post-Brexit replacement for CE marking)
WRAS | Water Regulations Advisory Scheme approval (required for components in contact with water supply)
Manufacturer Approval | Component is specifically approved for use with the particular model (especially important for spare parts)

## Slide 6: Legislation and compliance framework
Gas Safety (Installation and Use) Regulations
Regulations 26 & 34 specifically address the requirement to use safe, approved equipment in gas installations.
These regulations place legal obligations on gas engineers to ensure all components are compliant.
Non-compliance can result in criminal prosecution, with penalties including fines and imprisonment for serious breaches.

## Slide 7: Legislation and compliance framework
IGEM/UP/1B Standards
This industry standard outlines requirements for commissioning, pressure testing, and tightness checking of gas installations.
Components must be suitable for these testing procedures.
These standards provide specific guidance on component selection based on pressure ratings, material compatibility and installation requirements.

## Slide 8: Legislation and compliance framework
Building Regulations
Part J covers combustion appliances and fuel storage systems, while Part L addresses conservation of fuel and power.
Components must enable compliance with these regulations.
These regulations establish minimum standards for flueing systems, energy efficiency metrics, and emissions limitations for gas installations.

## Slide 9: Legislation and compliance framework
Gas Safe Rules
These rules establish engineer accountability and installation sign-off procedures. Engineers must be able to verify the compliance of all components used.
Failure to comply can result in At Risk (AR) or Immediately Dangerous (ID) classifications, requiring immediate remedial action.

## Slide 10: Efficiency and environmental impact
Component selection plays a crucial role in determining the overall efficiency and environmental impact of gas systems. Engineers have a professional responsibility to consider these factors when specifying and installing components.
Key efficiency considerations:
Condensing efficiency (influenced by fan design and heat exchanger material quality).
Modulation capability (particularly in advanced gas valves with smart controls).
Low-NOx burner technology (reducing harmful emissions).
Insulation quality in pipework and heat exchange components.
Energy-saving control systems (thermostatic, weather compensation, etc.).

## Slide 11: Efficiency and environmental impact
Why efficiency matters:
Reduced carbon footprint and greenhouse gas emissions.
Supports compliance with Energy Related Products (ERP) Directive.
Delivers lower energy bills and better outcomes for customers.
Contributes to UK carbon reduction targets.
Enhances the reputation of gas engineers as environmentally responsible professionals.

## Slide 12: Repairability and lifecycle thinking
Manufacturer-approved parts
Using genuine, manufacturer-approved components ensures compatibility, maintains warranty coverage, and provides assurance of appropriate safety testing.
These parts are designed specifically for the appliance, minimising the risk of malfunction or premature failure.

## Slide 13: Repairability and lifecycle thinking
Modular components
Selecting modular components allows for easier replacement without requiring a full system overhaul.
This approach reduces material waste, lowers repair costs, and minimises system downtime.
Modern boiler designs increasingly feature plug-and-play components that simplify maintenance.

## Slide 14: Repairability and lifecycle thinking
Durable materials
Components manufactured from high-quality, durable materials significantly reduce breakdown frequency and environmental waste.
Consider stainless steel heat exchangers over aluminium for longevity, or brass fittings rather than plastic for critical connections exposed to temperature fluctuations.

## Slide 15: Repairability and lifecycle thinking
Recyclable parts
Selecting components with recyclable materials improves sustainability in long-term planning.
Many manufacturers now provide information on material composition and recycling pathways for their components, allowing for responsible disposal at end-of-life.
Smart engineers choose components that are not only safe and compliant but also sustainable throughout their lifecycle.

## Slide 16: Sourcing components – best practice guidelines
Essential pre-purchase checks:
Manufacturer model compatibility (check technical specifications).
Part numbers and serial codes (verify against manufacturer documentation).
Certification status (confirm CE/UKCA marking and other relevant approvals).
Supplier credentials (purchase from authorised distributors only).
Material specifications (ensure compatibility with existing system).
Warranty conditions (understand what is covered and for how long).

## Slide 17: Sourcing components – best practice guidelines
Gas Safe inspectors may request documentation proving the use of compliant components during audit visits.
Maintain records of part numbers, supplier details and certification for all installations.

## Slide 18: Component failure risk assessment
Initial risk: Non-compliant part selection
Using non-certified components immediately places the installation at risk.
Engineers may face immediate liability for knowingly installing non-compliant parts, regardless of whether failure occurs.
Short-term consequences
Component failure within weeks or months can lead to system lockouts, inefficient operation, or intermittent faults that are difficult to diagnose.
This period typically falls within warranty periods, creating conflict between customers and engineers.

## Slide 19: Component failure risk assessment
Medium-term impacts
Continued operation with substandard components may result in damage to other system parts, increased emissions, efficiency losses, and potential safety hazards. These issues may emerge after warranty periods expire.
Long-term system integrity
The cumulative effect of poor component selection includes premature system replacement, potential property damage from leaks or fires, and invalidation of building insurance policies. The reputational damage to engineers can be permanent.

## Slide 20: Environmental impact of component selection
Emissions
Component quality directly affects combustion efficiency and emissions levels. Poor-quality burners and heat exchangers can increase NOx emissions, while inefficient gas valves may lead to incomplete combustion and increased carbon monoxide production.
Energy consumption
High-quality components with precise tolerances ensure optimal fuel usage. Modulating pumps, fans and gas valves can reduce energy consumption by 15-30% compared to older on/off technologies.

## Slide 21: Environmental impact of component selection
Lifecycle impact
Durable components reduce the environmental footprint associated with manufacturing, shipping and disposal of replacement parts. Stainless steel heat exchangers, for example, may last 15+ years compared to 7-10 years for aluminium alternatives.
End-of-life considerations
Components with recyclable materials and clear disposal guidelines reduce landfill waste. Many manufacturers now participate in take-back schemes for proper processing of electronic and hazardous components.

## Slide 22: Component certification process explained
Understanding how components receive certification helps engineers appreciate the importance of using approved parts. The certification process involves rigorous testing to ensure safety, reliability and performance.
Key stages of certification
Design assessment: Review of technical documentation against relevant standards.
Type testing: Physical testing of samples under various conditions.
Production facility assessment: Evaluation of manufacturing quality control.
Certification issue: Award of certification mark upon successful completion.
Ongoing surveillance: Regular retesting and factory audits.

## Slide 23: Component certification process explained
Testing parameters include:
Pressure resistance (hydraulic and pneumatic).
Temperature tolerance (cycling and extremes).
Material compatibility with gas types.
Electrical safety (where applicable).
Operational reliability over extended cycles.
Performance under adverse conditions.
Endurance and fatigue resistance.

## Slide 24: Identifying counterfeit components
The rise in counterfeit gas components presents a serious safety concern for the industry. Gas engineers need to develop skills to identify potentially dangerous counterfeit parts before installation.

## Slide 25: Identifying counterfeit components
Warning signs:
Unusually low prices (30%+ below standard market rates).
Packaging discrepancies (poor printing quality, spelling errors).
Missing or poorly applied certification marks.
Inconsistent weight or feel compared to genuine parts.
Irregular serial number patterns or missing batch codes.
Untraceable supply chain or unfamiliar online retailers.

## Slide 26: Identifying counterfeit components
Verification methods:
Verify through manufacturer's official verification tools.
Check serial numbers on manufacturer databases.
Purchase only from authorised distributors.
Use manufacturer apps to scan QR codes or barcodes.
Compare with known genuine components.
Request certification documentation from suppliers.

## Slide 27: Components and forward compatibility
Future-proof selection - Choose components compatible with emerging technologies.
Hydrogen readiness - Select components certified for potential hydrogen blending (up to 20% H₂).
Smart system integration - Ensure compatibility with developing smart home systems and IoT connectivity.
Regulatory anticipation - Consider forthcoming regulatory changes, such as enhanced efficiency requirements.
Full lifecycle planning - Evaluate the complete component lifecycle, including eventual replacement availability.

## Slide 28: Components and forward compatibility
As the gas industry evolves toward greater sustainability and integration with renewable systems, component selection must account for future technological developments and regulatory changes.
Engineers should consider the medium to long-term compatibility of components with emerging technologies such as hydrogen-ready systems, smart controls, and hybrid heating solutions.

## Slide 29: Key takeaways
Certification is non-negotiable
CE/UKCA marking and manufacturer approval are legal requirements under GSIUR, not optional extras. Using non-certified components is both illegal and dangerous.
Efficiency drives value
Component selection significantly impacts system efficiency and environmental performance. Higher quality components typically deliver better long-term value despite higher initial costs.

## Slide 30: Key takeaways
Documentation matters
Maintain comprehensive records of component specifications, certification and supplier details for each installation. This protects both you and your customers.
Future-proofing is essential
Select components with consideration for emerging technologies and regulatory changes, particularly regarding hydrogen compatibility and smart system integration.

## Slide 31: Summary
You should now be able to:
Explain why certification is required for gas components.
Identify relevant regulations and compliance standards.
Evaluate component suitability in terms of efficiency and environmental impact.
Apply knowledge of legislation to safe part selection.

## Slide 32
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.