## Slide 1
Occupational Specialism: Gas Engineering
K1.21 Types of fixtures and suitability for different building fabrics
PowerPoint 1.21a: Fixtures

## Slide 2: Starter
Today, we will examine the various types of fixings and the significance of selecting the appropriate one for each task.
Making the correct choice ensures safety, security, and compliance.
Reflecting on what you have previously learnt, can you identify the different types of fixings utilised in the gas industry?

## Slide 3: Objectives
By the end of this session, you should be able to:
Identify the main types of fixings used in building construction (screws, nails, solid wall fixings, plasterboard fixings, security bolts).
Describe the properties and advantages of each fixing type.
Explain the basic characteristics of different building fabrics (wooden partitions, plasterboard walls, brick walls, block walls).

## Slide 4: Screws
Screws are fasteners with threads that are driven into a material using either manual or electric screwdrivers.
They are available in multiple varieties (such as wood screws, self-tapping screws, and masonry screws) and sizes to suit different applications.

## Slide 5: Screws
Appropriate for:
Wooden partitions: Wood screws provide a strong hold in timber, making them perfect for timber frames and battens.
Brick/block walls (using wall plugs): Screws can be paired with plastic wall plugs to secure them in masonry.
Plasterboard (with drywall plugs or anchors): Certain screws are specifically crafted for use in drywall when combined with appropriate fixings.

## Slide 6: Nails
Nails are elongated metal rods featuring a pointed tip at one end and a flat head at the opposite end.
They are inserted into materials using a hammer or a nail gun.

## Slide 7: Nails
Benefits:
Simple and fast installation process.
Economical choice for extensive projects.
Offers greater flexibility under stress, which can be advantageous in specific wooden constructions.
Appropriate for:
Wooden dividers: Frequently utilised for framing, panelling, and securing timber mouldings.
Unsuitable for solid walls or plasterboard because of insufficient grip and the risk of damaging the surface.

## Slide 8: Solid wall fixings
These fasteners are intended for use with heavy, solid materials such as concrete, brick, and stone.
Typical varieties consist of:
Wall plugs (also known as rawl plugs)
Sleeve anchors
Through bolts and shield anchors.

## Slide 9: Solid wall fixings
Advantages:
Delivers an incredibly firm hold for challenging tasks.
Reliable in load-bearing structures.
Suitable for:
Brick walls: Ideal for fastening cabinets, boilers, and radiators.
Block walls: Used in situations requiring strong and stable anchoring.
Not advisable for plasterboard or wooden surfaces.

## Slide 10: Plasterboard fixings
These fasteners are designed specifically for hollow or soft wall materials, such as plasterboard.
The types include:
Self-drilling anchors
Toggle bolts
Spring toggles or snaptoggles

## Slide 11: Plasterboard fixings
Advantages:
Prevents the board from crumbling or experiencing pull-through.
Distributes weight over a wider surface area.
Suitable for:
Plasterboard walls: Ideal for installing shelves, curtain rods, or small fixtures.
Not recommended for use on brick or block walls.

## Slide 12: Security bolts
Security bolts are engineered to be resistant to tampering or tampering-proof.
Typically, they necessitate specialised tools and may feature anti-theft designs such as:
Clutch head screws
One-way bolts
Pin hex bolts

## Slide 13: Security bolts
Benefits:
Prevent unauthorised entry or theft.
Offer a polished appearance while ensuring public safety.
Appropriate for:
Brick or block walls: Ideal for securing outdoor or publicly accessible equipment.
Wooden surfaces: Useful for securing enclosures or panels.
Plasterboard (when using anchors): Suitable for tamper-resistant panels in commercial environments.

## Slide 14
Fixing type suitability overview
Fixing type | Wood | Plasterboard | Brick/Block
Screws | ✅ | ✅ (with plug) | ✅ (with plug)
Nails | ✅ | ❌ | ❌
Solid Wall Fixings | ❌ | ❌ | ✅
Plasterboard Fixings | ❌ | ✅ | ❌
Security Bolts | ✅ | ✅ (with anchor) | ✅

## Slide 15: Summary
You should now be able to:
Identify the main types of fixings used in building construction (screws, nails, solid wall fixings, plasterboard fixings, security bolts).
Describe the properties and advantages of each fixing type.
Explain the basic characteristics of different building fabrics (wooden partitions, plasterboard walls, brick walls, block walls).

## Slide 16
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.