## Slide 1
Occupational Specialism: Gas Engineering
K1.21 Types of fixtures and suitability for different building fabrics
PowerPoint 1.21b: Building fabrics

## Slide 2: Starter
Today, we will explore the different categories of building fabrics.
Understanding the specific type of building fabric we are repairing or working with allows us to determine the appropriate fixing type that we discussed earlier.

## Slide 3: Objectives
By the end of this session, you should be able to:
Recall the different types of fixtures used in gas engineering and construction.
Identify common building fabrics and describe their physical characteristics.
Compare and contrast different fixing methods and evaluate their effectiveness.

## Slide 4: Block walls
Block walls are usually made from concrete or lightweight aerated concrete blocks. They can vary in density but are generally solid.
Fixing considerations:
Can be brittle; care must be taken to avoid cracking.
Load capacity depends on block type (lightweight vs. dense concrete).
Applications:
Radiator brackets, pipe clips, frames, cupboards.

## Slide 5: Brick walls
Traditional fired clay bricks, either in solid or cavity form, found in internal and external walls.
Fixing considerations:
Mortar joints can weaken over time—avoid fixing into them directly.
Cavity walls require caution to avoid bridging insulation or damaging the inner skin.
Applications:
External pipework, hanging heavy items, boiler fixings.

## Slide 6: Wooden partitions
Stud walls made from timber, often faced with plasterboard. They are commonly found in internal room partitions.
Fixing considerations:
Fastening into the timber frame is preferred (locate studs first).
May not support heavy loads unless reinforced.
Applications:
Lightweight shelving, pipe clips, small cabinets.

## Slide 7: Plasterboard walls
Gypsum board fixed to timber or metal studs; hollow behind the board. Common in modern internal partitions.
Fixing considerations:
Low load-bearing capacity unless fixing into studs.
Easy to damage with excessive force.
Applications:
Light fittings, towel rails, small shelves (preferably on stud).

## Slide 8
Fixing type suitability overview
Building fabric | Best fixings | Notes
Block Walls | Solid wall fixings, screws with long plugs, frame fixings | Check block type; avoid brittle aerated blocks without correct anchors
Brick Walls | Wall plugs, frame fixings, chemical anchors | Avoid mortar joints; consider cavity wall implications
Wooden Partitions | Wood screws, nails, security bolts | Fix into studs for strength
Plasterboard Walls | Toggle bolts, spring toggles, self-drill plasterboard fixings, screws into studs | Do not overload plasterboard; always try to find studs

## Slide 9: Summary
You should now be able to:
Recall the different types of fixtures used in gas engineering and construction.
Identify common building fabrics and describe their physical characteristics.
Compare and contrast different fixing methods and evaluate their effectiveness.

## Slide 10
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.