## Slide 1
Occupational Specialism: Gas Engineering
K1.16 Scientific principles and concepts as applied to gas engineering
PowerPoint 1.16b: Types of combustion and reactions

## Slide 2: Starter
Today we’re going to start by thinking about the different types of flames we might encounter – both in safe environments and in hazardous ones.
Let’s begin with a question: ‘Describe a time you’ve seen a fire, explosion, or flare. What made it different from a typical blue gas flame?’
This could be something you’ve seen on a building site, in a workshop, at home, or even on the news.

## Slide 3: Objectives
By the end of this session, you should be able to:
Define and classify the five main types of combustion.
Compare slow and rapid combustion reactions.
Identify the risks and features of explosive combustion.
Explain the causes and implications of smouldering or diffusion flames in appliances.

## Slide 4: Recap – What is combustion?
Combustion is a key scientific concept in gas engineering, describing a chemical reaction that occurs between a fuel (usually a hydrocarbon gas like natural gas or LPG) and oxygen, which produces heat and light.
This process is essential for the functioning of gas appliances utilised in heating, cooking, and hot water systems.
In the following slides, we will explore the various types of combustion.

## Slide 5: What is combustion?
Complete combustion is the chemical reaction that occurs when a fuel burns in the presence of a sufficient supply of oxygen, allowing all the carbon in the fuel to convert to carbon dioxide (CO₂) and all the hydrogen to convert to water vapour (H₂O).
This reaction produces a clean, blue flame, maximum heat output, and minimal harmful emissions.

## Slide 6: What is combustion?
Incomplete combustion occurs when fuel burns with insufficient oxygen, leading to the production of carbon monoxide (CO), soot, and other harmful by-products instead of just carbon dioxide (CO₂) and water vapour (H₂O).
This process is less efficient, produces less heat, and can create serious health risks due to toxic gases. In gas appliances, it is often shown by a yellow or orange flame, indicating a need for maintenance or improved ventilation.

## Slide 7: What is combustion?
Stoichiometric combustion is the ideal chemical reaction in which a fuel burns with the exact amount of oxygen required for complete combustion, no more and no less.
This means all the carbon in the fuel is converted to carbon dioxide (CO₂) and all the hydrogen is converted to water vapour (H₂O), with no unburned fuel or excess oxygen in the products

## Slide 8: Five types of combustion in gas engineering
​
Combustion is defined as the process of igniting a fuel in combination with an oxidiser, most commonly oxygen, to produce heat and light. In gas engineering, understanding the principles of combustion is essential for ensuring the safety, efficiency, and adherence to regulations of various appliances.
Instead of merely evaluating the flame's colour or temperature, combustion can be classified according to the interaction between fuel and air, the rate of reaction, and the surrounding environmental conditions.
Throughout the industry, different types of combustion can be encountered, which we will delve into in the subsequent slides.

## Slide 9: 1. Chemical combustion
In a controlled environment, fuel combines with oxygen (for instance, in a boiler burner).
Commonly used in boilers, gas fires, and cookers equipped with premixed burners.
Regulated air-fuel mixture – produces a steady flame with high efficiency.
This method is safe and optimal.
​

## Slide 10: 2. Smouldering
Gradual oxidation at low temperatures without flames.
Extremely slow oxidation occurring without an open flame.
Happens due to a limited oxygen supply.
May take place in obstructed burners or areas with inadequate ventilation.
Risk: Can result in the accumulation of carbon monoxide. ​

## Slide 11: 3. Diffusion
Gas and air combine following ignition (for instance, in cookers and open flame devices).
Gas and air interact post-ignition.
This is typical in older open-flame devices or cookers.
These systems are less efficient and present a greater CO risk if ventilation is inadequate.
Uses: hob burners, decorative fires Maintenance Advice: Ensure air inlets are free of debris.

## Slide 12: 4. Spontaneous
Ignition can happen without an external spark or flame.
Chemical self-heating can ignite materials without a spark.
While it is uncommon in gas engineering, it can occur in:
Areas where oily rags are stored
Situations where heat accumulates in insulation
This phenomenon is more frequent with solid fuels, but it is crucial to be aware of it in confined environments.
Control measures: ensure proper storage and adequate ventilation.

## Slide 13: 5. Explosive
A rapid reaction can lead to a shockwave resulting from the ignition of a gas-air mixture.
When the gas-air mixture falls within the flammable range and is ignited, it results in an explosion.
Key factors include the Lower Explosive Limit (LEL) and Upper Explosive Limit (UEL).
For methane, the LEL is approximately 5%, while the UEL is around 15%.

## Slide 14: 5. Explosive
Common triggers include:
Delayed ignition.
Failure of the pilot light.
Leaks in enclosed spaces.

## Slide 15: Combustion Triangle
Fire Triangle (Combustion Triangle)
Illustrates the process of how fire ignites and is maintained
Element | Description
Fuel | Any combustible material (gas, liquid, solid) that can burn.
Oxygen | Supports combustion (usually from the air; approx. 21% oxygen).
Heat | The ignition source that raises the fuel to its ignition temperature.
Essential concept:
Eliminate any single one of the three components, and the fire will not ignite or will be extinguished.

## Slide 16: Applying knowledge to appliances
Task:
Associate these appliance issues with the appropriate type of combustion:
Clogged air inlet on a boiler.
An operational hob.
Delayed ignition of the pilot light leading to a boom.
Cloth’s left near flue outlets.
Completely premixed condensing boiler.

## Slide 17: Knowledge check quiz
Which type of combustion is used in condensing boilers?
What type occurs when air mixes with gas after ignition?
What does LEL stand for?
Name a cause of explosive combustion in domestic settings.

## Slide 18: Summary
You should now be able to:
Define and classify the five main types of combustion.
Compare slow and rapid combustion reactions.
Identify the risks and features of explosive combustion.
Explain the causes and implications of smouldering or diffusion flames in appliances.

## Slide 19
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.