## Slide 1
Occupational Specialism: Gas Engineering
K1.10 Safety devices applicable to gas systems, their characteristics and operation
PowerPoint 1.10b: Combustion and airflow safety – APS, FSD, CO detectors

## Slide 2: Starter
A boiler fan runs, but the burner won’t ignite. The system attempts ignition three times, then locks out.
Discuss:
What safety device might be preventing ignition?
What conditions must be met before the PCB allows the burner to light?

## Slide 3: Objectives
You should be able to:
Identify key combustion safety devices: APS, FSD, CO detector.
Explain how each device protects appliance’s operation.
Describe how to test and confirm the operation of these devices.
Apply system knowledge to troubleshoot and replace components safely.

## Slide 4: Air Pressure Switch (APS)
Function and operation
The Air Pressure Switch is a critical safety component that ensures proper ventilation before combustion is permitted to occur.
It functions as a differential pressure monitoring device connected to the PCB (Printed Circuit Board).

## Slide 5: Air Pressure Switch (APS)
Primary functions
Confirms sufficient airflow before ignition sequence.
Senses pressure differential created by the fan operation.
Prevents burner operation if flue is blocked or fan fails.
Acts as first safety check in combustion sequence.

## Slide 6: Air Pressure Switch (APS)
Integration
Connected to PCB via electrical connections.
Must prove sufficient draught for boiler to proceed.
Typically linked to fan via silicone tubing.
Calibrated to specific pressure thresholds.

## Slide 7: Air Pressure Switch (APS)
Testing methods
Simulate pressure with manometer.
Check continuity with fan off/on.
Inspect tubing for blockages or splits.
Verify correct voltage signals to PCB.

## Slide 8: Air Pressure Switch (APS)
A typical APS failure presents with specific fault indicators:
Burner lockout after multiple ignition attempts.
Fan runs continuously without ignition.
Specific error codes on digital displays (varies by manufacturer).
Cycling on/off behaviour without establishing flame.
When replacing an APS, engineers must ensure the replacement has identical pressure ratings and connection configurations to maintain system safety integrity.

## Slide 9: Flame Supervision Device (FSD)
Purpose and operation
The Flame Supervision Device serves as a critical safety mechanism that continuously monitors flame presence during appliance operation. It prevents the release of unburned gas if the flame is extinguished or fails to establish.
Type | Common Applications | Operating Principle
Thermocouple | Cookers, gas fires, older boilers | Generates millivolts when heated, holds gas valve open.
Flame rectification | Modern boilers, water heaters | Uses flame's conductivity to create DC current flow.
Thermal devices | Simple appliances, pilot lights | Uses bimetallic strip or expansion properties.

## Slide 10: Flame Supervision Device (FSD)
Process for thermocouple operation:
Thermocouple junction heats when exposed to flame.
Generates small electrical potential (15-30 millivolts).
Current maintains electromagnetic coil in gas valve.
Valve remains open only while current flows.
If the flame supervision signal is lost, the SSOV or gas valve will shut automatically within prescribed safety timeframes (typically under 1 second). This prevents the accumulation of unburned gas which could pose an explosion risk.

## Slide 11: Carbon Monoxide (CO) detector
Life-saving detection systems
Carbon monoxide detectors provide crucial protection against this odourless, colourless and lethal gas. Unlike APS and FSD, which are integrated into appliances, CO detectors are typically standalone devices installed in occupied spaces.
Alarm thresholds
50 ppm - Alarm after 60-90 minutes (long exposure).
100-300 ppm - Alarm within 10-40 minutes (medium exposure).
300+ ppm - Alarm within 3 minutes (immediate danger).

## Slide 12: Carbon Monoxide (CO) detector
Correct positioning
1-3 metres from fuel-burning appliance.
Ceiling mount or high wall placement (CO rises slightly).
Away from extractors, windows and draughts.
Within hearing range of sleeping areas.

## Slide 13: Carbon Monoxide (CO) detector
Testing requirements
Regular testing via test button (monthly recommended).
Replace batteries annually (if not hard-wired).
Replace entire unit every 5-10 years (check manufacturer).
Must comply with BS EN 50291 standards.

## Slide 14: Carbon Monoxide (CO) detector
CO detectors use electrochemical sensors that react to the presence of carbon monoxide by generating a current proportional to the gas concentration.
This triggers the alarm when dangerous levels are detected.
Critical safety requirement
All flueless appliances MUST have CO detection installed in the same room.
This includes flueless gas fires, some types of cookers, and certain types of space heaters.
This is a mandatory requirement under Gas Safety (Installation and Use) Regulations.

## Slide 15: Carbon Monoxide (CO) detector
Gas engineers have a professional obligation to advise customers about CO detector installation and to record this advice in documentation.
In rental properties, landlords are legally required to provide working CO detectors.

## Slide 16: Appliance operation chain (boiler example)
Understanding the sequential operation of gas appliances helps engineers identify where safety devices intervene in the process. Below is the typical sequence for a modern condensing boiler:
Demand signal: Heating demand initiated by room thermostat, programmer, or hot water demand from tap or cylinder thermostat.
Fan activation: Main fan starts to create the required air pressure differential for combustion ventilation.
APS verification: Air Pressure Switch confirms sufficient airflow is present by sensing pressure differential.

## Slide 17: Appliance operation chain (boiler example)
Gas valve opens: PCB signals gas valve to open, allowing gas flow to the burner assembly.
Ignition sequence: Spark electrode generates ignition source to light the gas-air mixture.
Flame detection: FSD confirms flame establishment through thermocouple or flame rectification signal.
Normal operation: Burner continues to operate with continuous monitoring until demand ends.

## Slide 18: Appliance operation chain (boiler example)
Safety chain principle
If any link in this operational chain fails, the appliance will enter lockout mode for safety.
Each stage must be successfully completed before the next can begin.
This sequential approach ensures multiple layers of protection against unsafe operation conditions.

## Slide 19: Testing and fault-finding
Proper testing procedures are essential for confirming the operational integrity of safety devices.
Always consult manufacturer's instructions for specific testing methods and parameters.

## Slide 20: Testing and fault-finding
Device | Test/indication | Action if faulty
APS | Check continuity with fan on/off, measure pressure differential with manometer | Replace switch, check tubing for blockages/splits, verify fan operation
FSD (Thermocouple) | Measure millivolt output (should be 15-30mV), check connection tightness | Replace thermocouple, clean connections, check electromagnet
FSD (Flame Rect.) | Check probe position, measure microamp current (typically 0.8-1.5μA) | Clean/replace probe, check wiring, verify flame pattern
CO Detector | Press test button, verify alarm and indicator lights | Replace immediately, notify client of risks, consider appliance issues

## Slide 21: Testing and fault-finding
Essential safety procedures
Always isolate gas and electricity before component removal.
Use appropriate test equipment (manometer, multimeter, etc.).
Document all test results and replacement components.
Verify operation after component replacement.
Follow manufacturer's test procedures precisely.
Never bypass or "jump out" safety devices as a temporary solution. This constitutes dangerous practice and is illegal under Gas Safety Regulations. Failed safety devices must be properly replaced and tested before returning appliances to service.

## Slide 22: Summary
You should now be able to:
Identify airflow and combustion safety devices.
Understand their role in burner safety logic.
Use manufacturer guidance to test and replace them safely.
Apply this knowledge to appliance diagnostics.

## Slide 23
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.