## Slide 1
Occupational Specialism: Gas Engineering
K1.6 Types of components and their suitability for different appliances and types of systems
PowerPoint 1.6b: Gas valves, ratio controls & multifunctional gas valves

## Slide 2: Objectives
By the end of this session, you should be able to:
Identify key control components in gas appliances.
Explain how multifunctional gas valves and air/gas ratio controls function.
Describe the sequence of gas delivery in controlled appliances.
You might also be able to:
Compare control setups between open and room-sealed appliances.
Diagnose how valve or control failure would present.

## Slide 3: Control components: foundation concepts
Definition and purpose:
Control components are the regulatory elements that manage and coordinate the safe and efficient delivery of gas to the burner.
They ensure proper combustion by:
Regulating gas flow rates and pressures
Controlling air/gas mixture ratios
Managing the ignition sequence.

## Slide 4: Control components: foundation concepts
Definition and purpose:
Modulating output based on demand
Providing safety shutoff mechanisms.
These components must operate with exceptional reliability as they are the primary defence against unsafe combustion conditions.

## Slide 5: Control components: foundation concepts
Key control components:
Multifunctional gas valve: Integrated control unit combining multiple gas management functions.
Air/gas ratio valve: Ensures proportional mixing for stoichiometric combustion.
Modulating gas valve: Varies the gas flow to match output requirements.
Servo pressure regulator: Adjusts gas pressure based on air input signals.

## Slide 6: Control components: foundation concepts
Key control components:
Solenoid valves: Electromagnetic valves for on/off control.
Pressure switches: Monitor pressure conditions and provide feedback.
Understanding these components is essential for diagnosing faults, performing maintenance, and ensuring appliances meet current UK gas safety regulations.

## Slide 7: Multifunctional gas valve (Multiblock)
A multifunctional gas valve is an integrated gas control assembly that combines multiple functions into a single unit.
It serves as the central hub for gas management in many appliances.

## Slide 8: Multifunctional gas valve (Multiblock)
Key components:
Manual shut-off valve: For service isolation.
Solenoid valves: For main and pilot gas control.
Pressure regulator: With adjustable spring and diaphragm.
Gas filter: To prevent contaminant ingress.
Test points: For pressure measurement and verification.
Thermoelectric device: In some models for flame supervision.

## Slide 9: Multifunctional gas valve (Multiblock)
Operation sequence:
Call for heat activates the control circuit.
Pilot solenoid opens to supply pilot burner.
Flame detection confirms pilot ignition.
Main solenoid opens to supply main burner.
Pressure regulator maintains set working pressure.
On shut-down, solenoids close to stop gas flow.

## Slide 10: Multifunctional gas valve (Multiblock)
Common in traditional domestic boilers, cookers, gas fires, and warm air heaters.
Manufacturer's instructions are essential for correct pressure settings and replacement procedures.

## Slide 11: Multifunctional gas valve (Multiblock): Detailed anatomy
The multifunctional gas valve represents a significant advancement in gas control technology, integrating multiple functions that previously required separate components.
Understanding the internal structure is essential for proper diagnosis and maintenance.

## Slide 12: Multifunctional gas valve (Multiblock): Detailed anatomy
Key structural elements include:
Inlet chamber: Where gas enters the valve at supply pressure.
Regulator section: Contains diaphragm, spring assembly and adjustment screw.
Solenoid chambers: Houses electromagnetic coils that lift valve seats when energised.
Filter mesh: Typically 50-100 micron filtration to prevent debris reaching valve seats.

## Slide 13: Multifunctional gas valve (Multiblock): Detailed anatomy
Outlet chamber: Where regulated gas exits at the correct working pressure.
Test nipples: Sealed points for pressure gauge connection.
Engineers must be able to identify these components for effective fault diagnosis and maintenance.

## Slide 14: Air/Gas ratio control valve
Purpose and application:
Air/gas ratio valves maintain a precise balance between combustion air and fuel gas to ensure efficient, safe, and low-emission burner operation. They are commonly found in modern condensing boilers, industrial burners, and premix combustion systems.
Air/gas ratio valves, also known as ratio regulators or cross-connected regulators, are designed to modulate the gas flow in direct proportion to the airflow. This ensures the burner receives the correct fuel-to-air mixture across its entire operating range.

## Slide 15: Air/Gas ratio control valve
Operational principles:
Impulse Control: A pressure impulse line connects the air supply to the gas valve. As airflow increases, the pressure in the impulse line rises, prompting the valve to open proportionally and allow more gas through.
Maintaining Stoichiometry: The goal is to approach the ideal combustion ratio (10:1 air to natural gas by volume), though real-world systems often run slightly lean or rich depending on application needs.

## Slide 16: Air/Gas ratio control valve
Operational principles:
Modulation: In modulating appliances, the fan speed is varied to adjust airflow. The air/gas valve responds automatically, maintaining the correct ratio without manual adjustment.
Fail-Safe Design: If airflow stops or drops below a threshold, the valve restricts or shuts off gas flow to prevent unsafe combustion or unburned gas release.

## Slide 17: Air/Gas ratio control valve
Air/gas ratio valves are integral to systems where combustion efficiency, emissions control, and safety are critical. Common applications include:
Condensing Boilers: Especially SEDBUK Band A-rated models; ensures optimal combustion across modulation range.
Premix Combustion Systems: Found in gas-fired water heaters, warm air units, and some CHP systems.
Industrial Burners & Furnaces.
Commercial Catering Equipment.

## Slide 18: Fan-assisted appliances: Ratio Control operation
Fan operation
The fan creates negative pressure that draws in combustion air.
Fan speed may vary based on demand signals from the PCB.
The air pressure generated becomes the reference signal for the ratio valve.

## Slide 19: Fan-assisted appliances: Ratio Control operation
Ratio valve response
The valve receives the air pressure signal and adjusts the gas diaphragm accordingly.
Higher air pressure = more gas flow; lower pressure = reduced gas flow.

## Slide 20: Fan-assisted appliances: Ratio Control operation
Combustion control
The burner receives the precisely proportioned mixture, maintaining a consistent air-to-gas ratio (typically 10:1).
This ensures complete combustion across the entire modulation range.

## Slide 21: Fan-assisted appliances: Ratio Control operation
The PCB (Printed Circuit Board) serves as the orchestrator of this process, monitoring multiple parameters including flow temperature, return temperature, and user demand settings to determine the appropriate modulation level.
This dynamic system is far more responsive than traditional fixed-pressure regulators, allowing modern appliances to achieve higher efficiencies and lower emissions.

## Slide 22: Sequence of operation: Room-sealed boiler
Demand signal - Thermostat or programmer initiates call for heat, sending a signal to the boiler PCB.
Pre-purge phase - Fan activates at high speed to clear combustion chamber of any residual gases (typically 10-30 seconds).
Air pressure verification - Air pressure switch closes, confirming sufficient air flow for safe combustion.
Control activation - PCB sends a signal to activate the ratio valve and prepare for gas flow.

## Slide 23: Sequence of operation: Room-sealed boiler
Ignition sequence - Spark electrode generates ignition spark while gas is released via ratio valve.
Flame establishment - Flame detection electrode confirms successful ignition, allowing continued operation.
Modulation phase - System modulates output based on demand, with ratio valve maintaining correct air-gas proportion.
If any stage fails, the system will typically lock out after several attempts, requiring a manual reset. This sequence highlights the interdependent nature of control components.

## Slide 24: Comparative analysis: Multiblock vs ratio valve
Feature | Multifunctional gas valve | Ratio valve
Common Applications | Older conventional boilers, gas fires, cookers, warm air units | Modern condensing boilers, high-efficiency systems
Operational Principle | Primarily mechanical/electromechanical | Pneumatic with electronic control
Pressure Regulation | Fixed or step regulation | Continuous modulation based on air pressure
Fuel Compatibility | Natural Gas, LPG (requires conversion) | Natural Gas, LPG (requires conversion)
Safety Features | Manual reset, solenoid valves, flame failure device | Integrated with PCB, air pressure monitoring, proportional control
Modulation Capability | Limited/stepped (high/low) | Continuous across wide range (typically 30-100%)
Response to Varying Conditions | Limited - maintains set pressure | Dynamic - adjusts to changing conditions
Installation Complexity | Moderate - mechanical settings | Higher - electronic integration

## Slide 25: Component failure: recognition and risk assessment
Multifunctional gas valve failures
Symptoms: No gas to burner, no ignition, lockout condition.
Causes: Blocked filter, seized regulator, faulty solenoid.
Risk level: ID (Immediately Dangerous) if gas leak is present.
Diagnosis: Check inlet/outlet pressures, solenoid resistance, manual operation.

## Slide 26: Component failure: recognition and risk assessment
Ratio valve failures
Symptoms: Yellow flame, unstable burning, fluctuating output.
Causes: Blocked air reference tube, damaged diaphragm, electronic fault.
Risk level: AR (At Risk) or ID - depending on CO production.
Diagnosis: Combustion analysis, check reference pressures, electronic continuity.

## Slide 27: Component failure: recognition and risk assessment
Solenoid failures
Symptoms: Pilot won't light, intermittent operation, lockout.
Causes: Burnt out coil, debris on valve seat, control circuit fault.
Risk level: AR (At Risk).
Diagnosis: Measure coil resistance, check for clicking sound on activation.

## Slide 28: Component failure: recognition and risk assessment
Pressure regulator failures
Symptoms: Over-pressure, explosive ignition, sooting, incomplete combustion.
Causes: Perforated diaphragm, incorrectly adjusted spring, seized components.
Risk level: ID (Immediately Dangerous) due to CO risk.
Diagnosis: Measure working pressure, check regulation under varying loads.

## Slide 29: Component failure: recognition and risk assessment
Under the Gas Industry Unsafe Situations Procedure (GIUSP), engineers are required to appropriately classify faults and take necessary actions.

## Slide 30: Diagnostic scenario: Georgia’s lockout
Scenario
Georgia reports that her boiler:
Starts the fan when there is a call for heat
Makes clicking sounds during ignition attempt
Fails to ignite the burner
Eventually displays "flame failure" error and locks out.

## Slide 31: Diagnostic scenario: Georgia’s lockout
The clicking sound suggests that the ignition sequence is initiating and the solenoid valve is attempting to open. This narrows the potential faults to:
Gas supply issues: Check gas meter, emergency control valve, and supply pressure.
Solenoid valve failure: Opening electrically but not mechanically.
Blocked gas filter: Preventing adequate gas flow despite valve opening.
Ignition electrode issues: Improper gap, carbon fouling, or cracked ceramic.
PCB fault: Not maintaining solenoid activation long enough.

## Slide 32: Diagnostic workflow for control component faults
Initial assessment
Gather customer information about fault symptoms
Check error codes and operational history
Verify gas supply to property
Review appliance documentation.

## Slide 33: Diagnostic workflow for control component faults
Visual inspection
Inspect for obvious damage or water ingress
Check electrical connections
Look for signs of overheating
Identify any modifications or prior repairs.

## Slide 34: Diagnostic workflow for control component faults
Basic testing
Measure standing and working pressures
Check voltage to control components
Listen for normal operational sounds
Observe ignition attempt sequence.

## Slide 35: Diagnostic workflow for control component faults
Advanced diagnostics
Test solenoid resistance values
Perform combustion analysis
Check air pressure switch operation
Verify proper PCB function.

## Slide 36: Diagnostic workflow for control component faults
Resolution
Replace faulty components as identified
Adjust pressures to manufacturer specifications
Verify proper operation after repair
Document all work performed.
Always adhere to the manufacturer's instructions when testing and replacing control components. Remember that diagnostic results must be thoroughly documented to comply with Gas Safe registration requirements.

## Slide 37: Air/Gas ratio control: Pneumatic principles
The air/gas ratio valve uses a pneumatic feedback system to maintain proportional control.
Reference pressure: The fan creates an air pressure signal that serves as the control reference.
Gas diaphragm: A flexible membrane responds to the air pressure signal.
Proportional valve: The diaphragm position controls the size of the gas aperture.
Feedback loop: As air pressure changes, gas flow adjusts automatically.
This creates a self-regulating system that maintains the correct stoichiometric ratio across varying load conditions without additional adjustment.

## Slide 38: Air/Gas ratio control: Pneumatic principles
Understanding these pneumatic principles is essential for correctly diagnosing issues related to combustion quality and appliance modulation problems. Engineers must be able to check reference pressures and verify the proper operation of ratio valves during service visits.
Key technical specifications: | 
Typical Ratio: | ~10:1 air-to-gas (varies by appliance)
Modulation Range: | 30-100% of rated output
Response Time: | < 1 second to pressure changes
Operating Temperature: | -15°C to 60°C
Reference Pressure Range: | Typically 0.5-10 mbar
Electrical Requirements: | 24V DC for electronic models

## Slide 39: Key learning points
Control components regulate gas flow, air mix, sequence of ignition, and burner behaviour.
Multifunctional gas valves integrate multiple functions including shut-off, regulation, and safety features.
Air/gas ratio valves ensure proper combustion by maintaining the correct stoichiometric mix.
The sequence of operation in modern appliances involves multiple control components working in coordination.
Different types of appliances use different control strategies appropriate to their design.

## Slide 40: Summary
You should now be able to:
Identify key control components in gas appliances.
Explain how multifunctional gas valves and air/gas ratio controls function.
Describe the sequence of gas delivery in controlled appliances.
You might also be able to:
Compare control setups between open and room-sealed appliances.
Diagnose how valve or control failure would present.

## Slide 41
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.