## Slide 1
Occupational Specialism: Gas Engineering
K1.6 Types of Components and Their Suitability for different appliances and types of systems
PowerPoint 1.6c: Flame supervision and pressure switches

## Slide 2: Starter
Sam complains that their gas fire has started leaving soot stains on the wall. The flame looks big and yellow.
What might be failing here?
Which components are responsible for checking safe operation?

## Slide 3: Objectives
By the end of this session, you should be able to:
Identify key safety components in gas appliances.
Explain the function of FSDs, APS, thermostats and lockout logic.
Describe how safety chains protect users from gas leaks or combustion risks.
You might also be able to:
Analyse appliance lockout causes using component behaviour.
Classify risks based on component failure (AR / ID).

## Slide 4: What are safety components?
Safety components are critical devices engineered to detect unsafe operating conditions and automatically shut down gas flow or appliance operation when hazards are detected.
Primary functions
Detect flame presence/absence
Sense air pressure for proper ventilation
Monitor temperature thresholds
Trigger shut-down sequences or lockout via PCB.

## Slide 5: What are safety components?
GIUSP classifications
At Risk (AR): Situation that presents a danger that may become ID.
Immediately Dangerous (ID): Actual danger to life or property.
Component bypass or failure often results in ID classification.

## Slide 6: What are safety components?
Legal requirements
Gas Safety (Installation and Use) Regulations 1998
Building Regulations Document J
BS 5440 Parts 1 & 2
Manufacturer's installation instructions.
As a Gas Safe registered engineer, you are legally responsible for ensuring these safety components are functioning correctly before certifying an appliance as safe to use.

## Slide 7: Flame Supervision Devices (FSD)
FSDs prove that a flame is present and prevent dangerous gas build-up if ignition fails or flame is lost.
Types:
Thermocouple FSDs: Common in older appliances and decorative gas fires.
Thermopile: Multiple junctions for higher voltage output.
Ionisation probes: Standard in modern condensing boilers.
Optical sensors: Used in some industrial applications.

## Slide 8: Flame Supervision Devices (FSD)
Operation time:
Must detect flame within specified proving time (typically 5-10 seconds).
GIUSP implications:
Any FSD bypass or fault is classified as ID (Immediately Dangerous) under GIUSP, requiring immediate disconnection of the appliance.

## Slide 9: Flame Supervision Devices (FSD)
Failure risks:
Carbon monoxide poisoning
Gas explosion hazard
Breach of Gas Safety Regulations
Loss of Gas Safe registration.

## Slide 10: Thermocouple FSD operation
Working principle:
Thermocouples operate on the Seebeck effect - generating a small DC voltage (25-30mV) when heated by a flame.

## Slide 11: Thermocouple FSD operation
Operational sequence:
Pilot light heats thermocouple junction.
Thermocouple generates mV voltage.
Voltage energises holding coil in gas valve.
Electromagnetic force keeps valve open.
If flame extinguishes, voltage drops.
Spring in valve closes gas supply.

## Slide 12: Thermocouple FSD operation
Common faults:
Carbon deposits on thermocouple tip.
Loose connections at interrupter/valve.
Electromagnetic fatigue in solenoid.

## Slide 13: Thermocouple FSD operation
The thermocouple must be positioned correctly in the pilot flame to generate sufficient voltage.
The connection to the gas valve must be tight (hand-tight plus 1/4 turn with spanner) to ensure good electrical contact.
Testing
Thermocouples should generate 12-30mV when heated. Test with a multimeter by disconnecting from the valve and measuring the output voltage.

## Slide 14: Ionisation flame detection
Working principle
Flame ionisation detection uses the electrical conductivity of a flame to prove its presence. A gas flame contains ionised particles that conduct electricity.

## Slide 15: Ionisation flame detection
Components:
Flame rod: Metal probe positioned in flame.
PCB circuit: Applies AC voltage and monitors current.
Earth reference: Usually the burner itself.

## Slide 16: Ionisation flame detection
Operational sequence:
AC voltage (220-240V) applied to flame rod.
Flame ionisation creates rectification effect.
Small DC current flows (1-5μA) through flame.
PCB detects this current as flame proof.
Without flame, circuit opens and gas valve closes.

## Slide 17: Ionisation flame detection
Common faults:
Carbon build-up on flame rod (insulating effect).
Poor earth connection to burner.
Damaged ceramic insulator.
Incorrectly positioned flame rod.
PCB flame detection circuit failure.

## Slide 18: Ionisation flame detection
Testing:
Measure microamp current using a microammeter in series with the flame rod.
Readings should be 1-5μA DC.
Lower readings may cause intermittent lockout.

## Slide 19: Air Pressure Switches (APS)
Purpose
APS devices verify that the fan is running and creating proper airflow before allowing ignition in fan-assisted appliances.
Working principle
Fan creates a pressure differential.
Diaphragm in APS moves in response.
Contacts close, completing the electrical circuit.
Signal confirms to PCB that the fan is operational.

## Slide 20: Air Pressure Switches (APS)
Operation
The switch remains open until sufficient differential pressure is detected. This prevents ignition if the fan or flue is blocked or restricted.
GIUSP implications
Bypassing an APS is classified as ID under GIUSP. This defeats a critical safety device designed to prevent combustion products from spilling into the property.

## Slide 21: Air Pressure Switches (APS)
Common faults
Blocked pressure sensing tubes
Perished diaphragm
Seized mechanical parts
Incorrect pressure settings
Fan not creating sufficient pressure.

## Slide 22: APS in operation sequence
Step 1: Fan start
When heat demand is detected, PCB signals the fan to start before any ignition attempt. The fan creates differential pressure in the flue system.
Step 2: Pressure detection
Positive pressure (flue) and negative pressure (inlet) are monitored via small silicone tubes. The pressure difference must reach a threshold value (typically 10-40 Pa).

## Slide 23: APS in operation sequence
Step 3: Switch closure
When sufficient pressure differential is detected, APS diaphragm moves and electrical contacts close. This completes the circuit to the PCB.
Step 4: PCB verification
PCB verifies that APS is closed. If closed, ignition sequence proceeds. If open, appliance enters lockout state after several attempts.

## Slide 24: APS in operation sequence
If the APS fails to close within a set time period (typically 30-60 seconds), the boiler will enter a lockout state requiring manual reset.
This prevents dangerous operation with insufficient combustion air.

## Slide 25: Thermostats and overheat protection
Operating thermostats
Control temperature in DHW or CH systems:
Electronic (NTC thermistors): Variable resistance sensors used in modern appliances.
Mechanical (bi-metallic): Physical expansion/contraction in older appliances.
Capillary: Fluid-filled systems used in cylinders and some boilers.

## Slide 26: Thermostats and overheat protection
NTC Thermistor operation
Negative Temperature Coefficient devices decrease resistance as temperature increases.
PCB monitors this resistance to determine water temperature.

## Slide 27: Thermostats and overheat protection
Overheat thermostats
Safety devices that trigger when the temperature exceeds a safe threshold:
Typically trip at 90-110°C.
Usually require manual reset (not automatic).
Connected directly to safety circuit.
Override normal operating controls.

## Slide 28: Thermostats and overheat protection
Common applications:
DHW cylinders and tanks
System boilers and heat exchangers
Heat-only boilers and thermal stores
Solid fuel back boilers.

## Slide 29: Safety chains in gas appliances
A safety chain is a sequence of interdependent components that must all function correctly for the appliance to operate safely.
Fan operation
Fan starts and begins to evacuate combustion products and draw in fresh air.
APS verification
Air Pressure Switch closes to confirm proper airflow is established.

## Slide 30: Safety chains in gas appliances
PCB assessment
PCB verifies all safety inputs and authorises gas valve opening.
Flame proof
Flame must be detected by an ionisation probe or a thermocouple within a safe time.

## Slide 31: Safety chains in gas appliances
Temperature monitoring
Thermistors and overheat stats continuously monitor for safe operation temperatures.
If any link in this safety chain fails, the appliance should enter a lockout condition requiring manual intervention. This prevents unsafe cycling and potential hazard creation.

## Slide 32: Lockout and reset functionality
What is lockout?
A safety shutdown condition requiring manual reset after a fault is detected.
It prevents automatic restart attempts that could create unsafe conditions.

## Slide 33: Lockout and reset functionality
Common lockout triggers:
Failed flame detection (3-5 attempts typically)
APS not closing within time limit
Overheat thermostat activation
Water pressure below minimum (low-water cutoff)
Fan speed verification failure
Multiple ignition failures.

## Slide 34: Lockout and reset functionality
Diagnostic indicators
Modern appliances display fault codes to identify the specific safety component that triggered lockout:
LED flashing sequences
Digital display codes
Manufacturer-specific diagnostics.

## Slide 35: Lockout and reset functionality
Reset procedure:
Identify and rectify underlying fault
Press dedicated reset button
Some appliances require power cycling
Record fault in service documentation.

## Slide 36: Scenario task: "Georgia's boiler locks out"
Scenario
Georgia reports that her combi boiler attempts to start but shuts down after a clicking sound.
After pressing the reset button, the same sequence repeats.
Group task
Identify possible safety component faults.
Describe how you would test them.
Decide if the situation is AR or ID.

## Slide 37: Component testing and diagnosis
Thermocouple testing:
Open circuit test: 0Ω resistance
Output voltage: 12-30mV when heated
Connection resistance: less than 0.5Ω
Visual inspection for damage/carbon.

## Slide 38: Component testing and diagnosis
Ionisation probe testing:
Visual inspection for damage/carbon
Gap measurement (3-4mm typical)
Microamp reading: 1-5μA during operation
Resistance to earth: should be open circuit.

## Slide 39: Component testing and diagnosis
APS testing:
Visual check of tubes for blockage/damage
Continuity test across terminals when activated
Pressure test using manometer or pressure gauge
Functional test during commissioning.

## Slide 40: Component testing and diagnosis
Thermistor testing:
Resistance measurement at room temperature (10kΩ typical at 25°C).
Resistance should decrease as temperature increases.
Compare to manufacturer's resistance chart.

## Slide 41: Component testing and diagnosis
Overheat thermostat testing:
Continuity test across terminals (should be closed)
No continuity if tripped
Reset should restore continuity
Trip temperature verification (specialist equipment).
Always isolate electrical supply before testing components with a multimeter.
Never bypass safety devices even temporarily for testing purposes.

## Slide 42: Key learning points
Flame Supervision Devices (FSDs) detect flame presence to stop gas flow if no flame is found, ensuring safety. Air Pressure Switches (APS) confirm proper ventilation before ignition to prevent CO buildup. Thermostats and Temperature Controls regulate normal and emergency temperatures using mechanical or digital sensors. Safety Chains and Lockouts link safety devices, so any failure triggers a lockout needing manual reset.
As a Gas Safe engineer, you must ensure these systems comply with safety regulations.

## Slide 43: Summary
You should now be able to:
Identify key safety components in gas appliances.
Explain the function of FSDs, APS, thermostats and lockout logic.
Describe how safety chains protect users from gas leaks or combustion risks.
You might also be able to:
Analyse appliance lockout causes using component behaviour.
Classify risks based on component failure (AR / ID).

## Slide 44
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.