## Slide 1
Occupational Specialism: Gas Engineering
K1.8 Factors that affect the choice and suitability of components included in a system
PowerPoint 1.8a: Location, gas type, appliance and size

## Slide 2: Starter
Fault scenario
“A 24 kW room-sealed boiler is installed in a loft. The engineer fits a standard open-flue terminal and a non-condensate-rated fan.”
Discussion questions:
What components are potentially unsuitable here?
How does the location influence component selection?
What could go wrong?

## Slide 3: Objectives
By the end of the session, you should be able to:
Explain how installation location affects component choice.
Identify how gas type impacts component suitability.
Match components to appliance type and size.
Select components that are appropriate for the system’s intended use.

## Slide 4: Location-based component selection
Location | Key considerations
Kitchen cupboard | Ventilation clearance, fan noise, condensate routing, compact components
Loft space | Frost protection, vertical flue requirements, condensate trap, insulation
Outdoor meter box | Water-resistant components, corrosion-proof terminals, UV protection
Garage or shed | Insulation, exposed pipework protection, venting requirements, security
Basement | Adequate ventilation, condensate pumps, flood protection, moisture resistance
Environmental conditions at the installation site strongly influence component selection. Components must endure temperature, humidity, and element exposure while ensuring safe operation over their service life.

## Slide 5: Location-based component selection
Key examples:
Frost stats for loft installations prevent freezing of condensate pipes.
Weatherproof terminal caps protect external flues from rain ingress.
Compact components with reduced clearances for tight kitchen installations.
Condensate pumps for installations below drainage level.

## Slide 6: Gas type considerations
Gas type is a fundamental consideration that affects virtually every component in the gas train.
The chemical properties, pressure requirements, and combustion characteristics of different gases necessitate specific component designs.
Using components not rated for the supply gas creates serious safety risks and will invalidate manufacturer warranties.

## Slide 7: Gas type considerations
Natural Gas (NG)
Lower pressure (21 mbar), lighter gas with 37.5 MJ/m³ calorific value.
Standard-sized injectors.
Lower pressure regulator settings.
Specific burner configurations.

## Slide 8: Gas type considerations
LPG (Propane)
Higher energy content (93.2 MJ/m³), denser gas requiring:
Smaller injector apertures.
Higher pressure regulators (37 mbar).
Different air/gas ratio settings.

## Slide 9: Gas type considerations
LPG (Butane)
Higher energy content (121.8 MJ/m³), used in portable applications:
Smallest injector apertures.
28 mbar pressure regulation.
Not suitable below 5°C.

## Slide 10: Gas type considerations
Compatibility warning
Components must be explicitly rated for the gas type used.
Rubber seals may deteriorate with incorrect gas.
Wrong injectors cause sooting or flame lift.
Incorrect valves may leak or fail prematurely.
⚠️ Always confirm gas compatibility in the Manufacturer's Instructions (MI). ⚠️

## Slide 11: Appliance type determines component use
Each appliance type has a unique operational profile requiring specific components. These parts work as a system, and using generic substitutes can compromise safety and protective functions. Selecting components from the wrong category risks unsafe operation, non-compliance, and early failure.
For example, a space heater ODS sensor is inappropriate in a room-sealed boiler due to different combustion conditions. Likewise, a boiler’s modulating gas valve would not suit a cooker, which needs precise manual control.

## Slide 12: Appliance type determines component use
Combi boiler
Flow sensors (Hall effect/turbine)
Modulating gas valve
Diverter valve (hydraulic or motorised)
Plate heat exchanger
Low water pressure sensor
Fan with venturi.

## Slide 13: Appliance type determines component use
Space heater
Oxygen Depletion Sensor (ODS)
Fixed flame control
Pilot assembly
Thermopile/thermoelectric device
Piezo ignition
Simple gas cock.

## Slide 14: Appliance type determines component use
Gas fire
Thermocouple
Multi-functional valve
Decorative fuel effect burner
Heat exchanger (glass-fronted)
Catalytic converter (flueless)
Remote control receiver.

## Slide 15: Appliance type determines component use
Cooker
Burner caps and rings
Flame Supervision Devices (FSDs)
Manual ignition or spark module
Thermostat (for oven)
Multi-port injector assembly
Governor (for varying flame).

## Slide 16: Matching component size to system load
Critical sizing factors:
Appliance kW rating (heat input/output)
Component flow rate capacity
Pipe sizing and pressure drop allowance
Maximum operating pressure
Turndown ratio requirements
Heat release pattern (continuous/intermittent).

## Slide 17: Matching component size to system load
A gas valve rated for 10 kW will catastrophically under-supply a 30 kW boiler, causing dangerous cycling, incomplete combustion and component failure.
Oversized components can be equally problematic - an oversized burner may cause poor combustion efficiency, excessive emissions, and improper flame characteristics in a small appliance.

## Slide 18: Matching component size to system load
Essential label checks:
Component | Critical ratings
Gas Valve | kW rating, pressure range, voltage
Fan | Air volume, static pressure, power
Pump | Head, flow rate, power consumption
Burner | Heat input range, gas type, turndown
Heat Exchanger | kW rating, water content, material

## Slide 19: Component selection – Combi boilers
The domestic condensing combination boiler represents one of the most complex gas appliance systems, requiring careful component selection to ensure safe, efficient operation.
When selecting replacement parts or specifying a new installation, engineers must consider the components on the following two slides.

## Slide 20: Component selection – Combi boilers
Primary components
Gas valve: Must match kW rating and gas type of the appliance. Modern units are typically modulating with electronic control.
Fan: Must handle correct air volume for proper combustion, be condensate resistant, and match the electronic control parameters.
Burner: Material must withstand high temperatures and condensate, with correct flame pattern for NOx reduction.
Heat exchangers: Primary must handle operating pressure/temperature; secondary (plate) sized for hot water demand.

## Slide 21: Component selection – Combi boilers
Controls and safety devices
PCB: Must be compatible with all sensors and actuators, with correct software version.
Pressure sensor: Must operate within correct range (typically 0.8-3.0 bar) with appropriate electrical output.
Thermistors: Must have correct resistance values at operating temperatures (usually NTC type).
Condensate trap: Must have adequate capacity and reliable water seal to prevent flue gas escape.

## Slide 22: Appliance/component relationship matrix
The relationship between appliance types and component requirements demonstrates the importance of selecting the correct components for each specific application.
Understanding these relationships is essential for component selection that maintains the appliance's intended safety functions and operational characteristics.
Component substitution without considering these relationships may introduce hazards or reduce efficiency.

## Slide 23: Appliance/component relationship matrix
This matrix highlights key components for different appliance categories:
Appliance type | Safety components | Operational components | Special considerations
Condensing Boiler | Flue gas sensor, flame rectification, air pressure switch | Modulating gas valve, pre-mix burner, fan, condensate trap | Acid-resistant materials for heat exchanger, secondary heat exchanger for condensing operation
Gas Fire (Open Flued) | ODS, thermocouple, spillage detection | Multi-functional control, injector, burner assembly | Heat-resistant glass panels, draught diverter design, decorative components
Cooking Range | FSDs on all burners, thermostat for oven, gas cock | Multi-port injectors, flame spreaders, control knobs | Heat-resistant seals, specific ignition systems, oven thermostat calibration
Water Heater | Thermocouple/thermopile, high limit stat, flue spillage switch | Diaphragm water valve, venturi, thermostat | Water pressure/flow requirements, anti-scald protection, energy cut-off
Warm Air Heater | Limit stat, sail switch, roll-out detector | Air circulation fan, heat exchanger, filter | Air distribution design, noise reduction, multi-zone capability

## Slide 24: Environmental impact on component selection
The physical environment where components operate significantly influences their material requirements, durability expectations, and functional parameters.
This consideration becomes increasingly important for components exposed to harsh conditions.

## Slide 25: Environmental impact on component selection
Coastal installations
Components near the sea require enhanced corrosion resistance due to salt-laden air:
Marine-grade stainless steel fittings.
Special protective coatings on exposed metal.
More frequent maintenance intervals.
Sealed electrical connections with IP65+ rating.

## Slide 26: Environmental impact on component selection
Dusty environments
Workshops, garages, and industrial settings require:
Enhanced filtration on air intakes.
Sealed bearings on rotating components.
Protected ignition systems.
Easy-clean surfaces for maintenance.

## Slide 27: Flow characteristics and component sizing
Fundamental considerations
The relationship between flow rate, pressure, and component capacity is fundamental to proper system operation. When selecting components that handle gas or water flow, engineers must:
Calculate maximum demand based on appliance rating.
Allow for appropriate pressure drop across components.
Consider momentary peak demand scenarios.
Account for diversity factors in multi-appliance systems.
Verify component capacity exceeds maximum demand by a safe margin.

## Slide 28: Flow characteristics and component sizing
Undersized components create flow restrictions, pressure drops, and can lead to dangerous cycling, overheating, or incomplete combustion.
Example calculations
For a 30kW combi boiler with peak DHW demand:
Gas requirement | ~3.0 m³/h (natural gas)
Water flow rate | ~12 l/min at 35°C rise
Pipe sizing | 22mm for water, 22mm for gas
Valve capacity | Must exceed 30kW
Pump head | 5-6 metres typical requirement
Each component in the flow path must be sized to maintain proper operation at maximum demand without excessive restriction.

## Slide 29: Component selection decision factors
Identify appliance type and rating: Determine the category of appliance (boiler, fire, cooker, etc.) and its heat input/output requirements.
Evaluate installation environment: Assess location factors (indoor/outdoor, temperature extremes, humidity, exposure to elements).
Confirm gas type and pressure: Verify whether Natural Gas or LPG will be used and the supply pressure available.
Check manufacturer's requirements: Review technical documentation for specific component requirements and compatibility constraints.

## Slide 30: Component selection decision factors
Verify regulatory compliance: Ensure components meet current standards, codes of practice, and have appropriate certification.
Select and install appropriate components: Choose components that satisfy all identified requirements and install according to manufacturer's instructions.
This systematic approach ensures that all relevant factors are considered when selecting components.
Following this decision tree helps prevent the common errors that lead to dangerous installations, non-compliance with regulations, or premature component failure.

## Slide 31: Common component selection errors
Error: Incorrect gas type components
Natural Gas components used on LPG systems or vice versa.
Consequences: Dangerous combustion, sooting, flame lift, appliance damage, potential fire/explosion hazard.
Error: Undersized components
Using components with insufficient capacity for the appliance rating.
Consequences: Poor performance, cycling, overheating, incomplete combustion, premature failure.

## Slide 32: Common component selection errors
Error: Non-condensate resistant components
Using standard components in condensing appliances.
Consequences: Corrosion, electrical failure, leakage, component degradation.
Error: Incompatible flue components
Mixing flue types or using incorrect terminals.
Consequences: Flue gas leakage, carbon monoxide risk, condensate damage, non-compliance.

## Slide 33: Common component selection errors
Error: Location-inappropriate components
Using indoor components in outdoor locations.
Consequences: Water ingress, corrosion, electrical shorts, freezing damage.
Error: Non-manufacturer approved parts
Using generic replacements instead of specified parts.
Consequences: Warranty invalidation, compatibility issues, premature failure.

## Slide 34: Common component selection errors
These errors represent the most common component selection failures encountered in the field.
They highlight the importance of thorough knowledge and careful consideration of all selection factors.
Proper component selection is not merely about functionality; it's fundamentally about safety and compliance.

## Slide 35: Gas industry case study: Component selection
Background
In 2019, a residential property in West Yorkshire experienced a serious incident resulting from improper component selection during a boiler replacement.
The engineer installed a standard natural gas valve in an LPG boiler system.

## Slide 36: Gas industry case study: Component selection
Investigation findings
The engineer failed to verify gas type before component selection.
The valve was visually similar but had different internal specifications.
The component was not labeled as LPG compatible.
The installation was commissioned without proper gas tightness testing.
Gas leakage occurred through the valve due to material incompatibility.

## Slide 37: Gas industry case study: Component selection
Consequences
Gas leak led to an explosion causing structural damage.
Two occupants suffered serious burns.
Engineer prosecuted under Gas Safety Regulations.
£25,000 fine plus costs and suspended prison sentence.
Permanent revocation of Gas Safe registration.

## Slide 38: Gas industry case study: Component selection
Preventative measures
This incident could have been prevented through:
Proper identification of gas type before component selection.
Verification of component compatibility with manufacturer.
Use of specifically LPG-rated components.
Thorough commissioning procedures including leak testing.
Following manufacturer's instructions explicitly.

## Slide 39: Gas industry case study: Component selection
This case study illustrates the serious real-world consequences of improper component selection.
It emphasises that component selection is not merely a technical consideration but a critical safety responsibility with potential legal implications.

## Slide 40: Core selection factors
Location factors: Environmental conditions where the component will operate, including temperature extremes, humidity, exposure to elements, and space constraints.
Gas type: Compatibility with Natural Gas or LPG, including appropriate pressure ratings, material compatibility, and specific design features.
Appliance type: Specific requirements based on whether the component is for a boiler, fire, cooker, water heater or other appliance category.
Size and rating: Appropriate capacity for the system's requirements, ensuring components can handle the flow, pressure, and heat demands.

## Slide 41: Core selection factors
Standards compliance: Adherence to relevant British Standards, EU regulations, and industry codes of practice for quality and safety.
Manufacturer specifications: Compliance with the appliance manufacturer's specific requirements and recommendations for replacement parts.

## Slide 42: Summary
You should now be able to:
Explain how installation location affects component choice.
Identify how gas type impacts component suitability.
Match components to appliance type and size.
Select components that are appropriate for the system’s intended use.

## Slide 43
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.