## Slide 1
Occupational Specialism: Gas Engineering
K1.9 Waste and Waste Products
PowerPoint 1.9: Understanding waste in gas systems

## Slide 2: Starter
What waste can a gas boiler produce during normal operation?
In pairs, list as many types of waste as you can. Then decide which are:
Solid
Liquid
Gas.
Extension: How could each type impact people or the environment?

## Slide 3: Objectives
By the end of this session, you should be able to:
Identify waste and by-products generated by gas appliances.
Describe how waste products influence maintenance planning.
Explain the health, safety and environmental implications of different waste types.
Analyse interactions of waste with other systems and people on-site.

## Slide 4: Types of waste products in gas systems
Three key waste forms:
Magnetite (Fe₃O₄): Iron oxide sludge from corrosion in wet systems.
Corrosive smells: Indicators of leaks or breakdown (e.g. hydrogen sulphide).
Bacteria: Found in stagnant or poorly maintained water/gas systems.
Real-world example: Simon services a combi boiler and finds thick black sludge in the pump housing. This is magnetite caused by internal corrosion due to poor inhibitor use.

## Slide 5: 1. Magnetite (Fe₃O₄)
What is it? A black sludge formed from the corrosion of steel components.
Where it forms: Radiators, steel pipes, heat exchangers.
Risks:
  Blocked pipework and pump strain.
  Reduced heat transfer.
  Risk of boiler lockout.
Maintenance link:
  Powerflushing, system filters, corrosion inhibitors.
  Check during annual service.

## Slide 6: 2. Corrosive smells
What is it? Hydrogen sulphide (H₂S) and other gases released by corroding parts.
Odour: Rotten egg smell. Where found: Burners, water heaters, flueways.
Risks:
  Sign of incomplete combustion.
  Early warning of component failure.
  May mimic a gas leak smell.
Action:
  Investigate burner condition and seals.
  Combustion analysis to confirm safety.

## Slide 7: 3. Bacteria (biofilm and microbial growth)
Where it grows: Low-flow areas of heating and hot water systems
What causes it: Warm, stagnant water — often in stored systems
Risks:
  Poor heat output.
  Blocked pipes or heat exchangers.
  Risk of Legionella or odours.
Prevention:
  Thermal disinfection cycles.
  Biocide dosing.
  Regular flushing and maintenance.

## Slide 8: Environmental and legal considerations
Waste disposal and duty of care
Gas engineers must follow environmental law:
WEEE Regulations for electronic components.
Controlled Waste (Duty of Care) Regulations.
COSHH for harmful waste (e.g. sealants, sludge inhibitors).

## Slide 9: Environmental and legal considerations
Sustainable practice in gas engineering:
Recycle electronic PCBs where possible.
Use long-life parts to reduce disposal.
Return parts to suppliers (e.g. boilers with exchange warranty).

## Slide 10: Interaction with other parties
Waste products affect:
End users – indoor air quality, water quality, reliability.
Other contractors – drainage, electrical systems.
The environment – landfill, emissions, leakage risk.
Scenario activity: Georgia installs a new boiler and connects it to the existing pipework. After a month, the user complains of smells.
What waste issue could be occurring? Who should be involved?

## Slide 11: Safe handling and transport of waste
Containers must be:
Labelled correctly (e.g. 'Hazardous Waste')
Resistant to leaks/spills
Secured in vans (racking or boxed).
Vehicle requirements:
Waste carrier licence (if transporting), No cross-contamination with tools or food, Compliant with ADR regulations for dangerous goods.
Discussion point: What could happen if chemical waste spills in a work van?

## Slide 12: Waste disposal regulations and best practice
Key laws:
Environmental Protection Act 1990.
Hazardous Waste Regulations 2005.
COSHH for chemical substances.
WEEE Regulations for electronic waste.

## Slide 13: Waste disposal regulations and best practice
Engineer’s duties:
Segregate waste (electrical, chemical, sharps).
Return components to manufacturers if under scheme.
Use licensed recycling centres.
Real-Life Breach: A contractor dumps rusted flue liners at a site skip. Who is liable?

## Slide 14: Recording waste handling (Compliance)
Must-have records:
Job sheets with disposal notes.
Waste Transfer Notes (WTNs).
Hazardous Waste Consignment Notes (HWCNs).
Where they’re used:
Employer audits (e.g. Gas Safe inspections).
Legal defence against environmental claims.
Manufacturer warranty returns.

## Slide 15: Sustainability and gas engineering
Encourage greener approaches:
Specify recyclable materials
Use concentrated/low-waste products
Fit magnetic filters to reduce system waste
Future thinking:
What could be done to reduce waste in hydrogen-ready boilers?

## Slide 16: Summary
You should now be able to:
Identify waste and by-products generated by gas appliances.
Describe how waste products influence maintenance planning.
Explain the health, safety and environmental implications of different waste types.
Analyse interactions of waste with other systems and people on-site.

## Slide 17
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.