## Slide 1
Occupational Specialism: Gas Engineering
K1.1 Typical hazards and risks associated with working with gas systems and how these can be mitigated
PowerPoint 1.1a: Asbestos

## Slide 2
Objectives
By the end of this session, you should be able to:
Identify types of asbestos, where it can be found, and why it is dangerous.
Know what to do if you find asbestos during your work and how to handle it safely.
Recognise the importance of preventive measures to avoid exposure to asbestos and the serious diseases it can cause.

## Slide 3
      Starter
Do you know what to do if you find asbestos during your work?
Do you know what it looks like and where you might find it?

## Slide 4
      Control of Asbestos Regulations 2006
Asbestos regulations include:
a ban on the use of asbestos
the management of asbestos in the workplace
asbestos licensing.
If asbestos is in good condition, it can remain in place and must be appropriately labelled.

## Slide 5
      Asbestos – what is it?
Asbestos is a group of naturally occurring, fibrous minerals that were once widely used in construction and other industries due to their heat, fire, and chemical resistance.
The 3 most common types we come across are:
Chrysotile – white
Crocidolite – blue
Amosite - brown
20
Tradespeople lose their lives each week due to previous exposure.

## Slide 6: Types of asbestos
Most hazardous:
Amosite (Brown Asbestos)
Most dangerous:
Crocidolite (Blue Asbestos)
Most common:
Chrysotile (White Asbestos)

## Slide 7
      Asbestos – what is it?
Chrysotile – White Asbestos
White Asbestos is widely used in roofs, ceilings, walls, floors, gaskets, boiler seals, and insulation for pipes, ducts, and appliances.
Amosite – Brown Asbestos
Commonly used in cement sheets and pipe insulation. Also present in insulating board, ceiling tiles, and thermal insulation products.
Crocidolite – Blue Asbestos
This material was utilised in various spray-on coatings, pipe insulation, plastic products, and cement applications.

## Slide 8
      Asbestos – what is it?
Asbestos was used in numerous new and renovated commercial and residential buildings prior to its prohibition in 1999.
Many premises, along with older plant and equipment, still contain asbestos, often concealed within the building's structure and not immediately visible.
Gas engineers and plumbers may encounter asbestos, particularly when working in older properties.

## Slide 9
      Asbestos – why is it dangerous?
In the UK, asbestos exposure is the leading cause of work-related fatalities. Each year, illnesses linked to asbestos cause the deaths of about 5,000 people.
These illnesses are incurable and usually take decades to manifest.
Asbestos poses little risk if left unattended and in good shape. However, asbestos fibres may be discharged and inhaled once it is disturbed. This may result in cancer and lung disease, both of which are potentially deadly.
You are unaware that asbestos is present since you cannot see, smell, or feel the fibres in the air or on your clothing.

## Slide 10
      Asbestos – what are the risks?
When asbestos-containing materials are disturbed, fibres are released into the air.
Breathing these fibres can cause serious diseases that often take decades to appear, and treatment is usually limited once diagnosed.
Preventive measures are essential now. Exposure can lead to fatal conditions such as mesothelioma, lung cancer, asbestosis, and pleural thickening.
Smokers exposed to asbestos face an even higher risk of lung cancer.

## Slide 11
      Asbestos – where can you find it?
Asbestos cement can be located in various areas around the home, including on water tanks, pipe lagging, sprayed around boilers or water tanks, toilet seats and cisterns, bath panels, behind fireplaces, and fuse boxes.
Additionally, it may be found in loose-fill insulation, textured decorative coatings like Artex, ceiling tiles, airing cupboards, partition walls, window panels, and vinyl floor tiles.

## Slide 12
      Before you start work
Check if asbestos is present and assess its type and condition before starting work.
In non-domestic buildings, those responsible must inform you about asbestos.
If details are missing but you suspect asbestos, survey the area or assume all materials contain it and take maximum precautions.
Conduct a risk assessment to confirm if work can be done without exposure.
If exposure can’t be avoided, identify who is at risk and the potential level of exposure.
Use this assessment to choose safe work methods and control risks effectively.

## Slide 13
      What if I find asbestos?
Stop work immediately.
Put up a warning sign and ensure nobody enters the area.
You should only carry out work on asbestos if you have had the appropriate information, instruction and training.

## Slide 14
      What do I do if I disturb asbestos?
If asbestos is accidentally disturbed and released, handle it promptly and correctly.
Lower-risk materials (fibres firmly bound and in good condition) include:
Asbestos cement
Bitumen products
Papers and textiles
Small-scale releases of asbestos insulating board
Clean-up of these materials typically does not require a licensed contractor.

## Slide 15
      What do I do if I disturb asbestos?
Warn affected individuals and ensure anyone without PPE/RPE leaves the area immediately.
Identify the cause of the uncontrolled release and regain control as soon as possible.
Minimise asbestos spread through proper decontamination and clean up dust and debris (see Asbestos Essentials method sheet).
Decontaminate any contaminated individuals and ensure rags, clothing, and PPE are either cleaned or disposed of as contaminated waste.

## Slide 16
      Remember
You can’t see or smell asbestos fibres in the air.
The effects of being exposed to asbestos take many years to show up – avoid breathing it in now.
Smokers who are exposed to asbestos fibres are at a much greater risk of developing lung cancer.
Asbestos is only a danger when fibres are made airborne and breathed in.
As long as the asbestos is in good condition and it is located somewhere where it can’t be damaged easily, then it shouldn’t be a risk to you.

## Slide 17
      Asbestos
Now answer the following questions again:
Do you know what to do if you find asbestos during your work?
Do you know what it looks like and where you might find it?

## Slide 18: Summary
You should now be able to:
Identify types of asbestos, where it can be found, and why it is dangerous.
Know what to do if you find asbestos during your work and how to handle it safely.
Recognise the importance of preventive measures to avoid exposure to asbestos and the serious diseases it can cause.

## Slide 19
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.