## Slide 1
Occupational Specialism: Gas Engineering
K1.1 Typical hazards and risks associated with working with gas systems and how these can be mitigated
PowerPoint 1.1c: Carbon monoxide poisoning

## Slide 2
Objectives
By the end of this session, you should be able to:
Explain the process of carbon monoxide poisoning.
Describe the symptoms of carbon monoxide poisoning.
Demonstrate the steps to take if carbon monoxide poisoning is suspected.
Evaluate the effectiveness of carbon monoxide alarms in detecting CO.
Apply safety measures to prevent carbon monoxide poisoning.

## Slide 3
Carbon monoxide
Carbon monoxide (CO) is a colourless, odourless, tasteless, and toxic gas that results from the incomplete burning of carbon-containing fuels like gas, oil, wood, and coal.
While these fuels are generally safe when used properly, incomplete combustion can lead to the production of harmful levels of CO.
Once CO is inhaled, it interferes with the blood's ability to transport oxygen to various cells, tissues, and organs.

## Slide 4
Carbon monoxide
Carbon monoxide (CO) cannot be detected through sight, taste, or smell, yet it poses a significant threat to life.
According to statistics from the HSE, approximately seven individuals die each year from CO poisoning related to gas appliances that are improperly installed, maintained, or inadequately ventilated.
Prolonged exposure to levels that are not immediately lethal can have severe health consequences, including the risk of paralysis and brain damage.

## Slide 5
Carbon monoxide
Signs of incomplete combustion and potential CO production include:
Yellow or orange flames (except for fuel effect fires or flueless appliances).
Soot or yellow/brown stains on or around appliances.
Pilot lights that frequently blow out.
Increased condensation on windows.

## Slide 6
Symptoms of carbon monoxide (CO) poisoning
The initial symptoms of carbon monoxide (CO) poisoning can resemble those of various common conditions, often leading to misdiagnosis. These symptoms may be mistaken for food poisoning, viral infections, influenza, or general fatigue. It is important to be aware of the following symptoms:
Headaches or dizziness
Nausea
Tiredness
Breathlessness
Loss of consciousness
Visual problems
Erratic behaviour
Pains in the chest or stomach.

## Slide 7
Carbon monoxide (CO) poisoning
It is crucial to act promptly:
• Turn off the gas appliance if it is safe to do so.
• Open doors and windows to allow ventilation.
• Leave the property and move outside into fresh air.
Seek medical advice immediately. Contact the NHS 111 service if you suspect carbon monoxide (CO) poisoning.
If someone exhibits severe symptoms, such as difficulty breathing, sudden confusion, or loss of consciousness, call 999 or proceed to the nearest Accident & Emergency (A&E) department.

## Slide 8
Detecting carbon monoxide (CO)
So how do we detect carbon monoxide?
Carbon monoxide alarms warn of potential carbon monoxide leaks. According to the manufacturer's guidelines, these devices should be installed in various locations within your home.
They function similarly to fire or smoke alarms by emitting an alert when they detect carbon monoxide, which is a colourless, odourless, and tasteless poisonous gas.

## Slide 9
Carbon monoxide (CO) alarms
Modern carbon monoxide alarms are similar in appearance to smoke detectors, although it's important to note that typical smoke detectors do not detect carbon monoxide.
It is advisable to install a carbon monoxide alarm in any room that has a gas appliance, following the manufacturer's installation instructions closely.
Typically, carbon monoxide alarms have a lifespan ranging from 5 to 10 years.
To ensure their effectiveness, make sure that any carbon monoxide alarm you buy features a Kitemark that meets the standards BS EN 50291-1:2010 (for residential settings) and/or BS EN 50291-2:2010 (for use in caravans and boats).

## Slide 10
Carbon monoxide (CO) alarms

## Slide 11
Carbon monoxide alarms in rented accommodation
The Smoke and Carbon Monoxide Alarm (Amendment) Regulations 2022 came into effect on 1 October 2022. All applicable landlords are required to:
Install at least one smoke alarm on every floor of their properties where there is a room designated for living. This has been a legal obligation in the private rental sector since 2015.
Place a carbon monoxide alarm in any living accommodation that includes a fixed combustion appliance (excluding gas cookers).
Repair or replace smoke alarms and carbon monoxide alarms once they are reported faulty.
Local authorities enforce these requirements and can impose fines of up to £5,000 if a landlord does not comply with a remedial notice.

## Slide 12: Summary
You should now be able to:
Explain the process of carbon monoxide poisoning.
Describe the symptoms of carbon monoxide poisoning.
Demonstrate the steps to take if carbon monoxide poisoning is suspected.
Evaluate the effectiveness of carbon monoxide alarms in detecting CO.
Apply safety measures to prevent carbon monoxide poisoning.

## Slide 13
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.