## Slide 1
Occupational Specialism: Gas Engineering
K1.1 Typical hazards and risks associated with working with gas systems and how these can be mitigated
PowerPoint 1.1f: Working at height

## Slide 2
Objectives
By the end of this session, you should be able to:
Know the equipment used for tasks performed at height.
Follow step-by-step instructions for assembling, setting up, and operating equipment related to height.
Make recommendations for assembling and utilising mobile tower scaffolds.

## Slide 3
What is working at height?
Working at height applies to:
Any task performed in a location where without appropriate safety measures, an individual could fall a distance that may result in personal injury. You are considered to be working at height if you:
Operate above ground or floor level.
Are at risk of falling from an edge, through an opening, or onto a fragile surface.
Could fall from ground level into an opening in a floor or a pit in the ground.

## Slide 4
The Working at Height Regulations 2005 (WAHR)
These regulations apply to any work at height that poses a fall risk causing injury. They establish a legal duty for employers, employees, and managers to ensure safety.
The rules cover all height-related tasks and include:
Safety guards and fall protection systems.
Safety harnesses.
Proper planning.
Risk assessments and method statements (RAMS).
Inspections of equipment.

## Slide 5
What is the best way to prevent falls from height?
Is it possible to prevent working at height from the outset?
Aim to perform as many tasks as you can from ground level. Here are some practical examples:
Using extendable tools from the ground to remove the need for a ladder.
Installing cables at ground level.
Lowering a lighting mast to ground level.
Assembling edge protection at ground level.

## Slide 6
What is the best way to prevent falls from height?
Can falls be prevented? Yes, by:
Using a safe workplace, like a strong roof with permanent guardrails, or
Employing fall prevention equipment.
Examples of collective protection in a safe workplace include:
Concrete roofs with edge protection or mezzanine floors with guards.
Collective protection using equipment involves:
Mobile elevating work platforms (MEWPs), tower scaffolds, and scaffolds.
For personal protection, a work restraint system can prevent workers from accessing fall hazards.

## Slide 7
What is the best way to prevent falls from height?
How can you reduce the distance and/or impact of a fall?
When a persistent fall risk exists, measures must reduce both distance and impact.
Examples of collective protection include:
Safety nets or soft-landing systems like airbags near the work level.
Personal protection options include:
Industrial rope access for facades
Fall-arrest systems using a high anchor point.

## Slide 8
What is the best way to prevent falls from height?
Using ladders and stepladders.
For low-risk tasks that are brief in duration, ladders and stepladders can be a reasonable and effective choice.

## Slide 9
What is the best way to prevent falls from height?
If your risk assessment indicates that using a ladder is appropriate, you should further minimise the risk by ensuring you:
select the correct type of ladder for the task
possess the necessary skills
handle the provided equipment safely and adhere to a safe working system
are fully informed about the risks and the measures in place to mitigate them.

## Slide 10
Falls from height
Falling from a height remains one of the leading causes of fatal injuries in the workplace.
In the 2022/23 period, the Health and Safety Executive (HSE) reported that falls from height were responsible for 40 deaths, constituting 30% of all workplace fatalities.

## Slide 11
Access equipment
As a gas engineer, you may need to use various types of equipment to reach elevated areas, including:
Stepladders
Roof ladders
Trestle scaffolds
Mobile tower scaffolds
Fixed scaffolds
Elevated platforms.

## Slide 12
Using ladders
Each year, approximately 14 people lose their lives, and around 1,200 sustain serious injuries at work due to falls from leaning ladders or stepladders.
Many of these incidents may stem from:
Inadequate planning.
Using inappropriate equipment for the task.
Misapplication of the equipment.
In your opinion, what are the primary factors that contribute to these fatalities and injuries?

## Slide 13
Factors contributing to ladder injuries
A ladder that is leaning may slip either from the top or the bottom.
A leaning ladder can tip over or detach at the top.
Reaching too far.
There may be an issue with the ladder itself.
Slipping or losing balance.
A stepladder may wobble if it has missing feet or is not fully opened.
Using a stepladder sideways in relation to the task at hand.

## Slide 14
Ladders – checks before use
At the beginning of the workday or after any changes, users should conduct the following checks:
Inspect the stiles for bending or damage to prevent buckling.
Examine the feet for wear or absence, ensuring proper contact with the ground on various surfaces.
Assess the rungs for any bends, wear, or looseness that could affect stability.
Review the locking mechanisms for damage and ensure all bars are engaged.
Inspect the stepladder platform for splits or buckling that may lead to instability.
Check the steps or treads for contamination and ensure fixings are secure to prevent slipping hazards.

## Slide 15
Placement of leaning ladders
Safely positioning a leaning ladder – The ladder demonstrates the proper 1 in 4 angle (securing details omitted for clarity).
Positioning a leaning ladder on a back slope—when placed on a back slope, the ladder illustrates a maximum angle of 6°.
Positioning a leaning ladder on a side slope – the ladder indicates a maximum angle of 16° when positioned on a side slope.
Ladder secured at the top stiles (suitable for working purposes, not for accessing).

## Slide 16
Ladder suitability and classification
Class 1 – suitable for industrial use, with a maximum weight capacity of 175kg.
Class 2 – designed for commercial purposes, holding up to 150kg.
Class 3 – intended for domestic use, accommodating up to 125kg.
Materials used in manufacturing include:
Wood.
Aluminium.
Fibreglass (colour coded yellow for electricians).
Ladders are intended for short-duration tasks only, with a maximum usage time of 30 minutes.

## Slide 17
Roof ladders
This ladder is intended for use on a sloped roof and should be approached from a scaffold rather than a ladder.
The roof ladder features two wheels at its upper end, enabling it to be manoeuvred up the roof without harming the slates or tiles.
On the opposite side of the wheels, the ladder is designed with a hook that securely fits over the ridge of the roof, preventing the ladder from sliding down.

## Slide 18
Mobile tower scaffold
Competence – what does it involve?
An individual is considered competent when they have sufficient knowledge or technical training, relevant practical experience, and the necessary authority to:
Carry out their responsibilities with the appropriate level of accountability.
Detect potential risks linked to the task at hand.
Identify any errors or gaps in the work, grasp the health and safety consequences arising from those issues, and be able to suggest corrective measures to mitigate those consequences.

## Slide 19
Mobile tower scaffold
There are several categories of mobile tower scaffolds, which consist of:
Vertical ladder towers
Inclined ladder towers
Stairway towers
Frame access towers.
These scaffolds are available in various widths (double or single):
Double usually measures between 1.3m and 1.45m wide
Single typically ranges from 0.8m to 0.85m wide.

## Slide 20
Double width mobile tower scaffold
This frame design consists of two platforms placed adjacent to each other, with one requiring a trapdoor for access.
Ensure proper access to the tower.
The hinged trapdoor MUST open outward.
Platforms without trapdoors can be positioned next to the hinged one or serve as intermediate platforms.
The minimum width of each platform is 600mm.
The maximum vertical distance between platforms is 4m.

## Slide 21
Moving a mobile tower scaffold
Prior to relocating a mobile tower scaffold, several key factors must be considered:
Clear the platforms of individuals and items.
Lower the height to a maximum of 2m if stabilisers are not in place.
Apply force at or close to the base.
Avoid using mechanical methods for movement.

## Slide 22
Moving a mobile tower scaffold
What factors should you think about before utilising a tower scaffold?
Maximum height.
Securing the structure.
Risk of electrocution.
Safety of the public.
Wind conditions.
Weight capacity.

## Slide 23
Inspecting a mobile tower scaffold
Conduct an inspection following assembly and prior to use.
Prepare a written report before concluding your shift.
Provide the report to the intended recipient within 24 hours.
Perform re-inspections at a minimum of every seven days.
It is not necessary to re-inspect with each relocation.
Ensure a copy of the inspection report is securely stored.

## Slide 24
You should now be able to:
Know the equipment used for tasks performed at height.
Follow step-by-step instructions for assembling, setting up, and operating equipment related to height.
Make recommendations for assembling and utilising mobile tower scaffolds.
Summary

## Slide 25
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.