## Slide 1
Occupational Specialism: Gas Engineering
K1.3 Emergency procedures for unsafe situations
PowerPoint 1.3b: Emergency actions and procedures

## Slide 2: Starter
Scenario:
Upon reaching Simon's residence, you are met with the smell of gas.
Simon mentions that he detected the odour originating from the kitchen, specifically around the gas hob.
​In pairs, talk about the potential reasons for the gas leak and the appropriate steps to address the issue.

## Slide 3: Objectives
By the end of this session, you should be able to:
Recall correct procedures in the event of a gas escape or unsafe situation.
Demonstrate the steps to safely isolate a gas supply.
Interpret guidance documents such as GIUSP and GSIUR.

## Slide 4: Immediate actions in unsafe situations
If you believe there is a gas leak, risk of explosion, or presence of carbon monoxide, you should:
Shut off the gas supply at the Emergency Control Valve (ECV).
Ensure proper ventilation by opening doors and windows if it's safe to do so.
Refrain from using any electrical switches, including lights and phones.
Evacuate the area if needed.
Call the Gas Emergency Service at 0800 111 999 if necessary.
Apply “Do Not Use” labels and warning signs, and document all actions taken.

## Slide 5: Steps for safely isolating a gas installation
1. Locate the isolation point
Find the gas meter and its emergency control valve (ECV), typically situated next to the meter or at the entry point to the flat.
2. Shut off the gas supply
Switch off the ECV, making sure it is in the off position, which is usually marked by a visual indicator on the valve.
3. Secure the isolation
Employ an appropriate lock-off device, like a padlock, to keep the ECV in the off position.

## Slide 6: Steps for safely isolating a gas installation
4. Post warning notices
Place a warning notice on the ECV and any associated equipment to show that the gas supply is isolated and should not be disturbed.
5. Confirm the isolation
Before starting any work, verify that the gas supply is indeed isolated. This might require the use of a gas detector or other specialised tools to check for gas flow.

## Slide 7: Key guidance documents
The Gas Industry Unsafe Situations Procedure (GIUSP) guides gas engineers in recognising and addressing unsafe gas installations.
It assists engineers in categorising defects and implementing suitable measures to ensure safety, which may include disconnecting gas supplies if necessary.
This procedure is applicable when managing unsafe gas appliances, chimneys, flues, and piping in both residential and commercial environments. It classifies unsafe conditions as follows:
ID – Immediately Dangerous
AR – At Risk

## Slide 8: Key guidance documents
The Gas Safety (Rights of Entry) Regulations 1996 provide gas transporters and relevant authorities with the authority to access premises for particular reasons tied to gas safety.
This includes actions aimed at preventing gas leaks and conducting inspections or disconnections of gas fittings.
These regulations are designed to protect public safety and to facilitate essential responses to potential gas hazards.

## Slide 9: Key guidance documents
The Gas Safety (Installation and Use) Regulations 1998 (GSIUR) represent a collection of guidelines in the UK aimed at ensuring the safe installation, maintenance, and operation of gas systems, encompassing appliances, fittings, and flues in both residential and specific commercial settings.
These regulations impose responsibilities on several stakeholders, including landlords, employers, and self-employed persons, to guarantee that gas installations are secure and adhere to the established standards.

## Slide 10: Question
Why is it critical to avoid using light switches or mobile phones in a suspected gas leak?
What’s the emergency gas number in the UK?
What does GIUSP stand for?
Name two things you must NOT do during a gas leak.
Which regulation governs gas safety in the UK?

## Slide 11: Summary
You should now be able to:
Recall correct procedures in the event of a gas escape or unsafe situation.
Demonstrate the steps to safely isolate a gas supply.
Interpret guidance documents such as GIUSP and GSIUR.

## Slide 12
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.