## Slide 1
Occupational Specialism: Gas Engineering
K1.22 Connection techniques
PowerPoint 1.22: Connection techniques

## Slide 2: Starter
You're sent to complete a boiler install where the gas pipe is steel, the heating pipes are copper, and the plumber left you a bag of compression fittings, solder elbows, and a press-fit tool.
What would you use and why?

## Slide 3: Objectives
By the end of this session, you should be able to:
Recall different types of jointing methods used in gas systems, including threading, soldering, compression, press-fit, PTFE tape, and jointing compounds.
Understand how each connection technique works and the importance of lead-free solder in all applications.
Identify how to safely transition between different pipe materials (e.g. steel to copper).

## Slide 4: Importance of inspection during commissioning
Thorough inspection serves as the final verification before system handover and operation, ensuring that all components are correctly installed and functioning as intended.
This critical process helps prevent potential hazards by enabling early detection of faults or deficiencies that might otherwise remain hidden.
Proper inspection ensures compliance with both manufacturer specifications and national regulatory requirements, establishing a documented trail of quality assurance.

## Slide 5: Overview of common inspection methods
1. Visual inspection
The foundation of all inspection activities, involving direct observation of components and systems to identify visible defects, abnormalities or installation issues.
2. Non-destructive testing
Specialised techniques that reveal hidden defects without damaging the equipment, including ultrasonic, magnetic particle and radiographic testing.

## Slide 6: Overview of common inspection methods
3. Functional testing
Operational verification to ensure systems perform as designed under various conditions, testing functionality, safety features and performance parameters.

## Slide 7: Visual inspection: purpose and scope
Fundamental assessment
Visual inspection involves direct observation to identify surface defects, misalignments, incorrect installations, or abnormalities that could compromise system integrity.
Foundation for further testing
Acts as the primary screening method that often determines the need and focus for more complex inspection techniques and specialised testing.
Universal application
Employed at every major commissioning step from initial installation verification through to final system handover and certification.

## Slide 8: Visual aids and tools
Basic tools
Human eye supplemented with torches, magnifiers, and inspection mirrors for accessing confined spaces
Advanced equipment
Digital cameras, borescopes and endoscopes for remote or difficult-to-reach locations
Lighting requirements
Portable, adjustable lighting to ensure adequate visibility of all inspection points

## Slide 9: Preparation for inspection
Review the manufacturer’s documentation
Thorough consultation of the manufacturer's instructions and recommendations, which provide specific inspection criteria and acceptance standards for equipment.
Examine technical records
Analysis of engineering drawings, specifications, and previous inspection reports to understand system layout and critical inspection points.
Understand system parameters
Familiarisation with equipment history, operating conditions and design limitations to focus inspection on areas of potential concern.

## Slide 10: Developing an inspection plan
A comprehensive inspection plan is tailored to the specific gas system being commissioned, taking into account:
system type and complexity (domestic, commercial, industrial)
potential damage mechanisms and failure modes
risk assessment outcomes and critical safety points
input from specialists regarding material compatibility and corrosion
regulatory requirements and industry best practices.

## Slide 11: Inspection documentation
Standardised checklists
Comprehensive inspection checklists developed with reference to industry standards (such as IGE/UP/1B for gas installations) and manufacturer specifications.
Tailored to specific system components.
Include pass/fail criteria for objective assessment.

## Slide 12: Inspection documentation
Detailed recording
Thorough documentation of all findings including:
observed deviations from specifications
photographic evidence of defects
measurements and test results.

## Slide 13: Inspection documentation
Audit trail
Maintenance of complete records to ensure traceability for:
future maintenance planning
regulatory compliance verification
warranty validation and dispute resolution.

## Slide 14: Safety during inspections
System preparation
Before inspection commences, systems must be properly isolated and depressurised following formal procedures. Lockout/tagout protocols ensure equipment remains safe during inspection.

## Slide 15: Safety during inspections
Access safety
Ensure secure access to inspection points via proper scaffolding, platforms or fall protection systems for elevated areas.

## Slide 16: Commissioning system: stages requiring inspection
Mechanical completion
Initial inspection to verify that all components are properly installed according to design specifications before any testing begins.
Confirms construction quality.
Verifies material compliance.
Ensures drawing adherence.

## Slide 17: Commissioning system: stages requiring inspection
Pre-commissioning
Detailed inspection focusing on system integrity, leak detection, and component fit-ups
Pressure testing of pipework
Valve operation verification
Instrument calibration checks

## Slide 18: Commissioning system: stages requiring inspection
Commissioning
Final inspection of system functionality under operating conditions.
Performance verification.
Safety systems testing.
Operational parameter checks.

## Slide 19: Application of visual inspection in commissioning
Initial walkthrough
Comprehensive visual assessment at the beginning of commissioning to identify obvious defects and establish baseline condition.
Defect tracking
Creation and management of punch lists documenting all visual defects and incomplete work requiring rectification before final acceptance.
Joint validation
Collaborative inspection involving both commissioning and construction teams to ensure all stakeholders agree on system status and required remediation.

## Slide 20: Key areas assessed visually in gas systems
Piping runs and supports
Verification of proper routing, adequate support spacing, and correct slope for drainage where required.
Joints, fittings and valves
Examination of connection integrity, proper seating, and correct assembly according to specifications.
Equipment orientation and layout
Confirmation that all components are positioned correctly with proper clearances for operation and maintenance.

## Slide 21: Manufacturer's Instructions: The gold standard
Primary authority
Manufacturer's instructions always take precedence over generic checklists or standards when conducting inspections, as they provide equipment-specific requirements.
Critical component focus
Specific guidance for safety-critical components often includes detailed inspection protocols, acceptance criteria and testing methodologies unique to the equipment.

## Slide 22: Manufacturer's Instructions: The gold standard
New technology guidance
Essential information for proper inspection of novel or unique systems that may not be covered by general industry standards or inspector experience.

## Slide 23: Valve inspection during commissioning
Valves represent critical control points in gas systems and require thorough inspection during commissioning:
verification that pressure and temperature ratings match system requirements
confirmation of proper installation orientation (flow direction)
checking accessibility for operation and maintenance
testing of smooth operation through full range of motion
verification of leak-free connections and seals
confirmation that locking devices and tamper-proof features are in place.
.

## Slide 24: Soldered jointing: lead-free solder
Heating Heat evenly around the fitting until flux bubbles, indicating the right temperature.
Solder application Touch lead-free solder to the joint; it will melt and fill the gap by capillary action.
Cooling and inspection Let the joint cool naturally, then check for a complete, clean solder ring without defects.

## Slide 25: Soldered jointing: lead-free solder
A properly executed soldered joint will show a continuous, even fillet of solder around the entire circumference of the joint.
Any gaps or incomplete filling indicate potential leak paths that must be remediated before commissioning.
Visual inspection should be followed by pressure testing to verify joint integrity.

## Slide 26: Compression jointing: principle
Compression jointing is a common mechanical method that creates gas-tight seals without heat or special tools by using physical pressure.
Tightening a compression nut compresses a soft metal olive between the pipe and fitting, forming two seals – one with the pipe and one with the fitting – to ensure a secure, leak-resistant connection.

## Slide 27: Compression jointing: principle
Components of a compression joint:
Compression fitting: Brass body with machined internal profile
Compression olive: Soft copper or brass ring that deforms under pressure
Compression nut: Applies axial force to compress the olive
For gas applications in the UK, compression fittings must comply with BS EN 1254-2 standards.

## Slide 28: Compression jointing: principle
These fittings are available in two primary types:
Type A (non-manipulative): Standard compression fittings where the olive deforms during assembly.
Type B (manipulative): Requires the pipe end to be flared or shaped before assembly.
Type A fittings are more common in gas applications due to their simpler installation requirements.

## Slide 29: Press-fit jointing: modern technique
Press-fit jointing is a key advancement in pipe connection, offering a flame-free, quicker alternative to soldering and compression fittings.
Widely used in UK gas engineering, it uses specially designed fittings with elastomeric O-rings and powered pressing tools to create secure, gas-tight seals through mechanical compression and deformation.

## Slide 30: Press-fit jointing: modern technique
Installation process:
Cut pipe squarely and deburr thoroughly.
Check and clean pipe end – surface quality is critical.
Check O-ring is present and undamaged in the fitting.
Mark insertion depth on pipe for visual verification.
Insert pipe fully into fitting socket to marked depth.
Position pressing tool jaws perpendicular to the pipe axis.
Complete pressing cycle – tools typically prevent incomplete crimping.
Visually inspect crimped connection profile against manufacturer's guidelines.

## Slide 31: PTFE tape: thread sealing
Polytetrafluoroethylene (PTFE) tape is widely used in gas engineering for sealing threaded connections due to its chemical resistance, temperature stability, low friction, and gas impermeability.
For gas systems, only yellow PTFE tape rated for gas use and meeting BS 7786:2006 standards should be used.

## Slide 32: PTFE tape: thread sealing
Application technique:
Clean threads thoroughly to remove dirt, old sealant, and metal particles.
Hold tape taut and begin at the second thread from the end (leaving first thread exposed).
Wrap in the direction of the thread spiral (clockwise for standard right-hand threads).
Apply with moderate tension, overlapping each wrap by approximately 50%.
Use 3–4 wraps for standard connections, more for larger diameters.
Tear or cut tape and press end firmly onto threads.
Assemble joint promptly, aligning carefully to prevent tape damage.

## Slide 33: Jointing compound: use and types
Common types:
Non-hardening: Stay flexible for easy disassembly, ideal for maintenance.
Semi-hardening: Create a strong seal yet allow disassembly with tools, resistant to vibration.
Anaerobic: Harden without oxygen for a solid seal but hinder disassembly.
PTFE-based: Blend PTFE particles with paste for combined benefits.
Modern products avoid solvents and VOCs for safety and environmental compliance.

## Slide 34: Transitions: why and when needed
Transitions between different pipe materials in gas systems require specialised joints to prevent failures caused by incompatibility or stress.
Common scenarios include connecting polyethylene mains to metal pipes, joining copper to steel, and linking new materials to old pipework.
Types of joints used range from flexible non-hardening to durable anaerobic and PTFE-based options, all designed to ensure safety and ease of maintenance without harmful solvents.

## Slide 35: Transitions: why and when needed
Key challenges:
Joining different materials involves issues like galvanic corrosion, varying thermal expansion causing stress, incompatible joint methods, maintaining pressure ratings, and meeting diverse regulations.
Overcoming these requires specialised fittings, correct installation, and knowledge of material properties.

## Slide 36: Example: material transition
Common material transitions:
Brass to Steel: Used at gas meter outlets with female BSP threads on steel and compression fittings on brass.
Copper to Steel: Connects copper pipes to steel risers using soldering or compression on copper and BSP threads on steel.
Polyethylene to Metal: Links underground PE mains to metal systems with compression fittings and reinforcing inserts.
Copper to CSST: For flexible gas setups, featuring compression or press-fit copper ends and connectors for CSST.

## Slide 37: Summary
You should now be able to:
Recall different types of jointing methods used in gas systems, including threading, soldering, compression, press-fit, PTFE tape, and jointing compounds.
Understand how each connection technique works and the importance of lead-free solder in all applications.
Identify how to safely transition between different pipe materials (e.g. steel to copper).

## Slide 38
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.