## Slide 1
Occupational Specialism: Gas Engineering
K1.4 Types of tools and equipment and materials
PowerPoint 1.4: Tools, equipment and materials

## Slide 2: Starter
You’ve been called to a domestic property to carry out a gas boiler installation.
Before you leave the workshop, your manager asks: “What tools and equipment are you taking, and why?”
Write down or discuss:
5 essential tools or items of equipment you would take
For each one, explain what it’s used for
What could go wrong if you didn’t bring or use the correct tool?

## Slide 3: Objectives
By the end of this session, you should be able to:
Recall the key tools used for gas systems.
Describe how each tool is used correctly and safely.
Explain when and why each tool should be used.
Evaluate the suitability of tools for different tasks.

## Slide 4: Hand tools
Safety
In your role as a gas engineer, you will handle various hand tools. Each tool carries a risk if not used properly, maintained regularly, or treated with care.
Your training will include detailed guidance on the proper use of these tools, the risks involved, and the necessary upkeep to ensure safety.

## Slide 5: Core tools for access and measurement
1. Pressure gauges
Use: Measure standing, operating, and burner pressure
Types: U-gauge, digital manometer
Best practice: Use the correct scale, calibrate regularly
Link: Used during tightness testing and commissioning

## Slide 6: Core tools for access and measurement
2. Combustion Performance Analyser
Use: Checks O₂, CO, CO₂ levels; confirms complete combustion
Display: Gives flue gas readings and CO/CO₂ ratio
Standard: Must be UKCA marked and calibrated
Common tasks: Commissioning, fault-finding, service checks
Legal link: IGEM/UP/1B and manufacturer’s instructions

## Slide 7: Core tools for access and measurement
3. Gas leak detector
Use: Sniffs for unburnt gas at joints, fittings, appliances
Tool types: Electronic handheld detectors or spray solution
Note: Detectors are sensitive but cannot replace a tightness test
Safety link: Used during leak investigations or as part of the Unsafe Situations Procedure

## Slide 8: Core tools for access and measurement
4. Temporary continuity bonds
Purpose: Prevent electrical arcing when breaking continuity during pipework alteration
Use: Clamps across meter unions or pipe sections
Regulation: Required under BS 6891
Why it matters: Stops ignition of stray current when disconnecting bonded components

## Slide 9: Core tools for access and measurement
5. Step ladders and mobile scaffolding
Purpose: Access ceiling voids, boilers, meter cupboards
Standards: Conform to BS EN 131 and working at height regs
Key checks: Stability, working height, flooring
Note: Choose scaffold towers for longer-duration tasks

## Slide 10: Tools for cutting, shaping and joining pipework
1. Pipe cutter
Use: Accurately cuts copper, stainless or plastic pipe
Type: Wheel cutter or pipe slice
Why it’s used: Produces a clean, burr-free cut
Best practice: Rotate steadily, avoid over-tightening
Risk: Incorrect use can deform the pipe or produce an uneven face

## Slide 11: Tools for cutting, shaping and joining pipework
2. Hacksaw
Use: Cutting metal, steel or hard plastic pipe
Why it’s used: Useful where access is tight or cuts are irregular
Notes: Use appropriate blade (e.g. 24 TPI for steel)
Aftercare: Always deburr and file edges after cutting

## Slide 12: Tools for cutting, shaping and joining pipework
3. Blowtorch
Use: Soldering joints (lead-free) in copper pipe systems
Fuel: Butane/propane mix
Why it’s used: Rapid, reliable heat for creating capillary joints
Caution: Must use with heat-resistant mat and eye protection
Legal note: All soldering must be lead-free per WRAS and Water Fittings Regs

## Slide 13: Tools for cutting, shaping and joining pipework
4. Spanners and Water pump pliers
Use: Tightening fittings (compression, valves)
Water pump pliers: Adjustable, wide-grip for large nuts
Spanners: Open-ended or adjustable
Good practice: Always use two tools (one to hold, one to turn)
Hazard: Over-tightening can distort joints or damage threads

## Slide 14: Tools for cutting, shaping and joining pipework
5. Bending machine
Use: Creates smooth pipe bends without kinks
Manual machines: Hand-held or floor-mounted
Why it’s used: Reduces the number of fittings, improves gas flow
Material suitability: Mainly copper or mild steel
Industry link: Saves time and reduces leak risks

## Slide 15: Tools for cutting, shaping and joining pipework
6. Drill and Hammer
Use:
  Drill: For wall fixing brackets or flues
  Hammer: Driving fixings or tapping parts into place
Drill types: Cordless SDS, percussion
Safety: Use correct bit and PPE
Task link: Required when clipping pipe to walls, installing backplates or setting up supports

## Slide 16: Material properties and tool suitability
1. Durability and Hardness
Tools must withstand repeated use without breaking or deforming.
Examples:
  Spanners and pliers: Forged steel, rust-resistant.
  Drill bits: Hardened high-speed steel (HSS).

## Slide 17: Material properties and tool suitability
2. Accuracy and Precision
Measurement tools must give repeatable, reliable readings.
Examples:
  Manometers: Must be calibrated.
  Pipe cutters: Must track evenly.

## Slide 18: Material properties and tool suitability
3. Heat resistance
Tools like blowtorches and soldering mats must resist flame and high temperatures.
Important for fire safety and longevity.

## Slide 19: Material properties and tool suitability
4. Non-conductive or Bonded
Tools used near gas meters or bonded pipework must avoid causing arcing.
Use temporary continuity bonds or insulated grips.

## Slide 20: Suitability for tasks
Tool | Suitable for | Unsuitable for
Pipe slice | Fast cutting of soft copper | Stainless steel pipe
Water pump pliers | Adjusting large nuts | Fine-threaded brass fittings
Blowtorch | Lead-free soldering | Use near flammable insulation
Pressure gauge | Measuring mbar pressure | Detecting gas leaks visually

## Slide 21: Summary
You should now be able to:
Recall the key tools used for gas systems.
Describe how each tool is used correctly and safely.
Explain when and why each tool should be used.
Evaluate the suitability of tools for different tasks.

## Slide 22
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.