## Slide 1
Occupational Specialism: Gas Engineering
K1.5 Operation and handling requirements of tools, equipment and materials
PowerPoint 1.5a: Safe use of gas engineering tools and equipment

## Slide 2: Introduction
Before any installation, service, or repair takes place, every gas engineer must ensure they have the right tools for the job and, more importantly, that they know how to use and care for them properly.
Gas engineering requires precision, safety, and compliance, and the tools we carry directly affect all three. But what makes a tool “essential”? Is it how often it’s used, how specialised it is, or how crucial it is for safety?
Let’s start by reflecting on your own experience and the knowledge you have in your toolkit. “What are the most important tools in your gas toolkit?”

## Slide 3: Objectives
By the end of this session, you should be able to:
Identify tools commonly used in gas engineering.
Explain how to use and handle tools safely.
Recognise the risks of poor handling.

## Slide 4: Digital manomenter
Measures gas pressure (usually in mbar or Pa). Used for checking standing pressure, working pressure, and pressure drops across components.
Usage examples:
Measuring the working pressure at a gas meter outlet
Checking inlet pressure on appliances (e.g. boilers, cookers)
Diagnosing drop due to undersized pipework or restrictions

## Slide 5: Digital manomenter
Best practice:
Always zero the device before use
Use appropriate tubing and ensure a gas-tight connection to the test nipple
Tip: Keep spare batteries in your kit – a low battery affects accuracy

## Slide 6: Adjustable and Fixed spanners
Used to tighten or loosen compression joints, unions, flanges, and nuts.
Types:
Adjustable crescent spanner
Box spanner
Open-ended and ring spanners

## Slide 7: Adjustable and Fixed spanners
Usage examples:
Installing a hob’s pipework or servicing a boiler gas valve
Undoing union fittings on test points
Best practice:
Use the correct size to avoid rounding nuts
Apply steady pressure—avoid overtightening
Tip: Use insulated versions when working around electrical components.

## Slide 8: Pressure testers (U-gauge, tightness testing kit)
Function:
Used for tightness testing new or modified gas pipework to ensure no leaks exist before live gas connection.
Usage examples:
2-minute let-by and 1-minute stabilisation test during initial install.
1-minute tightness test under live conditions.

## Slide 9: Pressure testers (U-gauge, tightness testing kit)
Best practice:
Connect at the meter test point using flexible tubing
Perform tests in accordance with GSIUR & IGEM/UP/1B for dwellings
Tip: Use soapy water on fittings for a visual leak check if readings drop. This is a non-aggressive leak detection fluid.

## Slide 10: Multimeter (Gas engineering-safe type)
Function:
Checks electrical characteristics: voltage (AC/DC), continuity, resistance, and sometimes current.
Usage examples:
Testing thermocouples or flame rectification circuits
Checking PCB connections and power to fans or solenoids
Verifying correct polarity and earthing

## Slide 11: Multimeter (Gas engineering-safe type)
Best practice:
Use only Gas-Safe-rated multimeters with insulated probes
Check meter settings carefully before testing
Tip: Always isolate appliances before electrical diagnosis unless a live test is required (with appropriate PPE and training).

## Slide 12: Flue Gas Analyser (FGA)
Measures and analyses the gases emitted from flues to assess combustion efficiency and safety.
What it measures:
O₂ (Oxygen)
CO (Carbon Monoxide)
CO₂ (Carbon Dioxide)
Flue gas temperature
Excess air
Combustion efficiency (%)

## Slide 13: Flue Gas Analyser (FGA)
Usage examples:
Boiler servicing and commissioning
Diagnosing poor combustion or blocked flues
Checking whether appliances are burning fuel correctly
Best practice:
Calibrate annually, zero before use in fresh air, insert probe into flue sampling point following manufacturer’s guidelines.
Tip: Many analysers allow you to print or store readings – ideal for service reports or Gas Safe evidence.

## Slide 14: Manufacturer’s instructions and legal compliance
Gas engineers must never rely on experience alone.
Manufacturer’s instructions are a primary source of compliance, and ignoring them can lead to unsafe situations, legal consequences, and breach of certification standards.

## Slide 15: Why follow the manufacturer’s instructions?
Each tool, appliance, or component is designed with specific handling, usage, and maintenance procedures.
These instructions ensure the product is used safely, correctly, and within its limits.
Ignoring guidance may invalidate warranties, cause damage, or result in non-compliance with regulations.

## Slide 16: Legal requirements: GSIUR Regulations 26 & 27
Regulation 26 – General safety
Requires all gas work to be carried out in a way that does not cause danger to any person.
This includes using tools and equipment in line with professional standards and the manufacturer’s requirements.
Regulation 27 – Examination of appliances
Mandates that engineers must:
Check appliances are safe to use
Ensure appliances operate properly and efficiently
Take appropriate action if an appliance is unsafe or installed incorrectly.

## Slide 17: IGEM G/11 – Industry Standard
The Institution of Gas Engineers and Managers (IGEM) G/11 standard reinforces the importance of:
Using tools and equipment that are suitable, safe, and serviceable.
Following manufacturer instructions at all stages (installation, commissioning, servicing).
Keeping records to demonstrate compliance and defend against liability.

## Slide 18: IGEM G/11 – Industry Standard
G/11 also classifies unsafe situations, which could result from:
Using out-of-date tools
Ignoring instructions on flue sampling locations
Skipping required checks (e.g. analyser readings, tightness tests)

## Slide 19: Case study 1
Scenario Georgia installs a new gas boiler and flue but ignores the manufacturer's minimum flue clearance guidance. The flue terminates too close to a window.
Result
Dangerous combustion products may enter the building
GSIUR and Building Regs Part J breached
Classified as Immediately Dangerous (ID) under IGEM G/11
Risk of enforcement, fine, or de-registration from Gas Safe

## Slide 20: Best practice summary
Always read and follow tool/appliance instructions.
Keep manuals in a digital folder or printed on-site.
Check GSIUR Regs and IGEM guidance if unsure.
Record actions and settings during commissioning.
Use instructions to justify decisions in audits or investigations.

## Slide 21: Storage and on-the-job care
Even the best tools can become useless – or dangerous – if they are not stored, transported, or looked after properly.
Good storage and tool care routines show professionalism, improve efficiency, and ensure compliance with safety expectations in real-world gas engineering environments.

## Slide 22: Van / toolkit storage: Safe transport of equipment
When transporting gas tools between jobs:
Use secure toolboxes, lockable drawers, or racking systems in the van to prevent movement during transit.
Ensure heavier items are stored low and secured to avoid injuries or tool damage during sudden braking.
Label equipment cases clearly — especially those containing calibrated instruments like flue gas analysers and manometers.
Separate clean and dirty/wet tools to avoid corrosion or contamination.

## Slide 23: Tool protection: Magnetic strips, foam inserts
Organising and safeguarding tools on-site can greatly minimise wear and tear:
These methods also promote efficient work, allowing for faster retrieval and storage of tools during tasks.
​
Storage method | Purpose | Example use
Magnetic strips | Keep lightweight hand tools visible and secure | Spanners, screwdrivers
Foam casing | Prevent shock damage to sensitive devices | Digital manometers, FGAs
Lockboxes | Secure high-value or calibrated tools | Multimeters, leak detectors

## Slide 24: Preventing damage on site
Tool care must continue during active work, especially in dusty, wet or hazardous environments:
Use mats, kneeling pads, or folding tables to keep tools off wet or dirty ground.
Don’t leave delicate instruments (e.g. gas analysers) exposed — return them to cases after each reading.
Avoid placing tools where they might fall, be kicked, or run over (e.g. under floorboards, scaffold boards). Inspect and clean tools before returning them to storage.
Tip: Create a habit of doing a 'Tool Check' at the start and end of each job — like a pilot’s pre-flight checklist.

## Slide 25: Common risks and accidents
Even experienced engineers can cause faults or hazards when tools are misused, damaged, or poorly maintained.
Understanding these common risks helps learners avoid accidents, work professionally, and meet industry standards.

## Slide 26: Dropped gauges and instruments
What happens
Pressure gauges, digital manometers, and flue gas analysers are sensitive.
Dropping them — even from a short height — can affect internal calibration or cause invisible cracks.
Consequences
False readings during tightness tests or combustion checks, misdiagnosis of faults, unsafe installations, voided calibration certificates.

## Slide 27: Dropped gauges and instruments
Preventive action
Always return instruments to padded cases.
Don’t carry tools in back pockets or on ladders.
Use lanyards or anti-drop straps when working at height.

## Slide 28: Incorrect hose use (gas test hoses)
What happens
Hoses may become cracked, brittle, or contaminated over time.
Some engineers use incorrect size hoses, causing loose connections or leaks.
Consequences
Gas leaks during pressure testing
Exposure to flammable gases
Failed tightness tests
Breach of GSIUR and IGEM standards.

## Slide 29: Incorrect hose use (gas test hoses)
Preventive action
Check hoses for wear before every job
Use the correct hose diameter for the test point
Replace hoses as per manufacturer guidance.

## Slide 30: Case study 2
Simon, a junior gas engineer, accidentally drops a digital manometer onto a concrete floor. He uses it anyway, unaware that the internal sensor is damaged. His pressure reading shows 21mbar when it should be 26mbar. He leaves a boiler commissioned incorrectly.
Discussion questions:
What went wrong?
Who is responsible?
What could Simon have done differently?
How should his employer respond?

## Slide 31: Summary
You should now be able to:
Identify tools commonly used in gas engineering.
Explain how to use and handle tools safely.
Recognise the risks of poor handling.

## Slide 32
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.