## Slide 1
Occupational Specialism: Gas Engineering
K1.1 Typical hazards and risks associated with working with gas systems and how these can be mitigated
PowerPoint 1.1b: Explosions

## Slide 2
Objectives
By the end of this session, you should be able to:
Define what constitutes an explosion and explain the types relevant to gas engineering (chemical, physical, confined space, etc.).
Identify the common causes of explosions in gas systems, including gas leaks, ignition sources, and equipment failure.
Understand the properties of gases (such as flammability limits, ignition temperatures, and gas-to-air ratios) that influence explosion risk.
Know how to respond in an emergency, including immediate actions, evacuation protocols, and reporting procedures.

## Slide 3
Explosions
When working with gas systems, we need to be aware of the risks of explosions while carrying out our daily duties.
Natural gas and LPG are highly flammable and pose a serious risk to ourselves and others.

## Slide 4
What are explosions?
What defines an explosion?
An explosion refers to the rapid release of energy that leads to an abrupt rise in pressure, temperature, and volume.
This phenomenon is typically accompanied by a shock wave, sound, and may also involve fire or flying debris.
In the field of gas engineering, explosions can happen when combustible gases combine with air in the correct ratios and are ignited.

## Slide 5
Explosions relevant to gas engineering
Chemical explosions
Result from a chemical reaction, typically combustion.
In gas-related situations, this frequently occurs when natural gas or LPG combines with air and ignites.
This is the most prevalent type of explosion in both domestic and commercial gas events.

## Slide 6
Explosions relevant to gas engineering
Confined space explosions
Any explosion in a restricted area where pressure can't dissipate.
Increases the force and damage of the explosion.
Common in basements, cupboards, service voids, etc.

## Slide 7
Explosions relevant to gas engineering
Physical explosions
Caused by pressure build-up without a chemical reaction, e.g. an over-pressurised boiler or a gas cylinder rupturing.

## Slide 8
Explosions relevant to gas engineering
Vapour Cloud Explosions (VCEs)
Occur when a cloud of flammable gas spreads, then ignites.
Can cause flash fires or larger explosions depending on the environment.

## Slide 9
Common causes of explosions in gas systems
Understanding the causes of gas-related explosions is key to preventing accidents and ensuring safe working practices.

## Slide 10
Common causes of explosions
Gas leaks
Uncontrolled release of flammable gas into the atmosphere by:
Damaged or poorly installed pipework.
Loose fittings or joints.
Failing to test for tightness after installation or repair.
Leaked gas can form a flammable mixture with air, which is highly explosive.

## Slide 11
Common causes of explosions
Ignition sources
Any source of heat, flame, spark, or static electricity. Such as:
Electrical switches or appliances.
Smoking or open flames.
Static from clothing or tools.
A flammable gas-air mix only needs a small spark to ignite.

## Slide 12
Common causes of explosions
Equipment failure
Faulty or poorly maintained appliances and systems. Such as:
Gas valves not shutting off properly.
Pressure regulators malfunctioning.
Cracked heat exchangers allowing gas into combustion chambers.
Lack of regular servicing increases risk.

## Slide 13
Common causes of explosions
Human error
Mistakes during installation, maintenance, or repair.
Not following industry standards or manufacturer guidelines.
Inadequate testing or failure to isolate supply.
Lack of ventilation
Confined or sealed spaces can allow gas build-up.
No air movement means leaked gas doesn’t disperse, raising explosion risk.

## Slide 14
Gas properties – cause of explosion risk
Flammability limits
The range of gas concentration in air that can ignite.
Two key values:
Lower Explosive Limit (LEL): Minimum gas concentration needed to ignite.
Upper Explosive Limit (UEL): Maximum concentration that can ignite.

## Slide 15
Gas properties – cause of explosion risk
Example (Methane):
LEL = 5%
UEL = 15%
A methane-air mixture between 5%–15% is explosive if ignited.

## Slide 16
Gas properties – cause of explosion risk
Ignition temperature
This refers to the lowest temperature required to ignite a gas without the presence of a spark or flame.
Every type of gas possesses a unique ignition temperature.
For instance:
Methane = about 537°C
Propane = about 470°C

## Slide 17
Gas properties – cause of explosion risk
Gas-to-Air ratio
For a gas to burn or explode efficiently, it must be mixed with the right amount of air.
Too little or too much air = no ignition.
Stoichiometric mixture = perfect gas-to-air ratio for complete combustion.
Methane = approx. 1:10 (gas:air).

## Slide 18
Gas properties – cause of explosion risk
Vapour density
Heavier gases (like propane) can sink and accumulate in low areas.
Lighter gases (like methane) rise but may still gather in confined roof spaces.
Knowing this helps assess ventilation needs and risk zones.

## Slide 19
Gas properties – cause of explosion risk
Remember
A gas is only explosive when:
It's within its flammable range.
The correct air mix is present.
An ignition source is available.

## Slide 20
UK Legislation and Regulations
DSEAR (Dangerous Substances and Explosive Atmospheres Regulations 2002)
This regulation is relevant to workplaces where there is a potential for explosive atmospheres.

## Slide 21
UK Legislation and Regulations
Employers are required to:
Recognise explosion hazards (such as gas leaks and vapour clouds).
Conduct comprehensive risk assessments.
Classify dangerous zones (Zone 0, 1, 2).
Establish control measures (including ventilation and ATEX-compliant equipment).
Offer training and appropriate signage to employees.
This applies to all combustible gases and vapours, including natural gas and LPG.

## Slide 22
UK Legislation and Regulations
Gas Safety (Installation and Use) Regulations 1998 (GSIUR)
This regulation establishes the legal guidelines for the safe installation, maintenance, and use of gas systems.

## Slide 23
UK Legislation and Regulations
Key responsibilities:
All gas work must be conducted by a Gas Safe registered engineer.
Appliances should be installed and maintained safely.
Regular testing and tightness checks are necessary.
Any leaks or unsafe appliances must be reported and addressed immediately.
The HSE (Health & Safety Executive) enforces these regulations, and violations may lead to prosecution.

## Slide 24
UK Legislation and Regulations
Health and Safety at Work Act 1974
The primary legislation governing workplace safety.
Both employers and employees are required to:
Implement appropriate measures to mitigate injury and hazards.
Adopt safe working practices, particularly when handling gas.

## Slide 25
What to do – gas leak or explosion risk
Immediate steps
Cease all work right away.
Avoid using electrical switches (such as lights, tools, or alarms) as they might trigger sparks.
If it is safe, turn off the gas supply at the emergency control valve (ECV).
Ensure the area is ventilated:
Open windows and doors to help disperse any gas.
Do not use mechanical fans unless they are ATEX-rated and allowed.
Alert others nearby to evacuate in a calm manner.

## Slide 26
What to do – gas leak or explosion risk
Evacuation protocols
Evacuate the building/area quickly and safely.
Use designated escape routes.
Do not use lifts.
Go to the assembly point and remain there until further instructions.
Do not re-enter the area until it has been declared safe by a responsible person (e.g. emergency services, responsible gas engineer).

## Slide 27
What to do – gas leak or explosion risk
Reporting procedures
Call 999 in case of fire, explosion, or if you smell gas in a public place.
Report to the National Gas Emergency Service: 0800 111 999 (24/7).
Provide location, details of the leak, and any risk to life or property.
Notify the supervisor/site manager immediately.
Record the incident as per workplace procedure (incident report form, risk log, etc.).
If required, notify the Health & Safety Executive (HSE) under RIDDOR.

## Slide 28
What to do – gas leak or explosion risk
Safety first – Essential advice
Do not overlook the smell of gas.
Consistently perform pre-work tightness checks and risk evaluations.
Ensure that fire extinguishers and first aid kits are easily accessible.
Always adhere to the emergency procedures established by the company.

## Slide 29: Summary
You should now be able to:
Define what constitutes an explosion and explain the types relevant to gas engineering (chemical, physical, confined space, etc.).
Identify the common causes of explosions in gas systems, including gas leaks, ignition sources, and equipment failure.
Understand the properties of gases (such as flammability limits, ignition temperatures, and gas-to-air ratios) that influence explosion risk.
Know how to respond in an emergency, including immediate actions, evacuation protocols, and reporting procedures.

## Slide 30
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.