## Slide 1
Occupational Specialism: Gas Engineering
K1.1 Typical hazards and risks associated with working with gas systems and how these can be mitigated
PowerPoint 1.1e: Manual handling

## Slide 2
Objectives
By the end of this session, you should be able to:
Identify the factors to take into account when organising a lift.
Describe the procedures involved in kinetic lifting techniques for safe manual handling.
Examine the possible personal injury risks associated with lifting and handling.
Clarify the safe lifting practices used in team lifts and the application of mechanical aids.

## Slide 3
What is manual handling?
Manual handling refers to:
‘The act of moving a load—such as a person, animal, or object—from one place to another using lifting, handling, pushing, pulling, or bodily force’.
Manual lifting is a major cause of workplace injuries, with around 56,000 annual reports of work-related musculoskeletal disorders (MSDs) in the construction sector. There is no truly ‘safe’ weight limit for manual handling, so alternative methods are recommended.

## Slide 4
The Manual Handling Operations Regulations 2002
The Manual Handling Operations Regulations 2002 (MHOR) outline specific responsibilities for employers and employees.
Responsibilities of employers:
Where feasible, prevent employees from engaging in manual handling tasks that may pose a risk to their health and safety.
Conduct assessments to document any significant risks.
Take reasonable measures to eliminate or minimise the risk of injury.
Ensure that employees are given sufficient information to perform manual handling operations safely.

## Slide 5
The Manual Handling Operations Regulations 2002
Responsibilities of employees:
Employees must adhere to the safe working systems established by their employer.
They should utilise the equipment supplied by the employer.
Any hazards encountered must be reported.
Employees must ensure that their actions do not pose a risk to others.

## Slide 6
Considerations for manual handling
Before lifting an item properly, you should take into account the following:
Is it possible to lift the load safely without surpassing the maximum load limits from your current position?
Would using a mechanical aid reduce the risk of injury?
Is the path free from obstacles? Make sure to plan your route.
Is there a need for any specialised training to perform this lift?
Have I reviewed the risk assessment documentation related to this item?

## Slide 7
Are there any more considerations?
Recognise your own strengths and weaknesses.
Determine if you can handle the task alone or if assistance is necessary.
Ensure you know the weight of the item prior to lifting it.
Use gloves to safeguard your hands.
Wear safety boots to protect your feet.

## Slide 8
Manual handling: Assessing the task
When manually managing loads, keep in mind: T I L E
Task – What is the frequency of the task, and how much twisting or bending is involved?
Individual capability – Consider the person's gender, age, and level of experience.
Load – What is the weight? Is there a good grip? Is it bulky or heavier on one side?
Environment – Are conditions hot or cold? Is the floor uneven, windy, or are there stairs?

## Slide 9
Manual handling: Know your capabilities
The Manual Handling Operations Regulations 2002 do not state a given maximum load that is safe to lift.
Consideration must be given to a number of factors such as personal strength, age, ability etc.
Refer to the HSE’s guidance on manual lifting capabilities.
Notes: https://www.hse.gov.uk/pubns/indg143.PDF Page 7

## Slide 10
Manual handling: Weight
The position of the body plays a crucial role in ensuring both comfort and safety during a lift.
Improper positioning can impact the lift's capacity. Refer to the HSE’s guidelines on distances of hands from the base of the spine.
As a result, the term 'kinetic' lifting is employed to refer to the appropriate lifting positions.

## Slide 11
Manual handling: Kinetic lifting
Utilise proper lifting techniques:
Stand with your feet shoulder-width apart and one leg slightly ahead to ensure stability.
Begin with correct posture.
Keep your head elevated while lifting.
Refrain from twisting your back or leaning to the side, particularly when your back is bent.
Set the item down first, then make any necessary adjustments.

## Slide 12
Manual handling: Kinetic lifting
To prevent injuries, the following guidelines should be adhered to:
Prepare for the lift.
Be aware of where the load will be positioned.
Chart the course – clear away any obstacles and remove all packaging materials.
Position your feet appropriately – keep them apart to create a balanced and stable foundation for lifting, with the front leg extended as far forward as is comfortable.

## Slide 13
Manual handling: Kinetic lifting
Lifting
Bend at the knees and position yourself in front of the object, ensuring your feet are spaced apart with one foot placed adjacent to the object (in front of the other foot).
Grasp the load as close to your body as you can.
Maintain a straight back throughout the process—allow your leg muscles to perform the lifting.
Propel yourself forward with your back foot and transition in a single fluid motion.

## Slide 14
Manual handling: Kinetic lifting
Carrying
Maintain your arms close to your body.
Securely grasp the object: use your palms and the bases of your fingers to grip.
Refrain from twisting or leaning, as this can put strain on your back. Instead, pivot by moving your feet rather than your torso.
Prevent pinching your fingers when setting the object down.
Ensure you can see clearly ahead while holding the load.
Set the load down gently. If needed, make adjustments to its position after it has been placed down.

## Slide 15
Manual handling: Kinetic lifting
Transporting loads on your back
Maintain a straight posture by gently lifting the crown of your head and tucking in your chin.

## Slide 16
Manual handling: 2-person lift
When performing a manual lift with two people, it’s important to prepare in advance, communicate clearly and adopt a safe posture.
Utilise correct lifting techniques, keep the item close to your body and maintain a straight back.

## Slide 17
Manual handling: 2-person lift
Essential steps:
Evaluate the load: Examine the weight, dimensions, shape, and any potential risks associated with the object.
Plan the path: Make sure the area is clear and has enough space for lifting.
Select a lifting technique: Determine the most suitable grip and method for lifting.
Communicate effectively: Share the lifting plan and any worries with your lifting partner.
Coordinate the lift: Agree on a signal to lift simultaneously.

## Slide 18
Manual handling: Fatigue and breaks
There is no specific duration that must be adhered to for optimal lifting intervals.
It is important to consider the nature of the work and how often lifts are performed.
Physical capabilities will vary among different engineers, influencing their lifting experience.
In cases of repeated lifting, ensure that breaks are provided to allow for recovery.

## Slide 19
Manual handling: Mechanical lifting aids
Lifting equipment
There is a wide range of small lifting tools designed to aid in material handling both on-site and in workshops. These should only be utilised if you possess the necessary qualifications.
A sack truck is useful for transporting boilers, small cylinders, or bagged materials.
A hydraulic lift is suitable for elevating heavy items from various heights.

## Slide 20
Manual handling: Mechanical lifting aids
Hydraulic lifting equipment is available for hire if necessary.
Certain wholesalers might utilise hydraulic systems fitted on the backs of trucks for the delivery of tubes or appliances.

## Slide 21
You should now be able to:
Identify the factors to take into account when organising a lift.
Describe the procedures involved in kinetic lifting techniques for safe manual handling.
Examine the possible personal injury risks associated with lifting and handling.
Clarify the safe lifting practices used in team lifts and the application of mechanical aids.
Summary

## Slide 22
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.