## Slide 1
Occupational Specialism: Gas Engineering
K1.1 Typical hazards and risks associated with working with gas systems and how these can be mitigated
PowerPoint 1.1h: Dust

## Slide 2
Objectives
By the end of this session, you should be able to:
Define dust within the context of gas engineering and construction.
State the various types of dust that we might come across.
Choose an appropriate face covering to mitigate the hazards associated with dust.

## Slide 3
Dust
Dust poses more than just an inconvenience; it can significantly endanger your lung health. This PowerPoint outlines how to manage these risks and explains the reasons behind it.
According to the Control of Substances Hazardous to Health (COSHH) Regulations, it is essential to safeguard against the dangers presented by hazardous construction dust.

## Slide 4
Dust
Gas engineers, particularly those operating in older structures, might come across a range of dust types, such as asbestos, silica, wood dust, and particles generated from activities like cutting, drilling, and grinding, along with black dust arising from copper sulphide.

## Slide 5
Common types of dusts
Asbestos
Commonly present in structures built prior to the year 2000, asbestos is often located in insulation products such as pipe lagging and boiler insulation.
Silica
Silica dust is a naturally occurring mineral present in materials like sand, sandstone, granite, as well as in construction substances like concrete and mortar. It is produced during activities such as cutting, drilling, and grinding.

## Slide 6
Common types of dusts
Wood dust
Wood dust is frequently encountered in construction, originating from both softwood and hardwood, and can be produced during a range of activities.
Black dust
This type of dust arises from the degradation of copper sulphide, often found in older plumbing systems, and can lead to malfunctions and failures in gas appliances.

## Slide 7
Common types of dusts
Additional dust sources
Dust generated during the cutting, drilling, and grinding of different materials.
Dust produced from demolition and remodelling activities.
Dust originating from insulation substances (such as glass or mineral wool).
Dust from paints and sealants.

## Slide 8
Effects of dust
Consistently inhaling construction dust can lead to serious health issues, including lung cancer, asthma, Chronic Obstructive Pulmonary Disease (COPD), and silicosis.
Due to the nature of their work, construction workers face a heightened risk of developing these conditions, as many typical construction activities generate significant dust levels.
These illnesses can result in lasting disabilities and premature death. It is estimated that more than 500 construction workers lose their lives annually due to silica dust exposure.

## Slide 9
Respiratory protective equipment (RPE)
As a gas engineer, respiratory protective equipment (RPE) plays a vital role in protecting us from inhaling harmful substances. It should only be used when all other control measures have been fully implemented.
RPE encompasses various types of respirators (filtering devices) and breathing apparatus, offering a range of choices from disposable half masks to powered respirators and full breathing apparatus.

## Slide 10
Respiratory protective equipment (RPE) – Fit testing
Respiratory protective equipment (RPE) must offer sufficient protection for each individual user. If there are leaks, the RPE cannot safeguard the wearer. One of the primary reasons for leaks is improper fit; therefore, tight-fitting facepieces must conform well to the wearer's face to function effectively.
Given the variety of shapes and sizes among individuals, it is improbable that a single type or size of RPE facepiece will suit everyone. Conducting fit testing is essential to confirm that the chosen equipment is appropriate for the user.

## Slide 11
Types of RPE
Face covering masks
Before March 2020, most people had never used safety masks. During the pandemic, masks became essential for entering public spaces. It’s important to distinguish certified respirators, which are PPE, from common face coverings or surgical masks used during Covid.
Respirators protect against airborne hazards like smoke, dust, and viruses, while surgical masks (EN 14683) mainly protect others by blocking biological particles. Fashion masks may offer some virus protection but provide little defence against dust or fumes.

## Slide 12
Types of RPE
Disposable masks
Disposable dust masks are often the most cost-effective option for respiratory protection. To function properly, they must fit snugly on the wearer’s face, requiring a face fit test for proper sealing and protection.
There are three categories of particulate filtration for disposable and semi-disposable masks. Total inward leakage includes face seal leakage, exhalation valve leakage (if applicable), and filter penetration.

## Slide 13
Types of RPE
Disposable masks
Class | Min Efficiency | Max Inward Leakage | Total Protection
FFP1 | 80% | 22% | 58%
FFP2 | 94% | 8% | 86%
FFP3 | 99% | 2% | 97%
P1 class respirators are suitable for use in areas with non-toxic, non-fibrogenic dust.
P2 class respirators safeguard against harmful particles, including dust, smoke, bacteria, and mould.
P3 class respirators provide the highest level of protection against toxic substances, including known carcinogens like asbestos, as well as wood dust and silica in masonry.

## Slide 14
Types of RPE
Reusable non-replacement filter half mask
Reusable non-replaceable filter half masks, or 'semi-disposable' masks, meet EN 405 standards. They feature integrated combination filters for particulates and gases, reducing contamination risk.
A common setup is A2/P3: P3 offers top dust protection, while A2 guards against organic vapours. This combination is widely used in construction for its effectiveness against site hazards.

## Slide 15
Types of RPE
Reusable half masks with replaceable filters
Reusable half masks that meet European standard EN 140 allow for filter replacement, providing versatility based on protection needs. Various gas and vapour filters can be purchased separately.
For dusty conditions, dust pre-filters can attach to the gas and vapour cartridge, creating a combination filter. This helps prevent early clogging of the pricier carbon filters. If there's no risk from gases or vapours, individual particulate filters are also an option.

## Slide 16
Respiratory protective equipment (RPE) – APF
In the UK, the Standard Assigned Protection Factor (APF) assists employers in meeting the Control of Substances Hazardous to Health Regulations 2002 (COSHH), which focus on managing chemical exposure and safeguarding workers' health.
The APF serves as an assessment of the level of protection offered by a respirator.
When properly fitted (through a face fit test) and worn correctly, an FFP1 respirator can decrease exposure to airborne particles by a factor of 4, an FFP2 by a factor of 10, and an FFP3 by a factor of 20.

## Slide 17
You should now be able to:
Define dust within the context of gas engineering and construction.
State the various types of dust that we might come across.
Choose an appropriate face covering to mitigate the hazards associated with dust.
      Summary

## Slide 18
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.