## Slide 1
Occupational Specialism: Gas Engineering
K1.1 Typical hazards and risks associated with working with gas systems and how these can be mitigated
PowerPoint 1.1i: Electrocution

## Slide 2
Objectives
By the end of this session, you should be able to:
Identify the necessary electrical testing equipment.
Explain the concepts of ‘safe to touch’ and ‘safe isolation’.
Know how to work safely with electricity.
Know the procedures to follow in the event that someone comes into contact with electricity and sustains electrocution.

## Slide 3
Electrical hazards in gas engineering
In 1998, a gas utility engineer responded to a reported gas emergency at a residential property.
While attempting to gain access to a gas meter installed underneath the kitchen sink of the property, the engineer placed his hand on the sink and the emergency control valve.
Due to a fault in the property’s electrical installation, the engineer received a significant electric shock, which, tragically, proved fatal.

## Slide 4
Electrocution
Electric shocks can be lethal, and several registered gas engineers have tragically lost their lives due to complications related to the electrical supply of the appliances they were servicing.
Legislation, including the Health and Safety at Work etc Act (HSWA) and the Electricity at Work Regulations (EWR), establishes essential guidelines aimed at safeguarding individuals in the workplace.

## Slide 5
Electricity at Work Regulation 1989
The Electricity at Work Regulation 1989 provides regulations under the HASAWA, which include:
Regulation 13 – Precautions for work on equipment made dead
Regulation 14 – Work on or near live conductors
Regulation 16 – Persons to be competent to prevent danger and injury.

## Slide 6
Keep the working environment safe
Ensure that there is adequate space for both access and egress while on the job.
This involves maintaining control over the work area, which may necessitate the installation of temporary barriers.
Additionally, it is vital to inform nearby individuals about the work being performed and any potential hazards related to it.

## Slide 7
Use the correct tools
Gas engineers are required to use tools that meet the relevant product standards. This is particularly important for electrical testing instruments such as voltage indicators, multimeters, and test leads.
When selecting electrical testing equipment, it is crucial to ensure that it has been manufactured and certified in accordance with the standards outlined in TB 118.

## Slide 8
Check earth connections
It is essential to verify that the electrical supply to the gas appliance is properly earthed.
This is particularly crucial when handling metal-cased devices like a boiler, which must have a reliable earth connection.
Such equipment is typically classified as Class 1 equipment.

## Slide 9
Safety protocol phrases
The phrases "safe to touch" and "safe electrical isolation" are essential safety protocols for handling electrical equipment.
They are designed to protect personnel by verifying that no dangerous voltages are present before any part of the installation is touched.

## Slide 10
“Safe to touch”
Purpose
To confirm that a component of electrical equipment or installation does not carry dangerous voltage.
How it's done
A "safe to touch" check is performed using a non-contact voltage detector to examine casing or metal parts for voltage.
Significance
Ensures engineers can handle equipment safely, thereby reducing the risk of electric shock.
Example
Before touching a boiler casing, a gas engineer uses a non-contact voltage detector to confirm no hazardous voltage.

## Slide 11
Safe isolation procedure
Obtain permission from the appropriate authority before commencing work, as essential services may need to remain uninterrupted. In certain cases, securing a work permit may also be necessary.
Identify the isolation point, then turn it off and secure it.
Attach warning labels to inform others that the electrical installation has been isolated.
Ensure the isolation is secure by keeping the key to the lock with you at all times.
Verify that your voltage indicator or test lamp is functioning correctly by using a proving unit or a known live source.
Confirm that the system or equipment is DEAD by using an approved voltage indicator or test lamp.
Test the outgoing side of the isolation device (such as a fuse, main switch, or MCB) to ensure it is DEAD.

## Slide 12
Safe isolation procedure
Conduct the following tests
Test single-phase installations to verify that there is no voltage present between:
Earth and Line
Earth and Neutral
Neutral and Line
Recheck the voltage indicator on the proving unit.
When disconnecting the main energy source, it is also crucial to isolate any secondary sources, such as uninterruptible power supplies and microgenerators.
Only after the system or equipment has been isolated should work commence.

## Slide 13
Electrocution – Safe Isolation
Purpose
To disconnect an electrical installation or section from the power supply, ensuring no current is present.
Process
Identify the isolation point (circuit breaker, fuse, or switch), cut off the supply, and confirm conductors are de-energised using approved testing equipment.
Significance
Prevents electric shock and ensures safety for anyone working on or near the isolated system.
Lock-off devices
Use lock-off devices (e.g. padlocks) at isolation points to prevent accidental re-energisation.

## Slide 14
What to do if someone is electrocuted
Ensure safety
Do not touch the person if they’re still in contact with electricity.
Cut off power at the mains if possible.
If you can’t turn off power, use a non-conductive item (dry wooden pole, broom handle, or plastic mat) to push them away.
Stay at least 20 feet away if high-voltage lines are active.
Call for help
Dial 999 or 112 for emergency medical assistance immediately.

## Slide 15
What to do if someone is electrocuted
Evaluate and administer First Aid
Ensure the person is clear of the electrical hazard, then check breathing and pulse.
If unresponsive with no pulse or breathing, start CPR immediately.
If conscious but in shock (pale, sweating, dizzy), lay them down, elevate legs, and keep them warm and calm.
Cover burns with a clean, dry cloth; do not remove clothing stuck to skin.
Move only if they are in immediate danger.

## Slide 16
You should now be able to:
Identify the necessary electrical testing equipment.
Explain the concepts of ‘safe to touch’ and ‘safe isolation’.
Know how to work safely with electricity.
Know the procedures to follow in the event that someone comes into contact with electricity and sustains electrocution.
Summary

## Slide 17
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.