## Slide 1
Occupational Specialism: Gas Engineering
K1.2 Safe working practices associated with working with gas systems
PowerPoint 1.2: Working safely

## Slide 2: Starter
Why is gas work more regulated than most trades?
Consider risks like explosions, carbon monoxide poisoning, and fire.
Think about the public impact of gas incidents in homes or workplaces.

## Slide 3: Objectives
By the end of this session, you should be able to:
Recall safe working practices in gas engineering environments.
Explain the role of RAMS (risk assessments and method statements).
Describe the selection and purpose of PPE for gas-related work.
Interpret Building Regulations and their application in gas safety.
Evaluate how unsafe practices can harm people, property, and reputation.

## Slide 4: Building regulations and safe practice
GSIUR regulates gas safety in both residential and commercial settings.
Approved Document J outlines standards for fuel storage and combustion appliances.
CDM Regulations aim to eliminate risks throughout the entire lifecycle of a project.
Contractors are required to adhere to IGEM guidance and stay informed through bulletins.
Failure to comply may result in enforcement notices and potential legal action.

## Slide 5: Gas Safety (Installation and Use) Regulations 1998
The regulations apply to anyone working on gas installations, including installers, service providers, maintenance staff, repair technicians, landlords, and both employed and self-employed workers.
They set standards for the safe installation, maintenance, and operation of gas appliances, ensuring they are well-built, durable, and suitable for the gas type.
In essence, the GSIUR ensures gas systems are installed and maintained safely to protect people and prevent accidents.

## Slide 6: Approved Document J
Approved Document J, part of UK Building Regulations, provides guidance on safely installing and operating combustion appliances and fuel storage systems.
It covers air supply, discharge of combustion by-products, fire protection, and system information.
The document applies to appliances that use solid fuel, gas, and oil, as well as fuel storage systems.
Its aim is to ensure the safe use of the building for occupants, while reducing pollution and preventing carbon monoxide poisoning.

## Slide 7: The Construction (Design and Management) Regulations 2015
The CDM (Construction Design and Management) Regulations, especially CDM 2015, set health and safety rules for all UK construction projects. Their goal is to ensure safety is considered at every stage, from planning to completion.
These regulations outline the responsibilities of duty holders, including clients, designers, principal contractors, and contractors, in managing risks and maintaining a safe work environment.

## Slide 8: The Institute of Gas Engineers and Managers
The Institute of Gas Engineers and Managers (IGEM) is a professional engineering institution dedicated to promoting and maintaining high standards of competence within the gas industry.
IGEM achieves this by providing technical standards, offering professional development opportunities, and advocating for the interests of the gas industry.
https://www.igem.org.uk/

## Slide 9: Documentation: RAMS
RAMS stands for Risk Assessment Method Statement, which is a crucial health and safety document designed to outline the procedures necessary to safely perform a particular activity or task.
RAMS can be used alongside the risk assessment process.

## Slide 10: Documentation: RAMS
Risk assessments are designed to identify hazards and assess their potential severity and likelihood of occurrence.
Method statements provide a comprehensive outline of the safe execution of tasks.
Documentation should consider COSHH, PUWER, and Manual Handling Regulations.
Revisions are necessary when there are changes in conditions, tasks, or personnel.
This process helps ensure compliance and fosters a culture centred on safety.

## Slide 11: RAMS – Risk assessment
Risk assessments serve to document hazards found in the workplace, evaluate the probability and seriousness of risks, and develop appropriate control measures to either eliminate or mitigate those risks.

## Slide 12: RAMS – Safe Systems of Work
Method statements, often known as a Safe System of Work, enhance the details provided in risk assessments by elaborating on hazard identification and management strategies.
They specify how particular tasks can be performed safely, outlining necessary control measures, safety precautions, and the implementation of control equipment.

## Slide 13: RAMS – Safe Systems of Work
Ensure that permit-to-work systems, isolation procedures, and appropriate signage are implemented and maintained.
Gas safe isolation should incorporate lock-off mechanisms and cautionary signs.
Documentation is required for visual inspections and leak assessments.
All tools must be calibrated, subjected to periodic PAT testing, and inspected regularly.
Conducting toolbox talks helps to raise awareness about new site-specific hazards.

## Slide 14: Personal Protective Equipment (PPE)
PPE serves as the final barrier against particular hazards.
Examples include safety goggles, heat-resistant gloves, and flame-retardant apparel.
Hearing protection is essential when operating power tools.
The appropriate PPE is determined by the risks outlined in the RAMS.
Respiratory Protection Equipment (RPE) is necessary for situations involving gas leaks, asbestos, or working in confined spaces.

## Slide 15: Impact of unsafe practice
Failure to properly isolate gas can result in fire hazards or explosions.
Unreported issues could lead to exposure to carbon monoxide.
Clients might lose confidence in installers who take shortcuts.
The HSE may issue notices for improvement or prohibitions.
Project delays, penalties, or even loss of life may ensue.

## Slide 16: Summary of safe working practices
Effective safety practices integrate an understanding of regulations with necessary precautions to ensure a safe environment.
All site personnel should understand and comply with documents such as RAMS.
Personal Protective Equipment (PPE) should be specific to the task and kept in good condition.
Regulations such as Part J and CDM impact all areas of gas-related work.
Continuous training and Continuing Professional Development (CPD) are crucial for upholding safety standards.

## Slide 17: Knowledge check
What PPE would you wear when working on a boiler flue outside?
Why is it critical to lock off gas and electrical systems before servicing?

## Slide 18: Summary
You should now be able to:
Recall safe working practices in gas engineering environments.
Explain the role of RAMS (risk assessments and method statements).
Describe the selection and purpose of PPE for gas-related work.
Interpret Building Regulations and their application in gas safety.
Evaluate how unsafe practices can harm people, property, and reputation.

## Slide 19
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.