## Slide 1
Occupational Specialism: Gas Engineering
K1.3 Emergency procedures for unsafe situations
PowerPoint 1.3a: Legal reporting and documentation requirements

## Slide 2: Starter
Below are three short gas-related visit notes written by a gas engineer.
Read each one and write down:
What’s missing from the report?
What could go wrong if the missing information is not included.
Example 1: “Attended property. Found a leak. Turned gas off. Advised customer.” What’s missing?
Example 2: “The appliance is not safe to use, so I left it turned off.” What’s missing?
Example 3: “Boiler flue damaged and spilling fumes in loft. Spoke to landlord, no work done.” What’s missing?

## Slide 3: Objectives
By the end of the session, you should be able to:
Outline the purpose of reporting procedures in gas engineering.
Explain the legal requirements for documentation under GIUSP and RIDDOR.
Complete job sheets and unsafe situation reports.
Evaluate the consequences of failing to report incidents accurately.

## Slide 4: Legal frameworks and regulations
Regulation | Summary
GIUSP | Guides classification and action on unsafe gas situations: ID, AR, NCS.
GSIUR | Legal requirement for gas work to be safe and appropriately documented.
RIDDOR | Requires reporting of dangerous occurrences to the HSE.
When to report under RIDDOR:
Gas escape causing explosion or injury.
Carbon monoxide poisoning.
Dangerous gas fittings or appliances.

## Slide 5: Key documentation and forms
Document | Purpose
Job Sheet | Records all works, issues found, actions taken.
Warning Notice | Placed on faulty appliances (“Do Not Use” labels).
Unsafe Situations Report | Official record classifying and explaining the risk.
RIDDOR Form (F2508G) | Sent to HSE for serious incidents.
Gas Safety Record (CP12) | Used in rental properties to confirm safety checks.
Remember – “If it’s not written down, it didn’t happen.”

## Slide 6: Job sheet
Purpose: To document the specifics of a visit, including identified faults, actions performed, materials utilised, and any suggestions.
Contents: Date and time of the visit, customer information and property location, engineer's name along with their Gas Safe registration number, description of the problem, classification of the issue (ID, AR, NCS), work completed, recommendations for next steps, and customer signature.

## Slide 7: Warning notice
Purpose: To distinctly mark an appliance or system that poses safety risks. This ensures legal protection for both the end user and the engineer.
Features: Wording stating, "Do Not Use" (usually on a red label), type of hazard (such as gas leakage or carbon monoxide risk), description of the appliance/system, reason for the warning, date and time, engineer's name and Gas Safe number, and customer signature (or a note if declined).

## Slide 8: Unsafe situations report (as per GIUSP)
Purpose: To officially record the identification, categorisation, and measures taken regarding a gas safety hazard.
Typically includes: Site address and customer contact information. Appliance or system related to the issue. Description of the unsafe condition. GIUSP classification (ID, AR). Immediate actions undertaken (e.g. isolation, repair). Customer's acceptance or refusal of the action. Signature sections for both the engineer and the customer. Reference to the guidance adhered to (e.g. TB001 from Gas Safe Register).

## Slide 9: RIDDOR report (F2508G)
Purpose: To notify the Health and Safety Executive (HSE) about hazardous gas-related events. This reporting is compulsory under the following circumstances: A person dies or sustains serious injuries due to gas; a fire or explosion occurs because of gas; or a gas fitting is identified as dangerous, regardless of whether any harm has occurred.
Submitted by: Registered gas engineers, employers, or duty holders.

## Slide 10: Gas safety record (CP12)
Purpose: To offer evidence of safety inspections for landlords, housing associations, or managing agents.
Legally required for: All rented residential properties.
Frequency: Conducted annually by Gas Safe Registered engineers.
Contents include: Details of the engineer and their business registration. List of appliances (make/model/location). Safety checks performed. Results (pass/fail). Any identified defects and subsequent actions taken. Confirmation of flue and ventilation assessments. Date for the next inspection.

## Slide 11: RIDDOR
In the field of gas engineering, RIDDOR (Reporting of Injuries, Diseases and Dangerous Occurrences Regulations) encompasses regulations mandating the reporting of particular incidents associated with gas work to the Health and Safety Executive (HSE).
This includes cases where an individual has died or sustained serious injuries from a gas-related incident, along with dangerous events such as the unexpected, uncontrolled release of a large volume of gas.

## Slide 12: RIDDOR – Reporting incidents
Dangerous gas fittings
RIDDOR requires reporting incidents where gas appliances or fittings are deemed dangerous due to design, construction, installation, modification, or servicing.
Gas escapes
Accidents involving the escape of gas, especially if it leads to death, loss of consciousness, or hospitalisation.

## Slide 13: RIDDOR – Reporting incidents
Incomplete combustion
Incidents where gas appliances are not burning the fuel correctly, or where the products of combustion are not being adequately removed (e.g. spillage of flue gases).
Unsafe installations
Situations where gas appliances are not properly installed or connected, such as using unsuitable materials like garden hose for connections.

## Slide 14: RIDDOR – Reporting incidents
Defective flues
Faulty flues or chimneys that don't properly vent combustion products.
Unsafe devices
Appliances where safety devices like flame failure or supervision devices have been rendered inoperative.
Accidental gas leakage
Any sudden and uncontrolled release of flammable gas or liquid that could cause harm.

## Slide 15: RIDDOR – Reporting incidents
Who should report?
Employers, including gas suppliers and the employers of Gas Safe registered engineers.
The self-employed, including self-employed Gas Safe registered engineers.
The responsible person in control of work premises.

## Slide 16: RIDDOR – Reporting incidents
How to report
Incidents can be reported online through the HSE website.
A telephone reporting service is available for fatal/specified and major incidents.
Gas Safe registered engineers should also report dangerous gas fittings to Gas Safe Register or HSE if they don't meet RIDDOR criteria.

## Slide 17: Summary
You should now be able to:
Outline when and how to report gas incidents.
Use job sheets and unsafe situation notices.
Apply GIUSP classifications confidently.
Understand why documentation is vital for safety and legal compliance.

## Slide 18
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.