## Slide 1
Occupational Specialism: Gas Engineering
K1.20 Implications of legislation, standards and manufacturer’s instructions alongside additional guidance to employers and those working with gas systems
PowerPoint 1.20a: Core gas legislation

## Slide 2: Starter
"What laws or rules do you think a gas engineer must follow when working in someone’s home or business?"
Instructions:
Think quietly for 1 minute.
Pair up and discuss your ideas.
Share with the class – list all answers on the board (no wrong answers at this stage).

## Slide 3: Objectives
By the end of this session, you should be able to:
Recall the key UK gas safety laws and their purpose.
Describe the roles of legislation in ensuring public and worker safety.
Summarise the key requirements of GSIUR.
Interpret basic legal duties for employers and engineers.

## Slide 4: Gas Safety (Installation and Use) Regulations 1998
The Gas Safety (Installation and Use) Regulations 1998 (GSIUR) outline the legal obligations in the UK regarding the installation, upkeep, and operation of gas systems, appliances, and flues.
These regulations are crucial for individuals employed as gas engineers and are integrated into the legal framework established by the Health and Safety at Work Act 1974.

## Slide 5: Gas Safety (Installation and Use) Regulations 1998
What the Regulations cover:
1. Gas appliances
Safe installation and maintenance of appliances (e.g. boilers, cookers, fires).
Appliances must be suitable for the purpose and installed in accordance with manufacturer instructions and recognised standards.

## Slide 6: Gas Safety (Installation and Use) Regulations 1998
What the Regulations cover:
2. Pipework and flues
Proper design, materials, and workmanship in pipework installation.
Installation of adequate flueing and ventilation.
Requirements for tightness testing and purging of gas systems.

## Slide 7: Gas Safety (Installation and Use) Regulations 1998
What the Regulations cover:
3. Work on gas installations
Only engineers registered with the Gas Safe Register may carry out gas work (Regulation 3).
Engineers must be competent and qualified to undertake specific categories of gas work.

## Slide 8: Gas Safety (Installation and Use) Regulations 1998
What the Regulations cover:
4. Landlord duties
Annual gas safety checks on appliances and flues.
Provide Gas Safety Records to tenants within 28 days of the check or before new tenants move in.
Maintain appliances and installations in a safe condition.

## Slide 9: Gas Safety (Installation and Use) Regulations 1998
What the Regulations cover:
5. Emergency controls and safety devices
Emergency control valves (ECVs) must be accessible.
Safety devices (e.g. flame failure devices, CO detectors) must be maintained in working order.

## Slide 10: Gas Safety (Installation and Use) Regulations 1998
What the Regulations cover:
6. Unsafe situations
Gas engineers must follow the Gas Industry Unsafe Situations Procedure (GIUSP).
If a dangerous appliance is found, it must be labelled, made safe, and the responsible person must be informed.

## Slide 11: Gas Safety (Installation and Use) Regulations 1998
What the Regulations cover:
7. Reporting and Records
Certain incidents (e.g. explosions or serious gas leaks) must be reported under RIDDOR.
Engineers must keep records of work where required.

## Slide 12: Gas Safety (Installation and Use) Regulations 1998
Key regulations:
Regulation 3 – Only competent individuals (Gas Safe Registered) are permitted to perform gas work.
Regulation 26 (1–9) – Installations must not pose a risk; ensure safe combustion; provide sufficient ventilation; and have proper flueing.
Regulation 36 – Responsibilities of landlords include conducting annual inspections, maintaining records, and ensuring maintenance.

## Slide 13: Health and Safety at Work Act 1974
The Health and Safety at Work Act 1974 (HASAWA) is essential for gas engineers in the UK.
It mandates that employers and self-employed engineers must, as far as reasonably possible, ensure the health, safety, and welfare of themselves, their staff, and the public.
This includes providing safe work systems, proper handling and storage of gas, and adequate training and supervision.

## Slide 14: Health and Safety at Work Act 1974
Gas engineers should implement HASAWA principles in their work:
Installation: Safely install gas appliances per manufacturer guidelines and regulations (e.g. GSIUR).
Commissioning and Testing: Utilise safe isolation methods and combustion analysis to mitigate risks like explosions or CO poisoning.
Maintenance and Repair: Perform risk assessments and use appropriate PPE.
Decommissioning: Ensure installations are safe and prevent the re-use of hazardous systems.

## Slide 15: Health and Safety at Work Act 1974
Grasping HASAWA goes beyond merely being aware of the legislation; it involves prioritising safety, safeguarding others, and upholding professional standards.
Gas engineers are required to implement it on a daily basis to guarantee safe operations, adhere to regulations, and minimise risks to both life and property.

## Slide 16: Rights of Entry Regulations
The Gas Safety (Rights of Entry) Regulations 1996 grant authorised personnel legal powers to enter premises for specific purposes relating to gas safety.
These regulations support the enforcement of the Gas Safety (Installation and Use) Regulations 1998 (GSIUR) and are crucial for ensuring public protection where gas risks are present.

## Slide 17: Rights of Entry Regulations
Purpose of the Gas Rights of Entry Regulations
The regulations empower authorised gas personnel, such as:
Gas suppliers
Gas transporters
Gas engineers working under the direction of a relevant authority (e.g. the HSE).

## Slide 18: Rights of Entry Regulations
To enter domestic and commercial premises to:
Inspect the gas installation and appliances
Carry out maintenance or safety checks
Cap off or disconnect a dangerous supply or appliance
Respond to a reported gas escape or other emergency.

## Slide 19: Rights of Entry Regulations
Legal powers granted
Under the regulations:
Entry must be at a reasonable time, except in an emergency.
If entry is refused, a warrant can be obtained from a Magistrate’s Court.
The warrant authorises forced entry, usually with police support, if there is:
  A suspected gas leak
  An unsafe gas installation
  Non-compliance with a legal gas safety notice

## Slide 20: Rights of Entry Regulations
Emergency access
In emergency situations, authorised persons can enter without prior notice to prevent loss of life or serious injury, for example:
  A report of a gas smell or explosion.
  Detection of high carbon monoxide levels.
  Dangerous appliances in use.

## Slide 21: Rights of Entry Regulations
Legal conditions and responsibilities
The person entering must carry and present official identification.
The premises must be left secure if forced entry has occurred.
Reasonable steps must be taken to minimise damage.
If damage is caused, the person or company responsible for the entry may be liable for repair costs, unless the owner was at fault.

## Slide 22: Rights of Entry Regulations
Why this matters to gas engineers
Understanding these regulations is essential because:
It clarifies legal boundaries and duties.
It ensures engineers understand the procedure when reporting or dealing with immediately dangerous (ID) situations.
It reinforces the importance of compliance, cooperation, and communication with occupants, clients, and emergency services.

## Slide 23: Role of Gas Safe Register in legal compliance
The role of a gas engineer in legal compliance is central to ensuring the safety, reliability, and legality of gas systems and appliances in the UK.
Gas engineers have a legal and ethical duty to follow specific laws, regulations, and industry standards in every aspect of their work.
As a gas engineer, legal compliance is your duty. You must follow gas safety laws, work only if you're registered, keep accurate records, maintain your competence, and always put people’s safety first. It’s not just good practice – it’s the law.

## Slide 24: Summary
You should now be able to:
Recall the key UK gas safety laws and their purpose.
Describe the roles of legislation in ensuring public and worker safety.
Summarise the key requirements of GSIUR.
Interpret basic legal duties for employers and engineers.

## Slide 25
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.