## Slide 1
Occupational Specialism: Gas Engineering
K1.20 Implications of legislation, standards and manufacturer’s instructions alongside additional guidance to employers and those working with gas systems
PowerPoint 1.20b: British Standards and IGEM guidance

## Slide 2: Starter
What do you think is the difference between a law and a standard? Can you think of any examples from the gas industry?
Instructions:
Spend 1 minute thinking individually.
Pair up and discuss your thoughts.
Share your ideas with the class – list on the board under two columns: Law and Standard.

## Slide 3: Objectives
By the end of this session, you should be able to:
Identify relevant British Standards and IGEM documents.
Explain the role of standards in ensuring consistent quality.
Apply selected standards to example installation tasks.

## Slide 4: British Standards
British Standards (BS) are essential for gas engineers as they provide industry-recognised best practices for the design, installation, commissioning, and maintenance of gas systems.
While they are not laws, many are referenced in legislation and can be used in court to demonstrate whether work was done to a reasonable and expected standard.
Below is a comprehensive list of key British Standards applicable to gas engineers in the UK.

## Slide 5: British Standards
1. BS 6891
Title: Specification for the installation and maintenance of low-pressure gas installation pipework up to 35 mm (R1¼) in domestic premises (2nd family gas)
Use:
Domestic gas pipework design and installation
Defines pipe sizing, routing, ventilation, and sleeving requirements

## Slide 6: British Standards
2. BS 5440 Parts 1 & 2
BS 5440-1: Flues BS 5440-2: Ventilation for gas appliances
Use:
Sets requirements for flueing and ventilation in gas installations
Applies to natural gas and LPG appliances

## Slide 7: British Standards
3. BS 7967
Title: Guide for the use of electronic portable combustion gas analysers for the measurement of carbon monoxide in dwellings and the combustion performance of domestic gas-fired appliances.
Use:
Details how to use flue gas analysers correctly
Supports accurate commissioning and servicing

## Slide 8: British Standards
4. BS 6172
Title: Installation, servicing and maintenance of domestic gas cooking appliances (2nd and 3rd family gases).
Use:
Provides best practice for fitting gas cookers and hobs
Covers installation checks and commissioning steps

## Slide 9: British Standards
5. BS 7969
Title: Installation and maintenance of domestic gas-fired boilers of rated input not exceeding 70 kW net.
Use:
Guidance on safe installation of boilers
Commonly used in conjunction with the manufacturer’s instructions

## Slide 10: British Standards
6. BS 7671 (IET Wiring Regulations)
Use:
While primarily electrical, gas engineers must understand Part 7 (Special installations) and safe electrical isolation when working with electrically controlled gas appliances

## Slide 11: British Standards
7. BS 5839-6
Title: Fire detection and fire alarm systems for buildings. Code of practice for the design, installation, commissioning and maintenance of fire detection and fire alarm systems in domestic premises
Use:
Relevant where gas engineers install CO alarms and interlinked systems with boilers

## Slide 12: British Standards
8. BS EN 13501 / BS EN 15502
These harmonised European Standards apply to boilers and gas-fired appliances, now integrated with UK guidance under UKCA marking.

## Slide 13: British Standards
9. BS EN 1775
Title: Gas supply systems. Gas pipework for buildings – Maximum operating pressure ≤ 5 bar
Use:
Safety, design and material selection for pipework in buildings
Common for commercial and multi-occupancy premises

## Slide 14: British Standards
10. BS 8499
Title: Visual inspection of gas appliances – Guide to best practice
Use:
Procedures and checklists for gas engineers conducting visual inspections prior to commissioning or maintenance

## Slide 15: IGEM Standards
IGEM Standards tell you how to work safely and professionally with gas. While the law says what you must do, IGEM guides show you how to do it right – especially when testing, purging, installing, and dealing with unsafe situations.

## Slide 16: IGEM Standards
IGEM Standard | Title | Relevance to Gas Engineers
IGEM/G/1 | Competence of Individuals | Competency framework
IGEM/UP/1 | Tightness & Strength Testing | Large systems
IGEM/UP/1A | Tightness Testing (≤1m³) | Domestic installations
IGEM/UP/1B | Commercial Tightness Testing | >1m³ systems
IGEM/UP/2 | Gas Pipework & Boosters | High-rise and plant rooms
IGEM/UP/4 | Domestic Appliance Installation | Homes
IGEM/UP/6 | Compression Fittings | Pipework jointing
IGEM/UP/10 | NG/LPG in Dwellings | Off-grid / LPG systems
IGEM/UP/11 | Educational Establishments | Schools & labs
IGEM/G/11 | Unsafe Situations Procedure | Mandatory for safety
IGEM/TD/13 | Suspected Fumes | CO investigation

## Slide 17: Building Regulations
For gas engineers in the UK, Building Regulations are a vital part of legal compliance, ensuring gas installations are safe, efficient, and suitable for domestic and commercial buildings.
These regulations apply to the design, installation, inspection, and commissioning of gas systems and appliances.
Over the next few slides are a breakdown of the main Building Regulations relevant to gas engineers.

## Slide 18: Building Regulations
1. Part A – Structure
Key relevance:
Prevents structural damage during installation
Drilling or notching of joists must follow safe zones
Example: When routing gas pipework through joists or walls, engineers must ensure they don't weaken the structure or breach structural rules.

## Slide 19: Building Regulations
2. Part B – Fire safety
Key relevance:
Placement of gas appliances must not compromise fire escape routes
Materials used must have appropriate fire resistance
Example: A gas boiler installed in an escape corridor must be enclosed with fire-resistant materials if required.

## Slide 20: Building Regulations
3. Part C – Site preparation and moisture resistance
Key relevance:
Prevents moisture affecting gas pipework or appliances
Gas meter boxes must be properly sealed to prevent water ingress

## Slide 21: Building Regulations
4. Part D – Toxic substances
Key relevance:
Applies to the prevention of exposure to substances like asbestos
Engineers must know how to identify and avoid disturbing hazardous materials

## Slide 22: Building Regulations
5. Part E – Resistance to the passage of sound
Key relevance:
Gas appliances or flues in party walls must not breach acoustic insulation standards
Example: A boiler flue passing through a party wall must be properly sealed to maintain soundproofing.

## Slide 23: Building Regulations
6. Part F – Ventilation
Key relevance:
Ensures there is adequate air supply for combustion and room ventilation
Applies to open-flued and flueless appliances
Example: A room-sealed boiler needs less ventilation than an open-flued fire, but minimum ventilation still applies.

## Slide 24: Building Regulations
7. Part G – Sanitation, hot water safety, and water efficiency
Key relevance:
Gas water heaters must deliver hot water safely and efficiently
Anti-scald protection and safe operating temperatures are required

## Slide 25: Building Regulations
8. Part H – Drainage and waste disposal
Key relevance:
Condensate from high-efficiency gas boilers must be disposed of via appropriate drainage
Prevents backflow or freezing of condensate pipes

## Slide 26: Building Regulations
9. Part J – Combustion appliances and fuel storage systems (MOST CRUCIAL FOR GAS ENGINEERS)
Key relevance:
Covers safe installation of boilers, fires, flues, chimneys, hearths, and ventilation
Mandatory for all combustion appliances, especially gas
Example: A flue terminal must be a safe distance from windows, doors, and air bricks in line with Part J.

## Slide 27: Building Regulations
10. Part L – Conservation of fuel and power
Key relevance:
Encourages energy-efficient gas appliances
Boiler installations must meet minimum SEDBUK ratings and include thermostatic controls
Example: A new boiler must have time and temperature controls fitted and comply with minimum efficiency standards.

## Slide 28: Building Regulations
11. Part M – Access to and use of buildings
Key relevance:
Ensures installations do not hinder access for people with disabilities.
Example: A boiler in a public building must be installed in a way that maintains accessibility.

## Slide 29: Building Regulations
12. Part P – Electrical safety in dwellings
Key relevance:
Covers electrical work on gas appliances (e.g. boiler wiring, isolation switches)
Gas engineers must understand safe isolation procedures

## Slide 30: Building Regulations
13. Part Q – Security
Key relevance:
Mainly applies to doors/windows, but if engineers are routing pipework near openings, security regulations may apply

## Slide 31: Building Regulations
14. Part S – Infrastructure for EV Charging
Key relevance:
Limited relevance, but gas engineers in new-build projects must be aware of coordination with EV charging infrastructure when installing external gas pipework

## Slide 32: Building Regulations
As a gas engineer, you're not just fitting appliances – you're ensuring the work complies with Building Regulations to protect people, property, and the environment. Part J is your core guide, but others like Parts F, L and P are just as important in your day-to-day decisions.

## Slide 33: Hierarchy of legal documents
In UK gas engineering – and the wider construction and safety industries – professionals are expected to understand the hierarchy of legal and guidance documents. This hierarchy explains which documents carry the most legal authority, and how laws, regulations, codes of practice, standards, and guidance interact.

## Slide 34: Hierarchy of legal documents
1. Acts of Parliament (Primary Legislation)
Example:
Health and Safety at Work etc. Act 1974 (HASAWA)
Role:
Sets the legal framework for health, safety and welfare in all workplaces
Legally binding – must be complied with
Breach may result in prosecution, fines, or imprisonment

## Slide 35: Hierarchy of legal documents
2. Statutory Instruments (Secondary Legislation / Regulations)
Example:
Gas Safety (Installation and Use) Regulations 1998 (GSIUR)
Building Regulations 2010
Role:
Provide detailed rules under the Act
Define specific duties for employers, engineers, and landlords
Legally enforceable

## Slide 36: Hierarchy of legal documents
3. Approved Codes of Practice (ACoPs)
Example:
L56: Safety in the Installation and Use of Gas Systems and Appliances (for GSIUR)
Role:
Published by the Health and Safety Executive (HSE)
Not law, but have a special legal status:
  If you follow the ACoP, you’re likely to comply with the law
  If you don’t, you must prove that your method was equally safe

## Slide 37: Hierarchy of legal documents
4. British Standards (BS) and Industry Standards
Examples:
BS 6891 (low-pressure gas pipework)
IGEM/UP/1A (tightness testing)
Role:
Provide technical details and best practices
Not legally binding, unless referenced in law or contracts
Widely used in court to determine reasonable practice

## Slide 38: Hierarchy of legal documents
5. Manufacturer’s Instructions
Example:
Installation manual for a Vaillant gas boiler Role:
Must be followed when installing or maintaining appliances
GSIUR states that gas work must comply with the manufacturer’s instructions
Legally binding by association with regulation

## Slide 39: Hierarchy of legal documents
6. Guidance Documents (e.g. HSE, Gas Safe, Technical Bulletins)
Examples:
HSE Gas Safety Guidance Notes
Gas Safe Technical Bulletins
Role:
Help interpret regulations and explain good practice
Not legally binding, but supports compliance and reduces risk

## Slide 40: Hierarchy of legal documents
Level | Type | Example | Legal weight
1️⃣ | Acts of Parliament | HASAWA 1974 | Primary legislation – absolute
2️⃣ | Regulations (Statutory Instruments) | GSIUR 1998 | Secondary legislation – enforceable
3️⃣ | Approved Codes of Practice (ACoPs) | L56 | Strong legal status – presumed compliance
4️⃣ | Standards (BS / IGEM) | BS 6891 / IGEM/UP/1A | Best practice – court admissible
5️⃣ | Manufacturer’s Instructions | Boiler manual | Mandatory via GSIUR
6️⃣ | Guidance Notes / Bulletins | Gas Safe TBs, HSE | Advisory – helps ensure compliance

## Slide 41: Summary
You should now be able to:
Identify relevant British Standards and IGEM documents.
Explain the role of standards in ensuring consistent quality.
Apply selected standards to example installation tasks.

## Slide 42
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.