## Slide 1
Occupational Specialism: Gas Engineering
K1.20 Implications of legislation, standards and manufacturer’s instructions alongside additional guidance to employers and those working with gas systems
PowerPoint 1.20d: Employer responsibilities and legal consequences

## Slide 2: Starter
What could happen if a gas engineer installed a boiler and ignored the manufacturer’s flue position instructions?
Think about:
Safety risks
Legal consequences
Who could be affected
How might this be discovered

## Slide 3: Objectives
By the end of this session, you should be able to:
Describe the legal responsibilities of employers and Gas Engineers.
Explain the implications of failing to follow guidance.
Discuss real-world examples of enforcement actions.

## Slide 4: Employer duties
In the gas industry, employers of gas engineers have a range of legal, moral, and professional duties to ensure that work is carried out safely, competently, and in line with all relevant laws and standards. These responsibilities come under several key pieces of legislation, especially the Health and Safety at Work etc. Act 1974 and the Gas Safety (Installation and Use) Regulations 1998 (GSIUR).

## Slide 5: Employer duties
Legal Duty of Care (HASAWA 1974 – Section 2)
Employers must:
Ensure, so far as is reasonably practicable, the health, safety, and welfare of their employees.
Provide:
  A safe working environment
  Safe systems of work
  Properly maintained equipment
  Clear information and supervision.

## Slide 6: Employer duties
Ensure engineers are competent and registered (GSIUR Reg 3)
Gas engineers must be:
  Competent to do the work
  Gas Safe registered
  Only allowed to carry out work for which they are certified and qualified.
Employers must not allow unregistered individuals to carry out gas work under any circumstances.

## Slide 7: Employer duties
Provide suitable tools and equipment
Tools must be:
  Appropriate for the task (e.g. flue gas analyser, pressure gauge)
  In good working condition
  Regularly inspected, calibrated, and maintained.

## Slide 8: Employer duties
Keep records and support compliance
Employers must ensure:
  Gas Safety Records are properly completed
  Installation and commissioning records are kept
  Records are stored securely and retained for the minimum legal timeframes.

## Slide 9: Employer duties
Risk Assessments and Method Statements (RAMS)
Employers must:
  Assess risks to staff and customers
  Produce safe working procedures
  Provide PPE and ensure it is worn.

## Slide 10: Employer duties
An employer isn’t just a boss – they’re legally responsible for your safety, training, equipment, and compliance.
If they fail in these duties, they could face enforcement action, just like the engineer.

## Slide 11: Employee duties
In the gas engineering sector, employees – including gas engineers, apprentices, and trainees – have clear legal responsibilities under UK law.
These duties ensure they work safely, competently, and professionally, helping to protect themselves, colleagues, customers, and the public.

## Slide 12: Employee duties
Take reasonable care for health and safety (HASAWA 1974 – Section 7)
Employees must:
Take reasonable care of their own health and safety
Avoid doing anything that could endanger others (e.g. unsafe gas work, poor isolation, tampering with safety devices)
Follow safe working practices and use tools/PPE properly.

## Slide 13: Employee duties
Follow instructions and training provided by the employer
Gas engineers must:
Follow training, risk assessments, and safe systems of work
Only carry out tasks they are trained and authorised to do
Apply the manufacturer’s instructions, industry standards, and employer procedures.

## Slide 14: Employee duties
Work within competence and registration scope (GSIUR Reg. 3)
Only carry out gas work that you are competent and certified to do.
If unsure, stop work and report it to a supervisor or senior engineer.
Never allow unqualified individuals to assist with regulated gas work.

## Slide 15: Employee duties
Use PPE and equipment correctly
Employees must:
Wear Personal Protective Equipment (PPE) as required
Use tools properly and report damaged or unsafe equipment
Handle test instruments (e.g. flue gas analyser, pressure gauge) with care.

## Slide 16: Employee duties
Report hazards, incidents, or unsafe situations
If an unsafe situation arises, you must:
  Stop the work
  Report to your manager or supervisor
  Follow the Gas Industry Unsafe Situations Procedure (GIUSP)
Report gas escapes, near misses, or safety concerns immediately.

## Slide 17: Employee duties
Maintain professional conduct and record-keeping
Fill in all required documents accurately (e.g. Gas Safety Records, commissioning sheets).
Respect customer property and maintain a professional attitude.
Never falsify documentation – this is a criminal offence.

## Slide 18: Employee duties
As a gas engineer, your duties don’t stop at the toolkit. You must work safely, stay within your training, report issues, and follow every rule — because people’s lives depend on it.

## Slide 19: Consequences of non-compliance
Non-compliance in gas engineering — whether it’s breaking the law, ignoring standards, or failing to follow the manufacturer’s instructions — can lead to serious legal, professional, financial, and safety consequences.
It’s crucial to understand that every decision made on-site has real-world consequences.

## Slide 20: Consequences of non-compliance
Offence | Consequences
Breach of GSIUR 1998 | Fines, prohibition notices, criminal prosecution
Working while not Gas Safe registered | £5,000+ fine per offence, imprisonment up to 6 months
Unsafe gas work under HASAWA 1974 | Unlimited fines or imprisonment (up to 2 years)
Failure to report dangerous situations (RIDDOR) | Enforcement action by HSE
Legal consequences example: An engineer installs a boiler without a CO alarm and causes carbon monoxide exposure — this can lead to prosecution under both GSIUR and HASAWA.

## Slide 21: Consequences of non-compliance
Professional consequences
Gas Safe Register sanctions:
  Suspension or removal from the register
  Public listing as a non-compliant engineer
  Formal investigations or audits
Loss of employment:
  Dismissal for gross misconduct
  Difficulty finding future work in the industry

## Slide 22: Consequences of non-compliance
Professional consequences
Loss of competence certification:
  Expired or invalid ACS qualifications
  Inability to legally carry out gas work

## Slide 23: Consequences of non-compliance
Financial consequences:
Cost of legal defence and court proceedings
Paying for repairs, fines, and compensation
Increased insurance premiums
Loss of income if suspended or struck off

## Slide 24: Consequences of non-compliance:
Safety consequences
Risk of:
  Gas leaks
  Explosions
  Carbon monoxide poisoning
  Fire or structural damage
Harm to:
  Customers, occupants, co-workers
  The general public (especially in commercial or public buildings)

## Slide 25: Consequences of non-compliance
Reputational consequences
Damage to personal and company reputation
Loss of public trust and future business
Negative media coverage in serious incidents
Example: Gas Safe regularly names and shames rogue traders in local newspapers and online.

## Slide 26: Consequences of non-compliance
Non-compliance isn’t just “doing it wrong” — it can destroy careers, harm lives, and break the law.
Every gas engineer is responsible for doing the job safely, according to the law, and with full accountability.
Answer this:
“What could happen to a customer, the engineer, and the employer if the flue of a gas boiler was installed incorrectly?”

## Slide 27: Case study 1
Case Study 1: Unregistered Gas Engineer imprisoned
Location: West Yorkshire Outcome: 12-month prison sentence, 18-month driving ban Details:
The individual falsely claimed to be Gas Safe registered.
Installed gas appliances unsafely in multiple homes.
A flue was installed incorrectly, posing a CO poisoning risk.
Prosecuted by HSE under the Gas Safety (Installation and Use) Regulations 1998 and Consumer Protection laws.
Key Learning: Never carry out gas work without a valid Gas Safe registration. Lying about being registered is a criminal offence.

## Slide 28: Case study 2
Case Study 2: Heating company fined for dangerous boiler work
Company: 1st Call Gas Services Ltd Location: Sheffield Fine: £40,000 + costs Details:
Engineers installed a boiler with defective flueing, risking CO exposure.
Failed to follow the manufacturer’s instructions and Part J of Building Regulations.
No commissioning or safety checks were recorded.
HSE found multiple breaches of GSIUR and HASAWA.
Key Learning: Ignoring flue positioning guidance and failing to commission correctly can result in serious risk and heavy fines.

## Slide 29: Case study 3
Case Study 3: Landlord and Gas Engineer Fined for unsafe gas fire
Location: Lincolnshire Fines: Landlord: £6,000, Gas Engineer: £4,000 Details:
A tenant reported headaches caused by carbon monoxide from an unsafe gas fire.
Investigation revealed the fire hadn’t been serviced or tested.
The engineer failed to apply visual inspection and combustion checks as per BS 7967 and MI.
The landlord had not arranged the annual gas safety check.
Key Learning: Both engineers and landlords share responsibility. Failing to inspect and test appliances can lead to dangerous outcomes.

## Slide 30: Case study 4
Case Study 4: CO fatality leads to corporate manslaughter charges
Location: Scotland Outcome: Large-scale investigation, company fined £800,000 Details:
Incorrect flue installation led to carbon monoxide leaking into a property.
A tenant died as a result.
Investigation found systematic failures in training, supervision, and quality control.
Corporate manslaughter charges were filed under Health and Safety legislation.
Key Learning: Failing to supervise and inspect gas work can result in death – and companies can be held criminally responsible.

## Slide 31: Risk mitigation
Risk mitigation in gas engineering is about identifying hazards and taking steps to reduce or eliminate the risk of harm to people, property, and the environment.
Understanding risk mitigation is essential to working safely, professionally, and within the law.

## Slide 32: Risk mitigation
Follow legislation and approved procedures.
Work within competence and registration.
Always follow manufacturer’s instructions.
Conduct safety checks at every stage.
Maintain accurate documentation.
Use the right tools and calibrate them.
Apply the GIUSP when needed.
Keep knowledge and training up to date.

## Slide 33: Risk mitigation
Risk mitigation isn’t just about avoiding accidents — it’s about proving that you’ve done everything right.
By following the law, using correct procedures, and recording your work, you protect yourself, your customer, and your career.

## Slide 34: Summary
You should now be able to:
Describe the legal responsibilities of employers and Gas Engineers.
Explain the implications of failing to follow guidance.
Discuss real-world examples of enforcement actions.

## Slide 35
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.