## Slide 1
Occupational Specialism: Gas Engineering
K1.17 Types of pipework
PowerPoint 1.17: Pipework materials, fittings and fixings for gas systems

## Slide 2: Starter
Ash is working on a new commercial installation.
The site is considering switching from copper to corrugated stainless steel pipework.
What factors should they consider?

## Slide 3: Objectives
By the end of this session, you should be able to:
Identify four types of pipework used in gas installations.
Explain which fittings and fixings are used with each type.
Compare pipe materials in terms of suitability, installation, and performance.
Apply safety and regulatory considerations when selecting pipework.

## Slide 4: Copper pipework
Use: Most common in domestic gas systems (≤ 35 mm)
Features: Durable, clean inside surface, good for soldering or compression.
Fittings:
  Compression
  Capillary (lead-free solder only)
  Press-fit
Fixings:
  Copper pipe clips, saddle clips, brass brackets
Notes: Must be sleeved through walls and protected from corrosion.

## Slide 5: Steel pipework
Use: Commercial, industrial, or high-pressure applications
Features: Strong, flame-resistant, heavy-duty
Fittings:
  Threaded (BS EN 10241)
  Welded or flanged (for fixed systems)
Fixings:
  Munson rings, steel brackets
Notes: Must be painted or wrapped to prevent corrosion; requires threading machines or welding skills.

## Slide 6: Pliable corrugated stainless steel (CSST)
Use: Flexible alternative for hard-to-reach areas or refurbishment
Features: Pre-formed bends, fewer joints = fewer leak points
Fittings:
  Manufacturer-specific compression collars or push-fits
Fixings:
  Plastic stand-offs or rubber-lined brackets (to prevent abrasion)
Notes: Must be installed per MI and not kinked; needs electrical continuity bonding.

## Slide 7: Polyethylene (PE) pipework
Use: Underground gas services (external only)
Features: Corrosion-proof, flexible, used with electrofusion or mechanical fittings
Fittings:
  Electrofusion joints
  Mechanical couplers
Fixings:
  Usually buried in ducting with marking tape
Regulation: Not used inside buildings; must comply with IGEM/TD/3.

## Slide 8: Comparison table
Pipe type | Typical use | Fittings | Fixings | Notes
Copper | Domestic | Compression, solder | Plastic/copper clips | Lead-free solder only
Steel | Commercial | Threaded, flanged | Munson rings | Requires protection
CSST | Flexible internal | Proprietary | Stand-off brackets | No kinking
PE | Underground | Electrofusion | Ducted/buried | Not for internal use

## Slide 9: Regulatory and safety notes
Sleeving: Required through walls and voids
Bonding: Required across joints and plastic sections (e.g. PE to copper)
Fire resistance: Steel is preferred in high-risk commercial or fire-rated zones
Manufacturer’s Instructions (MI): Must always be followed

## Slide 10: Summary
You should now be able to:
Identify four types of pipework used in gas installations.
Explain which fittings and fixings are used with each type.
Compare pipe materials in terms of suitability, installation, and performance.
Apply safety and regulatory considerations when selecting pipework.

## Slide 11
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.