## Slide 1
Occupational Specialism: Gas Engineering
K1.18 Flow rates and their relationship to pipework and system design
PowerPoint 1.18: Gas flow, pressure drop and system design

## Slide 2: Starter
Sam notices that the gas flame at the cooker looks weak when the boiler is on.
What could be happening?
Notes: Introduce the concept of flow rate, pressure loss, and pipe sizing.

## Slide 3: Objectives
By the end of this session, you should be able to:
Define gas flow rate and how it is measured.
Explain how pipework design affects pressure and flow.
Interpret pressure loss data and apply pipe sizing principles.
Evaluate how poor flow affects combustion performance.

## Slide 4: What is flow rate?
Flow rate (Q) is the volume of gas delivered over time.
Measured in m³/h (cubic metres per hour)
Affected by:
  Appliance demand
  Pipe length and diameter
  Number and type of fittings
  Material type and roughness

## Slide 5: The relationship between pressure and flow
As flow increases, pressure drop increases.
Pressure is lost due to:
  Friction along internal walls
  Turbulence at fittings or bends
  Changes in direction or pipe size
Permissible drop for NG:
1 mbar between the meter outlet and the appliance

## Slide 6: Pipework effects on flow
Factor | Impact
Longer pipe runs | More pressure drop
Small diameter pipe | Higher resistance to flow
More fittings or elbows | Each causes turbulence and loss
Rough internal surfaces | Increases drag (steel > copper)

## Slide 7: Worked example – pressure drop
A 24 kW appliance at 37.5 MJ/m³ requires a flow rate of: Q = 24 ÷ 37.5 = 0.64 m³/h
You design the pipe run with:
18 m equivalent length
22 mm copper pipe
3 elbows
Using the gas flow table, the pipe supports: 0.75 m³/h at 18 m length → OK
But if you drop to 15 mm pipe, pressure loss may exceed 1 mbar → 🔴 Not compliant

## Slide 8: Design tips
Always start pipe sizing from the most remote appliance
Use equivalent lengths for fittings:
  90° elbow = ~0.5 m
  Tee = ~1 m
Follow pipe sizing charts in BS 6891 or MI
For multiple appliances, consider:
  Diversity factors
  Combined demand
  System balancing

## Slide 9: Summary
You should now be able to:
Define gas flow rate and how it is measured.
Explain how pipework design affects pressure and flow.
Interpret pressure loss data and apply pipe sizing principles.
Evaluate how poor flow affects combustion performance.

## Slide 10
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.