## Slide 1
Occupational Specialism: Gas Engineering
K1.23 Inspection techniques and how they are applied in
Commissioning systems
PowerPoint 1.23: Visual inspection techniques for commissioning

## Slide 2: Starter
You’ve just walked into a property to commission a new wall-hung combi boiler.
Without using any tools, list what you would visually inspect before switching the gas on.

## Slide 3: Objectives
By the end of this session, you should be able to:
Identify key visual inspection points in commissioning.
Describe how to apply the manufacturer’s instructions to appliance inspection.
Evaluate system condition and appliance integrity.
Record inspection results to meet industry expectations.

## Slide 4: What is visual inspection?
Visual inspection is a systematic, non-invasive examination conducted before any operational testing or commissioning procedures. It serves as the first critical safety check in the gas engineering process.
A thorough visual inspection enables engineers to identify potential hazards, non-compliance issues, or installation faults without introducing additional risks that might occur during live testing. This preventative approach is fundamental to gas safety protocols in the UK.

## Slide 5: What is visual inspection?
Key principles
Always conducted before any operational or invasive testing.
Requires no specialised equipment beyond basic tools.
Relies on engineer knowledge of standards and manufacturer requirements.
Documentation begins at this stage with photographic evidence where appropriate.

## Slide 6: What is visual inspection?
Appliance assessment
Overall condition, secure fixings, complete casing, signs of tampering or unauthorised modification.
System configuration
Correct layout, appropriate materials, proper support/fixing methods, clearances maintained.

## Slide 7: What is visual inspection?
Flue and ventilation
Proper installation, appropriate sizing, absence of obstructions, compliance with placement requirements.
Physical condition
Signs of damage, corrosion, poor workmanship, inappropriate repairs or alterations.

## Slide 8: What is visual inspection?
Documentation
Presence and accessibility of required labels, data plates, user instructions and warning notices.
Visual inspection findings determine whether it's safe to proceed with live testing procedures such as tightness testing, purging, or combustion analysis.

## Slide 9: Visual inspection checklist: what to inspect
Area | Inspection points | Common issues
Appliance Casing | Secure fixings, intact seals, complete casing, no damage. | Missing screws, damaged panels, incorrect assembly.
Burner & Ignition | Electrodes condition, burner surface, signs of sooting or discolouration. | Cracked electrodes, damaged burner mesh, carbon deposits.
Flue System | Secure connections, correct routing, proper seals, terminal location. | Unsealed joints, incorrect slope, improper terminal clearances.
Ventilation | Size verification, permanent nature, clear airflow path. | Blocked grilles, undersized openings, sealed vents.
Labels & Data Plates | Rating plate legibility, warning notices, user instructions. | Missing data plates, illegible information, absent warning labels.
Controls & Valves | Accessibility, visual condition, correct orientation. | Inaccessible isolation valves, damaged controls, missing caps.
Pipework & Meter | Material compliance, appropriate support, correct bonding. | Improper sleeving, inadequate clipping, missing bonding.

## Slide 10: Visual inspection checklist: what to inspect
When conducting a visual inspection, work systematically through each area using a consistent approach.
Begin with external components and gradually move to internal elements when necessary.
Document your observations for each inspection point before proceeding to operational tests.

## Slide 11: Manufacturer's Instructions (MI): The primary standard
Role of Manufacturer's Instructions
Manufacturer's Instructions (MI) serve as the definitive reference point for visual inspection standards. They specify the exact requirements for installation, clearances, component accessibility, and servicing procedures unique to each appliance model.

## Slide 12: Manufacturer's Instructions (MI): The primary standard
The MI takes precedence over general industry standards when there are specific requirements for a particular appliance. Failing to adhere to MI guidance may:
Invalidate manufacturer warranties.
Create safety hazards not covered by general standards.
Result in non-compliance with Gas Safety Regulations.
Lead to inefficient operation or premature component failure.

## Slide 13: Manufacturer's Instructions (MI): The primary standard
Critical MI content
Specific clearance requirements for service access.
Required sealing methods and materials.
Mounting specifications and fixing requirements.
Component adjustment limitations.
Flue terminal positioning requirements.
Model-specific ventilation needs.
Always obtain and refer to the current version of the MI.
Manufacturers frequently update instructions to address emerging issues or incorporate design changes.

## Slide 14: Documenting visual inspection evidence
Digital documentation
Modern commissioning practices increasingly utilise digital platforms for recording inspection findings. These systems offer benefits including:
Standardised data collection formats
Secure cloud storage of inspection records.
Integration with company management systems.
Ability to attach photographic evidence directly.
Automated compliance checking against standards.

## Slide 15: Documenting visual inspection evidence
Photographic evidence
Visual documentation provides indisputable evidence of inspection findings. Best practices include:
Photographing data plates for model verification.
Capturing identified faults from multiple angles.
Including reference points for scale/location context.
Maintaining chronological sequence of images.
Ensuring proper lighting and focus for clarity.

## Slide 16: Documenting visual inspection evidence
A comprehensive inspection record should include:
Appliance details (make, model, serial number).
Installation location information.
Date and time of inspection.
Engineer identification and Gas Safe registration.
Specific MI version referenced during inspection.
Detailed notes on each inspection point.
Any variances from standards or MI requirements.
Recommendations for remedial actions where applicable.

## Slide 17: Common fault examples and required actions
1. Missing appliance case screws
Risk assessment: Medium risk – may compromise case seal Integrity and allow products of combustion to escape.
Required action: Refit appropriate screws before commencing operation. If original screws are unavailable, source correct replacements per MI specifications.
Documentation: Note replacement in commissioning record, verify complete case integrity after repair.

## Slide 18: Common fault examples and required actions
2. Flue seal distortion
Risk assessment: High risk – potential for products of combustion to escape into the living space.
Required action: Do not operate the appliance. Isolate the gas supply if already connected. Replace damaged seal components following MI guidelines.
Documentation: Photograph damage, record detailed description of issue and remedial actions taken.

## Slide 19: Common fault examples and required actions
3. Burner sooting present
Risk assessment: Medium to high risk – indicates incomplete combustion and potential CO production.
Required action: Record condition, clean according to MI procedure, conduct full combustion analysis after cleaning to verify correction.
Documentation: Note the extent of sooting, possible causes, cleaning procedure followed, and post-cleaning test results.

## Slide 20: Common fault examples and required actions
4. Ventilation undersized
Risk assessment: High risk – insufficient combustion air may lead to incomplete combustion and CO production.
Required action: Calculate correct ventilation requirements per BS 5440-2. Advise the responsible person of the deficiency and required corrections.
Documentation: Record specific ventilation measurements, calculations showing deficiency, and communication with the responsible person.

## Slide 21: Common fault examples and required actions
For all identified faults, engineers must make clear decisions about whether it's safe to proceed with commissioning or if the issue must be resolved first.
This judgement should be based on a thorough risk assessment considering potential consequences and regulatory requirements.

## Slide 22: Key visual inspection principles
Systematic approach
Follow a standardised inspection checklist to ensure comprehensive coverage of all critical inspection points without omissions.
MI application
Always refer to the current manufacturer's instructions as the primary standard against which to evaluate installation compliance.

## Slide 23: Key visual inspection principles
Evidence collection
Document findings clearly with detailed notes and photographic evidence to create a verifiable record of inspection.
Safety prioritisation
Identify and rectify faults that could compromise safety before proceeding with operational testing.

## Slide 24: Key visual inspection principles
Next steps in your development
To further develop your visual inspection skills:
Practice using manufacturer-specific checklists for different appliance types.
Familiarise yourself with common fault patterns and their visual indicators.
Develop a personal system for thorough documentation of findings.
Review case studies of incidents where visual inspection could have prevented safety issues.

## Slide 25: Summary
You should now be able to:
Identify key visual inspection points in commissioning.
Describe how to apply the manufacturer’s instructions to appliance inspection.
Evaluate system condition and appliance integrity.
Record inspection results to meet industry expectations.

## Slide 26
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.