## Slide 1
Occupational Specialism: Gas Engineering
K1.25 – Testing of installation
PowerPoint 1.25b: Flue flow and spillage

## Slide 2: Starter
Georgia is servicing an open-flued space heater in a lounge with a ceiling fan. She turns on the extractor fan and starts a spillage test. After a few minutes, she notices that smoke is entering the room.
What might be happening here?
Why could the fan cause a problem?
How do spillage tests help detect this?

## Slide 3: Objectives
By the end of this session, you should be able to:
Describe the purpose of flue flow and spillage tests on open-flued appliances
Identify the correct tools and conditions required to carry out tests
Demonstrate how to conduct flue flow and spillage tests in accordance with industry procedures
Evaluate test results and determine appropriate actions where a fault is found

## Slide 4: Open flue chimney inspection
Verifying the safe functioning of open flue systems is essential.
The main goal is to guarantee that all combustion products (POC) are properly vented outside through a flue terminal or chimney pot.
To confirm the correct operation of these flue systems, two key tests are necessary:
Flue flow test
Spillage test. ​

## Slide 5: Open flue – flue flow testing
A flue flow test is conducted to assess whether a flue or chimney can safely expel the products of combustion (POC) from an appliance.
This test verifies that the chimney system is free from blockages, does not leak into nearby rooms, terminates properly, and has the necessary draft or ‘pull’.
To perform the test, a smoke pellet capable of generating at least 5m³ of smoke within 30 seconds is used.

## Slide 6: Open flue – flue flow testing
Close all doors and windows in the room in which the appliance is located.
Examine the chimney path to check for any visible damage.
For class one brick chimneys, review the internal catchment zones to confirm the flue is free of blockages.
Check the flue to verify that no damper plates are installed, or if present, that they are fully wedged open.

## Slide 7: Open flue – flue flow testing
Insert a lit smoke pellet into the catchment area or draught diverter of the appliance, ensuring the appliance is switched off.
Inspect the full length of the chimney, including any upstairs bedrooms, for signs of smoke.
Step outside to confirm that smoke is escaping from only one chimney pot.

## Slide 8: Open flue – flue flow test procedure
If smoke appears to be exiting from the appropriate terminal and there is no smoke present in the test room, or in any other room or area through which the flue or chimney passes – particularly the loft space, ​then the test can be considered successful.

## Slide 9: Open flue – spillage testing
A spillage test evaluates how effectively a flue operates and checks whether combustion products are being safely vented from an open flued appliance.
​The manufacturer’s guidelines provide engineers with directions on the proper placement of a smoke match or smoke-emitting device to ensure an accurate and reliable test.

## Slide 10: Open flue – spillage testing
After reviewing the manufacturer’s guidelines, make sure all doors and windows in the room are securely closed. Any fans present should be switched on, and likewise, any open-flued appliances in the vicinity should also be activated during the test.
Once the appliance has been operating for 5–10 minutes, proceed with the test.
Place a lit match, secured in an appropriate holder, beneath the lower edge of the draught diverter. The flue should draw in all the smoke, with only the occasional small wisp escaping, to verify that it is functioning properly.

## Slide 11: Open flue – spillage testing
If there are fans in an adjacent room, the spillage test should be conducted again with the door to that room open. This approach aims to simulate the worst-case scenario to guarantee the safe discharge of POC at all times.
Occasionally, a spillage test may fail, indicated by smoke from a match not being drawn in, which means the POC is leaking into the living space.

## Slide 12: Open flue – spillage testing
A smoke match holder is typically crafted from a short section of 8–10mm copper tubing to shield the engineer’s hand from excessive heat during testing.
If the spillage test does not pass, allow the appliance to run for a longer period before performing the test again.
If the test continues to fail, turn off any nearby fans to determine whether they are contributing to the issue.

## Slide 13: Open flue – spillage testing
Another approach is to open a window in the same room to check if it draws in smoke.
If it does, this indicates inadequate ventilation, and the size of the open window will determine the additional ventilation needed. According to BS 5440 part 1, a 50cm² vent may help address the spillage issue.
A failed spillage test might also suggest a partially or completely blocked flue or appliance spigot.
Additionally, an improperly placed terminal or the use of an incorrect terminal can contribute to spillage problems.

## Slide 14: Room sealed chimneys
Fanned draught room sealed (positive pressure)
These appliances may pose a risk due to the internal fan pressurising the boiler casing. If there is a leak in the boiler case seal, products of combustion (POC) can escape into the room.
Examine the outer terminal for any damage and ensure it is appropriately located.
Verify the integrity of the boiler case seal by running the appliance and using a smoke taper or the back of your hand to detect any positive draught escaping from a damaged part of the case seal.

## Slide 15: Summary
You should now be able to:
Describe the purpose of flue flow and spillage tests on open-flued appliances.
Identify the correct tools and conditions required to carry out tests.
Demonstrate how to conduct flue flow and spillage tests in accordance with industry procedures.
Evaluate test results and determine appropriate actions where a fault is found.

## Slide 16
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.