## Slide 1
Occupational Specialism: Gas Engineering
K1.27 Cleaning of components without compromising the
system and associated tools, equipment and materials
PowerPoint 1.27b: Appliance-specific cleaning tasks and post-clean checks

## Slide 2: Starter
Tracy services a gas boiler. She wipes the burner and flame sensor but forgets to check the electrode gap. The boiler runs briefly, then locks out.
Discussion questions:
What component was affected?
Why did the boiler lock out?
What post-cleaning checks should Tracy have completed?

## Slide 3: Objectives
By the end of this session, you should be able to:
Apply safe and effective cleaning techniques to common gas appliance components.
Demonstrate post-cleaning checks such as combustion analysis and component reassembly.
Record service actions using standard logs and inspection templates.
Evaluate whether an appliance is safe to return to service after cleaning.

## Slide 4: Common appliance components to clean
Appliance type | Component | Cleaning task | Special considerations
Combi boiler | Burner, electrode, condensate trap | Brush burner, wipe electrode, flush trap. | Check for scale buildup in heat exchanger; ensure trap is reprimed.
Gas fire | Pilot assembly, burner ports | Remove debris, clean ODS sensor. | Verify flame pattern after cleaning; check thermocouple response.
Water heater | Injector, burner tray | Check for scale or soot, clean ports. | Look for signs of water damage or corrosion on connections.
Cooker hob | Burner rings, caps | Clean for food debris, inspect ignition spark. | Ensure correct reassembly of burner parts; check electrode alignment.

## Slide 5: Common appliance components to clean
Always refer to manufacturer’s instructions (MI) for specific cleaning methods and recommended cleaning intervals.
Using incorrect cleaning agents or techniques can damage components and create safety hazards.

## Slide 6: Electrode and ignition servicing
Critical cleaning procedures
Remove electrode carefully using appropriate tools
Clean with a fine abrasive pad or a dry lint-free cloth
Never use wet cleaning methods on electrical components
Avoid touching ceramic insulators with bare hands
Check for cracks, carbon tracking or damage

## Slide 7: Electrode and ignition servicing
Essential checks
Gap spacing (use calibrated feeler gauge)
Alignment with flame path (per manufacturer specifications)
Terminal integrity and secure connections
Ceramic insulator condition (no cracks or carbon paths)

## Slide 8: Consequences of faulty electrodes
A properly maintained electrode is crucial for both ignition and flame detection. Failures can lead to:
Failed ignition sequence
Intermittent lockouts
Misfiring during operation
Increased carbon monoxide risk
Wasted gas during ignition attempts
Premature component failure
Always re-fit securely using manufacturer-specified torque settings or positioning guidance.

## Slide 9: Condensate trap and condensing boiler areas
Visual inspection
Remove the trap and visually check for sludge, microbial growth, and blockages.
Look for discolouration indicating potential corrosion or acidic buildup. Inspect all seals and O-rings for integrity.

## Slide 10: Condensate trap and condensing boiler areas
Cleaning process
Flush thoroughly with clean water until discharge runs clear.
Never use chemical cleaners unless specifically approved by the manufacturer.
Remove stubborn deposits with a soft brush designed for condensate systems.

## Slide 11: Condensate trap and condensing boiler areas
Critical safety step
Reprime the trap (fill with clean water) to prevent flue gas escape.
This water seal is essential for preventing carbon monoxide from entering the dwelling.
Never leave a trap dry after servicing.

## Slide 12: Condensate trap and condensing boiler areas
System verification
Check pipe and joint seals for leakage or corrosion. Verify that the trap is seated correctly and that all connections are secure. Confirm that condensate can flow freely through the entire discharge system.
Condensate is acidic (pH 3.5-5) and can cause premature component failure if allowed to accumulate. In winter months, external condensate pipes may freeze and block, causing the boiler to shut down. Advise customers on proper preventative measures in cold weather.

## Slide 13: Burner and heat exchanger zones
Cleaning techniques
When servicing burner assemblies and heat exchangers:
Use a soft brush or vacuum with appropriate attachments to clear soot/carbon from the burner
Clean fins on the heat exchanger (if allowed by manufacturer instructions)

## Slide 14: Burner and heat exchanger zones
Cleaning techniques
Remove dust from the air intake and fan assemblies
Inspect the gas manifold and injectors for blockages
Check seals between the burner and the combustion chamber

## Slide 15: Burner and heat exchanger zones
Important cautions
Never use water on electrical fan motors or venturi
Avoid abrasive cleaning on delicate components
Do not disturb factory-sealed components
Follow the manufacturer’s guidelines for cleaning access

## Slide 16: Burner and heat exchanger zones
Warning signs requiring further investigation
During cleaning, be alert for these indicators of potential problems:
Burnt or discoloured metal on the burner or exchanger
Deformed burner ports indicate overheating
Uneven flame pattern (requires combustion analysis)

## Slide 17: Burner and heat exchanger zones
Warning signs requiring further investigation
Excessive sooting indicates incomplete combustion
Scale buildup restricts water flow
Corrosion at joints or welds
Damaged or deteriorating gaskets and seals

## Slide 18: Post cleaning checks
Thorough verification is essential after component cleaning to ensure safe and efficient operation:
1. Visual inspection
Purpose: Confirm all parts are correctly reassembled and properly sealed.
Method: Systematic visual check of all components that were removed or disturbed during cleaning.
Look for: Missing screws, damaged gaskets, loose connections, or improper component positioning.

## Slide 19: Post cleaning checks
2. Electrode gap check
Purpose: Ensures proper ignition and flame sensing capabilities
Method: Use an appropriate feeler gauge for precise measurement according to the manufacturer’s specifications
Typical values: 3.5-4.5mm for spark electrodes, but always verify against specific appliance requirements

## Slide 20: Post cleaning checks
3. Combustion analysis
Purpose: Confirms safe and efficient combustion parameters
Method: Use a calibrated flue gas analyser (FGA) to measure CO, CO₂, and combustion ratio
Standards: CO/CO₂ ratio must be below 0.004 (0.4%) for safe operation

## Slide 21: Post cleaning checks
4. Tightness testing
Purpose: Verifies gas integrity if pipework was disturbed during cleaning
Method: Pressure drop test using manometer or electronic testing device
When required: Any time gas-carrying components are disconnected

## Slide 22: Post cleaning checks
5. Operational test
Purpose: Demonstrates complete system functionality
Method: Full cycle test observing ignition sequence, fan operation, pump function and burner performance
Duration: Allow appliance to complete at least one full heating cycle
All checks must be documented with actual readings and observations, not just pass/fail indicators.

## Slide 23: Recording and documentation
Essential documentation
Thorough record-keeping is a legal requirement and professional responsibility.

## Slide 24: Recording and documentation
Required information
Specific components cleaned and methods used
Parts replaced or requiring future attention
Test results with actual values (not just pass/fail)
Observations about appliance condition
Recommendations for future maintenance
Evidence of customer notification for any issues

## Slide 25: Recording and documentation
Documentation formats
Manufacturer's service logbook
Gas Safety Record (CP12 for landlord properties)
Company-specific service reports
Electronic records with digital signatures

## Slide 26: Recording and documentation
Best practice tips
Enhance your documentation with these professional approaches:
Attach before/after photographs of significant issues or repairs
Use consistent terminology aligned with manufacturer documentation
Record serial numbers and model information for all serviced components

## Slide 27: Recording and documentation
Best practice tips
Note any verbal instructions given to occupants
Include combustion analysis printouts where available
Document any parts ordered or scheduled return visits
Maintain records for a minimum of 6 years (2 years beyond statutory requirement)
Remember: In legal proceedings, "if it isn't documented, it didn't happen." Thorough records protect both the engineer and customer.

## Slide 28: Knowledge check: component cleaning quiz
Condensate trap maintenance
Question: What must you do after cleaning a condensate trap?
Options:
Leave it empty to dry completely
Refill (prime) it with clean water
Add anti-freeze solution
Apply silicone sealant

## Slide 29: Knowledge check: component cleaning quiz
Electrode gap verification
Question: Which tool would you use to confirm the electrode gap?
Options:
Multimeter
Pressure gauge
Feeler gauge
Thermal imaging camera

## Slide 30: Knowledge check: component cleaning quiz
Combustion indicators
Question: What result would a poor flame picture indicate?
Options:
Excessive gas pressure
Incomplete combustion
Oversized injector
Normal variation

## Slide 31: Knowledge check: component cleaning quiz
Component cleaning safety
Question: Can you clean a sealed fan motor with water?
Options:
Yes, if properly dried afterwards
Yes, but only with distilled water
No, never use water on electrical components
Yes, if the manufacturer allows it

## Slide 32: Knowledge check: component cleaning quiz
Trap priming importance
Question: Why is re-priming the condensate trap essential?
Options:
Prevents flue gas escape
Increases efficiency
Reduces noise
Prevents scale buildup

## Slide 33: Knowledge check: component cleaning quiz
Condensate trap maintenance
Question: What must you do after cleaning a condensate trap?
Correct answer: Refill (prime) it with clean water
Explanation: The water creates a vital seal, preventing flue gases from escaping into the dwelling.

## Slide 34: Knowledge check: component cleaning quiz
Electrode gap verification
Question: Which tool would you use to confirm the electrode gap?
Correct answer: Feeler gauge
Explanation: A calibrated feeler gauge provides precise measurement of the gap to manufacturer specifications.

## Slide 35: Knowledge check: component cleaning quiz
Combustion indicators
Question: What result would a poor flame picture indicate?
Correct answer: Incomplete combustion
Explanation: An abnormal flame pattern often indicates incomplete combustion, which can lead to CO production.

## Slide 36: Knowledge check: component cleaning quiz
Component cleaning safety
Question: Can you clean a sealed fan motor with water?
Correct answer: No, never use water on electrical components
Explanation: Water can damage electrical components and create safety hazards even in "sealed" units.

## Slide 37: Knowledge check: component cleaning quiz
Trap priming importance
Question: Why is re-priming the condensate trap essential?
Correct answer: Prevents flue gas escape
Explanation: The water seal prevents potentially lethal carbon monoxide from entering the living space.

## Slide 38: Gas fire and decorative appliance cleaning
Pre-cleaning assessment
Before cleaning, check for signs of spillage, sooting, or discolouration.
Perform a spillage test before dismantling.
Ensure the appliance is cool and isolated from the gas supply.

## Slide 39: Gas fire and decorative appliance cleaning
Cleaning procedure
Remove decorative elements carefully (coals, pebbles, logs).
Clean pilot assembly, ODS sensor, and thermocouple using soft brush and vacuum.
Inspect and clean primary aeration openings and burner ports.

## Slide 40: Gas fire and decorative appliance cleaning
Post-cleaning verification
Perform a visual flame check for the correct colour and pattern.
Repeat spillage test under operating conditions.
Check pilot stability and flame supervision device operation.
Document flame picture observations.

## Slide 41: Gas fire and decorative appliance cleaning
Decorative fuel effects must be arranged precisely according to manufacturer instructions.
Even minor deviations from the specified pattern can disrupt flame paths, create localised hotspots, and potentially lead to incomplete combustion with dangerous carbon monoxide production.

## Slide 42: Commercial appliance considerations
Additional requirements
Commercial gas appliances present unique cleaning challenges:
Higher operating temperatures and pressures
Larger heat exchangers with multiple passes
More complex burner assemblies
Integrated control systems requiring specialist knowledge
Multiple safety circuits and interlocks

## Slide 43: Commercial appliance considerations
Documentation requirements
Commercial settings typically require:
More detailed service records
Compliance with site-specific safety protocols
Evidence of competency (e.g. COMCAT certification)
Risk assessments for service activities
Method statements for complex cleaning operations

## Slide 44: Commercial appliance considerations
Specialised cleaning approaches
Chemical cleaning of heat exchangers may be approved for certain commercial systems
Dedicated flushing points for heat exchanger cleaning
Ultrasonic cleaning for complex burner assemblies
Scheduled rotation of redundant systems to allow for thorough cleaning
Specialised tools for accessing confined spaces

## Slide 45: Commercial appliance considerations
Critical safety considerations
Lock-out/tag-out procedures must be followed
Confined space entry protocols for larger appliances
Higher CO and NOx emission potential requires precise verification
Multiple pressure testing points requiring systematic checking

## Slide 46: Common errors and preventative measures
Error | Consequence | Prevention measure
Incorrect electrode gap | Ignition failure, lockouts, unsafe combustion | Always use a feeler gauge to verify spacing to manufacturer specifications.
Dry condensate trap | CO leakage into dwelling, acid damage to components | Implement mandatory re-priming checklist step with visual verification.
Improper fuel effect placement | Flame impingement, sooting, CO production | Take reference photos before disassembly, follow diagrams exactly.
Inadequate combustion analysis | Undetected unsafe operation | Perform full FGA testing after any component cleaning or adjustment.
Poor documentation | Liability issues, repeat service visits | Use standardised digital forms with mandatory fields for all key checks.
Over-tightening components | Damaged threads, cracked parts, gas leaks | Use calibrated torque tools and follow manufacturer specifications.
Using incorrect cleaning agents | Material damage, health hazards, warranty voidance | Only use manufacturer-approved cleaning methods and substances.

## Slide 47: Common errors and preventative measures
Implementing a methodical approach with verification at each stage can eliminate most common servicing errors.
Consider using the "clean, check, document" mantra for each component to ensure nothing is overlooked.

## Slide 48: Summary and key takeaways
Component-specific cleaning
You should now be able to safely and effectively clean all key gas appliance components following manufacturer instructions and industry best practices, recognising the specific requirements for different appliance types.

## Slide 49: Summary and key takeaways
Critical post-cleaning verification
You have learned the essential post-cleaning checks, including visual inspection, electrode gap verification, combustion analysis, and operational testing, that ensure appliances function safely and efficiently.

## Slide 50: Summary and key takeaways
Professional documentation
You understand how to document all servicing actions, test results, and observations completely and accurately using appropriate formats to maintain compliance and demonstrate professional competence.

## Slide 51: Summary and key takeaways
Safety-first decision making
You can confidently evaluate whether an appliance is safe to return to service after cleaning, based on comprehensive testing and a thorough understanding of safety parameters and acceptable performance criteria.

## Slide 52: Summary
You should now be able to:
Apply safe and effective cleaning techniques to common gas appliance components.
Demonstrate post-cleaning checks such as combustion analysis and component reassembly.
Record service actions using standard logs and inspection templates.
Evaluate whether an appliance is safe to return to service after cleaning.

## Slide 53
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.