## Slide 1
Occupational Specialism: Gas Engineering
K1.28 Fault-finding techniques, their suitability for different situations and how they are applied in practice
PowerPoint 1.28b: Electrical fault-finding using a multimeter

## Slide 2: Starter
Today, we'll explore how to use a multimeter effectively to diagnose and solve common electrical issues in gas appliances.
"Simon reports that his boiler shows power but won't spark or ignite. The user interface lights up but nothing happens when calling for heat or hot water."
Which component might have failed?
Would you test resistance, voltage or continuity?
Where would you take your first reading?

## Slide 3: Objective
By the end of this session, you should be able to:
Identify electrical components commonly tested during fault-finding.
Use a multimeter safely for resistance, voltage and continuity checks.
Interpret readings to diagnose electrical faults.
Apply manufacturer values to verify component condition.

## Slide 4: Electrical test equipment – safety guidance
HSE GS38
Provides practical safety guidance for using electrical test equipment on low-voltage systems, emphasising the use of insulated probes, robust leads, and safe working practices to prevent electric shock and arcing.
BS EN 61010-1
Sets the design and safety standards for such equipment, ensuring it is built to withstand electrical, mechanical, and thermal risks through rigorous testing and certification. Together, they ensure safe use and reliable manufacture of electrical test tools.

## Slide 5: Common components to test
Component | Likely fault | Test type
Electrode / spark gap | No ignition | Continuity
Fan | No flue proving | Resistance
Gas valve coil | Won't open | Resistance
Thermistor (NTC) | Wrong temp or lockout | Resistance (Ω)
Switch / thermostat | No demand signal | Voltage & continuity
Fuse / PCB track | Dead circuit | Continuity

## Slide 6: Multimeter basics
Setting up your multimeter:
Set to correct function:
Ω = resistance, V = voltage, 🔔 (diode) = continuity
Always test your meter first on a known source
Set the correct range or use auto-ranging
Touch probes firmly to connection points
Ensure the appliance is safely isolated unless voltage testing

## Slide 7: Multimeter basics
Setting up your multimeter:
Set to correct function:
Ω = resistance, V = voltage, 🔔 (diode) = continuity
Always test your meter first on a known source
Set the correct range or use auto-ranging
Touch probes firmly to connection points
Ensure appliance is safely isolated unless voltage testing
A multimeter is an essential diagnostic tool that combines voltage, resistance and continuity testing functions in one device.

## Slide 8: Resistance testing (Ω)
What it measures
Resistance testing measures the opposition to current flow through a component, measured in ohms (Ω).
Thermistors
Solenoids (gas valve coils)
Fans
Electrodes

## Slide 9: Resistance testing (Ω)
Example readings
Fan winding: 70–120 Ω typical
NTC sensor: 10 kΩ at 25°C
Gas valve coil: 800-1500 Ω typical
Compare to Manufacturer's Instructions (MI)

## Slide 10: Voltage testing (AC & DC)
Used to check:
Live supply to PCB (230V AC)
Switched live output to fan or gas valve
Low-voltage components (e.g. 24V DC sensors)
Warning:
Only test voltage with power ON, must prove safe to touch first, wear PPE (insulated gloves, safety glasses), observe live testing precautions, ensure dry working conditions

## Slide 11: Continuity and switch testing
Continuity testing confirms whether a circuit path is unbroken. The multimeter emits an audible beep when continuity is present.
Used on:
Fuses
Switches (room stat, flow switch, APS)
Overheat thermostats
Electrode circuits
PCB tracks
Important: Continuity testing must ONLY be performed with the appliance powered down and safely isolated from the electricity supply.

## Slide 12: Working with Manufacturer's Instructions (MI)
MI documentation
The manufacturer will specify exact values for:
Component resistance ranges
Expected voltage outputs
Sensor response curves

## Slide 13: Working with Manufacturer's Instructions (MI)
Taking measurements
Record readings carefully under appropriate conditions:
Use the correct meter setting
Take readings at specified points
Note ambient conditions (for NTC sensors)

## Slide 14: Working with Manufacturer's Instructions (MI)
Compare and diagnose
If reading falls outside the specified range:
Component likely faulty
Check wiring connections
Consider environmental factors
Always refer to the specific manufacturer's instructions for the appliance you're working on, as values can vary significantly between models and manufacturers.

## Slide 15: NTC thermistor testing
About NTC thermistors:
Negative Temperature Coefficient (NTC) thermistors decrease in resistance as temperature increases. They're critical for monitoring and controlling boiler temperature.
Typical reading: 10 kΩ at 25°C
As the temperature rises, resistance falls
Follow the manufacturer's resistance/temperature curve
When testing, remove the thermistor from the water pipe or housing to ensure accurate ambient temperature readings, or use a temperature compensation chart.

## Slide 16: Gas valve coil testing
Test procedure
Ensure the appliance is completely isolated from the electrical supply
Disconnect wiring from gas valve
Set the multimeter to the resistance (Ω) function
Connect probes to valve coil terminals
Compare reading to the manufacturer's specification

## Slide 17: Gas valve coil testing
Typical values
Single solenoid valve: 800-1500 Ω
Dual solenoid valve:
Main coil: 800-1500 Ω
Modulating coil: 3000-6000 Ω
Zero or infinity reading indicates open/short circuit = faulty valve

## Slide 18: Fan motor testing
What to check:
Fan motors are critical for combustion air supply and flue gas removal. Testing helps diagnose issues with starting, running or speed control.
Motor winding resistance: 70-120 Ω typical
Hall effect sensor (if present): 5-15 kΩ
Voltage supply: 230V AC or specified DC voltage
Tacho feedback signal (if variable speed)

## Slide 19: Fan motor testing
A common fan fault is seized bearings, which can be identified by attempting to rotate the fan manually when cold.
Always check for physical obstructions before electrical testing.

## Slide 20: PCB and fuse testing
Fuse testing
Set the multimeter to continuity mode. A good fuse will show continuity (beep). No continuity indicates a blown fuse. Check for underlying causes before replacing.
PCB testing
Test input voltage (230V) and output voltages to components (230V or low voltage). Check for visible damage like burnt tracks or components.

## Slide 21: Electrode and flame sensing testing
Ignition electrode:
Check for continuity through the electrode
Look for cracks in ceramic insulation
Test spark gap (3-4mm typically)
Check resistance to earth (should be high)

## Slide 22: Switch and thermostat testing
Room thermostats
Test for continuity across switch contacts when calling for heat. Digital thermostats may require voltage testing of the output signal.
Limit thermostats
Should show continuity at normal temperatures. No continuity indicates the thermostat has tripped or failed. Check for underlying overheating issues.

## Slide 23: Switch and thermostat testing
Flow switches
Test for continuity when water flow is present. No continuity with flow indicates faulty switch or mechanical obstruction.
Air Pressure Switches (APS)
Test for continuity when fan is running and correct differential pressure is achieved. No continuity suggests blocked flue or faulty switch.

## Slide 24: Systematic fault-finding approach
Gather information
Understand the symptoms and when they occur. Check error codes and user operation. Review service history.
Visual inspection
Check for obvious signs of damage, loose connections, or burnt components before electrical testing.

## Slide 25: Systematic fault-finding approach
Identify potential causes
Use fault codes and symptoms to identify likely components. Review technical bulletins for known issues.
Test methodically
Test each potential component systematically. Start with simplest checks first (fuses, power supply).
Repair and verify
Replace faulty components and verify correct operation. Test full sequence of operation.

## Slide 26: Mini quiz: multimeter practice
What setting should you use to test a thermistor?
Think about what property of a thermistor changes with temperature.
What must you do before testing live voltage?
Consider safety precautions required for working with electricity.
A fan coil reads 22 Ω but MI says 80–120 Ω — what does this suggest?
Consider what electrical fault could cause this significant reduction in resistance.

## Slide 27: Safety precautions
Live testing safety
Wear appropriate PPE (insulated gloves)
Use one hand technique where possible
Ensure dry working conditions
Use insulated tools and meter probes
Verify meter operation before testing

## Slide 28: Common pitfalls to avoid
Incorrect meter settings
Always verify your multimeter is set to the correct function and range before testing. Testing resistance with a voltage setting can damage the meter.
Poor probe contact
Ensure probe tips make firm contact with test points. Oxidation or dirt can cause false readings. Clean connections before testing.

## Slide 29: Common pitfalls to avoid
Ignoring environmental factors
Temperature affects resistance readings, especially for thermistors. Account for ambient conditions when comparing to manufacturer's values.
Rushing the diagnosis
Take time to work methodically through potential causes. Jumping to conclusions can lead to unnecessary parts replacement and repeat visits.

## Slide 30: Summary
You should now be able to:
Identify electrical components commonly tested during fault-finding.
Use a multimeter safely for resistance, voltage and continuity checks.
Interpret readings to diagnose electrical faults.
Apply manufacturer values to verify component condition.

## Slide 31
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.