## Slide 1
Occupational Specialism: Gas Engineering
K1.28 Fault-finding techniques, their suitability for different situations and how they are applied in practice
PowerPoint 1.28c: Gas pressure and flow-based fault-finding

## Slide 2: Starter
Today's fault scenario
Georgia installs a new gas fire. The customer reports that the flame is weak and yellow, and it takes too long to warm the room. Georgia tested the gas rate and says it's within limits.
Consider:
What else could be causing the poor performance?
Which pressure tests could help diagnose the issue?
What role does flow rate play in this scenario?

## Slide 3: Objective
By the end of this session, you will be able to:
Explain how pressure and flow impact appliance performance.
Carry out standing, operating and burner pressure tests.
Check gas rate and flow rate using industry-standard methods.
Interpret test results to identify system faults.

## Slide 4: Pressure testing overview
Test Type | Purpose | Key Information
Standing Pressure | Verifies incoming supply pressure before ignition | All appliances off; baseline measurement
Operating Pressure | Assesses pressure during operation | Measured with appliance(s) running
Burner Pressure | Confirms internal control at appliance | Specific to each appliance model
Tightness Test | Identifies gas leaks in system | Required after work on gas system
All pressure measurements taken in millibars (mbar) using a manometer or digital pressure gauge.

## Slide 5: Standing pressure testing
Key requirements:
Measured at meter test nipple
All gas appliances must be off
Typical for Natural Gas: 20–23 mbar
LPG (Propane): 37 mbar nominal
Results must be stable and within specification
Values outside range indicate supply issues
A properly connected manometer showing standing pressure within normal range for natural gas.

## Slide 6: Operating pressure testing
Procedure
Connect manometer to meter test point
Record standing pressure first
Turn on appliance(s) at maximum rate
Record new pressure reading

## Slide 7: Operating pressure testing
Requirements
Maximum drop of 1 mbar from standing pressure (NG systems)
Must remain above the minimum required by appliance
Measurement must stabilise
Fault indications
Drop >1 mbar: Undersized pipework
Fluctuating reading: Regulator fault
Excessive drop: Restriction or blockage

## Slide 8: Burner pressure testing
Key points:
Measured at appliance test nipple (often on gas valve)
Confirms proper gas valve and burner regulation
Manufacturer's instructions (MI) must be followed
Pressure varies by appliance model and type
Readings must stabilise after burner ignition
Some modern appliances may not have test points

## Slide 9: Burner pressure testing
Fault indications:
Too low: valve fault, blockage, or regulator issue
Too high: valve adjustment error or faulty regulator
Unstable: intermittent blockage or control problem
No change: disconnected/faulty controls

## Slide 10: Gas Rate Testing (Natural Gas)
When to use
Used when burner pressure is not adjustable or when manufacturers specify gas rate rather than pressure.
Equipment required
Access to meter test dial, stopwatch, calculator, and manufacturer's instructions.

## Slide 11: Gas rate testing – practical application
Example calculation:
For a 30kW boiler with measured gas consumption of 0.01m³ over 12 seconds:
This is approximately 10% higher than the rated input – potentially indicating an issue with gas pressure or appliance adjustment.

## Slide 12: Gas rate testing – practical application
Acceptable variation:
±5% of manufacturer's stated input rate is typically acceptable
>+5%: Excessive gas consumption, inefficiency
<-5%: Potential underfiring, performance issues

## Slide 13: Flow rate and water pressure testing
Flow rate measurement
Use flow cup or measuring jug and stopwatch to determine litres per minute. Normal DHW flow rate: 8–12 L/min for most domestic systems.

## Slide 14: Flow rate and water pressure testing
Water pressure assessment
Check cold mains pressure and compare to the manufacturer's requirements. Most combi boilers require a minimum of 1-1.5 bar dynamic pressure.
Low flow rates or pressures can significantly impact performance, particularly in combi boilers and water heaters. Always check against the manufacturer's instructions.

## Slide 15: Flow rate factors
Common causes of flow rate issues:
Plate heat exchanger blockage (limescale)
Incorrect flow restrictors installed
Insufficient cold mains pressure
Partially closed isolation valves
Filter/strainer blockage
Diverter valve problems
Pipework restrictions or airlocks

## Slide 16: Flow rate factors
Testing approach:
Check cold mains flow first to establish baseline
Compare hot water flow at various outlets
Assess pressure drop across filters/strainers
Consult manufacturer's flow specifications
Consider local water hardness factors

## Slide 17: Common pressure and flow faults
Symptom | Possible Cause | Diagnostic Test
Weak yellow flame | Low burner pressure or blocked injector | Burner pressure test, injector inspection
Flame lifts/blows out | High burner pressure or incorrect air/gas mix | Burner pressure test, CO/CO₂ analysis
Poor DHW performance | Low flow rate or scaling in heat exchanger | Flow rate measurement, pressure differential test
Pressure drop >1 mbar | Undersized pipework or excessive demand | Standing vs operating pressure comparison
Intermittent operation | Fluctuating pressure or flow | Extended pressure monitoring, flow stability test

## Slide 18: Case study: Georgia’s gas fire
Customer complaint
Weak yellow flame, insufficient heat output, despite gas rate within limits.
Initial diagnostics
Burner pressure test reveals pressure at low end of acceptable range.
Further investigation
Operating pressure test shows significant drop when fire at maximum (1.8 mbar drop).

## Slide 19: Case study: Georgia’s gas fire
Root cause
22mm supply pipe reduced to 15mm, creating a restriction with a high-demand appliance.
Solution
Installation of correctly sized pipework to the fire location resolves the pressure drop.
This case demonstrates why gas rate testing alone may not identify all issues – pressure testing provides crucial additional diagnostic information.

## Slide 20: Pressure testing equipment
U-Gauge water manometer
Traditional tool for pressure measurement.
Each 10mm water column = 1 mbar.
Requires careful levelling and proper connection techniques.

## Slide 21: Pressure testing equipment
Digital manometer
Modern digital pressure gauge with direct mbar readings.
Offers higher precision and ease of use.
Many can record maximum/minimum values.
Both tools require proper connection to test points using appropriate hoses and fittings. Always check for leaks at connection points before testing.

## Slide 22: Practical: Burner pressure testing
Safety precautions:
Ensure safe isolation procedures before connecting equipment
Check for gas tightness after connecting/removing test equipment
Work in a well-ventilated area
Have appropriate tools readily available
Follow manufacturer's instructions explicitly

## Slide 23: Practical: Burner pressure testing
Procedure:
Locate appliance test point (typically on gas valve)
Loosen test point screw (don't remove completely)
Connect manometer hose securely
Zero/level manometer
Ignite appliance and set to maximum rate
Record stabilised pressure reading
Compare to manufacturer's specification

## Slide 24: Flow rate testing procedure
Select test point
Choose an appropriate outlet for testing (typically a kitchen sink or bath tap for domestic hot water systems).
Set temperature
Set the appliance to deliver hot water at normal operating temperature (typically 40–50o C).

## Slide 25: Flow rate testing procedure
Measure flow
Using a flow cup or measuring jug, time how long it takes to fill to a specific volume (e.g. 6 litres).
Calculate rate
Calculate litres per minute: Volume (L) ÷ Time (seconds) × 60 = L/min
Example: If 6 litres takes 45 seconds to collect, flow rate = 6 ÷ 45 × 60 = 8 L/min

## Slide 26: Knowledge check
Pressure drop – What is the maximum pressure drop allowed from standing to operating pressure in a natural gas system?
Burner pressure – Where is burner pressure typically measured on a gas appliance?
Flow rate issues – What does a low DHW flow rate in a combi boiler typically indicate?
Testing methods – Why would we test gas rate instead of burner pressure on some modern appliances?

## Slide 27: Knowledge check – Answers
Maximum pressure drop: 1 mbar for natural gas systems from standing to operating pressure.
Burner pressure location: At the appliance test nipple, typically located on the gas valve assembly.
Low DHW flow rate causes: Potential plate heat exchanger blockage, restrictors, or insufficient cold mains pressure.
Gas rate vs pressure testing: Many modern appliances don't have adjustable burner pressure or lack test points; manufacturers specify gas rate instead.

## Slide 28: Summary: Pressure and flow-based fault-finding
Pressure testing
Standing pressure: 20-23 mbar (NG)
Operating pressure: Max 1 mbar drop
Burner pressure: Per manufacturer specs
Use an appropriate manometer or gauge

## Slide 29: Summary: Pressure and flow-based fault-finding
Flow assessment
Gas rate formula for kW calculation
DHW flow rate: Typically 8-12 L/min
Consider local water conditions
Check against manufacturer data

## Slide 30: Summary: Pressure and flow-based fault-finding
Fault diagnosis
Systematic approach to testing
Multiple tests may be required
Document all readings accurately
Consider the system as a whole
Remember: Always consult and follow the manufacturer's instructions (MI) for specific test procedures and expected values.

## Slide 31: Summary
You should now be able to:
Measure and analyse gas pressures safely.
Check flow rate and gas rate using the correct tools.
Identify pressure or flow-related faults.
Apply MI specifications to test results.

## Slide 32
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.