## Slide 1
Occupational Specialism: Gas Engineering
K1.5 Operation and handling requirements of tools, equipment and materials
PowerPoint 1.5b: Maintenance and calibration of tools and equipment

## Slide 2: Starter
You’ve just finished testing a new gas pipe installation using a digital manometer. The tool shows a steady 21 mbar – but the tool hasn’t been calibrated for 3 years.
Quick discussion (Pairs or Group):
What might be the consequences?
Who is responsible?
What steps should have been taken before testing?

## Slide 3: Objectives
By the end of this session, you should be able to:
Describe routine inspection and maintenance procedures for gas tools.
Explain how and why tools are calibrated.
Understand how tools should be safely stored on-site and in transit.

## Slide 4: Inspection checklist – what to look for
Check for: | Why it matters
Cracked Casings | Can expose components to moisture, dirt or physical shock
Frayed Leads | Electric shock or false readings
Blocked/Dirty Sensors | Leads to inaccurate measurements
Missing Calibration Labels | May void test results and compliance
Corrosion or Loose Parts | Indicates poor storage or unsafe usage
Daily/weekly tool inspection

## Slide 5: Calibration – What, Why and When
What is calibration? Setting a measuring instrument to match an accurate standard.
Tools that need regular calibration:
Flue Gas Analysers, Digital Manometers, Gas Leak Detectors, Multimeters
Frequency: Typically once every 12 months – required for Gas Safe and most employer policies.

## Slide 6: Consequences of incorrect calibration
Issue | Result
Inaccurate Pressure or Combustion Reading | Unsafe installation – leads to gas escape or CO risk
Appliance Setup Errors | Poor performance or customer complaints
Regulatory Breach | Could be classed as Immediately Dangerous (ID) under IGEM G/11
Invalid Warranty or Evidence Trail | May result in fines, job loss, or de-registration from Gas Safe

## Slide 7: Maintenance logs and compliance
The importance of maintaining logs
Logs demonstrate due diligence in audits, assist in incident investigations, and aid in planning calibration schedules.
Essential information to document:
Tool identification and serial number
Date of inspection or calibration
Name of the engineer
Issues identified and actions taken

## Slide 8: Maintenance logs and compliance
Who oversees it?
Competent Person (as defined by HSE and Gas Safe)
Employer’s Health & Safety officer or senior engineer

## Slide 9: Equipment maintenance
Equipment type | Maintenance required
Combustion performance analyser | Calibrate annually or per MI. Incorrect readings may lead to misdiagnosis or CO safety issues.
Pressure gauges | Visually inspect for cracks or dislodged fluid. Protect from freezing and store upright.
Leak detectors | Replace batteries and test sensor response.​ Spray bottles must be stored upright and cleaned.
Cutting tools | Clean cutting wheels and lubricate pivot points.​ Store in dry conditions to prevent rust.

## Slide 10: Storage requirements (Workshop and Site)
Correct storage includes:
Dry, locked cupboards or cases (indoors or in vehicles).
Environmental protection – e.g. protect FGAs from frost or damp.
Original packaging or padded boxes for sensitive equipment.
Clearly labelled toolkits and cases.

## Slide 11: Case study – unsafe situation due to neglected equipment
Scenario
Mark is an installer who uses an FGA last calibrated 2.5 years ago. He records a “safe” combustion reading on a new boiler and signs it off.
Two days later, the appliance is flagged for dangerously high CO output during a homebuyer’s survey.
What should Mark have done before using the analyser?
How can the company prevent this in future?
What would the Gas Safe Register likely do?

## Slide 12: Summary
You should now be able to:
Describe routine inspection and maintenance procedures for gas tools.
Explain how and why tools are calibrated.
Understand how tools should be safely stored on-site and in transit.

## Slide 13
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.